| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Single hop Subscription management |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-05-10 |
| Abstract:* | The contribution proposes some Interoperability Test Descriptions for Single hop Subscription management to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution consists of some test descriptions about Single-Hop Subscription  resource management, to be included into the TS-0013.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

# Test Descriptions

## Single Hop configuration testing

### Subscription Management

#### Subscription Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE creates a remote Subscription resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.11.1 [2] 7.3.8.2.1 |
| Pre-test conditions: | AE has created an application resource <AE> on remote CSE AE has created a container resource <container> on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Subscription Create Request to create a <Subscription> resource on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI <remoteCSE>/<AE>/<container>?rty=23 Host : Registrar CSE Payload: resource <Subscription> to be created |
|  |  | CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Query: rty=23 Payload: <Subscription> resource to be created |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded POST request contains Request URI <remoteCSE>/<AE>/<container>?rty=23 Host : remote CSE Payload: Resource < Subscription > to be created |
|  |  | CoAP | Forwarded POST request contains Method: 0.02 (POST) Uri-Host: Remote CSE host Uri-Port: Remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Query: rty=23 Payload: < Subscription > resource to be created |
|  |  | MQTT |  |
| 4 |  | Verify | Check that the <Subscription> resource is created in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<Subscription> Payload: Created <Subscription> (assigned and/or modified attributes) |
|  |  | CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AE> Location-Path: <Container> Location-Path: <Subscription> |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> /<Subscription> Payload: Created <Subscription> (assigned and/or modified attributes) |
|  |  | CoAP | Registrar CSE forawards response to AE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AE> Location-Path: <Container> Location-Path: <Subscription> |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |

#### Subscription Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE retrieves a remote Subscription resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.11.2 [2] 7.3.8.2.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on remote CSE AE has created a container resource <container> on remote CSE AE has created a subscription resource <subscription> on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Subscription Retrieve Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <remoteCSE>/<AE>/<container>/<Subscription> Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded GET request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : remote CSE Payload: empty |
|  |  | CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: empty |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <Subscription> resource |
|  |  | CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.01 Payload: <Subscription> resource |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <Subscription> resource |
|  |  | CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.01 Payload: <Subscription> resource |
|  |  | MQTT |  |
| 6 |  | Verify | AE indicates successful operation |

#### Subscription Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE updates a remote Subscription resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.11.3 [2] 7.3.8.2.3 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on remote CSE AE has created a container resource <container> on remote CSE AE has created a subscription resource <subscription> on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Subscription Update Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : Registrar CSE Payload: modified <Subscription> resource |
|  |  | CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: modified <Subscription> resource |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded PUT request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : remote CSE Payload: modified <Subscription> resource |
|  |  | CoAP | Forwarded PUT request contains Method: 0.03 (PUT) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: modified <Subscription> resource |
|  |  | MQTT |  |
| 4 |  | Verify | Check that the <Subscription> resource is updated in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: modified <Subscription> (assigned and/or modified attributes) |
|  |  | CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <Subscription> (assigned and/or modified attributes) |
|  |  | CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |

#### Subscription Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE deletes a remote <Subscription> resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.11.4 [2] 7.3.8.2.4 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on remote CSE AE has created a container resource <container> on remote CSE AE has created a subscription resource <subscription> on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Subscription delete request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded DELETE request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : Remote CSE Payload: empty |
|  |  | CoAP | Forwarded DELETE request contains Method: 0.04 (DELETE) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: empty |
|  |  | MQTT |  |
| 4 |  | Verify | Check that the <Subscription> resource is deleted from remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | CoAP | Registrar CSE Forwards response to AE containing: Response Code = 2.05 |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |

============== == End of  1st Part: Proposed Test Descriptions ==================