| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Single hop Discovery management |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-05-10 |
| Abstract:* | The contribution proposes some Interoperability Test Descriptions for Single hop Discovery test to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution consists of some test descriptions about Single-Hop Discovery resource management, to be included into the TS-0013.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

# Test Descriptions

## Single Hop configuration testing

### Discovery

#### Discovery of all resources

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE discovers resources located in remote CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a discovery request to discover all resources located in remote CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <remoteCSE>?fu=1 Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded GET request contains Request URI <remoteCSE>?fu=1 Host : remote CSE Payload: empty |
|  |  | CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Payload: empty |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: addresses of all the found resources |
|  |  | CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 Payload: addresses for all the found resources |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: addresses for all the found resources |
|  |  | CoAP | Registrar sends response containing: Response Code = 2.05 Payload: addresses for all the found resources. |
|  |  | MQTT |  |
| 6 |  | Verify | AE indicates successful operation |

#### Discovery with label filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE discovers resources located in remote CSE using label filter criteria |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created a Container resource <Container> having "key1" as label on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a discovery request to discover the <AE> resource using label filter criteria in remote CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <remoteCSE>?fu=1&lbl=key1 Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lbl=key1 Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded GET request contains Request URI <remoteCSE>?fu=1&lbl=key1 Host : remote CSE Payload: empty |
|  |  | CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lbl=key1 Payload: empty |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: address of the <AE> resource |
|  |  | CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 Payload: address of the <AE> resource |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: address of the <Container> resource |
|  |  | CoAP | Registrar sends response to AE containing: Response Code = 2.05 Payload: address of the <Container> resource |
|  |  | MQTT |  |
| 6 |  | Verify | AE indicates successful operation |

#### Discovery with limit filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE discovers resources located in remote CSE using the limit filter criteria |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a discovery request to discover at most 2 resources in remote |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <remoteCSE>?fu=1&lim=2 Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lim=2 Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded GET request contains Request URI <remoteCSE>?fu=1&lim=2 Host : remote CSE Payload: empty |
|  |  | CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lim=2 Payload: empty |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: at most 2 addresses of the found resources |
|  |  | CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 Payload: at most 2 addresses of the found resources |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: at most 2 addresses of the found resources |
|  |  | CoAP | Registrar sends response to AE containing: Response Code = 2.05 Payload: at most 2 addresses of the found resources |
|  |  | MQTT |  |
| 6 |  | Verify | AE indicates successful operation |

#### Discovery with multiple filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE discovers resources located in remote CSE using multiple filter criteria |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created a Container resource <Container> having as labels "key1" and "key2" on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request to discover the <Container> resource using multiple filter criteria |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <remoteCSE>?fu=1&lbl=key1&lbl=key2&lim=1 Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lbl=key1 Uri-Query: lbl=key2 Uri-Query: lim=1 Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded GET request contains Request URI <remoteCSE>?fu=1&lbl=key1&lbl=key2&lim=1 Host : remote CSE Payload: empty |
|  |  | CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lbl=key1 Uri-Query: lbl=key2 Uri-Query: lim=1 Payload: empty |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: address of the <Container> resource |
|  |  | CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 Payload: address of the <Container> resource |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: address of the <Container> resource |
|  |  | CoAP | Registrar sends response to AE containing: Response Code = 2.05 Payload: address of the <Container> resource |
|  |  | MQTT |  |
| 6 |  | Verify | AE indicates successful operation |

============== == End of  1st Part: Proposed Test Descriptions ==================