| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Correct No-Hop Discovery test |
| Source:* | Mahdi Ben Alaya - LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-05-10 |
| Abstract:* | The contribution proposes some corrections for No hop Discovery testing |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution consists of some corrections for No-Hop Discovery resource management, to be included into the TS-0013.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

# Test Descriptions

## No Hop configuration testing

### Discovery

#### Discovery of all resources

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_14 |
| Objective: | AE discovers resources residing in Registrar CSE |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a discovery request to discover all accessible resources located in Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>?fu=1 Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: fu=1 Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Data object containing addresses of all the found resources. |
|  |  | CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Data object containing addresses of all the found resources. |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### Discovery with label filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_15 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using the label filter criteria |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Container resource <Container> having "key1" as label on Registrar CSE . |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request in order to discover the <AE> resource using the label filter criteria |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>?fu=1&lbl=key1 Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: fu=1 Uri-Query: lbl=key1 Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Data object containing address of <Container> |
|  |  | CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Data object containing address of <Container> |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### Discovery with limit filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_16 |
| Objective: | AE discovers accessible resources residing in Registrar CSE limiting the number of matching resources to the specified value. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request in order to discover at most 2 resources in registrar CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>?fu=1&lim=2 Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: fu=1 Uri-Query: lim=2 Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Trunked Data object containing only 2 addresses of found resources. |
|  |  | CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Data object containing only 2 addresses of found resources |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### Discovery with multiple filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_17 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using multiple Filter Criteria |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created a Container resource <Container> having "key1" and "key2" as labels in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request in order to discover resources located in Registrar CSE using multiple filter criteria |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>?fu=1&lbl=key1&lbl=key2&lim=1 Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: fu=1 Uri-Query: lbl=key1 Uri-Query: lbl=key2 Uri-Query: lim=1 Payload: empty |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Data object containing address of <Container> |
|  |  | CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Data object containing Address of <Container> |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

============== == End of  1st Part: Proposed Test Descriptions ==================