| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Test non blocking asynchronous requests for container |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-05-03 |
| Abstract:* | Testing of non blocking asynchronous requests for container resource. |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes Testing of non blocking asynchronous requests for retrieve, create, update and delete operations of container resource.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

## Non blocking configuration testing

### Asynchronous request

### Container management

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE retrieves a container resource using non blocking asynchronous request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a <Container> resource on registrar CSE. AE is reachable on the URI: "AE-Notification-URI" |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking asynchronous request to retrieve the <Container> resource in registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI: <CSEBase>/<Container>?rt=2 Host : registrar CSE X-M2M-RTU: AE-Notification-URI |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=2 oneM2M-RTURI: AE-Notification-URI |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <Request> resource |
|  |  | CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload: Reference to the created <Request> resource |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  | Verify | Registrar CSE sends notify request to AE |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: AE-Notification-URI Host : AE Payload: Notification data object. |
|  |  | CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: AE host Uri-Port: AE port Uri-Path: AE-Notification-URI Payload: Notification data object. |
|  |  | MQTT |  |
| 7 | Check Mca | Primitive |  |
|  |  | HTTP | AE sends notify response to Registrar CSE containing: Code = 200 |
|  |  | CoAP | AE sends notify response to Registrar CSE containing: Response Code= 2.05 |
|  |  | MQTT |  |
| 8 |  | Verify | Registrar CSE indicates successful operation |

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE creates a Container resource using non blocking asynchronous request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE is reachable on the URI: "AE-Notification-URI" |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking asynchronous request to create the <Container> resource in registrar CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: <CSEBase>?rt=2&rty=3 Host : registrar CSE X-M2M-RTU: AE-Notification-URI |
|  |  | CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: rt=2 Uri-Query: rty=3 oneM2M-RTURI: AE-Notification-URI |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <Request> resource |
|  |  | CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload <Request> reference |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  | Verify | Registrar CSE sends notify request to AE |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: AE-Notification-URI Host : AE Payload: Notification data object |
|  |  | CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: AE host Uri-Port: AE port Uri-Path: AE-Notification-URI Payload: Notification data object |
|  |  | MQTT |  |
| 7 | Check Mca | Primitive |  |
|  |  | HTTP | AE sends notify response to Registrar CSE containing: Code = 200 |
|  |  | CoAP | AE sends notify response to Registrar CSE containing: Response Code= 2.05 |
|  |  | MQTT |  |
| 8 |  | Verify | Registrar CSE indicates successful operation |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE updates a Container resource using non blocking asynchronous request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a Container resource <Container> on registrar CSE AE is reachable on the URI: "AE-Notification-URI" |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking asynchronous request to update the <Container> resource in registrar CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request method = PUT Request URI: <CSEBase>/<Container>?rt=2 Host : registrar CSE X-M2M-RTU: AE-Notification-URI |
|  |  | CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=2 oneM2M-RTURI: AE-Notification-URI |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <Request> resource |
|  |  | CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload <Request> reference |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  | Verify | Registrar CSE sends notify request to AE |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: AE-Notification-URI Host : AE Payload: Notification data object |
|  |  | CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: AE host Uri-Port: AE port Uri-Path: AE-Notification-URI Payload: Notification data object |
|  |  | MQTT |  |
| 7 | Check Mca | Primitive |  |
|  |  | HTTP | AE sends notify response to Registrar CSE containing: Code = 200 |
|  |  | CoAP | AE sends notify response to Registrar CSE containing: Response Code= 2.05 |
|  |  | MQTT |  |
| 8 |  | Verify | Registrar CSE indicates successful operation |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE deletes a Container resource using non blocking asynchronous request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a Container resource <Container> on registrar CSE AE is reachable on the URI: "AE-Notification-URI" |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking asynchronous request to delete the <Container> resource in registrar CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request method = DELETE Request URI: <CSEBase>/<Container>?rt=2 Host : registrar CSE X-M2M-RTU: AE-Notification-URI |
|  |  | CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=2 oneM2M-RTURI: AE-Notification-URI |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <Request> resource |
|  |  | CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload <Request> reference |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  | Verify | Registrar CSE sends notify request to AE |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: AE-Notification-URI Host : AE Payload: Notification data object |
|  |  | CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: AE host Uri-Port: AE port Uri-Path: AE-Notification-URI Payload: Notification data object |
|  |  | MQTT |  |
| 7 | Check Mca | Primitive |  |
|  |  | HTTP | AE sends notify response to Registrar CSE containing: Code = 200 |
|  |  | CoAP | AE sends notify response to Registrar CSE containing: Response Code= 2.05 |
|  |  | MQTT |  |
| 8 |  | Verify | Registrar CSE indicates successful operation |

============== == End of  1st Part: Proposed Test Descriptions ==================