| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Review and update of test descriptions from stage-3 perspective |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Josef Blanz, Qualcomm jblanz@qti.qualcomm.com |
| Date:* | 2015-05-10 |
| Abstract:* | This contribution shall reflect the required updates to the test descriptions in clause 8 of TS-0013 after review from stage-3 (PRO WG) perspective. Focus of this contribution is on primitives parameters and mappings when using HTTP binding. |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update clause 8 of TS-0013 with the proposed changes |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution reviews the current test descriptions and includes the required updates from stage-3 perspective, with focus on HTTP binding.

Note that this initial version of this contribution is incomplete. It just shows an example of required changes. The more complete changes of test descriptions will be included into a revision of this contribution.

- Proposal

================ Start of  proposed  text changes ==================

# 8	Test Descriptions

Editor’s Note: The content of this section can be modified according to the progress of this TS.

## No Hop configuration testing

### CSEBase Management

#### CSEBase Retrieve on Mca

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_01 |
| Objective: | AE retrieves the CSEBase resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.3.2 [2] 7.3.2 |
| Pre-test conditions: | CSEBase resource has been automatically created in CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a retrieve Request to CSE |
| 2 | Check Mca | Primitive | Operation (op) = 2 (Retrieve) To (to) = URI of requested <CSEBase> resource From (from) = AE-ID Request Identifier (rqi) = (token-string) |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI <CSEBase> Host : registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive | Response Status Code (rcs) = 2000 Request Identifier (rqi) = same string as received in request message Content (pc) = XML or JSON serialized representation of <CSEBase> resource |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 X-M2M-RSC: 2000 X-M2M-RI: (same token-string as in HTTP request) Content-Type; application/vnd.onem2m-res+xml; ty=5 or application/vnd.onem2m-res+json; ty=5 Payload: <CSEBase> resource as XML or JSON serialzed object |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  |  | Repeat step 1-5 creating container resource with short lifetime |
| 7 |  |  | Check the created resource is removed after the expiry of its lifetime |

### Application Entity Registration

#### AE Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_03 |
| Objective: | AE registers to its registrar CSE via an AE Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.1 [2] 7.3.4.2.1 |
| Pre-test conditions: | Void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a AE Create request to register to the Registrar CSE |
| 2 | Check Mca | Primitive | Operation (op) = 1 (Create) To (to) = URI of registrar CSE From (from) = AE-ID (optional) Request Identifier (rqi) = (token-string) Resource Type (ty) = 2 (AE) Content (pc) = XML or JSON serialized representation of <AE> resource attributes |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: <RegistrarCSE> Host : Registrar CSE Content-Type: application/vnd.onem2m-res+xml; ty=2 or application/vnd.onem2m-res+json; ty=2 Payload: attributes of <AE> resource to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <AE> resource is created in registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) Content-Location : <RegistrarCSE>/<AE> Payload: created <AE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### AE Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_04 |
| Objective: | AE retrieves <AE> resource via an AE Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.2 [2] 7.3.4.2.2 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an application Retrieve Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI : <CSEBase>/<AE> Host : registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code =200 Payload: <AE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### AE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_05 |
| Objective: | AE updates attribute in <AE> resource via an AE Update Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.3 [2] 7.3.4.2.3 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Update Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request method = PUT Request URI : <CSEBase>/<AE> Host : registrar CSE Payload: modified <AE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <AE> resource has been updated in registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: updated <AE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### AE Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_16 |
| Objective: | AE de-registers by deleting <AE> resource via an AE Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.4 [2] 7.3.4.2.4 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Delete Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request method = DELETE Request URI : <CSEBase>/<AE> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <AE> resource has been removed in registrar CSE. |
| 5 |  | Verify | AE indicates successful operation |

### Container Management

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_07 |
| Objective: | AE creates a container resource in registrar CSE via a container Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request to create container <container> |
| 2 | Check Mca | Primitive | Sent CREATE request contains To: <CSEBase>/<AE>?rty=container Fr: AE-ID Cn: container resource <container> to be created |
|  |  | HTTP | Sent POST request contains Request URI <CSEBase>/<AE>?rty=container Host : Registrar CSE Payload: container resource <container> to be created Content-Type= media-type |
|  |  | CoAP | Sent POST request contains Code = 2(POST) Uri-Path: <CSEBase> Uri-Path: <AE>?rty=container Payload: container resource <container> to be created Content Type option |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <container> resource is created in registrar CSE. |
| 4 | Check Mca | Primitive | Registrar sends response containing: To: AE-ID Fr: CSE-ID Cn: Created <container> |
|  |  | HTTP | Registrar sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container> Payload: Created <container> |
|  |  | CoAP | Registrar sends response containing: Code = 2.01 (2001 Created) Location-Path: <CSEBase> Location-Path: <AE> Location-Path: <contaner> The same Message ID as that of the previous request |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |
| 6 |  |  | Repeat step 1-5 creating container resource with short lifetime |
| 7 |  |  | Check the created resource is removed after the expiry of its lifetime |

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_08 |
| Objective: | AE retrieves information of a container resource via a container Retrieve Request (GET) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | A container resource <container> has been created in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Retrieve Request for resource <container> |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>/<AE>/<container> Host : Registar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: updated <AE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_09 |
| Objective: | AE updates attribute in application resource via a container Update Request (PUT) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | a container resource <container> has been created in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an container Update Request to update the lifetime of the resource. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Payload: modified <container> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <container> resource has been updated in registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Updated <container> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_10 |
| Objective: | AE deletes a specific container resource via a container Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | AE has created a container resource <container> in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an Container Delete Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registar CSE sends response containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <container > resource has been removed in registrar CSE. |
| 5 |  | Verify | AE indicates successful operation |

### ContentInstance Management

#### ContentInstance Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_11 |
| Objective: | AE adds a contentInstance resource <contentInstance> to a specific container in Registrar CSE via a contentInstance Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.2 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a contentInstance Create Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI <CSEBase>/<AE>/<container> ?rty=contentInstance Host : Registrar CSE Payload: ContentInstance resource <contentInstance> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <contentInstance> resource is created in registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Content-Location : CSEBase>/<AE>/<container>/<contentInstance> Payload: <contentInstance> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### ContentInstance Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_12 |
| Objective: | AE retrieves information of a contentInstance resource via a container Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.2 [2] 7.3.6.2.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE AE has created a contentInstance resource <contentInstance> residing under the <container> resource. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | App is requested to send a containerRetrieveRequest for retrieving the attributes/meta-data and the opaque data of a <contentInstance> resource |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>/<AE>/<container>/<contentInstance> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: <contentInstance> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  |  | Repeat steps 1-4 using <latest> instead of <contentInstance> to get the latest contentInstance. |
| 6 |  |  | Repeat steps 1-4 using <oldest> instead of <contentInstance> to get the oldest contentInstance. |

#### Content Instance Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_13 |
| Objective: | AE deletes contentInstance resource via a container Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.4 [2] 7.3.6.2.4 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE AE has created a contentInstance resource <contentInstance> residing under the <container> resource. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a contentInstance Delete Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI <CSEBase>/<AE>/<container>/<contentInstance> Host : registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <contentInstance> resource has been removed in registrar CSE. |
| 5 |  | Verify | AE indicates successful operation |

### Discovery

#### Discovery of all resources

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_14 |
| Objective: | AE discovers resources residing in Registrar CSE |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to initiate a procedure in order to discover resources under resource /discovery located in Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>/discovery Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Discovery resource including references to all resources residing in Registrar CSE |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### Discovery with Filter Criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_15 |
| Objective: | AE discovers resources residing in Registrar CSE using specific Filter criteria |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE with labels =key1 |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery procedure in order to discover resources under a known resource /discovery located in Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>/discovery?labels=key1 Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Discovery resource including references to <AE> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### Discovery with limit condition

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_16 |
| Objective: | AE discovers resources residing in Registrar CSE limiting the number of matching resources to the specified value. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | App is requested to send a DiscoveryRetrieveRequest in order to discover resources under resource /discovery located in localCSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>/discovery?limit =2 Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload Payload: Trunked Discovery resource including only 2 resource references |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### Discovery with multiple parameters

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_17 |
| Objective: | AE discovers resources residing in Registrar CSE using multiple Filter Criteria |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE with labels=key1 and labels =key2 |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | App is requested to send a Discovery procedure in order to discover resources under resource <discovery> located in Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>/<discovery>?labels =key1 &labels=key2&sizeBelow=1& filterUsage =discovery Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Discovery resource including a reference to <AE> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

### Subscription Management

#### Subscription Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_18 |
| Objective: | AE creates a subscription to Application Entity resource via subscription Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.2 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an application resource <AE> on registrar CSE AE has created a container resource <container> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a subscriptionCreateRequest |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI: <CSEBase>/<AE>/<container> ?rty=subscription Host : Registrar CSE Payload: subscription <subscription> resource to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <subscription> resource is created in Registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container>/ <subscription> Payload: Created < subscription > resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### Subscription Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_19 |
| Objective: | AE retrieves information about a subscription via subscription Retrieve Request such as expirationTime, labels, etc… |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.3 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a subscription Retrieve Request for retrieving information about a subscription <subscription> |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: <subscription> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### Subscription Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_20 |
| Objective: | AE updates information about a subscription via subscription Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.4 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a subscription Retrieve Request to update the lifetime of the resource. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: Modified <subscription> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <subscription> resource is updated in Registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Modified <subscription> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### Subscription Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_21 |
| Objective: | AE cancels subscription via an subscription Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.5 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a subscription Delete Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: Empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <subscription> resource has been removed in registrar CSE. |
| 5 |  | Verify | AE indicates successful operation |

### accessControlPolicy Management

#### accessControlPolicy Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_22 |
| Objective: | AE creates an accessControlPolicy resource |
| Configuration: | M2M_CFG_01, |
| References: | [1] 10.2.21.1 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an accessControlPolicy Create Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI <CSEBase>/<AE>?rty= accessControlPolicy Host : Registrar CSE Payload: application resource <accessControlPolicy> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <accessControlPolicy> resource is created in Registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<AE>/<accessControlPolicy> Payload: created <accessControlPolicy> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### accessControlPolicy Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_23 |
| Objective: | AE retrieves accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.2 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a accessControlPolicy Retrieve request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI <CSEbase>/<AE>/<accessControlPolicy> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code =200 Payload: <accessControlPolicy> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### accessControlPolicy Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_24 |
| Objective: | AE updates attribute in accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.3 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an accessControlPolicy Update request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request method = PUT Request URI <CSEbase>/<AE>/<accessControlPolicy> Host : Registrar CSE Payload: modified <accessControlPolicy> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <accessControlPolicy> resource is updated in Registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: updated <accessControlPolicy> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### accessControlPolicy Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_25 |
| Objective: | AE deletes accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.4 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an accessControlPolicy Delete request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request method DELETE Request URI <CSEBase>/<AE>/ <accessControlPolicy> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <accessControlPolicy> resource has been removed in registrar CSE. |
| 5 |  | Verify | AE indicates successful operation |

#### Unauthorized operation (Insufficient Access Rights)

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_26 |
| Objective: | AE delete request is rejected due to accessControlPolicy |
| Configuration: | M2M_CFG_01 |
| References: | [1] [2] ] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource < acp1> under <AE> on Registrar CSE, which forbids to delete container AE has created a container resource <container> in application <AE>, using the access right <acp1> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Delete Request for resource <container> |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 403 (Forbidden operation) Payload: ??? |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <container> resource has not been removed in registrar CSE. |
| 5 |  | Verify | AE indicates unsuccessful operation (Delete error – no privilege) |

### Group Management

#### Group Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_27 |
| Objective: | AE creates a group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.2 [2] 7.3.12.2.1 |
| Pre-test conditions: | void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a group Create Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI <CSEBase>?rty=group Host : Registrar CSE Payload: Group resource <group> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <group> resource is created in Registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<group> Payload: created <group> resource representation |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### Group Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_28 |
| Objective: | AE retrieves group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.3 [2] 7.3.12.2.2 |
| Pre-test conditions: | AE has created a Group resource <group> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a group Retrieve Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI <CSEBase>/<group> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code =200 Payload: <group> resource representation |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### Group Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_29 |
| Objective: | AE updates attribute in group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.4 [2] 7.3.12.2.3 |
| Pre-test conditions: | AE has created a group resource <group> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a group Update Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request method = PUT Request URI <CSEBase>/<group> Host : Registrar CSE Payload: modified group resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <group> resource is updated in Registrar CSE.. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: updated <group> resource representation |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### Group Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_30 |
| Objective: | AE deletes group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.5 [2] 7.3.12.2.4 |
| Pre-test conditions: | AE has created a group resource <group> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a group Delete Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request method = DELETE Request URI <CSEBase>/<group> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <group> resource is deleted in Registrar CSE. |
| 5 |  | Verify | AE indicates successful operation |

## Single hop configuration testing

### remoteCSE Management

#### remoteCSE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | Registree CSE registers to Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.1 [2] 7.3.3.2.1 |
| Pre-test conditions: | Void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Create request to register to the Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: <RegistrarCSE>?rty=remoteCSE Host : Registrar CSE Content Type option Payload: <remoteCSE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the remoteCSE resource is created in registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) Content-Location : <RegistrarCSE>/ <remoteCSE> Payload: created <remoteCSE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | Check if possible that the remoteCSE resource is created in registree CSE. |
| 6 |  | Verify | Registree CSE and Registrar CSE indicate successful operation |

#### remoteCSE Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_02 |
| Objective: | Registree CSE retrieve remoteCSE resource from Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.2 [2] 7.3.3.2.2 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Retrieve request to the Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) Payload: <remoteCSE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Registree CSE indicates successful operation |

#### remoteCSE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_03 |
| Objective: | MN-CSE registers to IN-CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.3 [2] 7.3.3.2.3 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Update request to the Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request method = PUT Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Content Type option Payload: modified <remoteCSE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the remoteCSE resource has been updated in registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 Content-Location <RegistrarCSE>/<remoteCSE> Payload: updated <remoteCSE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | Check if possible that the remoteCSE resource is also updated in registree CSE. |
| 6 |  | Verify | Registree CSE and Registrar CSE indicate successful operation |

#### remoteCSE Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_04 |
| Objective: | MN-CSE cancels registration to IN-CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.4 [2] 7.3.3.2.4 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Update request to the Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request method = DELETE Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the remoteCSE resource has been removed in registrar CSE. |
| 5 |  | Verify | Check if possible that the remoteCSE resource is also removed in registree CSE. |
| 6 |  | Verify | Registree CSE and Registrar CSE indicate successful operation |

### AE Management

#### AE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_02 |
| Objective: | AE creates a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.1.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Create Request to create an AE <AE> on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI <remoteCSE>?rty=AE Host : Registrar CSE Payload: resource <AE> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded POST request contains Request URI <remoteCSE>?rty=AE Host : remote CSE Payload: Resource <AE> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <AE> resource is created in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE> Payload: Created <AE> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: containing: Code = 201 Content-Location : <remoteCSE>/<AE> Payload: Created <AE> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the created resource is removed after the expiry of its lifetime |

#### AE Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_03 |
| Objective: | AE retrieves a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a AE Retrieve Request for resource <AE> |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <remoteCSE>/<AE> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded GET request contains Request URI <remoteCSE>/<AE> Host : remote CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <AE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <AE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 |  | Verify | AE indicates successful operation |

#### AE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_04 |
| Objective: | AE updates a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Update Request to update the resource. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request URI <remoteCSE>/<AE> Host : Registrar CSE Payload: modified <AE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded PUT request contains Request URI < remoteCSE >/<AE> Host : remote CSE Payload: modified <AE>resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <AE> resource is updated in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: modified <AE> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <AE> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |

#### AE Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_05 |
| Objective: | AE deletes a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Delete Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI <remoteCSE>/<AE> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded DELETE request contains Request URI <remoteCSE>/<AE> Host : Remote CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 |  | Verify | Check if possible that the <AE> resource is deleted in remote CSE. |
| 7 |  | Verify | AE indicates successful operation |

### Container Management

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | AE creates a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request to create container <container> on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI <remoteCSE>/<AE>?rty=container Host : Registrar CSE Payload: resource <container> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded POST request contains Request URI <remoteCSE>/<AE>?rty=container Host : remote CSE Payload: resource <container> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <container> resource is created in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to Registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |
| 8 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 9 |  | Verify | Check the created resource is removed after the expiry of its lifetime |

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_02 |
| Objective: | AE retrieves a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in < AE> in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Retrieve Request for resource <container> |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI <remoteCSE>/<AE>/<container> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded GET request contains Request URI <remoteCSE>/<AE>/<container> Host : remote CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <container> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <container> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 |  | Verify | AE indicates successful operation |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_03 |
| Objective: | AE updates a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in < AE> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Update Request to update the resource. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request URI <remoteCSE>/<AE>/<container> Host : Registrar CSE Payload: modified resource <container> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded PUT request contains Request URI <remoteCSE>/<AE>/<container> Host : remote CSE Payload: modified <container> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <container> resource is updated in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: modified <container> resource (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <container> resource (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_04 |
| Objective: | AE delete a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in < AE> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Delete Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI <remoteCSE>/<AE>/<container> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded DELETE request contains Request URI <remoteCSE>/<AE>/<container> Host : Remote CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 |  | Verify | Check if possible that the <container> resource is deleted in remote CSE.. |
| 7 |  | Verify | AE indicates successful operation |

### ContentInstance Management

#### ContentInstance Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_06 |
| Objective: | AE creates a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.2 [2] 7.3.7.2.1 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in <AE> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a ContentInstance Create Request to create a ContentInstance <contentInstance> on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI : <remoteCSE>/<AE>/<container> ?rty=contentInstance Host : Registrar CSE Payload: resource <contentInstance> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded POST request contains Request URI : <remoteCSE>/<AE>/<container>?rty=contentInstance Host : remote CSE Payload: resource <contentInstance> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <ContentInstance> resource is created in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<contentInstance> Payload: Created <contentInstance> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<contentInstance> Payload: Created <ContentInstance> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |
| 8 |  |  | Repeat step 1-7 creating ContentInstance resource with short lifetime |
| 9 |  | Verify | Check the created resource is removed after the expiry of its lifetime |

#### ContentInstance Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_07 |
| Objective: | AE retrieves a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.3 [2] 7.3.7.2.2 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in <AE> Resource <contentInstance> has been created in <container> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a ContentInstance Retrieve Request for resource <ContentInstance> |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI : <remoteCSE>/<AE>/<container>/<contentInstance> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded GET request contains Request URI <remoteCSE>/<AE>/<container>/<contentInstance> Host : remote CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <contentInstance> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <contentInstance> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 |  | Verify | AE indicates successful operation |

#### ContentInstance Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_09 |
| Objective: | AE deletes a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.5 [2] 7.3.7.2.4 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in <AE> Resource <contentInstance> has been created in <container> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a ContentInstance Delete Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI : <remoteCSE>/<AE>/<container>/<contentInstance> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded DELETE request contains Request URI : <remoteCSE>/<AE>/<container>/<contentInstance> Host : Remote CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 |  | Verify | Check if possible that the <contentInstance> resource is deleted in remote CSE. |
| 7 |  | Verify | AE indicates successful operation |

### Container Announce

#### Container Create with announceTo

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE creates a container resource and announces it to a remote CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE AE is registered to Registrar-CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request and announce the container |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI <Registrar-CSE>?rty=cnt Host : Registrar CSE Payload: resource <container> to be created (payload includes announeTo attribute with value <Hosting-CSE> and announcedAttribute with value of <announcable attribute> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Send POST request contains Request URI <Hosting-CSE>?rty=cntA Host : Hosting-CSE Payload: Resource <containerAnnc> to be created with <announcable attribute> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <containerAnnc> resource is created in Hosting-CSE with the <announcable attribute> |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <Hosting-CSE>/<containerAnnc> Payload: Created <containerAnnc> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE responds to AE containing: Code = 201 Content-Location : < Registrar-CSE >/<container> Payload: Created <container> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |
| 8 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 9 |  | Verify | Check the created resource is removed after the expiry of its lifetime. Check that the announced resource is removed after the expiry of its lifetime. |

#### Container Retrieve Announced Resource Information

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE retrieves announced container resource information |
| Configuration: | M2M_CFG_04 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | CSE1 is registered to CSE2 Resource <container1> has been created in CSE1 Resource <container1Annc> has been created in CSE2 AE2 is registered to CSE2 |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE2 is requested to send a container Retrieve Request for resource <container1Annc> |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request URI < CSE2>/<container1annc> Host : CSE2 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | CSE2 sends response to AE2 containing: Code = 200 Payload: <containerAnnc> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | AE2 indicates successful operation |
| 5 |  | Stimulus | AE2 is requested to send a Retrieve Request for resource <container1Annc> with Result Content set to “original-resource” |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | AE2 sends GET request containing: Request URI <CSE2>/<container1Annc> Result Content “original-resource” Host : CSE2 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 | Check Mcc | Primitive |  |
|  |  | HTTP | CSE2 forwards GET request to CSE1 containing: Request URI <CSE1>/<container1> Host : CSE1 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 8 | Check Mcc | Primitive |  |
|  |  | HTTP | CSE1 sends response to CSE2 containing: Code = 200 Payload: <container1> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 9 | Check Mca | Primitive |  |
|  |  | HTTP | CSE2 forwards response to AE2 containing: Code = 200 Payload: <container> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 10 |  | Verify | AE2 indicates successful operation |

#### Container Update AnnounceTo Attribute

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE announces container to a remote CSE by updating announceTo resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE Resource <container> has been created on Registrar-CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Update Request to update the resource. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request URI <Registrar-CSE> Host : Registrar CSE Payload: resource <container> containing announceTo attribute with value <Hosting-CSE> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Send POST request contains Request URI <Hosting-CSE>?rty=cntA Host : Hosting-CSE Payload: Resource <containerAnnc> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <containerAnnc> resource is created in Hosting-CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <Hosting-CSE>/<containerAnnc> Payload: Created <containerAnnc> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <container> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |
| 8 |  | Stimulus | AE is requested to send an container Update Request (PUT) to update the resource. |
| 9 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request URI <Registrar-CSE> Host : Registrar CSE Payload: resource <container> containing announceTo attribute with value empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 10 | Check Mcc | Primitive |  |
|  |  | HTTP | Send DELETE request contains Request URI <Hosting-CSE> Host : Hosting-CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 11 |  | Verify | Check if possible that the <containerAnnc> resource is deleted in Hosting-CSE. |
| 12 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 13 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <container> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 14 |  | Verify | AE indicates successful operation |

#### Container Delete AnnounceTo

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE deletes an container resource and de-announces it from a remote CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE Resource <container> has been created on Registrar-CSE Resource <containerAnnc> has been created in Hosting-CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an container Delete Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI <Registrar-CSE>/<container> Host : Registrar CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request URI < Hosting-CSE >/<containerAnnc> Host : Hosting-CSE Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: empty |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 |  | Verify | Check if possible that the <containerAnnc> resource is deleted in Hosting-CSE and <container> resource is deleted in Registrar-CSE |
| 7 |  | Verify | AE indicates successful operation |

================ End of  proposed  text changes ==================

# Comments

Is there payload ???