| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Multi-hop Container management |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-03-04 |
| Abstract:* | The contribution proposes some Interoperability Test Descriptions for Multi-hop Container management to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution consists of some test descriptions about Multi-Hop container resource management, to be included into the TS-0013.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

# Test Descriptions

## Multi Hop configuration testing

### Container Management

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_01 |
| Objective: | AE creates a container resource in remote CSE |
| Configuration: | M2M_CFG_06 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Request to create a container resource <container> on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent request contains Method: POST Request URI <remoteCSE>?rty=3 Host : Registrar CSE Payload: <container> resource to be created |
|  |  | CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: rty=3 Payload: <container> resource to be created |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Registrar CSE forwards request to transit CSE containing: Method: POST Request URI <remoteCSE>?rty=3 Host : transit CSE Payload: <container> resource to be created |
|  |  | CoAP | Registrar CSE forwards request to transit CSE containing: Method: 0.02 (POST) Uri-Host: transit CSE host Uri-Port: transit CSE port Uri-Path: <remoteCSE> Uri-Query: rty=3 Payload: <container> resource to be created |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Transit CSE forwards request to remote CSE containing: Method: POST Request URI <remoteCSE>?rty=3 Host : remote CSE Payload: <container> resource to be created |
|  |  | CoAP | Transit CSE forwards request to remote CSE containing: Method: 0.02 (POST) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: rty=3 Payload: <container> resource to be created |
|  |  | MQTT |  |
| 5 |  | Verify | Check if possible that the <container> resource is created in remote CSE. |
| 6 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to transit CSE containing: Code = 201 Content-Location : <remoteCSE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | CoAP | Remote CSE sends response to transit CSE containing: Response Code: 2.01 Location-Path: <remoteCSE> Location-Path: <container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | MQTT |  |
| 7 | Check Mcc | Primitive |  |
|  |  | HTTP | Transit CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | CoAP | Transit CSE sends response to registrar CSE containing: Response Code: 2.01 Location-Path: <remoteCSE> Location-Path: <container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | MQTT |  |
| 8 | Check Mca | Primitive |  |
|  |  | HTTP | transit CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | CoAP | transit CSE forwards response to AE containing: Response Code: 2.01 Location-Path: <RemoteCSE> Location-Path: <container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | MQTT |  |
| 9 |  | Verify | AE indicates successful operation |

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_02 |
| Objective: | AE retrieves a container resource in remote CSE |
| Configuration: | M2M_CFG_06 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | AE has created a Container resource <container> on remote CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Request to retrieve a container resource <container> on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent request contains Method: GET Request URI <remoteCSE>/<Container> Host : Registrar CSE Payload: Empty |
|  |  | CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Registrar CSE forwards request to transit CSE containing: Method: GET Request URI <remoteCSE>/<Container> Host : transit CSE Payload: Empty |
|  |  | CoAP | Registrar CSE forwards request to transit CSE containing: Method: 0.01 (GET) Uri-Host: transit CSE host Uri-Port: transit CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Transit CSE forwards request to remote CSE containing: Method: GET Request URI <remoteCSE>/<Container> Host : remote CSE Payload: Empty |
|  |  | CoAP | Transit CSE forwards request to remote CSE containing: Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | MQTT |  |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to transit CSE containing: Code = 200 Payload: <container> resource |
|  |  | CoAP | Remote CSE sends response to transit CSE containing: Response Code: 2.05 Payload: <container> resource |
|  |  | MQTT |  |
| 6 | Check Mcc | Primitive |  |
|  |  | HTTP | Transit CSE sends response to registrar CSE containing: Code = 200 Payload: <container> resource |
|  |  | CoAP | Transit CSE sends response to registrar CSE containing: Response Code: 2.05 Payload: <container> resource |
|  |  | MQTT |  |
| 7 | Check Mca | Primitive |  |
|  |  | HTTP | Transit CSE forwards response to AE containing: Code = 200 Payload: <container> resource |
|  |  | CoAP | Transit CSE forwards response to AE containing: Response Code: 2.05 Payload: <container> resource |
|  |  | MQTT |  |
| 8 |  | Verify | AE indicates successful operation |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_03 |
| Objective: | AE updates a container resource in remote CSE |
| Configuration: | M2M_CFG_06 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | AE updates a container resource on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a request to update the <container> resource on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent request contains Method: PUT Request URI <remoteCSE>/<Container> Host : Registrar CSE Payload: Updated <Container> |
|  |  | CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Updated <Container> |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Registrar CSE forwards request to transit CSE containing: Method: PUT Request URI <remoteCSE>/<Container> Host : transit CSE Payload: Empty |
|  |  | CoAP | Registrar CSE forwards request to transit CSE containing: Method: 0.03 (PUT) Uri-Host: transit CSE host Uri-Port: transit CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Updated <Container> |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Transit CSE forwards request to remote CSE containing: Method: PUT Host : remote CSE Request URI <remoteCSE>/<Container> Payload: Updated <Container> |
|  |  | CoAP | Transit CSE forwards request to remote CSE containing: Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Updated <Container> |
|  |  | MQTT |  |
| 5 |  | Verify | Check if possible that the <container> resource is updated in remote CSE. |
| 6 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to transit CSE containing: Code = 200 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | CoAP | Remote CSE sends response to transit CSE containing: Response Code: 2.05 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | MQTT |  |
| 7 | Check Mcc | Primitive |  |
|  |  | HTTP | Transit CSE sends response to registrar CSE containing: Code = 200 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | CoAP | Transit CSE sends response to registrar CSE containing: Response Code: 2.05 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | MQTT |  |
| 8 | Check Mca | Primitive |  |
|  |  | HTTP | Transit CSE forwards response to AE containing: Code = 200 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | CoAP | Transit CSE forwards response to AE containing: Response Code: 2.05 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | MQTT |  |
| 9 |  | Verify | AE indicates successful operation |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_04 |
| Objective: | AE retrieves a container resource in remote CSE |
| Configuration: | M2M_CFG_06 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | AE has created a Container resource <container> on remote CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a request to delete the <container> resource on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent request contains Method: DELETE Request URI <remoteCSE>/<Container> Host : Registrar CSE Payload: Empty |
|  |  | CoAP | Sent request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Registrar CSE forwards request to transit CSE containing: Method: DELETE Request URI <remoteCSE>/<Container> Host : transit CSE Payload: Empty |
|  |  | CoAP | Registrar CSE forwards request to transit CSE containing: Method: 0.04 (DELETE) Uri-Host: transit CSE host Uri-Port: transit CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | MQTT |  |
| 4 | Check Mcc | Primitive |  |
|  |  | HTTP | Transit CSE forwards request to remote CSE containing: Method: DELETE Request URI <remoteCSE>/<Container> Host : remote CSE Payload: Empty |
|  |  | CoAP | Transit CSE forwards request to remote CSE containing: Method: 0.04 (DELETE) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | MQTT |  |
| 5 |  | Verify | Check if possible that the <container> resource is deleted in remote CSE. |
| 6 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to transit CSE containing: Code = 200 Payload: Empty |
|  |  | CoAP | Remote CSE sends response to transit CSE containing: Response Code: 2.05 Payload: Empty |
|  |  | MQTT |  |
| 7 | Check Mcc | Primitive |  |
|  |  | HTTP | Transit CSE sends response to registrar CSE containing: Code = 200 Payload: Empty |
|  |  | CoAP | Transit CSE sends response to registrar CSE containing: Response Code: 2.05 Payload: Empty |
|  |  | MQTT |  |
| 8 | Check Mca | Primitive |  |
|  |  | HTTP | Transit CSE forwards response to AE containing: Code = 200 Payload: Empty |
|  |  | CoAP | Transit CSE forwards response to AE containing: Response Code: 2.05 Payload: Empty |
|  |  | MQTT |  |
| 9 |  | Verify | AE indicates successful operation |

============== == End of  1st Part: Proposed Test Descriptions ==================