| Input Contribution |
| --- |
| Meeting ID* | TST#17 |
| Title:* | TS-0013 binding message convention |
| Source:* | SeungMyeong JEONG, LG Electronics (seungmyeong.jeong@lge.com) |
| Uploaded Date:* | 2015-05-13 |
| Document(s) Impacted* | TS-0013 v.0.0.4 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate this contribution to TS-0013. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

This contribution suggests some conventions for each protocol binding messages.

## ----------------------- Start of text 1 -----------------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0004: "oneM2M Core Protocol".

[2]	oneM2M TS-0010: "MQTT Protocol Binding".

## ----------------------- End of text 1 -----------------------

## ----------------------- Start of text 2 -----------------------

# 5	Testing conventions

## 5.2	Binding message convention

In HTTP/CoAP/MQTT binding messages, this specification defines the convention for <variable>:

- <resourceType> represesnts a resource name (i.e., resourceName attribute) of a resource instance in that resourceType. For example, <CSEBase>/<AE> can represent “CSE1base/AE1” in structured resource ID format.

- <parameter> represents a value of a oneM2M request/response parameter. For example, <Request ID> can represent “0001” value of the Request ID parameter. Paremeter names are case sensitive and in long names as specified in Core Protocol TS [1].

- <ID> represents an AE-ID or CSE-ID in MQTT Topic names.

The value will be given at an initeroperability test event.

In MQTT protocol binding TS [2], all oneM2M request/response parameters are carried in the MQTT message payload since it has no message header concept. Therefore, MQTT message payload needs to be described more than HTTP and CoAP messages to describe those parameters in clause 8.  In HTTP and CoAP binding messages, payloads are described as “empty” or “<container> resource to be created” in  a very abstracted way.

Since the representation can be XML or JSON, payload should be abstracted to support XML and JSON. The following example is XML representation and its abstraction for creating a <container> resource.

| XML payload example for MQTT binding | <?xml version="1.0" encoding="UTF-8"?> <m2m:req xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.onem2m.org/xml/protocols CDT-requestPrimitive-v1_0_0.xsd"> <op>1</op> <to>CSE1Base</to> <fr>/CSE1/C_AE1</fr> <rqi>2001</rqi> <ty>3</ty> <nm>cont1</nm> <rti><rt>3</rt></rti> <pc> <cnt> <lbl>SmartMeter</lbl> <et>20141003T112033</et> </cnt> </pc> </m2m:req> |
| --- | --- |
| Abstracted payload example for MQTT binding | op = 1 to = CSE1Base fr = /CSE1/C_AE01 rqi = 3001 ty = 3 name = cont1 rti.rt = 3 pc.cnt.lbl = SmartMeter pc.cnt.et = 20141003T112033 |
| Abstracted payload example for MQTT binding adopting the payload convention | op = 1 to = <CSEBase> fr = <From> rqi = <Request ID> ty = 3 name = <Name> rti.rt = 3 pc = <Content> |

## ----------------------- End of text 2 -----------------------