| Input Contribution |
| --- |
| Meeting ID* | TST 17 |
| Title:* | ICS Proforma |
| Source:* | Ting Miao, Sungchan Choi, Jaeho Kim (novamartin@keti.re.kr) |
| Uploaded Date:* | 2015-05-12 |
| Document(s) Impacted* | TS-0017 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0017 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1. Introduction

This prensent document specifies the Implementation Conformance Statement (ICS) for oneM2M conformance testing, including information of status of capability specified in oneM2M TS[1, 2, 3].  oneM2M conformace testing aims for evaluating whether the Implementation Under Test (IUT) is conforming to oneM2M Technical Specifications.

This present document presents seven node roles defined in oneM2M TS[1] for determining the role of IUT. A capability list is also presented in this present to check whether the IUT supports the part or whole of the listed capabilities after the role of IUT is declared.

This present document could provide an overview of the features and options that are implemented by clients after each client fills out this document.

2. Declaimer

The content of capability statement presented  in Table A.5.2 shall be consistent with oneM2M Conformance Testing Functional Group List which already has presented in TST 16.3.

============== == Start of  1st Part: Proposed Annex A ==================

A.5	Tables

A.5.1 Roles and Reference Points

oneM2M roles and reference points defined in TS [1] is listed in table A.5.1.1 and A.5.1.2, specifically.

Table A.5.1. 1 oneM2M Node Role

| Item | Type | Mnemonic | Reference | Status | Support |
| --- | --- | --- | --- | --- | --- |
| 1 | ASN-CSE |  | [1] 3.2, [3] 6.3.3.2.2, [3] 7.3.4 | C.1 | O Yes O No |
| 2 | MN-CSE |  | [1] 3.2, [3] 6.3.3.2.2, [3] 7.3.4 | C.1 | O Yes O No |
| 3 | IN-CSE |  | [1] 3.2, [3] 6.3.3.2.2, [3] 7.3.4 | C.1 | O Yes O No |
| 4 | ASN-AE |  | [1] 3.2, [3] 6.3.3.2.2, [3] 7.3.4 | C.1 | O Yes O No |
| 5 | MN-AE |  | [1] 3.2, [3] 6.3.3.2.2, [3] 7.3.4 | C.1 | O Yes O No |
| 6 | IN-AE |  | [1] 3.2, [3] 6.3.3.2.2, [3] 7.3.4 | C.1 | O Yes O No |
| 7 | ADN-AE |  | [1] 3.2, [3] 6.3.3.2.2, [3] 7.3.4 | C.1 | O Yes O No |

C.1: It is mandatory to support exactly one of these roles.

Table A.5.1. 2 oneM2M Reference Points Supported per Node Role

| Node Role Reference Point | ASN-CSE | MN-CSE | IN-CSE | ASN-AE | MN-AE | IN-AE | ADN-AE |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Mca | M | M | M | M | M | M | M |
| Mcc | M | M | M | NA | NA | NA | NA |
| Mcn | M | M | M | NA | NA | NA | NA |
| Mcc’ | NA | NA | M | NA | NA | NA | NA |

M: Mandatory.

NA: Not Appliable.

A.5.2 Capability Statement

A list of capabilities defined in the oneM2M TS [1] are presented in Table A.5.2.1. The capability list can be used to check whether the IUT supports part or whole of the capabilities listed as below.

Table A.5.2. 1 Capabilities for oneM2M Conformance Testing

| Item | Capability | Mnemonic | Reference | Status | Support |
| --- | --- | --- | --- | --- | --- |
| 1 | Registration |  | [1] 10.2.1 | C.1 | O Yes O No |
| 2 | Data Management |  | [1] 10.2.4, [1] 10.2.19 | C.1 | O Yes O No |
| 3 | Subscription and Notification |  | [1] 10.2.11 | C.2 | O Yes O No |
| 4 | Group Management |  | [1] 10.2.7 | C.2 | O Yes O No |
| 5 | Discovery |  | [1] 10.2.6 | C.2 | O Yes O No |
| 6 | Location Management |  | [1] 10.2.10 | C.2 | O Yes O No |
| 7 | Device Management |  | [1]10.2.8 | C.2 | O Yes O No |
| 8 | Communication Management and Delivery Handling |  | [1] 10.2.5, [1] 10.2.20 | C.2 | O Yes O No |

C.1: Mandatory IF the IUT is declaimed to be developed conforming to oneM2M TS[1], [2], [3].

C.2: Optional IF the IUT is declaimed to be developed conforming to oneM2M TS[1], [2], [3].

============== == End of  1st Part: Proposed Annex A ==================