| Input Contribution |
| --- |
| Meeting ID* | TST17.3 |
| Title:* | Test Purposes contributions |
| Source:* | Miguel A. Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org Alexandre Berge, AMB Consulting, Alexandre.berge@amb-consulting.com Laurent Velez, ETSI, Laurent.Velez@etsi.org |
| Uploaded Date:* | 2015-06-26 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes and some text to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes some Test Purposes with their corresponding Test Configuration, PICS and PICS convention to be included in TS-0018 – Test Suite Structure and Test Purposes.

Proposal

================ Start of  1st  Part: Test Configurations ==================

# 5	Prerequisites and Test Configurations

## 5.1	Test Configurations

================ End of  1st  Part: Test Configurations ==================

================ Start of  2nd Part: ICS Reference ==================

### 7.1.5	ICS reference

Table A.1: Node

| Item | Name of field | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | ASN (Application Service Node) | 6.1 | o.1 |  |
| 2 | ADN (Application Dedicated Node) | 6.1 | o.1 |  |
| 3 | IN (Infrastructure Node) | 6.1 | o.1 |  |
| 4 | MN (Middle Node) | 6.1 | o.1 |  |
| o.1: Exactly one item shall be supported |

Table A.2: Functional entity type

| Prerequisite: A.1 |
| --- |
| Item | Name of field | Reference | Status | Support |
| 1 | AE | 5.2.1 | c.1 |  |
| 2 | CSE | 5.2.1 | c.2 |  |
| c.1: If A.1-1 or A.1-2 then m else o c.2: If A.1-2 x else m |

Table 3: Mnemonics for PICS reference

| Mnemonic | PICS item |
| --- | --- |
| PICS_AE | A.2/1 [PICS document] |
| PICS_CSE | A.2/2 [PICS document] |
| PICS_ASN | A.1/1 [PICS document] |
| PICS_ADN | A.1/2 [PICS document] |
| PICS_IN | A.1/3 [PICS document] |
| PICS_MN | A.1/4 [PICS document] |

================ End of  2nd Part: ICS Reference ==================

================ Start of  3rd Part: Test Purposes ==================

## 7.2	Test Purposes for oneM2M

Editor Note: The following TPs contain some test variables (using upper-case and italic) which will be instantiated during test execution.

| TP Id | TP/oneM2M/CSE/REG/01 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE registration (allowed App-ID, C-AE-ID-STEM not provided by AE) |
| Reference | TS1-10.1.1.2.2 - case C, 9.6.19 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions |
| with { the IUT being in the "initial state" and the IUT having a CSEBase resource containing a ServiceSubscribedProfile resource containing a ServiceSubscribedNode resource containing RuleLinks attribute pointing to a ServiceSubscribedAppRule resource containing applicableCredIDs attribute set to None containing allowedApp-IDs attribute indicating APP-ID containing allowedAEs attribute indicating C-AE-ID-STEM } |
| Expected behaviour |
| ensure that { when { the IUT receives a valid CREATE request from AE containing Resource-Type set to 2 (AE) and containing From set to empty and containing Content <AE> containing App-ID attribute set to APP-ID } then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) } } |

| TP Id | TP/oneM2M/CSE/REG/02 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE re-registration (allowed App-ID, C-AE-ID-STEM provided by AE) |
| Reference | TS1-10.1.1.2.2 - case d, 9.6.19 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions |
| with { the IUT being in the "initial state" and the IUT having a CSEBase resource containing a ServiceSubscribedProfile resource containing a ServiceSubscribedNode resource containing RuleLinks attribute pointing to a ServiceSubscribedAppRule resource containing applicableCredIDs attribute set to None containing allowedApp-IDs attribute indicating APP-ID containing allowedAEs attribute indicating C-AE-ID-STEM } |
| Expected behaviour |
| ensure that { when { the IUT receives a valid CREATE request from AE containing Resource-Type set to 2 (AE) and containing From set to C-AE-ID-STEM and containing Content <AE> containing App-ID attribute set to APP-ID } then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) } } |

| TP Id | TP/oneM2M/CSE/REG/03 |
| --- | --- |
| Test objective | Check that the IUT rejects an AE registration (not allowed App-ID) |
| Reference | TS1-10.1.1.2.2 – step 3, 9.6.19 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions |
| with { the IUT being in the "initial state" and the IUT having a CSEBase resource containing a ServiceSubscribedProfile resource not containing a ServiceSubscribedNode resource containing RuleLinks attribute pointing to a ServiceSubscribedAppRule resource containing applicableCredIDs attribute set to None containing allowedApp-IDs attribute indicating APP-ID } |
| Expected behaviour |
| ensure that { when { the IUT receives a valid CREATE request from AE containing Resource-Type set to 2 (AE) and containing Content <AE> containing App-ID attribute set to APP-ID } then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } } |

| TP Id | TP/oneM2M/CSE/REG/04 |
| --- | --- |
| Test objective | Check that the IUT rejects an AE registration (allowed App-ID, not allowed C-AE-ID-STEM provided by AE) |
| Reference | TS1-10.1.1.2.2 – step 3, 9.6.19 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions |
| with { the IUT being in the "initial state" and the IUT having a CSEBase resource containing a ServiceSubscribedProfile resource containing a ServiceSubscribedNode resource containing RuleLinks attribute pointing to a ServiceSubscribedAppRule resource containing applicableCredIDs attribute set to None containing allowedApp-IDs attribute indicating APP-ID not containing allowedAEs attribute indicating C-AE-ID-STEM } |
| Expected behaviour |
| ensure that { when { the IUT receives a valid CREATE request from AE containing Resource-Type set to 2 (AE) and containing From set to C-AE-ID-STEM and containing Content <AE> containing App-ID attribute set to APP-ID } then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } } |

| TP Id | TP/oneM2M/CSE/REG/05 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE registration (allowed App-ID, S-AE-ID-STEM not provided by AE) |
| Reference | TS1-10.1.1.2.2 - case a, 9.6.19 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions |
| with { the IUT being in the "initial state" and the IUT having a CSEBase resource containing a ServiceSubscribedProfile resource containing a ServiceSubscribedNode resource containing RuleLinks attribute pointing to a ServiceSubscribedAppRule resource containing applicableCredIDs attribute set to None containing allowedApp-IDs attribute indicating APP-ID containing allowedAEs attribute indicating a value starting with ‘S’ and containing wildcard } |
| Expected behaviour |
| ensure that { when { the IUT receives a valid CREATE request from AE containing Resource-Type set to 2 (AE) and containing From set to empty and containing Content <AE> containing App-ID attribute set to APP-ID } then { the IUT sends a CREATE request message to the IN-CSE containing Resource-Type set to 10002 (AEAnnc) and containing From set to ‘/S’ and containing Content <AEAnnc> containing App-ID attribute set to APP-ID containing nodeLink attribute set to containing Labels indicating ‘Credential-ID:None’ } } |

| TP Id | TP/oneM2M/CSE/CRE/01 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a RESOURCE_TYPE resource with resource name not provided by AE |
| Reference | TS1-10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions |
| with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation } |
| Expected behaviour |
| ensure that { when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and containing Resource-Type set to RESOURCE_TYPE and containing From set to AE-ID and not containing Name attribute and containing Content RESOURCE_TYPE } then { the IUT sends a Response message containing Name and containing Response Status Code set to 2001 (CREATED) } } |

| TP Id | TP/oneM2M/CSE/CRE/02 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a RESOURCE_TYPE resource with a non-existing resource name provided by AE |
| Reference | TS1-10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions |
| with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation and not containing a child resource containing Name attribute set to NAME } |
| Expected behaviour |
| ensure that { when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and containing Resource-Type set to RESOURCE_TYPE and containing From set to AE-ID and containing Name attribute set to NAME and containing Content RESOURCE_TYPE } then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) } } |

| TP Id | TP/oneM2M/CSE/CRE/03 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of a RESOURCE_TYPE resource with an existing resource name provided by AE |
| Reference | TS1-10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions |
| with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation and containing a child resource containing Name attribute set to NAME } |
| Expected behaviour |
| ensure that { when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and containing Resource-Type set to RESOURCE_TYPE and containing From set to AE-ID and containing Name attribute set to NAME and containing Content RESOURCE_TYPE } then { the IUT sends a Response message containing Response Status Code set to 5106 (ALREADY_EXISTS) } } |

| TP Id | TP/oneM2M/sCSE/CRE/04 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of a RESOURCE_TYPE resource when AE has no privileges |
| Reference | TS1-10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions |
| with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource PARENT_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute pointing to accessControlPolicy resource containing Privileges attribute containing accessControlRule containing accessControlOriginators indicating ‘all’ containing accessControlOperations not indicating CREATE } |
| Expected behaviour |
| ensure that { when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and containing Resource-Type set to RESOURCE_TYPE and containing From set to AE-ID and containing Content RESOURCE_TYPE } then { the IUT sends a Response message containing Response Status Code set to 4103 (ACCESS_DENIED) } } |

================ Start of  3rd Part: Test Purposes ==================

# Text boxes

Figure 1. Test configuration 1 (CF01)

IUT

TEST SYSTEM

AE

CSE

Mca

Mcc

IUT

TEST SYSTEM

AE

CSE

Mca

CSE

Figure 2. Test configuration 2 (CF02)