| Input Contribution |
| --- |
| Meeting ID* | TST18 |
| Title:* | Test description restructuring |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd. , yinjiaxin@huawei.com |
| Uploaded Date:* | 2015-7-10 |
| Document(s) Impacted* | WI-0022, TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text if agreed. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The contribution tries to restructure the clause 8 test description of TS-0013 in order to minimize the duplex between its sub-clauses while keep the current by put them into the correct place.

### -----------------------Start of change 1-------------------------------------------

# Test Descriptions

# Common Test Descriptions for no hop configuration

# Test Description for Create

    - Test Description for Update

    - Test Description for Retrieve

    - Test Description for Delete

# Test Description for Notify

### Test Description for Non-blocking Requests

## No Hop configuration testing

### <CSEBase> Test Description

#### Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_01 |
| Objective: | AE retrieves the CSEBase resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.3.2 [2] 7.3.2 |
| Pre-test conditions: | CSEBase resource has been automatically created in CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a retrieve Request to CSE CSE with name {CSEBaseName} |
| 2 | Mca | PRO Check Primitive | Operation (op) = 2 (Retrieve) To (to) = Resource-ID of requested <CSEBase> resource, assumed CSE-relative here From (from) = AE-ID of request originator Request Identifier (rqi) = (token-string) |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request-Target:{CSEBaseName} Host: Host Address of registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: AE-ID Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = same string as received in request message Content (pc) = Serialized Representation of <CSEBase> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 X-M2M-RSC: 2000 X-M2M-RI: value of rqi primitive parameter Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytes Payload: Serialized Representation of <CSEBase> resource |
|  |  | PRO Check | Registrar sends response containing: Response Code = 2.05 Payload: <CSEBase> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(<CSEBase> resource representation)> |
| 4 |  | IOP CheckIOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### <AE> Test Description

#### <AE> Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_02 |
| Objective: | AE registers to its registrar CSE via an AE Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | CSEBase resource has been created in CSE with name {CSEBaseName} AE does not have an AE-ID, i.e. it registers from scratch |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a AE Create request to register to the Registrar CSE |
| 2 | Mca | PRO Check Primitive | Operation (op) = 1 (Create) To (to) = Resource-ID of <CSEBase> resource of the registrar CSE From (from) = empty Request Identifier (rqi) = (token-string) Resource Type (ty) = 2 (AE) Content (pc) = Serialized Representation of applicable <AE> resource attributes |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request-Target:{CSEBaseName} Host: Host Address of Registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: empty Content-Type: application/vnd.onem2m-res+xml; ty=2 or application/vnd.onem2m-res+json; ty=2 Content-Length: size of payload in the message body in bytes Payload: Serialized Representation of applicable attributes of <AE> resource |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: rty=2 Payload: <AE> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase> fr = <AE-ID> rqi = <Request ID> ty = 2 pc = <Content> |
| 3 |  | IOP Check | Check if possible that the <AE> resource is created in registrar CSE. |
| 4 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2001 (CREATED) Request Identifier (rqi) = same string as received in request message Content (pc) = Serialized Representation of <AE> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2001 X-M2M-RI: value of rqi primitive parameter Content-Location: hierarchical URI of created <AE> resource as given in the @resourceName attribute included in Content primitive parameter Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length: size of payload in the message body in bytes Payload: Serialized Representation of the created <AE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.01 Location-Path: <CSEBase> Location-Path: <AE> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <AE> resource representation)> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <AE> Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_03 |
| Objective: | AE retrieves <AE> resource via an AE Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an application Retrieve Request |
| 2 | Mca | PRO Check Primitive | Operation (op) = 2 (Retrieve) To (to) = Resource-ID of requested <AE> resource, assumed CSE-relative here From (from) = AE-ID of request originator Request Identifier (rqi) = (token-string) |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request-Target: AE-resourceID Host: Host Address of registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: AE-ID Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase>/<AE> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = same string as received in request message Content (pc) = Serialized Representation of <AE> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code =200 X-M2M-RSC: 2000 X-M2M-RI: value of rqi primitive parameter Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytes Payload: Serialized Representation of <AE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: <AE> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <AE> resource representation> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <AE> Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_04 |
| Objective: | AE updates attribute in <AE> resource via an AE Update Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Update Request |
| 2 | Mca | PRO Check Primitive | Operation (op) = 3 (Update) To (to) = Resource-ID of requested <AE> resource, assumed CSE-relative here From (from) = AE-ID of request originator Request Identifier (rqi) = (token-string) Content (pc) = Serialized Representation of modified <AE> resource |
|  |  | PRO Check HTTP | Sent PUT request contains Request method = PUT Request-Target: AE-resourceID Host: Host Address of registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length: size of payload in the message body in bytes Payload: Serialized Representation of modified <AE> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Payload: modified <AE> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <CSEBase>/<AE> fr = <AE-ID> rqi = <Request ID> |
| 3 |  | IOP Check | Check if possible that the <AE> resource has been updated in registrar CSE. |
| 4 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2004 Request Identifier (rqi) = same string as received in request message Content (pc) = Serialized Representation of <AE> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 X-M2M-RSC: 2004 X-M2M-RI: value of rqi primitive parameter Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytes Payload: Serialized Representation of modified attributes of the <AE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(updated <AE> resource representation)> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <AE> Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_05 |
| Objective: | AE de-registers by deleting <AE> resource via an AE Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Delete Request |
| 2 | Mca | PRO Check Primitive | Operation (op) = 4 (Delete) To (to) = Resource-ID of requested <AE> resource, assumed CSE-relative here From (from) = AE-ID of request originator Request Identifier (rqi) = (token-string) |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method = DELETE Request-Target: AE-resourceID Host: Host Address of Registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: AE-ID Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase>/<AE> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2004 (DELETED) Request Identifier (rqi) = same string as received in request message |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 X-M2M-RSC: 2004 X-M2M-RI: value of rqi primitive parameter Payload: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <AE> resource representation)> |
| 4 |  | IOP Check | Check if possible that the <AE> resource has been removed in registrar CSE. |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### <container> Test Description

#### <container> Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_06 |
| Objective: | AE creates a container resource in registrar CSE via a container Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request to create container <container> |
| 2 | Mca | PRO Check Primitive | Sent CREATE request contains To: <CSEBase>/<AE>?rty=container Fr: AE-ID Cn: container resource <container> to be created |
|  |  | PRO Check HTTP | Sent POST request contains Request URI <CSEBase>/<AE>?rty=3 Host : Registrar CSE Payload: container resource <container> to be created Content-Type= media-type |
|  |  | PRO Check CoAP | Sent POST request contains Method 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase>Uri-Path: <AE>Uri-Query: rty=3 Payload: <container> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase>/<AE> fr = <AE-ID> rqi = <Request ID> ty = 3 pc = <Content(<content> resource representation)> |
| 3 |  | IOP Check | Check if possible that the <container> resource is created in registrar CSE. |
| 4 | Mca | PRO Check Primitive | Registrar sends response containing: To: AE-ID Fr: CSE-ID Cn: Created <container> |
|  |  | PRO Check HTTP | Registrar sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container> |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.01 (2001 Created) Location-Path: <CSEBase> Location-Path: <AE> Location-Path: <container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <content> resource representation> |
| 5 |  | IOP Check | AE indicates successful operation |
| 6 |  |  | Repeat step 1-5 creating container resource with short lifetime |
| 7 |  |  | Check the created resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### <container> Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_07 |
| Objective: | AE retrieves information of a container resource via a container Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | A container resource <container> has been created in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Retrieve Request for resource <container> |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <CSEBase>/<AE>/<container> Host : Registar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase>/<AE>/<container> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: updated <AE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: <container> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <container> resource representation)> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <container> Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_08 |
| Objective: | AE updates attribute in application resource via a container Update Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | a container resource <container> has been created in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an container Update Request to update the lifetime of the resource. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Payload: modified <container> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> Payload: <Container> resource updated |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <CSEBase>/<AE>/<container> fr = <AE-ID> rqi = <Request ID> pc = <Content> |
| 3 |  | IOP Check | Check if possible that the <container> resource has been updated in registrar CSE. |
| 4 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: Updated <container> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(updated <container> resource representation)> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <container> Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_09 |
| Objective: | AE deletes a specific container resource via a container Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | AE has created a container resource <container> in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an Container Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase>/<AE>/<container> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registar CSE sends response containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <AE> resource representation)> |
| 4 |  | IOP Check | Check if possible that the <container > resource has been removed in registrar CSE. |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### <contentInstance> Test Description

#### <contentInstance> Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_10 |
| Objective: | AE adds a contentInstance resource <contentInstance> to a specific container in Registrar CSE via a contentInstance Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.2 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a contentInstance Create Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request URI <CSEBase>/<AE>/<container>?rty=4 Host : Registrar CSE Payload: ContentInstance resource <contentInstance> to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> Uri-Query: rty=4 Payload: <contentInstance> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase>/<AE>/<container> fr = <AE-ID> rqi = <Request ID> ty = 4 pc = <Content(<contentInstance> resource representation> |
| 3 |  | IOP Check | Check if possible that the <contentInstance> resource is created in registrar CSE. |
| 4 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Content-Location : CSEBase>/<AE>/<container>/<contentInstance> Payload: <contentInstance> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.01 Location-Path: <CSEBase> Location-Path: <AE> Location-Path: <container> Location-Path: <contentInstance> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <contentInstance> resource representation)> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <contentInstance> Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_11 |
| Objective: | AE retrieves information of a contentInstance resource via a container Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.2 [2] 7.3.6.2.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE AE has created a contentInstance resource <contentInstance> residing under the <container> resource. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | App is requested to send a containerRetrieveRequest for retrieving the attributes/meta-data and the opaque data of a <contentInstance> resource |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <CSEBase>/<AE>/<container>/<contentInstance> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> Uri-Path <ContentInstance> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase>/<AE>/<container>/<contentInstance> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: <contentInstance> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: <container> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <contentInstance> resource representation)> |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  |  | Repeat steps 1-4 using <latest> instead of <contentInstance> to get the latest contentInstance. |
| 6 |  |  | Repeat steps 1-4 using <oldest> instead of <contentInstance> to get the oldest contentInstance. |
| IOP Verdict |  |
| PRO Verdict |  |

#### <contentInstance> Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_12 |
| Objective: | AE deletes contentInstance resource via a container Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.4 [2] 7.3.6.2.4 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE AE has created a contentInstance resource <contentInstance> residing under the <container> resource. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a contentInstance Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <CSEBase>/<AE>/<container>/<contentInstance> Host : registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <ContentInstance> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase>/<AE>/<container>/<contentInstance> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <contentInstance> resource representation)> |
| 4 |  | IOP Check | Check if possible that the <contentInstance> resource has been removed in registrar CSE. |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Discovery

#### Discovery of all resources

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_13 |
| Objective: | AE discovers resources residing in Registrar CSE |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a discovery request to discover all accessible resources located in Registrar CSE |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <CSEBase>?fu=1 Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: fu=1 Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <contentInstance> resource representation)> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: Data object containing addresses of all the found resources. |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Data object containing addresses of all the found resources. |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(list of resource addresses in structured resource ID format)> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Discovery with label filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_14 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using the label filter criteria |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Container resource <Container> having "key1" as label on Registrar CSE . |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request in order to discover the <AE> resource using the label filter criteria |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <CSEBase>?fu=1&lbl=key1 Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: fu=1 Uri-Query: lbl=key1 Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase> fr = <AE-ID> rqi = <Request ID> fc.fu = 1 |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: Data object containing address of <Container> |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Data object containing address of <Container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(list of resource addresses in structured resource ID format)> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Discovery with limit filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_15 |
| Objective: | AE discovers accessible resources residing in Registrar CSE limiting the number of matching resources to the specified value. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request in order to discover at most 2 resources in registrar CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <CSEBase>?fu=1&lim=2 Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: fu=1 Uri-Query: lim=2 Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase> fr = <AE-ID> rqi = <Request ID> fc.fu = 1 fc.lim = 2 |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: Trunked Data object containing only 2 addresses of found resources. |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Data object containing only 2 addresses of found resources |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(two resource addresses in structured resource ID format)> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Discovery with multiple filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_16 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using multiple Filter Criteria |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created a Container resource <Container> having "key1" and "key2" as labels in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request in order to discover resources located in Registrar CSE using multiple filter criteria |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <CSEBase>?fu=1&lbl=key1&lbl=key2&lim=1 Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: fu=1 Uri-Query: lbl=key1 Uri-Query: lbl=key2 Uri-Query: lim=1 Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase> fr = <AE-ID> rqi = <Request ID> fc.fu = 1 fc.lbl = key1 fc.lbl = key2 fc.szb = 1 |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: Data object containing address of <Container> |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Data object containing Address of <Container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code> pc = <Content(list of matching resource addresses in structured resource ID format)> |
| 4 |  | IOP Check2 | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### <subscription> Test Description

#### <subscription> Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_17 |
| Objective: | AE creates a subscription to Application Entity resource via subscription Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.2 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an application resource <AE> on registrar CSE AE has created a container resource <container> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a subscriptionCreateRequest |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request URI: <CSEBase>/<AE>/<container> ?rty=23 Host : Registrar CSE Payload: subscription <subscription> resource to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> Uri-Query: rty=23 Payload: <subscription> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase> fr = <AE-ID> rqi = <Request ID> ty = 23 pc = <Content(<subscription> resource representation)> |
| 3 |  | IOP Check | Check if possible that the <subscription> resource is created in Registrar CSE |
| 4 | Mca | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container>/ <subscription> Payload: Created < subscription > resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.01 Location-Path: <CSEBase> Location-Path: <AE> Location-Path: <container> Location-Path: <subscription> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <subscription> resource representation)> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <subscription> Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_18 |
| Objective: | AE retrieves information about a subscription via subscription Retrieve Request such as expirationTime, labels, etc… |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.3 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a subscription Retrieve Request for retrieving information about a subscription <subscription> |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <subscription> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase>/<AE>/<container>/<subscription> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: <subscription> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: <subscription> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <subscription> resource representation)> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <subscription> Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_19 |
| Objective: | AE updates information about a subscription via subscription Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.4 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a subscription Retrieve Request to update the lifetime of the resource. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: Modified <subscription> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <subscription> Payload: <subscription> updated resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <CSEBase>/<AE>/<container>/<subscription> fr = <AE-ID> rqi = <Request ID> pc = <Content(<subscription> resource representation)> |
| 3 |  | IOP Check | Check if possible that the <subscription> resource is updated in Registrar CSE. |
| 4 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: Modified <subscription> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <subscription> resource representation)> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <subscription> Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_20 |
| Objective: | AE cancels subscription via an subscription Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.5 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a subscription Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: Empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <subscription> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <subscription> resource representation)> |
| 4 |  | IOP Check | Check if possible that the <subscription> resource has been removed in registrar CSE. |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### <accessControlPolicy> Test Description

#### <accessControlPolicy> Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_21 |
| Objective: | AE creates an accessControlPolicy resource |
| Configuration: | M2M_CFG_01, |
| References: | [1] 10.2.21.1 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an accessControlPolicy Create Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI <CSEBase>/<AE>?rty= 1 Host : Registrar CSE Payload: application resource <accessControlPolicy> to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Query: rty=1 Payload: <accessControlPolicy> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase>/<AE> fr = <AE-ID> rqi = <Request ID> ty = 1 pc = <Content(<accessControlPolicy> resource representation)> |
| 3 |  | IOP Check | Check if possible that the <accessControlPolicy> resource is created in Registrar CSE. |
| 4 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<AE>/<accessControlPolicy> Payload: created <accessControlPolicy> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.01 Location-Path: <CSEBase> Location-Path: <AE> Location-Path: <accessControlPolicy > |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <accessControlPolicy> resource representation)> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <accessControlPolicy> Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_22 |
| Objective: | AE retrieves accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.2 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a accessControlPolicy Retrieve request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI <CSEbase>/<AE>/<accessControlPolicy> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <accessControlPolicy> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase>/<AE>/<accessControlPolicy> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code =200 Payload: <accessControlPolicy> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: <accessControlPolicy> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <accessControlPolicy> resource representation)> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <accessControlPolicy> Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_23 |
| Objective: | AE updates attribute in accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.3 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an accessControlPolicy Update request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request method = PUT Request URI <CSEbase>/<AE>/<accessControlPolicy> Host : Registrar CSE Payload: modified <accessControlPolicy> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <accessControlPolicy> Payload: <accessControlPolicy> updated resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <CSEBase>/<AE>/<accessControlPolicy> fr = <AE-ID> rqi = <Request ID> pc = <Content(<accessControlPolicy> resource representation)> |
| 3 |  | IOP Check | Check if possible that the <accessControlPolicy> resource is updated in Registrar CSE. |
| 4 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: updated <accessControlPolicy> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(updated <accessControlPolicy> resource representation)> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <accessControlPolicy Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_24 |
| Objective: | AE deletes accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.4 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an accessControlPolicy Delete request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method DELETE Request URI <CSEBase>/<AE>/ <accessControlPolicy> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent Delete request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <accessControlPolicy> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase>/<AE>/<accessControlPolicy> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code> pc = <Content(deleted <accessControlPolicy> resource representation)> |
| 4 |  | IOP Check | Check if possible that the <accessControlPolicy> resource has been removed in registrar CSE. |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Unauthorized operation (Insufficient Access Rights)

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_25 |
| Objective: | AE delete request is rejected due to accessControlPolicy |
| Configuration: | M2M_CFG_01 |
| References: | [1] [2] ] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource < acp1> under <AE> on Registrar CSE, which forbids to delete container AE has created a container resource <container> in application <AE>, using the access right <acp1> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Delete Request for resource <container> |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase>/<AE>/<container> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 403 (Forbidden operation) Payload: ??? |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 4.03 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(4103, ACCESS_DENIED> |
| 4 |  | IOP Check | Check if possible that the <container> resource has not been removed in registrar CSE. |
| 5 |  | IOP Check | AE indicates unsuccessful operation (Delete error – no privilege) |
| IOP Verdict |  |
| PRO Verdict |  |

### <group> Test Description

#### <group> Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_26 |
| Objective: | AE creates a group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.2 [2] 7.3.12.2.1 |
| Pre-test conditions: | void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a group Create Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI <CSEBase>?rty=9 Host : Registrar CSE Payload: Group resource <group> to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: rty=9 Payload: <group> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase> fr = <AE-ID> rqi = <Request ID> ty = 9 pc = <Content(<group> resource representation> |
| 3 |  | IOP Check | Check if possible that the <group> resource is created in Registrar CSE. |
| 4 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<group> Payload: created <group> resource representation |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.01 Location-Path: <CSEBase> Location-Path: <group> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <group> resource representation> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <group> Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_27 |
| Objective: | AE retrieves group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.3 [2] 7.3.12.2.2 |
| Pre-test conditions: | AE has created a Group resource <group> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a group Retrieve Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI <CSEBase>/<group> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <group> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase>/<group> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code =200 Payload: <group> resource representation |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: <group> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <group> resource representation> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <group> Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_28 |
| Objective: | AE updates attribute in group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.4 [2] 7.3.12.2.3 |
| Pre-test conditions: | AE has created a group resource <group> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a group Update Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request method = PUT Request URI <CSEBase>/<group> Host : Registrar CSE Payload: modified group resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <group> Payload: <group> updated resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <CSEBase>/<group> fr = <AE-ID> rqi = <Request ID> pc = <Content(<group> resource representation> |
| 3 |  | IOP Check | Check if possible that the <group> resource is updated in Registrar CSE.. |
| 4 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: updated <group> resource representation |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(updated <group> resource representation> |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <group> Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_29 |
| Objective: | AE deletes group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.5 [2] 7.3.12.2.4 |
| Pre-test conditions: | AE has created a group resource <group> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a group Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method = DELETE Request URI <CSEBase>/<group> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <group> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase>/<group> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(removed <group> resource representation> |
| 4 |  | IOP Check | Check if possible that the <group> resource is deleted in Registrar CSE. |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### <pollingChannel> Test Description

#### <pollingChannel> Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_30 |
| Objective: | AE creates a <pollingChannel> resource in registrar CSE via a Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.13.2 [2] 7.3.21.2.1 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a pollingChannel Create Request to create < pollingChannel > |
| 2 | Mca | PRO Check Primitive | Sent CREATE request contains To: <CSEBase>/<AE> ResourceType=pollingChannel Fr: AE-ID Cn: <pollingChannel> resource to be created |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: <CSEBase>?rty=15 Host : registrar CSE Payload: < pollingChannel > resource |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: rty=15 Payload: < pollingChannel > resource |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check if possible that the < pollingChannel > resource is created in Registrar CSE. |
| 7 | Mca | PRO Check Primitive | Sent CREATE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : OK Cn: Created <pollingChannel> |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/< pollingChannel > Payload: Created < pollingChannel > |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.01 Location-Path: <CSEBase> Location-Path: <AE> Location-Path: < pollingChannel > |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | Registrar CSE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <pollingChannel> Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_31 |
| Objective: | AE retrieves information of a pollingChannel resource via a Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.13.3 [2] 7.3.21.2.2 |
| Pre-test conditions: | A pollingChannel resource < pollingChannel > has been created in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a pollingChannel Retrieve Request for < pollingChannel > |
| 2 | Mca | PRO Check Primitive | Sent RETRIEVE request contains To: <CSEBase>/<AE>/<pollingChannel> Fr: AE-ID |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <CSEBase>/<AE>/<pollingChannel> Host : Registar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <pollingChannel> |
|  |  | PRO Check MQTT |  |
| 3 | Mca | PRO Check Primitive | Sent RETRIEVE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : OK Cn: <pollingChannel> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: <pollingChannel> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: <pollingChannel> resource |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <pollingChannel> Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_32 |
| Objective: | AE updates attribute in pollingChannel resource via a Update Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.13.4 [2] 7.3.21.2.3 |
| Pre-test conditions: | a pollingChannel resource < pollingChannel > has been created in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an pollingChannel Update Request to update the lifetime of the resource. |
| 2 | Mca | PRO Check Primitive | Sent UPDATE request contains To: <CSEBase>/<AE>/<pollingChannel> Fr: AE-ID Response Statuse Code : OK Cn: <pollingChannel> resource to be updated |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI <CSEBase>/<AE>/<pollingChannel> Host : Registrar CSE Payload: modified <pollingChannel> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <pollingChannel> Payload: <pollingChannel> resource updated |
|  |  | PRO Check MQTT |  |
| 3 |  | IOP Check | Check if possible that the <pollingChannel> resource has been updated in registrar CSE. |
| 4 | Mca | PRO Check Primitive | Sent UPDATE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : OK Cn: <pollingChannel> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: Updated <pollingChannel> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### <pollingChannel> Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_33 |
| Objective: | AE deletes a pollingChannel resource via a Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.13.5 [2] 7.3.21.2.4 |
| Pre-test conditions: | AE has created a pollingChannel resource < pollingChannel > in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an pollingChannel Delete Request |
| 2 | Mca | PRO Check Primitive | Sent DELETE request contains To: <CSEBase>/<AE>/<pollingChannel> Fr: AE-ID |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <CSEBase>/<AE>/< pollingChannel > Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: < pollingChannel > |
|  |  | PRO Check MQTT |  |
| 3 | Mca | PRO Check Primitive | Sent DELETE request contains To: <CSEBase>/<AE>/<pollingChannel> Fr: AE-ID Response Statuse Code : OK |
|  |  | PRO Check HTTP | Registar CSE sends response containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check if possible that the < pollingChannel > resource has been removed in registrar CSE. |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Long Polling on a PollingChannel Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_34 |
| Objective: | AE retrieves information of a pollingChannel resource via a Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.13.7 [2] 7.3.22.2.2 |
| Pre-test conditions: | A pollingChannel resource < pollingChannel > has been created in application <AE> on the Registrar CSE A subscription to a <container> resource has been created using the <pollingChannel> as a notificationURI in the subscription. A single <contentInstance> resource is created in the subscribed to resource. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a pollingChannelURI Retrieve Request for <pollingChannelURI> |
| 2 | Mca | PRO Check Primitive | Sent RETRIEVE request contains To: <CSEBase>/<AE>/<pollingChannel>/pollingChannelURI Fr: AE-ID |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <CSEBase>/<AE>/<pollingChannel>/pollingChannelURI Host : Registar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: < pollingChannel > URI-Path: pollingChannelURI |
|  |  | PRO Check MQTT |  |
| 3 | Mca | PRO Check Primitive | Sent RETRIEVE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : OK Cn: pending Notification request |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: Response PRO Check Primitive with Content set with Notification request |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Response PRO Check Primitive with Content set with Notification request |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  |  | Repeat steps 1-2. There is no pending request. When the Request Expiration Timestamp expires Registrar sends response indicating “REQUEST_TIMEOUT” |
| 6 | Mca | PRO Check Primitive | Sent RETRIEVE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : REQUEST_TIMEOUT |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 408 |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 4.04 oneM2M-RSC = 4008 |
|  |  | PRO Check MQTT |  |
| IOP Verdict |  |
| PRO Verdict |  |

    - <node> Test Description

    - <fanOutPoint> Test Description

    - <mgmtObj> Test Description

    - <remoteCSE> Test Description

#### remoteCSE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | Registree CSE registers to Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.1 [2] 7.3.3.2.1 |
| Pre-test conditions: | Void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Create request to register to the Registrar CSE |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: <RegistrarCSE>?rty=16 Host : Registrar CSE Content Type option Payload: <remoteCSE> resource |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: rty=16 Payload: <remoteCSE> resource to be created |
|  |  | PRO Check MQTT |  |
| 3 |  | IOP Check | Check if possible that the remoteCSE resource is created in registrar CSE. |
| 4 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) Content-Location : <RegistrarCSE>/ <remoteCSE> Payload: created <remoteCSE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.01 Location-Path: <CSEBase> Location-Path: <remoteCSE > |
|  |  | PRO Check MQTT |  |
| 5 |  | IOP Check | Check if possible that the remoteCSE resource is created in registree CSE. |
| 6 |  | IOP Check | Registree CSE and Registrar CSE indicate successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### remoteCSE Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_02 |
| Objective: | Registree CSE retrieve remoteCSE resource from Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.2 [2] 7.3.3.2.2 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Retrieve request to the Registrar CSE |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <remoteCSE> |
|  |  | PRO Check MQTT |  |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) Payload: <remoteCSE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: <remoteCSE> resource |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Registree CSE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### remoteCSE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_03 |
| Objective: | MN-CSE registers to IN-CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.3 [2] 7.3.3.2.3 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Update request to the Registrar CSE |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request method = PUT Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Content Type option Payload: modified <remoteCSE> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <remoteCSE> Payload: <remoteCSE> updated resource |
|  |  | PRO Check MQTT |  |
| 3 |  | IOP Check | Check if possible that the remoteCSE resource has been updated in registrar CSE. |
| 4 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 Content-Location <RegistrarCSE>/<remoteCSE> Payload: updated <remoteCSE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 5 |  | IOP Check | Check if possible that the remoteCSE resource is also updated in registree CSE. |
| 6 |  | IOP Check | Registree CSE and Registrar CSE indicate successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### remoteCSE Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_04 |
| Objective: | MN-CSE cancels registration to IN-CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.4 [2] 7.3.3.2.4 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Update request to the Registrar CSE |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method = DELETE Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <remoteCSE> |
|  |  | PRO Check MQTT |  |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check if possible that the remoteCSE resource has been removed in registrar CSE. |
| 5 |  | IOP Check | Check if possible that the remoteCSE resource is also removed in registree CSE. |
| 6 |  | IOP Check | Registree CSE and Registrar CSE indicate successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

## Single hop configuration testing

## Editor’s Note: The proposal is to merge this part with no hop configuration testing. Because single hop is no difference than the connect of two no hop configuration testing. There is no need to duplicate the work here. People who participate the testing could simply go through the test description by the combination to two no hops.

### AE Management

#### AE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_05 |
| Objective: | AE creates a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.1.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Create Request to create an AE <AE> on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request URI <remoteCSE>?rty=2 Host : Registrar CSE Payload: resource <AE> to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: rty=2 Payload: <AE> resource to be created |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded POST request contains Request URI <remoteCSE>?rty=2 Host : remote CSE Payload: Resource <AE> to be created |
|  |  | PRO Check CoAP | Forwarded POST request contains Method: 0.02 (POST) Uri-Host: Remote CSE host Uri-Port: Remote CSE port Uri-Path: <remoteCSE> Uri-Query: rty=2 Payload: <AE> resource to be created |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check if possible that the <AE> resource is created in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE> Payload: Created <AE> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AE> |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: containing: Code = 201 Content-Location : <remoteCSE>/<AE> Payload: Created <AE> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forawards response to AE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AE> |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the created resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### AE Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_06 |
| Objective: | AE retrieves a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a AE Retrieve Request for resource <AE> |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <remoteCSE>/<AE> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>/<AE> Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <AE> resource |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.01 Payload: <AE> resource |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <AE> resource |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.01 Payload: <AE> resource |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### AE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_07 |
| Objective: | AE updates a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Update Request to update the resource. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI <remoteCSE>/<AE> Host : Registrar CSE Payload: modified <AE> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Payload: modified <AE> resource |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded PUT request contains Request URI < remoteCSE >/<AE> Host : remote CSE Payload: modified <AE>resource |
|  |  | PRO Check CoAP | Forwarded PUT request contains Method: 0.03 (PUT) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Payload: modified <AE> resource |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check if possible that the <AE> resource is updated in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: modified <AE> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <AE> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### AE Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_08 |
| Objective: | AE deletes a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <remoteCSE>/<AE> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded DELETE request contains Request URI <remoteCSE>/<AE> Host : Remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded DELETE request contains Method: 0.04 (DELETE) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar CSE Forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | Check if possible that the <AE> resource is deleted in remote CSE. |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Container Management

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_09 |
| Objective: | AE creates a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request to create container <container> on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request URI <remoteCSE>/<AE>?rty=3 Host : Registrar CSE Payload: resource <container> to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Query: rty=3 Payload: <container> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <Remote CSE-ID>/<CSEBase> fr = <AE-ID> rqi = <Request ID> ty = 3 pc = <Content(<container> resource representation)> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded POST request contains Request URI <remoteCSE>/<AE>?rty=3 Host : remote CSE Payload: resource <container> to be created |
|  |  | PRO Check CoAP | Forwarded POST request contains Method: 0.02 (POST) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Query: rty=3 Payload: <container> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: op = 1 to = <Remote CSE-ID>/<CSEBase> fr = <AE-ID> rqi = <AE-ID>/<Request ID> pc = <Content(<container> resource representation)> |
| 4 |  | IOP Check | Check if possible that the <container> resource is created in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code: 2.01 Location-Path: <remoteCSE> Location-Path: <AE> Location-Path: <container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Remote CSE-ID> rqi = <AE-ID>/<Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <container> resource representation)> |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code: 2.01 Location-Path: <RemoteCSE> Location-Path: <AE> Location-Path: <container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Remote CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <container> resource representation)> |
| 7 |  | IOP Check | AE indicates successful operation |
| 8 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 9 |  | IOP Check | Check the created resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_10 |
| Objective: | AE retrieves a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in < AE> in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Retrieve Request for resource <container> |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <remoteCSE>/<AE>/<container> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Uri-Path: <Container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Remote CSE-ID>/<CSEBase>/<container> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>/<AE>/<container> Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Uri-Path: <Container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: op = 2 to = <Remote CSE-ID>/<CSEBase>/<container> fr = <AE-ID> rqi = <AE-ID>/<Request ID> |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <container> resource |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.05 Payload: <container> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <AE-ID>/<Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <container> resource representation)> |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <container> resource |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 Payload: <container> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <container> resource representation)> |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_11 |
| Objective: | AE updates a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in < AE> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Update Request to update the resource. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI <remoteCSE>/<AE>/<container> Host : Registrar CSE Payload: modified resource <container> |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Uri-Path: <Container> Payload: <Container> resource updated |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <Remote CSE-ID>/<CSEBase>/<container> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded PUT request contains Request URI <remoteCSE>/<AE>/<container> Host : remote CSE Payload: modified <container> resource |
|  |  | PRO Check CoAP | Forwarded PUT request contains Method: 0.03 (PUT) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Uri-Path: <Container> Payload: <Container> resource updated |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: op = 3 to = <Remote CSE-ID>/<CSEBase>/<container> fr = <AE-ID> rqi = <AE-ID>/<Request ID> |
| 4 |  | IOP Check | Check if possible that the <container> resource is updated in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: modified <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <AE-ID>/<Request ID> rsc = <Response Status Code(2000)> pc = <Content(updated <container> resource representation)> |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(updated <container> resource representation)> |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_12 |
| Objective: | AE delete a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in < AE> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <remoteCSE>/<AE>/<container> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <Remote CSE-ID>/<CSEBase>/<container> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded DELETE request contains Request URI <remoteCSE>/<AE>/<container> Host : Remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded DELETE request contains Method: 0.04 (DELETE) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: op = 4 to = <Remote CSE-ID>/<CSEBase>/<container> fr = <AE-ID> rqi = <AE-ID>/<Request ID> |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <AE-ID>/<Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <container> resource representation> |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code> pc = <Content(deleted <container> resource representation> |
| 6 |  | IOP Check | Check if possible that the <container> resource is deleted in remote CSE.. |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### ContentInstance Management

#### ContentInstance Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_13 |
| Objective: | AE creates a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.2 [2] 7.3.7.2.1 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in <AE> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a ContentInstance Create Request to create a ContentInstance <contentInstance> on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request URI : <remoteCSE>/<AE>/<container> ?rty=4 Host : Registrar CSE Payload: resource <contentInstance> to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Query: rty=4 Payload: <contentInstance> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <Remote CSE-ID>/<CSEBase>/<container> fr = <AE-ID> rqi = <Request ID> ty = 4 pc = <Content(<contentInstance> resource representation)> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded POST request contains Request URI : <remoteCSE>/<AE>/<container>?rty=4 Host : remote CSE Payload: resource <contentInstance> to be created |
|  |  | PRO Check CoAP | Forwarded POST request contains Method: 0.02 Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Query: rty=4 Payload: <contentInstance> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: op = 1 to = <Remote CSE-ID>/<CSEBase>/<container> fr = <AE-ID> rqi = <AE-ID>/<Request ID> pc = <Content(<contentInstance> resource representation)> |
| 4 |  | IOP Check | Check if possible that the <ContentInstance> resource is created in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<contentInstance> Payload: Created <contentInstance> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AE> Location-Path: <container> Location-Path: <contentInstance> |
|  |  | PRO Check MQTT | Sends a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Remote CSE-ID> rqi = <AE-ID>/<Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <contentInstance> resource representation)> |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<contentInstance> Payload: Created <ContentInstance> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AE> Location-Path: <container> Location-Path: <contentInstance> |
|  |  | PRO Check MQTT | Sends a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Remote CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <contentInstance> resource representation)> |
| 7 |  | IOP Check | AE indicates successful operation |
| 8 |  |  | Repeat step 1-7 creating ContentInstance resource with short lifetime |
| 9 |  | IOP Check | Check the created resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### ContentInstance Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_14 |
| Objective: | AE retrieves a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.3 [2] 7.3.7.2.2 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in <AE> Resource <contentInstance> has been created in <container> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a ContentInstance Retrieve Request for resource <ContentInstance> |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI : <remoteCSE>/<AE>/<container>/<contentInstance> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path <ContentInstance> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Remote CSE-ID>/<CSEBase>/<container>/<contentInstance> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>/<AE>/<container>/<contentInstance> Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path <ContentInstance> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: op = 2 to = <Remote CSE-ID>/<CSEBase>/<container>/<contentInstance> fr = <AE-ID> rqi = <AE-ID>/<Request ID> |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <contentInstance> resource |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.05 Payload: <container> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <AE-ID>/<Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <contentInstance> resource representation)> |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <contentInstance> resource |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 Payload: <container> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <contentInstance> resource representation)> |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### ContentInstance Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_15 |
| Objective: | AE deletes a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.5 [2] 7.3.7.2.4 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in <AE> Resource <contentInstance> has been created in <container> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a ContentInstance Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI : <remoteCSE>/<AE>/<container>/<contentInstance> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <ContentInstance> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <Remote CSE-ID>/<CSEBase>/<container>/<contentInstance> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded DELETE request contains Request URI : <remoteCSE>/<AE>/<container>/<contentInstance> Host : Remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded DELETE request contains Method: 0.04 (DELETE) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <ContentInstance> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: op = 4 to = <Remote CSE-ID>/<CSEBase>/<container>/<contentInstance> fr = <AE-ID> rqi = <AE-ID>/<Request ID> |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <AE-ID>/<Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <contentInstance> resource representation> |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code> pc = <Content(deleted <contentInstance> resource representation> |
| 6 |  | IOP Check | Check if possible that the <contentInstance> resource is deleted in remote CSE. |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Discovery

#### Discovery of all resources

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_16 |
| Objective: | AE discovers resources located in remote CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a discovery request to discover all accessible resources located in remote CSE |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <remoteCSE>?fu=1 Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>?fu=1 Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: Data object containing addresses of all the found resources |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 Payload: Data object containing addresses for all the found resources |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 Payload: Data object containing addresses for all the found resources |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Data object containing addresses for all the found resources. |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Discovery with label filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_17 |
| Objective: | AE discovers accessible resources located in remote CSE using label filter criteria |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created a Container resource <Container> having "key1" as label on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a discovery request to discover the <Container> resource using label filter criteria in remote CSE |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <remoteCSE>?fu=1&lbl=key1 Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lbl=key1 Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>?fu=1&lbl=key1 Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lbl=key1 Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: Data object containing address of the <AE> resource |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 Payload: Data object containing address of the <AE> resource |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: Data object containing address of the <Container> resource |
|  |  | PRO Check CoAP | Registrar sends response to AE containing: Response Code = 2.05 Payload: Data object containing address of the <Container> resource |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Discovery with limit filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_18 |
| Objective: | AE discovers accessible resources located in remote CSE using the limit filter criteria |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a discovery request to discover at most 2 resources in remote |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <remoteCSE>?fu=1&lim=2 Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lim=2 Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>?fu=1&lim=2 Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lim=2 Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: Data object containing at most 2 addresses of the found resources |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 Payload: Data object containing at most 2 addresses of the found resources |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: Data object containing at most 2 addresses of the found resources |
|  |  | PRO Check CoAP | Registrar sends response to AE containing: Response Code = 2.05 Payload: Data object containing at most 2 addresses of the found resources |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Discovery with multiple filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_19 |
| Objective: | AE discovers accessible resources located in remote CSE using multiple filter criteria |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created a Container resource having as labels "key1" and "key2" on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request to discover the <Container> resource using multiple filter criteria |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <remoteCSE>?fu=1&lbl=key1&lbl=key2&lim=1 Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lbl=key1 Uri-Query: lbl=key2 Uri-Query: lim=1 Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>?fu=1&lbl=key1&lbl=key2&lim=1 Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: fu=1 Uri-Query: lbl=key1 Uri-Query: lbl=key2 Uri-Query: lim=1 Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: Data object containing address of the <Container> resource |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 Payload: Data object containing address of the <Container> resource |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: Data object containing address of the <Container> resource |
|  |  | PRO Check CoAP | Registrar sends response to AE containing: Response Code = 2.05 Payload: Data object containing address of the <Container> resource |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Subscription Management

#### Subscription Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_20 |
| Objective: | AE creates a remote Subscription resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.11.1 [2] 7.3.8.2.1 |
| Pre-test conditions: | AE has created an application resource <AE> on remote CSE AE has created a container resource <container> on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Subscription Create Request to create a <Subscription> resource on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request URI <remoteCSE>/<AE>/<container>?rty=23 Host : Registrar CSE Payload: resource <Subscription> to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Query: rty=23 Payload: <Subscription> resource to be created |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded POST request contains Request URI <remoteCSE>/<AE>/<container>?rty=23 Host : remote CSE Payload: Resource < Subscription > to be created |
|  |  | PRO Check CoAP | Forwarded POST request contains Method: 0.02 (POST) Uri-Host: Remote CSE host Uri-Port: Remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Query: rty=23 Payload: < Subscription > resource to be created |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | that the <Subscription> resource is created in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<Subscription> Payload: Created <Subscription> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AE> Location-Path: <Container> Location-Path: <Subscription> |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> /<Subscription> Payload: Created <Subscription> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forawards response to AE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AE> Location-Path: <Container> Location-Path: <Subscription> |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Subscription Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_21 |
| Objective: | AE retrieves a remote Subscription resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.11.2 [2] 7.3.8.2.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on remote CSE AE has created a container resource <container> on remote CSE AE has created a subscription resource <subscription> on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Subscription Retrieve Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <remoteCSE>/<AE>/<container>/<Subscription> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <Subscription> resource |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.01 Payload: <Subscription> resource |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <Subscription> resource |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.01 Payload: <Subscription> resource |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Subscription Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_22 |
| Objective: | AE updates a remote Subscription resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.11.3 [2] 7.3.8.2.3 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on remote CSE AE has created a container resource <container> on remote CSE AE has created a subscription resource <subscription> on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Subscription Update Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : Registrar CSE Payload: modified <Subscription> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: modified <Subscription> resource |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded PUT request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : remote CSE Payload: modified <Subscription> resource |
|  |  | PRO Check CoAP | Forwarded PUT request contains Method: 0.03 (PUT) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remote CSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: modified <Subscription> resource |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check that the <Subscription> resource is updated in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: modified <Subscription> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <Subscription> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Subscription Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_23 |
| Objective: | AE deletes a remote Subscription resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.11.4 [2] 7.3.8.2. |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on remote CSE AE has created a container resource <container> on remote CSE AE has created a subscription resource <subscription> on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Subscription delete request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded DELETE request contains Request URI <remoteCSE>/<AE>/<container> /<Subscription> Host : Remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded DELETE request contains Method: 0.04 (DELETE) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AE> Uri-Path: <Container> Uri-Path: <Subscription> Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check that the <Subscription> resource is deleted from remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar CSE Forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Container Announce

#### Container Create with announceTo

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_24 |
| Objective: | AE creates a container resource and announces it to a remote CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE AE is registered to Registrar-CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request and announce the container |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request URI <Registrar-CSE>?rty=3 Host : Registrar CSE Payload: resource <container> to be created (payload includes announeTo attribute with value <Hosting-CSE> and announcedAttribute with value of <announcable attribute> |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <RegistrarCSE> Uri-Query: rty=3 Payload: resource <container> to be created (payload includes announeTo attribute with value <Hosting-CSE> and announcedAttribute with value of <announcable attribute> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase> fr = <AE-ID> ty = 3 rqi = <Request ID (A)> pc = <Content(<container> resource representation including announceTo attribute set to <Remote CSE-ID>/<CSEBase> and announcedAttribute attribute)> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Send POST request contains Request URI <Hosting-CSE>?rty=10003 Host : Hosting-CSE Payload: Resource <containerAnnc> to be created with <announcable attribute> |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Hosting-CSE host Uri-Port: Hosting-CSE port Uri-Path: < Hosting-CSE > Uri-Query: rty=10003 Payload: Resource <containerAnnc> to be created with <announcable attribute> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: op = 1 to = <Remote CSE-ID>/<CSEBase> fr = <Registrar CSE-ID> ty = 10003 rqi = <Request ID (B)> pc = <Content(<containerAnnc> resource representation)> |
| 4 |  | IOP Check | Check if possible that the <containerAnnc> resource is created in Hosting-CSE with the <announcable attribute> |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <Hosting-CSE>/<containerAnnc> Payload: Created <containerAnnc> |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.01 Location-Path: <Hosting-CSE> Location-Path: <containerAnnc> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: to = <Registrar CSE-ID> fr = <Remote CSE-ID> rqi = <Request ID (B)> rsc = <Response Status Code(2001)> pc = <Content(created <containerAnnc> resource representation)> |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE responds to AE containing: Code = 201 Content-Location : < Registrar-CSE >/<container> Payload: Created <container> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE responds to AE containing: Response Code = 2.01 Location-Path: < Hosting-CSE > Location-Path: <containerAnnc> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID (A)> rsc = <Response Status Code(2001)> pc = <Content(created <container> resource representation)> |
| 7 |  | IOP Check | AE indicates successful operation |
| 8 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 9 |  | IOP Check | Check the created resource is removed after the expiry of its lifetime. Check that the announced resource is removed after the expiry of its lifetime. |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Retrieve Announced Resource Information

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_25 |
| Objective: | AE retrieves announced container resource information |
| Configuration: | M2M_CFG_04 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | CSE1 is registered to CSE2 Resource <container1> has been created in CSE1 Resource <container1Annc> has been created in CSE2 AE2 is registered to CSE2 |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE2 is requested to send a container Retrieve Request for resource <container1Annc> |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI < CSE2>/<container1annc> Host : CSE2 Payload: empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE2-ID>/<CSE2-ID>” Payload: op = 2 to = <CSEBase>/<containerAnnc> fr = <AE2-ID> rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | CSE2 sends response to AE2 containing: Code = 200 Payload: <containerAnnc> resource |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE2-ID>/<CSE2-ID>” Payload: to = <SP-Relative-AE2-ID> fr = <CSE2-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <containerAnnc> resource representation> |
| 4 |  | IOP Check | AE2 indicates successful operation |
| 5 |  | Stimulus | AE2 is requested to send a Retrieve Request for resource <container1Annc> with Result Content set to “original-resource” |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | AE2 sends GET request containing: Request URI <CSE2>/<container1Annc> Result Content “original-resource” Host : CSE2 Payload: empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase>/<containerAnnc> fr = <AE-ID> rqi = <Request ID> rcn = 7 (original-resource) |
| 7 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | CSE2 forwards GET request to CSE1 containing: Request URI <CSE1>/<container1> Host : CSE1 Payload: empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<CSE2-ID>/<CSE1-ID>” Payload: op = 2 to = <CSE1-ID>/<CSEBase>/<container> fr = <CSE2-ID> rqi = <Request ID> |
| 8 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | CSE1 sends response to CSE2 containing: Code = 200 Payload: <container1> resource |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<CSE2-ID>/<CSE1-ID>” Payload: to = <CSE2-ID> fr = <CSE1-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <container> resource representation)> |
| 9 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | CSE2 forwards response to AE2 containing: Code = 200 Payload: <container> resource |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE2-ID>/<CSE2-ID>” Payload: to = <SP-Relative-AE2-ID> fr = <CSE2-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(retrieved <container> resource representation)> |
| 10 |  | IOP Check | AE2 indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Update AnnounceTo Attribute

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_26 |
| Objective: | AE announces container to a remote CSE by updating announceTo resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE Resource <container> has been created on Registrar-CSE and the <container> resource has no announceTo attribute value. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Update Request to update the resource. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI <Registrar-CSE> Host : Registrar CSE Payload: resource <container> containing announceTo attribute with value <Hosting-CSE> |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <CSEBase>/<container> fr = <AE-ID> rqi = <Request ID> pc = <Content(<container> resource representation including announceTo attribute value with <Hosting CSE-ID>/<CSEBase>)> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Send POST request contains Request URI <Hosting-CSE>?rty=cntA Host : Hosting-CSE Payload: Resource <containerAnnc> to be created |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Hosting CSE-ID>” Payload: op = 1 to = <Hosting CSE-ID>/<CSEBase> fr = <Registrar CSE-ID> rqi = <Request ID> pc = <Content(<containerAnnc> resource representation)> |
| 4 |  | IOP Check | Check if possible that the <containerAnnc> resource is created in Hosting-CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <Hosting-CSE>/<containerAnnc> Payload: Created <containerAnnc> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Hosting CSE-ID>” Payload: to = <Registrar CSE-ID> fr = <Hosting CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <containerAnnc> resource representation> |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <container> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(updated <container> resource representation> |
| 7 |  | IOP Check | AE indicates successful operation |
| 8 |  | Stimulus | AE is requested to send an container Update Request (PUT) to update the resource. |
| 9 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI <Registrar-CSE> Host : Registrar CSE Payload: resource <container> containing announceTo attribute with value empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <CSEBase>/<container> fr = <AE-ID> rqi = <Request ID> pc = <Content(<container> resource representation including announceTo attribute set as empty(NULL))> |
| 10 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Send DELETE request contains Request URI <Hosting-CSE> Host : Hosting-CSE Payload: empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Hosting CSE-ID>” Payload: op = 4 to = <Hosting CSE-ID>/<CSEBase>/<containerAnnc> fr = <Registrar CSE-ID> rqi = <Request ID> |
| 11 |  | IOP Check | Check if possible that the <containerAnnc> resource is deleted in Hosting-CSE. |
| 12 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Payload: empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Hosting CSE-ID>” Payload: to = <Registrar CSE-ID> fr = <Hosting CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <containerAnnc> resource representation> |
| 13 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <container> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(updated <container> resource representation> |
| 14 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Delete AnnounceTo

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_27 |
| Objective: | AE deletes an container resource and de-announces it from a remote CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE Resource <container> has been created on Registrar-CSE Resource <containerAnnc> has been created in Hosting-CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an container Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <Registrar-CSE>/<container> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase>/<container> fr = <AE-ID> rqi = <Request ID> |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI < Hosting-CSE >/<containerAnnc> Host : Hosting-CSE Payload: empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Hosting CSE-ID>” Payload: op = 4 to = <Hosting CSE-ID>/<CSEBase>/<containerAnnc> fr = <Registrar CSE-ID> rqi = <Request ID> |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Hosting CSE-ID>” Payload: to = <Registrar CSE-ID> fr = <Hosting CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <containerAnnc> resource representation)> |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP |  |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(deleted <container> resource representation)> |
| 6 |  | IOP Check | Check if possible that the <containerAnnc> resource is deleted in Hosting-CSE and <container> resource is deleted in Registrar-CSE |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### AccessControlPolicy Management

#### AccessControlPolicy Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_28 |
| Objective: | AE creates a remote AccessControlPolicy resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.21.1 [2] 7.3.2.2.1 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AccessControlPolicy Create Request to create an <AccessControlPolicy> resource on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request URI <remoteCSE>?rty=1 Host : Registrar CSE Payload: resource <AccessControlPolicy> to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: rty=1 Payload: <AccessControlPolicy> resource to be created |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded POST request contains Request URI <remoteCSE>?rty=1 Host : remote CSE Payload: Resource < AccessControlPolicy > to be created |
|  |  | PRO Check CoAP | Forwarded POST request contains Method: 0.02 (POST) Uri-Host: Remote CSE host Uri-Port: Remote CSE port Uri-Path: <remoteCSE> Uri-Query: rty=1 Payload: < AccessControlPolicy > resource to be created |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check if possible that the <AccessControlPolicy> resource is created in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AccessControlPolicy> Payload: Created <AccessControlPolicy> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AccessControlPolicy> |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: containing: Code = 201 Content-Location : <remoteCSE>/<AccessControlPolicy> Payload: Created <AccessControlPolicy> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forawards response to AE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <AccessControlPolicy> |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### AccessControlPolicy Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_29 |
| Objective: | AE retrieves a remote AccessControlPolicy resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.21.2 [2] 7.3.2.2.2 |
| Pre-test conditions: | Resource <AccessControlPolicy> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a AccessControlPolicy Retrieve Request for resource <AccessControlPolicy> |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <remoteCSE>/<AccessControlPolicy> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AccessControlPolicy> Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>/<AccessControlPolicy> Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AccessControlPolicy> Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <AccessControlPolicy> resource |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.01 Payload: <AccessControlPolicy> resource |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <AccessControlPolicy> resource |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.01 Payload: <AccessControlPolicy> resource |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### AccessControlPolicy Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_30 |
| Objective: | AE updates a remote AccessControlPolicy resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.21.3 [2] 7.3.2.2.3 |
| Pre-test conditions: | Resource <AccessControlPolicy> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AccessControlPolicy Update Request to update the resource. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI <remoteCSE>/<AccessControlPolicy> Host : Registrar CSE Payload: modified <AccessControlPolicy> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remote CSE> Uri-Path: <AccessControlPolicy> Payload: modified <AccessControlPolicy> resource |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded PUT request contains Request URI < remoteCSE >/<AccessControlPolicy> Host : remote CSE Payload: modified <AccessControlPolicy> resource |
|  |  | PRO Check CoAP | Forwarded PUT request contains Method: 0.03 (PUT) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remote CSE> Uri-Path: <AccessControlPolicy> Payload: modified <AccessControlPolicy> resource |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check if possible that the <AccessControlPolicy> resource is updated in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: modified <AccessControlPolicy> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <AccessControlPolicy> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### AccessControlPolicy Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_31 |
| Objective: | AE deletes a remote AccessControlPolicy resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.21.4 [2] 7.3.2.2.4 |
| Pre-test conditions: | Resource <AccessControlPolicy> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AccessControlPolicy Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <remoteCSE>/<AccessControlPolicy> Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <AccessControlPolicy> Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded DELETE request contains Request URI <remoteCSE>/<AccessControlPolicy> Host : Remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded DELETE request contains Method: 0.04 (DELETE) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <AccessControlPolicy> Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar CSE Forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Group  Management

#### Group  Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_32 |
| Objective: | AE creates a remote Group resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.21.1 [2] 7.3.2.2.1 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an Group Create Request to create an <Group > resource on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent POST request contains Request URI <remoteCSE>?rty=9 Host : Registrar CSE Payload: resource <Group > to be created |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: rty=9 Payload: <Group > resource to be created |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded POST request contains Request URI <remoteCSE>?rty=9 Host : remote CSE Payload: Resource < Group > to be created |
|  |  | PRO Check CoAP | Forwarded POST request contains Method: 0.02 (POST) Uri-Host: Remote CSE host Uri-Port: Remote CSE port Uri-Path: <remoteCSE> Uri-Query: rty=9 Payload: < Group > resource to be created |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check that the <Group > resource is created in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<Group > Payload: Created <Group > (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <Group > |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: containing: Code = 201 Content-Location : <remoteCSE>/<Group > Payload: Created <Group > (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forawards response to AE containing: Response Code = 2.01 Location-Path: <remoteCSE> Location-Path: <Group > |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Group  Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_33 |
| Objective: | AE retrieves a remote Group resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.21.2 [2] 7.3.2.2.2 |
| Pre-test conditions: | Resource <Group > has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Group Retrieve Request for resource <Group > |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent GET request contains Request URI <remoteCSE>/<Group > Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <Group > Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded GET request contains Request URI <remoteCSE>/<Group > Host : remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded GET request contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <Group > Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <Group > resource |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.01 Payload: <Group > resource |
|  |  | PRO Check MQTT |  |
| 5 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: <Group > resource |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.01 Payload: <Group > resource |
|  |  | PRO Check MQTT |  |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Group  Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_34 |
| Objective: | AE updates a remote Group resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.21.3 [2] 7.3.2.2.3 |
| Pre-test conditions: | Resource <Group > has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an Group Update Request to update the resource. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI <remoteCSE>/<Group > Host : Registrar CSE Payload: modified <Group > resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remote CSE> Uri-Path: <Group > Payload: modified <Group > resource |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded PUT request contains Request URI < remoteCSE >/<Group > Host : remote CSE Payload: modified <Group > resource |
|  |  | PRO Check CoAP | Forwarded PUT request contains Method: 0.03 (PUT) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remote CSE> Uri-Path: <Group > Payload: modified <Group > resource |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check that the <Group > resource is updated in remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: modified <Group > (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <Group > (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Group  Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_35 |
| Objective: | AE deletes a remote Group resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.21.4 [2] 7.3.2.2.4 |
| Pre-test conditions: | Resource <Group > has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an Group Delete Request |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI <remoteCSE>/<Group > Host : Registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <Group > Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Forwarded DELETE request contains Request URI <remoteCSE>/<Group > Host : Remote CSE Payload: empty |
|  |  | PRO Check CoAP | Forwarded DELETE request contains Method: 0.04 (DELETE) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <Group > Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check that the <Group > resource is deleted from remote CSE. |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Remote CSE sends response to registrar CSE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 6 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  |  | PRO Check CoAP | Registrar CSE Forwards response to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 7 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

## Multi Hop configuration testing

- Editor’s Note: The proposal is to merge this part with no hop configuration testing. The reason is the same as the one described in single hop configuration testing.

### Container Management

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_01 |
| Objective: | AE creates a container resource in remote CSE |
| Configuration: | M2M_CFG_06 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Request to create a container resource <container> on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent request contains Method: POST Request URI <remoteCSE>?rty=3 Host : Registrar CSE Payload: <container> resource to be created |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Query: rty=3 Payload: <container> resource to be created |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards request to transit CSE containing: Method: POST Request URI <remoteCSE>?rty=3 Host : transit CSE Payload: <container> resource to be created |
|  |  | PRO Check CoAP | Registrar CSE forwards request to transit CSE containing: Method: 0.02 (POST) Uri-Host: transit CSE host Uri-Port: transit CSE port Uri-Path: <remoteCSE> Uri-Query: rty=3 Payload: <container> resource to be created |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE forwards request to remote CSE containing: Method: POST Request URI <remoteCSE>?rty=3 Host : remote CSE Payload: <container> resource to be created |
|  |  | PRO Check CoAP | Transit CSE forwards request to remote CSE containing: Method: 0.02 (POST) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Query: rty=3 Payload: <container> resource to be created |
|  |  | PRO Check MQTT |  |
| 5 |  | IOP Check | Check if possible that the <container> resource is created in remote CSE. |
| 6 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to transit CSE containing: Code = 201 Content-Location : <remoteCSE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to transit CSE containing: Response Code: 2.01 Location-Path: <remoteCSE> Location-Path: <container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check MQTT |  |
| 7 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Transit CSE sends response to registrar CSE containing: Response Code: 2.01 Location-Path: <remoteCSE> Location-Path: <container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check MQTT |  |
| 8 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | transit CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | transit CSE forwards response to AE containing: Response Code: 2.01 Location-Path: <RemoteCSE> Location-Path: <container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check MQTT |  |
| 9 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_02 |
| Objective: | AE retrieves a container resource in remote CSE |
| Configuration: | M2M_CFG_06 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | AE has created a Container resource <container> on remote CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Request to retrieve a container resource <container> on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent request contains Method: GET Request URI <remoteCSE>/<Container> Host : Registrar CSE Payload: Empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards request to transit CSE containing: Method: GET Request URI <remoteCSE>/<Container> Host : transit CSE Payload: Empty |
|  |  | PRO Check CoAP | Registrar CSE forwards request to transit CSE containing: Method: 0.01 (GET) Uri-Host: transit CSE host Uri-Port: transit CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE forwards request to remote CSE containing: Method: GET Request URI <remoteCSE>/<Container> Host : remote CSE Payload: Empty |
|  |  | PRO Check CoAP | Transit CSE forwards request to remote CSE containing: Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | PRO Check MQTT |  |
| 5 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to transit CSE containing: Code = 200 Payload: <container> resource |
|  |  | PRO Check CoAP | Remote CSE sends response to transit CSE containing: Response Code: 2.05 Payload: <container> resource |
|  |  | PRO Check MQTT |  |
| 6 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE sends response to registrar CSE containing: Code = 200 Payload: <container> resource |
|  |  | PRO Check CoAP | Transit CSE sends response to registrar CSE containing: Response Code: 2.05 Payload: <container> resource |
|  |  | PRO Check MQTT |  |
| 7 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE forwards response to AE containing: Code = 200 Payload: <container> resource |
|  |  | PRO Check CoAP | Transit CSE forwards response to AE containing: Response Code: 2.05 Payload: <container> resource |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_03 |
| Objective: | AE updates a container resource in remote CSE |
| Configuration: | M2M_CFG_06 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | AE updates a container resource on remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a request to update the <container> resource on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent request contains Method: PUT Request URI <remoteCSE>/<Container> Host : Registrar CSE Payload: Updated <Container> |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Updated <Container> |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards request to transit CSE containing: Method: PUT Request URI <remoteCSE>/<Container> Host : transit CSE Payload: Empty |
|  |  | PRO Check CoAP | Registrar CSE forwards request to transit CSE containing: Method: 0.03 (PUT) Uri-Host: transit CSE host Uri-Port: transit CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Updated <Container> |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE forwards request to remote CSE containing: Method: PUT Host : remote CSE Request URI <remoteCSE>/<Container> Payload: Updated <Container> |
|  |  | PRO Check CoAP | Transit CSE forwards request to remote CSE containing: Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Updated <Container> |
|  |  | PRO Check MQTT |  |
| 5 |  | IOP Check | if possible that the <container> resource is updated in remote CSE. |
| 6 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to transit CSE containing: Code = 200 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Remote CSE sends response to transit CSE containing: Response Code: 2.05 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check MQTT |  |
| 7 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE sends response to registrar CSE containing: Code = 200 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Transit CSE sends response to registrar CSE containing: Response Code: 2.05 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check MQTT |  |
| 8 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE forwards response to AE containing: Code = 200 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | Transit CSE forwards response to AE containing: Response Code: 2.05 Payload: <container> resource (assigned and/or modified attributes) |
|  |  | PRO Check MQTT |  |
| 9 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_04 |
| Objective: | AE retrieves a container resource in remote CSE |
| Configuration: | M2M_CFG_06 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | AE has created a Container resource <container> on remote CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a request to delete the <container> resource on remote CSE. |
| 2 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Sent request contains Method: DELETE Request URI <remoteCSE>/<Container> Host : Registrar CSE Payload: Empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | PRO Check MQTT |  |
| 3 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Registrar CSE forwards request to transit CSE containing: Method: DELETE Request URI <remoteCSE>/<Container> Host : transit CSE Payload: Empty |
|  |  | PRO Check CoAP | Registrar CSE forwards request to transit CSE containing: Method: 0.04 (DELETE) Uri-Host: transit CSE host Uri-Port: transit CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | PRO Check MQTT |  |
| 4 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE forwards request to remote CSE containing: Method: DELETE Request URI <remoteCSE>/<Container> Host : remote CSE Payload: Empty |
|  |  | PRO Check CoAP | Transit CSE forwards request to remote CSE containing: Method: 0.04 (DELETE) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> Uri-Path: <Container> Payload: Empty |
|  |  | PRO Check MQTT |  |
| 5 |  | IOP Check | Check if possible that the <container> resource is deleted in remote CSE. |
| 6 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Remote CSE sends response to transit CSE containing: Code = 200 Payload: Empty |
|  |  | PRO Check CoAP | Remote CSE sends response to transit CSE containing: Response Code: 2.05 Payload: Empty |
|  |  | PRO Check MQTT |  |
| 7 | Mcc | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE sends response to registrar CSE containing: Code = 200 Payload: Empty |
|  |  | PRO Check CoAP | Transit CSE sends response to registrar CSE containing: Response Code: 2.05 Payload: Empty |
|  |  | PRO Check MQTT |  |
| 8 | Mca | PRO Check Primitive |  |
|  |  | PRO Check HTTP | Transit CSE forwards response to AE containing: Code = 200 Payload: Empty |
|  |  | PRO Check CoAP | Transit CSE forwards response to AE containing: Response Code: 2.05 Payload: Empty |
|  |  | PRO Check MQTT |  |
| 9 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### -----------------------End of change 1--------------------------------------------

# Comments

CSEBase resource ID is not part of hierarchical URI

Is there payload ???