| Input Contribution |
| --- |
| Meeting ID* | TST18 |
| Title:* | Test Description for CRUDN |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd. , yinjiaxin@huawei.com |
| Uploaded Date:* | 2015-7-10 |
| Document(s) Impacted* | WI-0022, TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text to TS-0013 if agreed. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The contribution if proposing a common CRUDN test description that applies to most of the resource operations.

### -----------------------Start of change 1-------------------------------------------

### Test Description for Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_C |
| Objective: | AE or CSE creates a <resource> in Registrar CSE which is the Hosting CSE . |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.1.1 |
| Pre-test conditions: | Registrartion Security |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE or CSE requests to create <resource> in Hosting CSE. |
| 2 | Mca | PRO Check Primitive | AE or CSE sends Create request to the Hosting CSE. fr: The ID of the AE or CSE who originates the request. to: The ID of the parent resource for Create op: Create cn: Representation of the resource to be created |
|  |  | PRO Check HTTP | Sent POST request contains Request method: POST Request URI: The ID of the parent resource of the <resource> Host : IP address or the FQDN of the Hosting CSE Query: rty=type of <resource> Payload: xml or json serilization of cn in the primitive. |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: IP address or the FQDN of the Hosting CSE Uri-Port: Registrar CSE port Uri-Path: The ID of the parent resource of the <resource> Uri-Query: rty=type of <resource> Payload: xml or json serilization of cn in the primitive |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = The ID of the parent resource of the <resource> fr = The ID of the AE or CSE who originates the request rqi = <Request ID> ty = 3 pc = <Content(<content> resource representation)> |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response to AE or CSE. rsc: 2001 “Created” cn: Representation of the Created resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 2001 Content-Location: ID of the created resource. Payload: Representation of the Created resource |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.01 (2001 Created) Location-Path: The ID of the created resource. Payload: Representation of the Created resource |
|  |  | PRO Check MQTT | Registrar CSE sends a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2001)> pc = <Content(created <content> resource representation> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Test Description for Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_U |
| Objective: | AE or CSE updates a <resource> in Registrar CSE which is the Hosting CSE . |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.1.3 |
| Pre-test conditions: | Registrartion Security |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE or CSE requests to update <resource> in Hosting CSE. |
| 2 | Mca | PRO Check Primitive | AE or CSE sends Update request to the Hosting CSE. fr: The ID of the AE or CSE who originates the request. to: The ID of the resource to be Updated op: Update cn: Representation of the resource to be created |
|  |  | PRO Check HTTP | Sent PUT request contains Request method: PUT Request URI: The ID of the resource to be Updated Host : IP address or the FQDN of the Hosting CSE Query: rty=type of <resource> Payload: xml or json serilization of cn in the primitive. |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: IP address or the FQDN of the Hosting CSE Uri-Port: Registrar CSE port Uri-Path: The ID of the <resource> Uri-Query: rty=type of <resource> Payload: xml or json serilization of cn in the primitive |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = The ID of the <resource> fr = The ID of the AE or CSE who originates the request rqi = <Request ID> ty = type of <resource> pc = <Content(<content> resource representation)> |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response to AE or CSE. rsc: 2004 “Changed” cn: Representation of the Updated resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 Payload: xml or json serilization of cn in the primitive |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.05 Payload: xml or json serilization of cn in the primitive |
|  |  | PRO Check MQTT | Registrar CSE sends a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = <Content(updated <resource> representation> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Test Description for Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_R |
| Objective: | AE or CSE retrieves a <resource> in Registrar CSE which is the Hosting CSE . |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.1.2 |
| Pre-test conditions: | Registrartion Security |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE or CSE requests to retrieve <resource> in Hosting CSE. |
| 2 | Mca | PRO Check Primitive | AE or CSE sends Retrieve request to the Hosting CSE. fr: The ID of the AE or CSE who originates the request. to: The ID of the resource to be Retrieved op: Retrieve |
|  |  | PRO Check HTTP | Sent GET request contains Request method: GET Request URI: The ID of the resource to be Retrieved Host : IP address or the FQDN of the Hosting CSE |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of the Hosting CSE Uri-Port: Registrar CSE port Uri-Path: The ID of the <resource> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = The ID of the <resource> fr = The ID of the AE or CSE who originates the request rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response to AE or CSE. rsc: 2000 “OK” cn: Representation of the Updated resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 Payload: xml or json serilization of cn in the primitive |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.00 Payload: xml or json serilization of cn in the primitive |
|  |  | PRO Check MQTT | Registrar CSE sends a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> pc = xml or json serilization of cn in the primitive |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Test Description for Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_D |
| Objective: | AE or CSE deletes a <resource> in Registrar CSE which is the Hosting CSE . |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.1.4 |
| Pre-test conditions: | Registrartion Security |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE or CSE requests to delete <resource> in Hosting CSE. |
| 2 | Mca | PRO Check Primitive | AE or CSE sends Delete request to the Hosting CSE. fr: The ID of the AE or CSE who originates the request. to: The ID of the resource to be Deleted op: Delete |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method: DELETE Request URI: The ID of the resource to be Deleted Host : IP address or the FQDN of the Hosting CSE |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: IP address or the FQDN of the Hosting CSE Uri-Port: Registrar CSE port Uri-Path: The ID of the <resource> |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = The ID of the <resource> fr = The ID of the AE or CSE who originates the request rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response to AE or CSE. rsc: 2002 “DELETED” |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.05 |
|  |  | PRO Check MQTT | Registrar CSE sends a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2002)> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### Test Description for Notify

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_N |
| Objective: | CSE sends a Notify to an AE or CSE |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.1.5 |
| Pre-test conditions: | Registrartion Security |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | CSE notifies a CSE or AE. |
| 2 | Mca | PRO Check Primitive | CSE sends Notify request to the AE or CSE. fr: The ID of the CSE who originates the request. to: The notification URI op: Notify cn : Notify content |
|  |  | PRO Check HTTP | Sent POST request contains Request method: POST Request URI: notification URI Host : IP address or the FQDN of the AE/CSE Payload: Notify content |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: IP address or the FQDN of the AE/CSE Uri-Port: Registrar CSE port Uri-Path: notification URI |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 5 to = notification URI fr = The ID of the CSE who originates the request rqi = <Request ID> |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response to AE or CSE. rsc: 2000 “OK” |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.00 |
|  |  | PRO Check MQTT | Registrar CSE sends a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = <SP-Relative-AE-ID> fr = <Registrar CSE-ID> rqi = <Request ID> rsc = <Response Status Code(2000)> |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### -----------------------End of change 1--------------------------------------------