| Input Contribution |
| --- |
| Meeting ID* | TST18 |
| Title:* | Test Description for NonBlockingRequest |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd. , yinjiaxin@huawei.com |
| Uploaded Date:* | 2015-7-10 |
| Document(s) Impacted* | WI-0022, TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the contribution to the TS if agreed. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

The contribution is modified from clause 8.2 of TS-0013

### -----------------------Start of change 1-------------------------------------------

### Test Description for Non-blocking Requests

#### Synchronous request

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_01 |
| Objective: | AE or CSE addresses a <resource> using non blocking synchronous request in Hosting CSE. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | A <resource> has been created on the Hosting CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE or CSE is requested to send a non blocking synchronous request to address the <resource> in Hosting CSE. |
| 2 | Mca | PRO Check Primitive | AE or CSE sends request primitive to the Hosting CSE. fr: The ID of the AE or CSE who originates the request. to: The ID of the addressed resource for Retrieve, Update, Delete, Notify or the ID of the parent resource for Create op: May be CRUDN depending on the actual operation. cn: Depend on the actual operation rt : 1 nonBlockingRequestSynch |
|  |  | PRO Check HTTP | Sent POST/PUT/GET/DELETE request contains Request method: Mapped from the op in the primitive following TS-0009. Request URI: The ID of the addressed resource for Retrieve, Update, Delete, Notify or the ID of the parent resource for Create Host : IP address or the FQDN of the Hosting CSE Query: rt = 1 ”nonBlockingRequestSynch” Payload: xml or json serilization of cn in the primitive. |
|  |  | PRO Check CoAP | Sent POST/PUT/GET/DELETE request contains Method: Mapped from the op in the primitive following TS-0008. Uri-Host: IP address or the FQDN of the Hosting CSE Uri-Port: Registrar CSE port Uri-Path: The ID of the addressed resource for Retrieve, Update, Delete, Notify or the ID of the parent resource for Create Uri-Query: Depend on the detailed resource type. Payload: xml or json serilization of cn in the primitive |
|  |  | PRO Check MQTT |  |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends acknowledgement to AE or CSE. rsc: 1000 “ACCEPTED” cn: Reference to the <request> resource. |
|  |  | PRO Check HTTP | Registrar CSE creates an internal <request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Mca | PRO Check Primitive | Retrieve request send to Registrar CSE to retrieve the <request> resource. fr: The ID of the AE or CSE who originates the request. to: The ID of <request> resource op: Retrieve. |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : registrar CSE Payload: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Request> reference Payload: empty |
|  |  | PRO Check MQTT |  |
| 7 | Mca | PRO Check Primitive | Response send back to the AE or CSE with the representation of the <request> resource. rsc: 2000 “OK” cn: Representation of <request> resource. |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 Payload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Asynchronous request

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_05 |
| Objective: | AE or CSE retrieves a <resource> using non blocking asynchronous request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE/CSE has created a <resource> on registrar CSE. AE/CSE is reachable on the URI: "AE-Notification-URI" |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking asynchronous request to address the <resource> in Hosting CSE. |
| 2 | Mca | PRO Check Primitive | AE or CSE sends request primitive to the Hosting CSE. fr: The ID of the AE or CSE who originates the request. to: The ID of the addressed resource for Retrieve, Update, Delete, Notify or the ID of the parent resource for Create op: May be CRUDN depending on the actual operation. cn: Depend on the actual operation rt : 2 nonBlockingRequestAsynch Editor’s Note : The notification URI is undefined in TS-0004. |
|  |  | PRO Check HTTP | Sent POST/PUT/GET/DELETE request contains Request method: Mapped from the op in the primitive following TS-0009. Request URI: The ID of the addressed resource for Retrieve, Update, Delete, Notify or the ID of the parent resource for Create Host : IP address or the FQDN of the Hosting CSE Query: rt = 2 “nonBlockingRequestAsynch” Payload: xml or json serilization of cn in the primitive. X-M2M-RTU: AE-Notification-URI |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=2 oneM2M-RTURI: AE-Notification-URI |
|  |  | PRO Check MQTT |  |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends acknowledgement to AE or CSE. rsc: 1000 “ACCEPTED” cn: Reference to the <request> resource. |
|  |  | PRO Check HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | IOP Check | Registrar CSE sends notify request to AE |
| 6 | Mca | PRO Check Primitive | Send Notify to AE fr: Hosting CSE ID to: notification URI of AE op: Notify cn: notification data object |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: AE-Notification-URI Host : AE Payload: Notification data object. |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: AE host Uri-Port: AE port Uri-Path: AE-Notification-URI Payload: Notification data object. |
|  |  | PRO Check MQTT |  |
| 7 | Mca | PRO Check Primitive | AE sends response to Registrar CSE rsc: 2000 “OK” |
|  |  | PRO Check HTTP | AE sends notify response to Registrar CSE containing: Code = 200 |
|  |  | PRO Check CoAP | AE sends notify response to Registrar CSE containing: Response Code= 2.05 |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | Registrar CSE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### -----------------------End of change 1--------------------------------------------