| Input Contribution |
| --- |
| Meeting ID* | TST#18 |
| Title:* | Group FanoutPoint Tests |
| Source:* | Bob Flynn, InterDigital, Bob.Flynn@InterDigital.com Dale Seed, InterDigital, Dale.Seed@InterDigital.com |
| Uploaded Date:* | 2015-07-12 |
| Document(s) Impacted* | TS-0013-V0.1.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some Interoperability Test Descriptions for <fanoutPoint> resource procedures to be added to TS-0013 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes testing of fanoutPoint resource management requests for create, retrieve, update and delete operations of the <fanoutPoint>.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

The following figure outlines the basic call flow:

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

## No Hop configuration testing

### FanoutPoint Management

#### FanoutPoint Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE creates a <contentInstance> resource in each group member |
| Configuration: |  |
| References: | [1] 10.2.7.6 [2] 7.3.14.3.1 |
| Pre-test conditions: | A group is created containing 2 members of type <container> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Create Request to create <contentInstance> in each group member |
| 2 | Check Mca | PRO Check Primitive | Sent request contains Operation (op) = 1 (Create) To (to) = <CSEBase>/<group>/fanoutPoint From (from) = <SP-Relative-AE-ID> Request Identifier (rqi) = (token-string) Resource Type (ty) = 4 (contentInstance) Content (pc) = Serialized Representation of applicable < contentInstance > resource attribute |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Request URI: <CSEBase>/<group>/fanoutPoint Host : registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; ty=4 or application/vnd.onem2m-res+json; ty=4 Content-Length: size of payload in the message body in bytes Message-body: ContentInstance resource <contentInstance> to be created |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <group> Uri-Path : fanoutPoint Uri-Query: rty=4 oneM2M-FR: container-ID oneM2M-RQI: value of rqi primitive parameter Payload: <contentInstance> resource to be created |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase>/<group>/fanoutPoint fr = <AE-ID> rqi = <Request ID> ty = 4 pc = <Content(<contentInstance> resource representation> |
| 4 |  | IOP Check | Check if possible that the <contentInstance> resource is created in each member hosting CSE |
| 7 | Check Mca | PRO Check Primitive | Response Statuse Code (rsc) : 2001 (CREATED) Request Identifier (rqi) = same string as received in request message Content (pc): aggregated response |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 201 X-M2M-RSC: 2001 X-M2M-RI: value of rqi primitive parameter Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length: size of payload in the message body in bytes Message-body: aggregated response |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.01 oneM2M-RSC = 2001 oneM2M-RQI: value of rqi primitive parameter Payload: aggregated response |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict | Verify that the aggregrate response includes responses from each member of the group |
| PRO Verdict |  |

#### FanoutPoint Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE retrieves the latest <contentInstance> resource from in each group member |
| Configuration: |  |
| References: | [1] 10.2.7.8 [2] 7.3.14.3.2 |
| Pre-test conditions: | A group is created containing 2 members of type <container> Each member container has at least 0..n content instances |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Retrieve ‘latest’ Request to the fanoutPoint of <group> resource |
| 2 | Check Mca | PRO Check Primitive | Operation (op) = 2 (Retrieve) To (to) = <CSEBase>/<group>/fanoutPoint/latest From (from) = AE-ID of request originator Request Identifier (rqi) = (token-string) |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request URI: <CSEBase>/<group>/fanoutPoint/latest Host : registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: ContentInstance-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <group> Uri-Path: fanoutPoint Uri-Path: latest oneM2M-FR: AE-ID oneM2M-RQI: value of rqi primitive parameter Payload: empty |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check |  |
| 7 | Check Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = same string as received in request message Content (pc) = Serialized Representation of aggregated response |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 X-M2M-RSC: 2000 X-M2M-RI: value of rqi primitive parameter Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytes Message-body: aggregated response |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.05 oneM2M-RQI: value of rqi primitive parameter oneM2M-RSC = 2000 Payload: aggregated response |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict | Verify that the aggregrate response includes responses from each member of the group |
| PRO Verdict |  |

#### FanoutPoint Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE updates an attribute in each member resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.9 [2] 7.3.14.3.3 |
| Pre-test conditions: | A group is created containing 2 members of type <container> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Update Request to the fanoutPoint of <group> resource to lifetime of the resource. |
| 2 | Check Mca | PRO Check Primitive | Sent UPDATE request contains Operation (op) = 3 (Update) To (to) = <CSEBase>/<group>/fanoutPoint From (from) = AE-ID of request originator Request Identifier (rqi) = (token-string) Content (pc) = Serialized Representation of modified <container> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = PUT Request URI <CSEBase>/<group>/fanoutPoint Host : Registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length: size of payload in the message body in bytes Payload: modified <container> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: < group > Uri-Path: fanoutPoint oneM2M-FR: AE-ID oneM2M-RQI: value of rqi primitive parameter Payload: modified <container> resource |
|  |  | PRO Check MQTT |  |
| 3 |  | IOP Check | Check if possible that both of the <container> resources have been updated in registrar CSE. |
| 4 | Check Mca | PRO Check Primitive | Sent UPDATE response contains Response Status Code (rsc) = 2004 Request Identifier (rqi) = same string as received in request message Content (pc) = aggregated response |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 X-M2M-RSC: 2004 X-M2M-RI: value of rqi primitive parameter Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytes Payload: aggregated response |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.04 oneM2M-RSC = 2004 oneM2M-RQI: value of rqi primitive parameter Payload: aggregated response |
|  |  | PRO Check MQTT |  |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict | Verify that the aggregrate response includes responses from each member of the group |
| PRO Verdict |  |

#### FanoutPoint Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE deletes a <contentInstance> from each member |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.10 [2] 7.3.14.3.4 |
| Pre-test conditions: | A group is created containing 2 members of type <container> Each member container has at least 0..n content instances |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Delete ‘oldest’ Request to the fanoutPoint of <group> resource |
| 2 | Check Mca | PRO Check Primitive | Sent DELETE request contains Operation (op) = 4 (Delete) To (to) = <CSEBase>/<group>/fanoutPoint/oldest From (from) = AE-ID of request originator Request Identifier (rqi) = (token-string) |
|  |  | PRO Check HTTP | Sent request contains Request URI <CSEBase>/<group>/fanoutPoint/oldest Host : Registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: AE-ID Payload: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <group> Uri-Path: fanoutPoint Uri-Path: oldest oneM2M-FR: contentInstance-ID oneM2M-RQI: value of rqi primitive parameter Payload: empty |
|  |  | PRO Check MQTT |  |
| 3 | Check Mca | PRO Check Primitive | Response Status Code (rsc) = 2002 (DELETED) Request Identifier (rqi) = same string as received in request message |
|  |  | PRO Check HTTP | Registrar sends response containing: Status Code = 200 X-M2M-RSC: 2002 X-M2M-RI: value of rqi primitive parameter Payload: aggregated response |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.02 oneM2M-RSC = 2002 oneM2M-RQI: value of rqi primitive parameter Payload: aggregated response |
|  |  | PRO Check MQTT |  |
| 4 |  | Verify | Check if possible that the oldest <contentInstance> resource has been removed in registrar CSE. |
| 5 |  | Verify | AE indicates successful operation |
| IOP Verdict | Verify that the aggregrate response includes responses from each member of the group |
| PRO Verdict |  |

============== == End of  1st Part: Proposed Test Descriptions ==================