| Input Contribution |
| --- |
| Meeting ID* | TST#18 |
| Title:* | Notification Tests |
| Source:* | Bob Flynn, InterDigital, Bob.Flynn@InterDigital.com Dale Seed, InterDigital, Dale.Seed@InterDigital.com |
| Uploaded Date:* | 2015-07-12 |
| Document(s) Impacted* | TS-0013-V0.1.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some Interoperability Test Descriptions for notification procedures to be added to TS-0013 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes testing of a notification request as a result of a create of a <contentInstance> within a <container> having a <subscription>.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

## No Hop configuration testing

### Notifcation Management

#### Notification Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE receives a notification request from the HOST CSE |
| Configuration: |  |
| References: | [1] 10.2.12 [2] 7.4.1 |
| Pre-test conditions: | A <subscription> is created as a child resource of a <container> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Create Request to create <contentInstance> in a <container>. This triggers or causes the HOST CSE to send a notification |
| 2 | Check Mca | PRO Check Primitive | Operation (op) = 5 (Notify) To (to) = <SP-Relative-AE-ID> From (from) = <Registrar CSE-ID> Request Identifier (rqi) = (token-string) Cn: notification representation |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Request-Target: <SP-Relative-AE-ID> Host: Host Address of AE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: <Registrar CSE-ID> Content-Type: application/vnd.onem2m-ntfy+xml; or application/vnd.onem2m-ntfy+json; Content-Length: size of payload in the message body in bytes Message-body: Serialized Representation of applicable attributes of notification data object |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: Registrar AE host Uri-Port: Registrar AE port Uri-Path: <AE-ID> oneM2M-FR: <Registrar CSE-ID> oneM2M-RQI: value of rqi primitive parameter Payload: Serialized Representation of applicable attributes of notification data object |
|  |  | PRO Check MQTT |  |
| 4 |  | IOP Check | Check if the notification representation |
| 7 | Check Mca | PRO Check Primitive | Sent CREATE response contains To: CSE-ID Fr: AE-ID Response Status Code : OK |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.01 |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check |  |
| IOP Verdict |  |
| PRO Verdict |  |

============== == End of  1st Part: Proposed Test Descriptions ==================