| Input Contribution |
| --- |
| Meeting ID* | TST18 |
| Title:* | Test Description for fanOutPoint |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd. , yinjiaxin@huawei.com |
| Uploaded Date:* | 2015-7-10 |
| Document(s) Impacted* | WI-0022, TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text if agreed. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1-------------------------------------------

## 7.1.2.x	CFG_SH_03

The configuration is about group management when AE or CSE is using a group to fan out requests to multiple members. The connection between AE/CSE and Group Hosting CSE, Group Hosting CSE and Member Hosting CSE may be multi hop connection following the definition in 7.1.3.

This configuration is mapped to cases include:

- AE/CSE sends request addressing <group>/fanOutPoint in Group Hosting CSE ,Group Hosting CSE then further fan out request to each Member Hosting CSE.

- The Member Hosting CSE sends notification to the Group Hosting CSE pertaining to the subscription made through the Group Hosting CSE. The Group Hosting CSE then further aggregates the notification and sends it back to AE/CSE.

### -----------------------End of change 1--------------------------------------------