| Input Contribution |
| --- |
| Meeting ID* | TST18 |
| Title:* | Test Description for mgmtObj |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd. , yinjiaxin@huawei.com |
| Uploaded Date:* | 2015-7-10 |
| Document(s) Impacted* | WI-0022, TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text if agreed. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1-------------------------------------------

## 7.1.2.x	CFG_SH_03

The configuration is about device management using external technologies.

This configuration is mapped to cases include:

- AE sends request addressing <mgmtObj> to IN-CSE. IN-CSE then further acts as a Management Server to send management commands to Managed Entity over the mc interface. The management command is defined in OMA DM, BBF TR069 or LWM2M.

### -----------------------End of change 1--------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## X.6	Management Session between Management Server and Management Client

Before the device management using external technologies is executed, it is required that a management session has already been established between the Management Server and Management Client. If there is no existing management session, the IN-CSE shall request to establish a management session between the Management Server and Management Client.

### -----------------------End of change 2--------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### <mgmtObj> Test Description

#### 8.2.12.1	<mgmtObj> Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_0x |
| Objective: | AE creates a <mgmtObj> resource |
| Configuration: | CFG_SH_03 |
| References: | [1] 10.2.8.2 |
| Pre-test conditions: | Management Session between Management Server and Management Client |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an <mgmtObj> Create Request to create an <mgmtObj> on IN-CSE. |
| 2 | Mca | PRO Check Primitive | fr: AE-ID to: <CSEBase of IN-CSE>/<node of Managed Entity> op: C cn: Representation of the <mgmtObj> resource |
|  |  | PRO Check HTTP | Sent POST request contains Request URI: <CSEBase of IN-CSE>/<node of Managed Entity>?rty=13 Host : FQDN or IP address of the IN-CSE Payload: xml or json serialization of the cn of the primitive. |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: FQDN or IP address of the IN-CSE Uri-Port: IN-CSE port Uri-Path: <CSEBase of IN-CSE>/<node of Managed Entity> Uri-Query: rty=13 Payload: xml or json serialization of the cn of the primitive |
|  |  | PRO Check MQTT |  |
| 3 |  | IOP Check | Check if possible that the <mgmtObj> resource is created in IN-CSE |
| 4 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Requests to create the corresponding MO using Add DM command. The mapping of <mgmtObj> and MO can be referenced from 5.3 of TS-0005. |
|  |  | PRO Check BBF TR069 | Requests to create the corresponding information model using AddObject RPC. The mapping of <mgmtObj> and information model or RPC can be referenced from clause 7 of TS-0006. |
|  |  | PRO Check OMA LWM2M | Requests to create the corresponding Objects using Create LWM2M Create operations. The mapping of <mgmtObj> and Object can be referenced from 6.3 of TS-0005. |
| 5 |  | IOP Check | Check if possible that the corresponding MO for OMA DM, information model for BBF TR069 or Object for OMA LWM2M is created on the Managed Entity. |
| 6 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Response with status code (200) OK. Details can be found in clause 5.4 TS-0005. |
|  |  | PRO Check BBF TR069 | Successful response of the RPC. Details can be found in clause 8.1 TS-0006. |
|  |  | PRO Check OMA LWM2M | Response with status code 2.01 Created. Details can be found in clause 6.4 TS-0005. |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2001 (CREATED) Content (pc) = Serialized Representation of <mgmtObj> resource |
|  |  | PRO Check HTTP | IN-CSE responds to AE containing: Code = 201 Content-Location : <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> Payload: Created <mgmtObj> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | IN-CSE responds to AE containing: Response Code = 2.01 Location-Path: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> Payload: Created <mgmtObj> (assigned and/or modified attributes) |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the created resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.2.12.2	<mgmtObj> Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_0x |
| Objective: | AE updates a <mgmtObj> resource |
| Configuration: | CFG_SH_03 |
| References: | [1] 10.2.8.4 |
| Pre-test conditions: | Management Session between Management Server and Management Client |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an <mgmtObj> Update Request to update an <mgmtObj> on IN-CSE. |
| 2 | Mca | PRO Check Primitive | fr: AE-ID to: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> op: U cn: Representation of the <mgmtObj> resource |
|  |  | PRO Check HTTP | Sent PUT request contains Request URI: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> Host : FQDN or IP address of the IN-CSE Payload: xml or json serialization of the cn of the primitive. |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: FQDN or IP address of the IN-CSE Uri-Port: IN-CSE port Uri-Path: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> Payload: xml or json serialization of the cn of the primitive |
|  |  | PRO Check MQTT |  |
| 3 |  | IOP Check | Check if possible that the <mgmtObj> resource is updated in IN-CSE |
| 4 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Requests to update the corresponding MO using Replace DM command. The mapping of <mgmtObj> and MO can be referenced from 5.3 of TS-0005. |
|  |  | PRO Check BBF TR069 | Requests to Update the corresponding information model using SetParameterValues RPC. The mapping of <mgmtObj> and information model or RPC can be referenced from clause 7 of TS-0006. |
|  |  | PRO Check OMA LWM2M | Requests to Update the corresponding Objects using LWM2M Write operations. The mapping of <mgmtObj> and Object can be referenced from 6.3 of TS-0005. |
| 5 |  | IOP Check | Check if possible that the corresponding MO for OMA DM, information model for BBF TR069 or Object for OMA LWM2M is Updated on the Managed Entity. |
| 6 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Response with status code (200) OK. Details can be found in clause 5.4 TS-0005. |
|  |  | PRO Check BBF TR069 | Successful response of the RPC. Details can be found in clause 8.1 TS-0006. |
|  |  | PRO Check OMA LWM2M | Response with status code 2.04 Changed. Details can be found in clause 6.4 TS-0005. |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2004 (UPDATED) Content (pc) = Serialized Representation of <mgmtObj> resource |
|  |  | PRO Check HTTP | IN-CSE responds to AE containing: Code = 200 X-M2M-RSC: 2004 Payload: Updated <mgmtObj> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | IN-CSE responds to AE containing: Response Code = 2.05 Payload: Updated <mgmtObj> (assigned and/or modified attributes) |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the Updated resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.2.12.3	<mgmtObj> Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_0x |
| Objective: | AE retrieves a <mgmtObj> resource |
| Configuration: | CFG_SH_03 |
| References: | [1] 10.2.8.3 |
| Pre-test conditions: | Management Session between Management Server and Management Client |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an <mgmtObj> Retrieve Request to retrieve an <mgmtObj> on IN-CSE. |
| 2 | Mca | PRO Check Primitive | fr: AE-ID to: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> op: R |
|  |  | PRO Check HTTP | Sent GET request contains Request URI: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> Host : FQDN or IP address of the IN-CSE |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: FQDN or IP address of the IN-CSE Uri-Port: IN-CSE port Uri-Path: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> |
|  |  | PRO Check MQTT |  |
| 3 |  | IOP Check | Check if possible that the <mgmtObj> resource is retrieved in IN-CSE |
| 4 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Requests to retrieve the corresponding MO using Get DM command. |
|  |  | PRO Check BBF TR069 | Requests to retrieve the corresponding information model using GetParametersValue RPC. |
|  |  | PRO Check OMA LWM2M | Requests to retrieve the corresponding Objects using Retrieve LWM2M Read operation. |
| 5 |  | IOP Check |  |
| 6 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Response with status code (200) OK with the information of the MO. Details can be found in clause 5.4 TS-0005. |
|  |  | PRO Check BBF TR069 | Successful response of the RPC with the information about the management related information. Details can be found in clause 8.1 TS-0006. |
|  |  | PRO Check OMA LWM2M | Response with status code 2.05 Content with the information of the Object. Details can be found in clause 6.4 TS-0005. |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Content (pc) = Serialized Representation of <mgmtObj> resource |
|  |  | PRO Check HTTP | IN-CSE responds to AE containing: Code = 200 Payload: Retrieved <mgmtObj> (assigned and/or modified attributes) |
|  |  | PRO Check CoAP | IN-CSE responds to AE containing: Response Code = 2.00 Payload: Retrieved <mgmtObj> (assigned and/or modified attributes) |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the retrieved resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.2.12.4	<mgmtObj> Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_0x |
| Objective: | AE deletes a <mgmtObj> resource |
| Configuration: | CFG_SH_03 |
| References: | [1] 10.2.8.5 |
| Pre-test conditions: | Management Session between Management Server and Management Client |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an <mgmtObj> Delete Request to delete an <mgmtObj> on IN-CSE. |
| 2 | Mca | PRO Check Primitive | fr: AE-ID to: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> op: D |
|  |  | PRO Check HTTP | Sent DELETE request contains Request URI: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> Host : FQDN or IP address of the IN-CSE |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: FQDN or IP address of the IN-CSE Uri-Port: IN-CSE port Uri-Path: <CSEBase of IN-CSE>/<node of Managed Entity>/<mgmtObj> |
|  |  | PRO Check MQTT |  |
| 3 |  | IOP Check | Check if possible that the <mgmtObj> resource is deleted in IN-CSE |
| 4 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Requests to delete the corresponding MO using Delete DM command. |
|  |  | PRO Check BBF TR069 | Requests to delete the corresponding information model using DeleteObject RPC. |
|  |  | PRO Check OMA LWM2M | Requests to delete the corresponding Objects using LWM2M Delete operation. |
| 5 |  | IOP Check | Check if possible that the corresponding MO for OMA DM, information model for BBF TR069 or Object for OMA LWM2M is deleted on the Managed Entity. |
| 6 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Response with status code (200) OK. Details can be found in clause 5.4 TS-0005. |
|  |  | PRO Check BBF TR069 | Successful response of the RPC. Details can be found in clause 8.1 TS-0006. |
|  |  | PRO Check OMA LWM2M | Response with status code 2.02 Deleted. Details can be found in clause 6.4 TS-0005. |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2004 (DELETED) |
|  |  | PRO Check HTTP | IN-CSE responds to AE containing: Status Code = 200 X-M2M-RSC: 2004 |
|  |  | PRO Check CoAP | IN-CSE responds to AE containing: Response Code = 2.05 |
|  |  | PRO Check MQTT |  |
| 8 |  | IOP Check | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the deleted resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

### -----------------------End of change 3--------------------------------------------