| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Single hop CSEBase management |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr monteil@laas.fr drira@laas.fr |
| Date:* | 2015-07-21 |
| Abstract:* | The contribution proposes Interoperability Test description for Single hop CSEBase management to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution proposes Interoperability Test description for Single hop CSEBase management to be added to TS-0013. The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

=========Start of  1st Part: Proposed Test Descriptions ==================

## Single Hop configuration testing

## CSEBase Management

## CSEBase Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | AE retrieves <CSEBase> resource using single hop. |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.3 [2] 7.3.3 |
| Pre-test conditions: | <CSEBase> resource has been automatically created in Hosting CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a CSEBase retrieve request |
| 2 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) : 2 (Retrieve) To (to) : <CSEBase> of hosting CSE From (from) : AE-ID Request Identifier (rqi) : Request-ID |
|  |  | PRO Check HTTP | Sent GET request contains Request method : GET Request-Target: <CSEBase> of hosting CSE Host: Host Address of registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> of hosting CSE oneM2M-FR: AE-ID oneM2M-RQI: Request-ID Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op : 2 to : <CSEBase> of hosting CSE fr : AE-ID rqi : Request-ID |
| 3 | Mcc | PRO Check Primitive | Forwarded Retrieve request to Hosting CSE contains Operation (op) : 2 (Retrieve) To (to) : <CSEBase> of hosting CSE From (from) : AE-ID of request originator Request Identifier (rqi) : Request-ID |
|  |  | PRO Check HTTP | Forwarded GET request to Hosting CSE contains Request method : GET Request-Target: <CSEBase> of hosting CSE Host: Address of remote CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-body: empty |
|  |  | PRO Check CoAP | Forwarded GET request to Hosting CSE contains Method: 0.01 (GET) Uri-Host: remote CSE host Uri-Port: remote CSE port Uri-Path: <remoteCSE> of hosting CSE oneM2M-FR: AE-ID oneM2M-RQI: Request-ID Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registrar CSE-ID>/<Hosting CSE-ID>” Payload: op : 2 to : <CSEBase> of hosting CSE fr : AE-ID rqi : Request-ID |
| 4 | Mcc | PRO Check Primitive | Remote CSE sends response to Registrar CSE containing: Response Status Code (rsc) : 2000 (OK) Request Identifier (rqi) : Request-ID Content (pc) : Serialized Representation of <CSEBase> resource |
|  |  | PRO Check HTTP | Remote CSE sends response to Registrar CSE containing: Status Code: 200 X-M2M-RSC: 2000 X-M2M-RI: Request-ID Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length: size of payload in the message body in bytes Message-body: Serialized Representation of <CSEBase> resource of hosting CSE |
|  |  | PRO Check CoAP | Remote CSE sends response to Registrar CSE containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: Request-ID Payload: Serialized Representation of <CSEBase> resource of hosting CSE |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registrar CSE-ID>/<Remote CSE-ID>” Payload: to: SP-Relative-AE-ID fr : Registrar CSE-ID rqi: Request-ID rsc: Response Status Code(2000) pc: Content(retrieved <CSEBase> resource representation of hosting CSE) |
| 5 | Mca | PRO Check Primitive | Registrar CSE forwards response to AE containing: Response Status Code (rsc) : 2000 (OK) Request Identifier (rqi) : Request-ID Content (pc) : Serialized Representation of <CSEBase> resource of hosting CSE |
|  |  | PRO Check HTTP | Registrar CSE forwards response to containing: Status Code: 200 X-M2M-RSC: 2000 X-M2M-RI: Request-ID Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length: size of payload in the message body in bytes Message-body: Serialized Representation of <CSEBase> resource of hosting CSE |
|  |  | PRO Check CoAP | Registrar CSE forwards response to AE containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: Request-ID Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized Representation of <CSEBase> resource of hosting CSE |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to: SP-Relative-AE-ID fr : Registrar CSE-ID rqi: Request-ID rsc: Response Status Code(2000) pc: Content(retrieved <CSEBase> resource representation of hosting CSE) |
| 6 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

=========End of  1st Part: Proposed Test Descriptions ==================