| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Non-blocking synchronous requests update |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr (LAAS-CNRS) monteil@laas.fr (LAAS-CNRS) drira@laas.fr (LAAS-CNRS) |
| Date:* | 2015-07-13 |
| Abstract:* | The contribution proposes Interoperability Test description for non-blocking synchronous requests to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution proposes an update of the non-blocking synchronous requests to be added to TS-0013. The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

## Non blocking configuration testing

### Synchronous request

### Container management

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_01 |
| Objective: | AE retrieves a <container> resource using non blocking synchronous request from registrar CSE. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a <Container> resource on registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous request to retrieve the <Container> resource from registrar CSE. |
| 2 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 2 (Retrieve) To (to) = <CSEBase>/<Container> From (from) = AE-ID Request Identifier (rqi) = Request-ID Response Type (rt) = 1 (non blocking synchronous) |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request-Target: <CSEBase>/<Container>?rt=1 Host : Host address of registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=1 oneM2M-FR: AE-ID oneM2M-RQI: Request-IDPayload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase>/<Container> fr = AE-ID rqi = Request ID rt=1 |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Status Code (rsc) = 1000 (Accepted) Request Identifier (rqi) = Request-ID Content (pc) = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= Request-ID Message-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC= 1000 oneM2M-RQI = Request-ID Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(1000) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to send a retrieve request to <Request> reference |
| 6 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 2 (Retrieve) To (to) = <Request> reference From (from) = AE-ID Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : Host address of registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Request> reference oneM2M-FR: AE-ID oneM2M-RQI: Request-ID Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Request> reference fr = AE-ID rqi = Request ID |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = Request-ID Content (pc) = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Code = 200 X-M2M-RSC: 2000 X-M2M-RI= Request ID Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytes Message-Body: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 oneM2M-RSC: 2000 oneM2M-RQI: Request ID Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+jsonPayload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(2000) pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_02 |
| Objective: | AE creates a <Container> resource using non blocking synchronous request in registrar CSE. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous request to create a <Container> resource <Container> in registrar CSE |
| 2 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 1 (Create) To (to) = <CSEBase> From (from) = AE-ID Request Identifier (rqi) = Request-ID Response Type (rt) = 1 (non blocking synchronous) Resource Type (ty) = 3 (container) Content (pc) = Serialized Representation of applicable <Container> resource attributes |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: <CSEBase>?rt=1 Host : Host address of registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Content Type = application/vnd.onem2m-res+xml; ty=3 or application/vnd.onem2m-res+json; ty=3 Message-Body: Serialized Representation of applicable <Container> resource attributes |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: rt=1 Content Type = application/vnd.onem2m-res+xml; ty=3 or application/vnd.onem2m-res+json; ty=3 Payload: Serialized Representation of applicable <Container> resource attributes |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase> fr = AE-ID rqi = Request ID ty = 3 rt=1 pc= Serialized Representation of applicable <Container> resource attributes |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Status Code (rsc) = 1000 (Accepted) Request Identifier (rqi) = Request-ID Content (pc) = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= Request-ID Message-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = Request-ID Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(1000) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 2 (Retrieve) To (to) = <Request> reference From (from) = AE-ID Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : Host address of registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Request> reference oneM2M-FR: AE-ID oneM2M-RQI: Request-ID Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Request> reference fr = AE-ID rqi = Request ID |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = Request-ID Content (pc) = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the created <Container> resource. |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Code = 200 X-M2M-RSC: 2000 X-M2M-RI= Request ID Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytes Message-Body: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the created <Container> resource. |
|  |  | PRO Check CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 oneM2M-RSC: 2000 oneM2M-RQI: Request ID Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the created <Container> resource. |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(2000) pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the created <Container> resource. |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_03 |
| Objective: | AE updates a <Container> resource using non blocking synchronous request in registrar CSE. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a <Container> resource in registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous request to update the <Container> resource. |
| 2 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 3 (Update) To (to) = <CSEBase>/<Container> From (from) = AE-ID Request Identifier (rqi) = Request-ID Response Type (rt) = 1 (non blocking synchronous) Content (pc) = Serialized Representation of updated <Container> resource attributes |
|  |  | PRO Check HTTP | Sent PUT request contains Request method = PUT Request URI: <CSEBase>/<Container>?rt=1 Host : Host address of registrar CSE Message-Body: Serialized Representation of updated <Container> resourceattributes |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=1 Content Type = application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; Payload: Serialized Representation of updated <Container> resource attributes |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <CSEBase>/<Container> fr = AE-ID rqi = Request ID rt=1 pc = Serialized Representation of updated <Container> resource attributes |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Status Code (rsc) = 1000 (Accepted) Request Identifier (rqi) = Request-ID Content (pc) = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= Request-IDMessage-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = Request-ID Payload Reference to the created <Request> resource |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(1000) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 2 (Retrieve) To (to) = <Request> reference From (from) = AE-ID Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : Host address of registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Request> reference oneM2M-FR: AE-ID oneM2M-RQI: Request-ID Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Request> reference fr = AE-ID rqi = Request ID |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = Request-ID Content (pc) = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the created <Container> resource. |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Code = 200 X-M2M-RSC: 2000 X-M2M-RI= Request ID Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytesMessage-Body: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the updated <Container> resource. |
|  |  | PRO Check CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 oneM2M-RSC: 2000 oneM2M-RQI: Request ID Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the updated <Container> resource. |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(2000) pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the created <Container> resource. |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_04 |
| Objective: | AE deletes a Container resource using non blocking synchronous request. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created <Container> resource on registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous request to delete the <Container> resource. |
| 2 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 4 (Delete) To (to) = <CSEBase>/<Container> From (from) = AE-ID Request Identifier (rqi) = Request-ID Response Type (rt) = 1 (non blocking synchronous) |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method = DELETE Request-Target: <CSEBase>/<Container>?rt=1 Host : Host address of registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=1 oneM2M-FR: AE-ID oneM2M-RQI: Request-ID Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase>/<Container> fr = AE-ID rqi = Request ID rt=1 |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Status Code (rsc) = 1000 (Accepted) Request Identifier (rqi) = Request-ID Content (pc) = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= Request-ID Message-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = Request-ID Payload: Reference to the created <Request> reference |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(1000) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 2 (Retrieve) To (to) = <Request> reference From (from) = AE-ID Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request-Target: <Request> reference Host : Host address of registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port oneM2M-FR: AE-ID oneM2M-RQI: Request-ID Uri-Path: <Request> reference |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Request> reference fr = AE-ID rqi = Request ID |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = Request-ID Content (pc) = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED). |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Code = 200 X-M2M-RSC: 2000 X-M2M-RI= Request ID Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytesMessage-Body: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED). |
|  |  | PRO Check CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 oneM2M-RSC: 2000 oneM2M-RQI: Request ID Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+jsonPayload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED). |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(2000) pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED). |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

============== == End of  1st Part: Proposed Test Descriptions ==================