| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Non-blocking asynchronous requests update |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr (LAAS-CNRS) monteil@laas.fr (LAAS-CNRS) drira@laas.fr (LAAS-CNRS) |
| Date:* | 2015-07-13 |
| Abstract:* | The contribution proposes an update of the non-blocking asynchronous requests to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution proposes an update of the non-blocking asynchronous requests to be added to TS-0013. The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

## Non blocking configuration testing

### Asynchronous request

### Container management

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_05 |
| Objective: | AE retrieves a <container> resource using non blocking asynchronous request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a <Container> resource on registrar CSE. AE is reachable on the URI: "AE-Notification-URI" |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking asynchronous request to retrieve the <Container> resource from registrar CSE |
| 2 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 2 (Retrieve) To (to) = <CSEBase>/<Container> From (from) = AE-ID Request Identifier (rqi) = Request-ID Response Type (rt) = 2 (non blocking asynchronous) NotificationURI (nu) = AE-Notification-URI |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request-Target: <CSEBase>/<Container>?rt=2 Host : Host address of registrar CSE X-M2M-RTU: AE-Notification-URI X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=2 oneM2M-FR: AE-ID oneM2M-RQI: Request-ID oneM2M-RTURI: AE-Notification-URI |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <CSEBase>/<Container> fr = AE-ID rqi = Request ID rt=2 nu= AE-Notification-URI |
|  | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Status Code (rsc) = 1000 (Accepted) Request Identifier (rqi) = Request-ID Content (pc) = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= Request-ID Message-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC= 1000 oneM2M-RQI = Request-ID Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(1000) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | IOP Check | Registrar CSE sends notify request to AE |
| 6 | Mca | PRO Check Primitive | Sent Notify request contains Operation (op) = 5 (Notify) To (to) = AE-Notification-URI From (from) = Registrar CSE-ID Request Identifier (rqi) = Request-ID Content (pc) = Notification data object. |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: AE-Notification-URI Host : Host address of AE X-M2M-RI: Request-ID X-M2M-Origin: Registrar CSE-ID Message-Body: Notification data object. |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: AE host Uri-Port: AE port Uri-Path: AE-Notification-URI oneM2M-FR: Registrar CSE-ID oneM2M-RQI: Request-ID Payload: Notification data object. |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< Registrar CSE-ID>/<SP-Relative-AE-ID>” Payload: op = 5 to = <Request> reference fr = AE-ID rqi = Request ID nu = AE-Notification-URI |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | AE sends notify response to Registrar CSE containing: Code = 200 X-M2M-RI = Request-ID Message-Body = empty |
|  |  | PRO Check CoAP | AE sends notify response to Registrar CSE containing: Response Code= 2.05 oneM2M-RQI = Request-ID Payload = empty |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/< Registrar CSE-ID>/<SP-Relative-AE-ID>” Payload: to = Registrar CSE-ID fr = AE-ID rqi = Request ID rsc = Response Status Code(2000) |
| 8 |  | IOP Check | Registrar CSE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_056 |
| Objective: | AE creates a <Container> resource using non blocking asynchronous request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE is reachable on the URI: "AE-Notification-URI" |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking asynchronous request to create the <Container> resource in registrar CSE. |
| 2 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 1 (Create) To (to) = <CSEBase> From (from) = AE-ID Request Identifier (rqi) = Request-ID Response Type (rt) = 2 (non blocking synchronous) Resource Type (ty) = 3 (container) Content (pc) = Serialized Representation of applicable <Container> resource attributes |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: <CSEBase>?rt=2 Host : Host address of registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID X-M2M-RTU: AE-Notification-URI Content Type = application/vnd.onem2m-res+xml; ty=3 or application/vnd.onem2m-res+json; ty=3 Message-Body: Serialized Representation of applicable <Container> resource attributes |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: rt=2 Content Type = application/vnd.onem2m-res+xml; ty=3 or application/vnd.onem2m-res+json; ty=3 oneM2M-RTURI: AE-Notification-URI Payload: Serialized Representation of applicable <Container> resource attributes |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase> fr = AE-ID rqi = Request ID ty = 3 rt=2 nu= AE-Notification-URI pc= Serialized Representation of applicable <Container> resource attributes |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Status Code (rsc) = 1000 (Accepted) Request Identifier (rqi) = Request-ID Content (pc) = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= Request-ID Message-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = Request-ID Payload <Request> reference |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(1000) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | IOP Check | Registrar CSE sends notify request to AE |
| 6 | Mca | PRO Check Primitive | Sent Notify request contains Operation (op) = 5 (Notify) To (to) = AE-Notification-URI From (from) = registrar CSE-ID Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: AE-Notification-URI Host : Host address of AE X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-Body: Notification data object |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: AE host Uri-Port: AE port Uri-Path: AE-Notification-URI oneM2M-FR: AE-ID oneM2M-RQI: Request-ID Payload: Notification data object |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< Registrar CSE-ID>/<SP-Relative-AE-ID>” Payload: op = 5 to = Registrar CSE-ID fr = AE-ID rqi = Request ID nu = AE-Notification-URI |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | AE sends notify response to Registrar CSE containing: Code = 200 X-M2M-RSC: 2000 X-M2M-RI= Request ID Message-Body = empty |
|  |  | PRO Check CoAP | AE sends notify response to Registrar CSE containing: Response Code= 2.05 Request Identifier (rqi) = Request-ID Payload = empty |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/< Registrar CSE-ID>/<SP-Relative-AE-ID>” Payload: to = Registrar CSE-ID fr = AE-ID rqi = Request ID rsc = Response Status Code(2000) |
| 8 |  | IOP Check | Registrar CSE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_07 |
| Objective: | AE updates a <Container> resource using non blocking asynchronous request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a Container resource <Container> on registrar CSE AE is reachable on the URI: "AE-Notification-URI" |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking asynchronous request to update the <Container> resource in registrar CSE. |
| 2 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 3 (Update) To (to) = <CSEBase>/<Container> From (from) = AE-ID Request Identifier (rqi) = Request-ID Response Type (rt) = 2 (non blocking asynchronous) Content (pc) = Serialized Representation of updated <Container> resource attributes |
|  |  | PRO Check HTTP | Sent PUT request contains Request method = PUT Request URI: <CSEBase>/<Container>?rt=2 Host : Host address of registrar CSE X-M2M-RTU: AE-Notification-URI Message-Body: Serialized Representation of updated <Container> resourceattributes |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=2 oneM2M-RTURI: AE-Notification-URI Content Type = application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; Payload: Serialized Representation of updated <Container> resource attributes |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <CSEBase>/<Container> fr = AE-ID rqi = Request ID rt=2 pc = Serialized Representation of updated <Container> resource attributes |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Status Code (rsc) = 1000 (Accepted) Request Identifier (rqi) = Request-ID Content (pc) = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= Request-ID Payload: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = Request-ID Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(1000) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | IOP Check | Registrar CSE sends notify request to AE |
| 6 | Mca | PRO Check Primitive | Sent Notify request contains Operation (op) = 5 (Notify) To (to) = AE-Notification-URI From (from) = registrar CSE-ID Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: AE-Notification-URI Host : Host address of AE X-M2M-RI: Request-ID X-M2M-Origin: Registrar CSE-IDPayload: Notification data object |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: AE host Uri-Port: AE port Uri-Path: AE-Notification-URI oneM2M-RQI = Request-ID oneM2M-Origin = Registrar CSE-ID Payload: Notification data object |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< Registrar CSE-ID>/<SP-Relative-AE-ID>” Payload: op = 5 to = AE fr = Registrar CSE-ID rqi = Request ID nu = AE-Notification-URI |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | AE sends notify response to Registrar CSE containing: Code = 200 X-M2M-RSC: 2000 X-M2M-RI= Request ID Message-Body = empty |
|  |  | PRO Check CoAP | AE sends notify response to Registrar CSE containing: Response Code= 2.05 oneM2M-RSC=2000 oneM2M-RQI = Request-ID Payload = empty |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/< Registrar CSE-ID>/<SP-Relative-AE-ID>” Payload: to = Registrar CSE-ID fr = AE-ID rqi = Request ID rsc = Response Status Code(2000) |
| 8 |  | IOP Check | Registrar CSE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_078 |
| Objective: | AE deletes a Container resource using non blocking asynchronous request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a <Container> resource on registrar CSE AE is reachable on the URI: "AE-Notification-URI" |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking asynchronous request to delete the <Container> resource in registrar CSE. |
| 2 | Mca | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 4 (Delete) To (to) = <CSEBase>/<Container> From (from) = AE-ID Request Identifier (rqi) = Request-ID Response Type (rt) = 2 (non blocking asynchronous |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method = DELETE Request URI: <CSEBase>/<Container>?rt=2 Host : Host address of registrar CSE X-M2M-RTU: AE-Notification-URI X-M2M-RI: Request-ID X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Container> Uri-Query: rt=2 oneM2M-RTURI: AE-Notification-URI oneM2M-FR: AE-ID oneM2M-RQI: Request-ID Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <CSEBase>/<Container> fr = AE-ID rqi = Request ID rt=2 |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Status Code (rsc) = 1000 (Accepted) Request Identifier (rqi) = Request-ID Content (pc) = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202X-M2M-RSC: 1000 X-M2M-RI= Request-ID Payload: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = Request-ID Payload <Request> reference |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(1000) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | IOP Check | Registrar CSE sends notify request to AE |
| 6 | Mca | PRO Check Primitive | Sent Notify request contains Operation (op) = 5 (Notify) To (to) = AE-Notification-URI From (from) = registrar CSE-ID Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: AE-Notification-URI Host : AE X-M2M-RI: Request-ID X-M2M-Origin: Registrar CSE-ID Payload: Notification data object |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: AE host Uri-Port: AE port Uri-Path: AE-Notification-URI oneM2M-RQI = Request-ID oneM2M-Origin = Registrar CSE-ID Payload: Notification data object |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/< Registrar CSE-ID>/<SP-Relative-AE-ID>” Payload: op = 5 to = AE fr = Registrar CSE-ID rqi = Request ID nu = AE-Notification-URI |
| 7 | Mca | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | AE sends notify response to Registrar CSE containing: Code = 200 X-M2M-RSC: 2000 X-M2M-RI= Request ID Message-Body = empty |
|  |  | PRO Check CoAP | AE sends notify response to Registrar CSE containing: Response Code= 2.05 oneM2M-RSC=2000 oneM2M-RQI = Request-ID Payload = empty |
|  |  | PRO Check MQTT | Sent an MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/< Registrar CSE-ID>/<SP-Relative-AE-ID>” Payload: to = Registrar CSE-ID fr = AE-ID rqi = Request ID rsc = Response Status Code(2000) |
| 8 |  | IOP Check | Registrar CSE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

============== == End of  1st Part: Proposed Test Descriptions ==================