| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Non-blocking synchronous requests with new template |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr (LAAS-CNRS) monteil@laas.fr (LAAS-CNRS) drira@laas.fr (LAAS-CNRS) gharbi.ghada@laas.fr (LAAS-CNRS) |
| Date:* | 2015-07-13 |
| Abstract:* | The contribution proposes an update for non-blocking synchronous requests according to the new template to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution proposes an update of the non-blocking synchronous requests according to the new template to be added to TS-0013. The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============ Start of  1st Part: Proposed Test Descriptions ===============

## Non blocking configuration testing

### Synchronous request

### Container management

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_01 |
| Objective: | AE creates a <Container> resource using non blocking synchronous request in registrar CSE. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous request to create a <Container> resource in registrar CSE |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 1 (Create) to = {CSEBaseName} fr= AE-ID rqi = (token-string) rt = 1 (non blocking synchronous) ty = 3 (container) pc = Serialized Representationof the <Container> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Reques-Target: {CSEBaseName}?rt=1 Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content Type = application/vnd.onem2m-res+xml; ty=3 or application/vnd.onem2m-res+json; ty=3 Message-Body: Serialized Representation of <Container> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} Uri-Query: rt=1 oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Content Type = application/vnd.onem2m-res+xml; ty=3 or application/vnd.onem2m-res+json; ty=3 Payload: Serialized Representation of <Container> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 1 (Create) to = {CSEBaseName} fr= AE-ID rqi = (token-string) rt = 1 (non blocking synchronous) ty = 3 (container) pc = Serialized Representationof the <Container> resource |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: rsc = 1000 (Accepted) rqi = token-string) same as received in request message pc = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= token-string) same as received in request message Message-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = token-string) same as received in request message Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 1000 (Accepted) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Mca | PRO Check Primitive | Sent Retrieve request contains op = 2 (Retrieve) to = <Request> reference fr = AE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: <Request> reference oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Request> reference fr = AE-ID rqi = (token-string) pc = empty |
| 7 | Mca | PRO Check Primitive | rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Status Code = 200 X-M2M-RSC: 2000 X-M2M-RI= (token-string) same as received in request message Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-Body: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2000 (OK) pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_01 |
| Objective: | AE retrieves a <container> resource using non blocking synchronous request from registrar CSE. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a <Container> resource in registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous request to retrieve the <Container> resource from registrar CSE. |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName}/URI of <container> resource fr= AE-ID rqi = (token-string) rt = 1 (non blocking synchronous) pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Reques-Target: {CSEBaseName}/URI of <Container> resource ?rt=1 Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/URI of <Container> resource Uri-Query: rt=1 oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 2 (Retrieve) to = {CSEBaseName}/URI of <Container> resource fr= AE-ID rqi = (token-string) rt = 1 (non blocking synchronous) pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: rsc = 1000 (Accepted) rqi = token-string) same as received in request message pc = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= token-string) same as received in request message Message-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = (token-string) same as received in request message Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = token-string) same as received in request message rsc = 1000 (Accepted) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to send a retrieve request to <Request> reference |
| 6 | Mca | PRO Check Primitive | Sent Retrieve request contains op = 2 (Retrieve) to = <Request> reference fr = AE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: <Request> reference oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Request> reference fr = AE-ID rqi = (token-string) pc = empty |
| 7 | Mca | PRO Check Primitive | rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Status Code = 200 X-M2M-RSC: 2000 X-M2M-RI= (token-string) same as received in request message Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-Body: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2000 (OK) pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_03 |
| Objective: | AE updates a <Container> resource using non blocking synchronous request in registrar CSE. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created a <Container> resource in registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous request to update the <Container> resource. |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 3 (Update) to = {CSEBaseName}/URI of <Container> resource fr= AE-ID rqi = (token-string) rt = 1 (non blocking synchronous) pc = Serialized Representation of the updated <Container> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = UPDATE Reques-Target: {CSEBaseName}/URI of <Container> resource?rt=1 Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content Type = application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; Message-Body: Serialized Representation of updated <Container> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.03 (UPDATE) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/URI of <Container> resource Uri-Query: rt=1 oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Content Type = application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; Payload: Serialized Representation of updated <Container> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 3 (Update) to = {CSEBaseName}/URI of <Container> resource fr= AE-ID rqi = (token-string) rt = 1 (non blocking synchronous) pc = Serialized Representation of updated <Container> resource |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: rsc = 1000 (Accepted) rqi = token-string) same as received in request message pc = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= token-string) same as received in request message Message-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = token-string) same as received in request message Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = token-string) same as received in request message rsc = 1000 (Accepted) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Mca | PRO Check Primitive | Sent Retrieve request contains op = 2 (Retrieve) to = <Request> reference fr = AE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: <Request> reference oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Request> reference fr = AE-ID rqi = (token-string) pc = empty |
| 7 | Mca | PRO Check Primitive | rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Status Code = 200 X-M2M-RSC: 2000 X-M2M-RI= (token-string) same as received in request message Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-Body: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2000 (OK) pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) and the "operationResult" parameter containing the <Container> resource. |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NB_04 |
| Objective: | AE deletes a Container resource using non blocking synchronous request. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created <Container> resource on registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous request to delete the <Container> resource. |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 4 (Delete) to = {CSEBaseName}/URI of <container> resource fr= AE-ID rqi = (token-string) rt = 1 (non blocking synchronous) pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = DELETE Reques-Target: {CSEBaseName}/URI of <Container> resource ?rt=1 Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.04 (DELETE) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/URI of <Container> resource Uri-Query: rt=1 oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 4 (Delete) to = {CSEBaseName}/URI of <Container> resource fr= AE-ID rqi = (token-string) rt = 1 (non blocking synchronous) pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: rsc = 1000 (Accepted) rqi = token-string) same as received in request message pc = Reference to the created <Request> resource |
|  |  | PRO Check HTTP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Status Code = 202 X-M2M-RSC: 1000 X-M2M-RI= token-string) same as received in request message Message-Body: Reference to the created <Request> resource |
|  |  | PRO Check CoAP | Registrar CSE creates an internal <Request> resource and sends acknowledgement response containing: Response Code = None oneM2M-RSC=1000 oneM2M-RQI = (token-string) same as received in request message Payload: Reference to the created <Request> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = token-string) same as received in request message rsc = 1000 (Accepted) pc = Reference to the created <Request> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to send a retrieve request to <Request> reference |
| 6 | Mca | PRO Check Primitive | Sent Retrieve request contains op = 2 (Retrieve) to = <Request> reference fr = AE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-Body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: <Request> reference oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Request> reference fr = AE-ID rqi = (token-string) pc = empty |
| 7 | Mca | PRO Check Primitive | rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) |
|  |  | PRO Check HTTP | Registrar CSE sends response to AE containing: Status Code = 200 X-M2M-RSC: 2000 X-M2M-RI= (token-string) same as received in request message Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-Body: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) |
|  |  | PRO Check CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2000 (OK) pc = <Request> resource with the parameter "requestStatus" set to 1 (COMPLETED) |
| 8 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

========= == End of  1st Part: Proposed Test Descriptions ================