| Input Contribution |
| --- |
| Meeting ID* | TST#18.1 |
| Title:* | TS-0013 mgmtObj new template |
| Source:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Uploaded Date:* | 2015-07-28 |
| Document(s) Impacted* | TS-0013-V0.1.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorperate the text if agreed. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

============== == Start of  1st Part: Proposed Test Descriptions ==================

### <mgmtObj> Test Description

#### 8.2.12.1	<mgmtObj> Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_0x |
| Objective: | AE creates a <mgmtObj> resource |
| Configuration: | CFG_SH_03 |
| References: | [1] 10.2.8.2 |
| Pre-test conditions: | Management Session between Management Server and Management Client |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an <mgmtObj> Create Request to create an <mgmtObj> on IN-CSE. |
| 2 | Mca | PRO Check Primitive | op: 1 (CREATE) fr: AE-ID to: {CSEBaseName}/{node} rqi = (token-string) ty = 13 (mgmtObj) pc: Serialized representation of the <mgmtObj> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Request-Target: {CSEBaseName}/{node} Host : IP address or FQDN of the IN-CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; ty=13 or application/vnd.onem2m-res+json; ty=13 Message-body: Serialized representation of the <mgmtObj> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{node} Content-type: application/vnd.onem2m-res+xml; ty = 13 or application/vnd.onem2m-res+json; ty = 13 oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: Serialized representation of <mgmtObj> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 1 (Create) to = {CSEBaseName}/{node} fr = AE-ID rqi = (token-string) ty = 13 (mgmtObj) pc = Serialized representation of <AE> resource |
| 3 |  | IOP Check | Check if possible that the <mgmtObj> resource is created in IN-CSE |
| 4 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Requests to create the corresponding MO using Add DM command. The mapping of <mgmtObj> and MO can be referenced from 5.3 of TS-0005. |
|  |  | PRO Check BBF TR069 | Requests to create the corresponding information model using AddObject RPC. The mapping of <mgmtObj> and information model or RPC can be referenced from clause 7 of TS-0006. |
|  |  | PRO Check OMA LWM2M | Requests to create the corresponding Objects using Create LWM2M Create operations. The mapping of <mgmtObj> and Object can be referenced from 6.3 of TS-0005. |
| 5 |  | IOP Check | Check if possible that the corresponding MO for OMA DM, information model for BBF TR069 or Object for OMA LWM2M is created on the Managed Entity. |
| 6 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Response with status code (200) OK. Details can be found in clause 5.4 TS-0005. |
|  |  | PRO Check BBF TR069 | Successful response of the RPC. Details can be found in clause 8.1 TS-0006. |
|  |  | PRO Check OMA LWM2M | Response with status code 2.01 Created. Details can be found in clause 6.4 TS-0005. |
| 7 | Mca | PRO Check Primitive | rsc = 2001 (CREATED) rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtObj> resource |
|  |  | PRO Check HTTP | IN-CSE sends response containing: Status Code = 201 (OK) X-M2M-RSC: 2001 X-M2M-RI: (token-string) same as received in request message Content-Location: URI of the created <mgmtObj> resource. Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <mgmtObj> resource |
|  |  | PRO Check CoAP | IN-CSE sends response containing: Response Code = 2.01 oneM2M-RSC: 2001 oneM2M-RQI: (token-string) same as received in request message Location-Path: URI of the created <mgmtObj> resource Payload: Serialized representation of <mgmtObj> resource |
|  |  | PRO Check MQTT | IN-CSE MQTT PUBLISH message: Topic: “/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rsc = 2001 (CREATED) rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtObj> resource |
| 8 |  | IOP Check | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the created resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.2.12.2	<mgmtObj> Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_0x |
| Objective: | AE updates a <mgmtObj> resource |
| Configuration: | CFG_SH_03 |
| References: | [1] 10.2.8.4 |
| Pre-test conditions: | Management Session between Management Server and Management Client |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an <mgmtObj> Update Request to update an <mgmtObj> on IN-CSE. |
| 2 | Mca | PRO Check Primitive | op: 3 (UPDATE) fr: AE-ID to: {CSEBaseName}/{node}/{mgmtObj} rqi = (token-string) pc: Serialized representation of the <mgmtObj> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = PUT Request-Target: {CSEBaseName}/{node}/{mgmtObj} Host : IP address or FQDN of the IN-CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; Message-body: Serialized representation of the <mgmtObj> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.03 (PUT) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{node}/{mgmtObj} Content-type: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: Serialized representation of <mgmtObj> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message Topic: “/oneM2M/req/<AE-ID>/<Registrar CSE-ID>” Payload: op = 3 (Update) to = {CSEBaseName}/{node}/{mgmtObj} fr = AE-ID rqi = (token-string) pc = Serialized representation of <mgmtObj> resource |
| 3 |  | IOP Check | Check if possible that the <mgmtObj> resource is updated in IN-CSE |
| 4 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Requests to update the corresponding MO using Replace DM command. The mapping of <mgmtObj> and MO can be referenced from 5.3 of TS-0005. |
|  |  | PRO Check BBF TR069 | Requests to Update the corresponding information model using SetParameterValues RPC. The mapping of <mgmtObj> and information model or RPC can be referenced from clause 7 of TS-0006. |
|  |  | PRO Check OMA LWM2M | Requests to Update the corresponding Objects using LWM2M Write operations. The mapping of <mgmtObj> and Object can be referenced from 6.3 of TS-0005. |
| 5 |  | IOP Check | Check if possible that the corresponding MO for OMA DM, information model for BBF TR069 or Object for OMA LWM2M is Updated on the Managed Entity. |
| 6 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Response with status code (200) OK. Details can be found in clause 5.4 TS-0005. |
|  |  | PRO Check BBF TR069 | Successful response of the RPC. Details can be found in clause 8.1 TS-0006. |
|  |  | PRO Check OMA LWM2M | Response with status code 2.04 Changed. Details can be found in clause 6.4 TS-0005. |
| 7 | Mca | PRO Check Primitive | rsc = 2004 (CHANGED) rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtObj> resource |
|  |  | PRO Check HTTP | IN-CSE sends response containing: Code = 200 X-M2M-RSC: 2004 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <mgmtObj> resource |
|  |  | PRO Check CoAP | IN-CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2004 oneM2M-RQI: (token-string) same as received in request message Payload: Serialized representation of <mgmtObj> resource |
|  |  | PRO Check MQTT | IN-CSE sends a MQTT PUBLISH message Topic: “/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2004 pc = Serialized representation of <mgmtObj> resource |
| 8 |  | IOP Check | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the Updated resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.2.12.3	<mgmtObj> Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_0x |
| Objective: | AE retrieves a <mgmtObj> resource |
| Configuration: | CFG_SH_03 |
| References: | [1] 10.2.8.3 |
| Pre-test conditions: | Management Session between Management Server and Management Client |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an <mgmtObj> Retrieve Request to retrieve an <mgmtObj> on IN-CSE. |
| 2 | Mca | PRO Check Primitive | op = 2 (RETRIEVE) to = {CSEBaseName}/{node}/{mgmtObj} fr = AE-ID rqi = (token-string) |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}/{node}/{mgmtObj} Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{node}/{mgmtObj} Content-type: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; oneM2M-FR: AE-ID oneM2M-RQI: (token-string) |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message: Topic: “/oneM2M/req/<AE-ID>/<Registrar CSE-ID>” Payload: op = 2 (Retrieve) to = {CSEBaseName}/{node}/{mgmtObj} fr = <AE-ID> rqi = (token-string) |
| 3 |  | IOP Check | Check if possible that the <mgmtObj> resource is retrieved in IN-CSE |
| 4 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Requests to retrieve the corresponding MO using Get DM command. |
|  |  | PRO Check BBF TR069 | Requests to retrieve the corresponding information model using GetParametersValue RPC. |
|  |  | PRO Check OMA LWM2M | Requests to retrieve the corresponding Objects using Retrieve LWM2M Read operation. |
| 5 |  | IOP Check |  |
| 6 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Response with status code (200) OK with the information of the MO. Details can be found in clause 5.4 TS-0005. |
|  |  | PRO Check BBF TR069 | Successful response of the RPC with the information about the management related information. Details can be found in clause 8.1 TS-0006. |
|  |  | PRO Check OMA LWM2M | Response with status code 2.05 Content with the information of the Object. Details can be found in clause 6.4 TS-0005. |
| 7 | Mca | PRO Check Primitive | rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtObj> resource |
|  |  | PRO Check HTTP | IN-CSE sends response containing: Status Code =200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Message-body: Serialized representation of <mgmtObj> resource |
|  |  | PRO Check CoAP | IN-CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Payload: Serialized representation of <mgmtObj> resource |
|  |  | PRO Check MQTT | IN-CSE sends a MQTT PUBLISH message: Topic: “/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rsc = 2000 rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtObj> resource |
| 8 |  | IOP Check | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the retrieved resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.2.12.4	<mgmtObj> Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_0x |
| Objective: | AE deletes a <mgmtObj> resource |
| Configuration: | CFG_SH_03 |
| References: | [1] 10.2.8.5 |
| Pre-test conditions: | Management Session between Management Server and Management Client |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an <mgmtObj> Delete Request to delete an <mgmtObj> on IN-CSE. |
| 2 | Mca | PRO Check Primitive | op = 4 (DELETE) to = {CSEBaseName}/{node}/{mgmtObj} fr = AE-ID rqi = (token-string) |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method = DELETE Request-Target: {CSEBaseName}/{node}/{mgmtObj} Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{node}/{mgmtObj} oneM2M-FR: AE-ID oneM2M-RQI: (token-string) |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message Topic: “/oneM2M/req/< AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = {CSEBaseName}/{node}/{mgmtObj} fr = AE-ID rqi = (token-string) |
| 3 |  | IOP Check | Check if possible that the <mgmtObj> resource is deleted in IN-CSE |
| 4 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Requests to delete the corresponding MO using Delete DM command. |
|  |  | PRO Check BBF TR069 | Requests to delete the corresponding information model using DeleteObject RPC. |
|  |  | PRO Check OMA LWM2M | Requests to delete the corresponding Objects using LWM2M Delete operation. |
| 5 |  | IOP Check | Check if possible that the corresponding MO for OMA DM, information model for BBF TR069 or Object for OMA LWM2M is deleted on the Managed Entity. |
| 6 | mc | PRO Check Primitive | N/A |
|  |  | PRO Check OMA DM | Response with status code (200) OK. Details can be found in clause 5.4 TS-0005. |
|  |  | PRO Check BBF TR069 | Successful response of the RPC. Details can be found in clause 8.1 TS-0006. |
|  |  | PRO Check OMA LWM2M | Response with status code 2.02 Deleted. Details can be found in clause 6.4 TS-0005. |
| 7 | Mca | PRO Check Primitive | rsc = 2002 (DELETED) rqi = (token-string) same as received in request message |
|  |  | PRO Check HTTP | IN-CSE sends response containing: Status Code = 200 X-M2M-RSC: 2002 X-M2M-RI: (token-string) same as received in request message |
|  |  | PRO Check CoAP | IN-CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2002 oneM2M-RQI: (token-string) same as received in request message |
|  |  | PRO Check MQTT | IN-CSE sends a MQTT PUBLISH message Topic: “/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2002 |
| 8 |  | IOP Check | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the deleted resource is removed after the expiry of its lifetime |
| IOP Verdict |  |
| PRO Verdict |  |

============== == End of  1st Part: Proposed Test Descriptions ==================