| Input Contribution |
| --- |
| Meeting ID* | TST18.2 |
| Title:* | TS-0018-Test Purposes contribution |
| Source:* | Miguel A. Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org Alexandre Berge, AMB Consulting, Alexandre.berge@amb-consulting.com Laurent Velez, ETSI, Laurent.Velez@etsi.org |
| Uploaded Date:* | 2015-08-20 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes and some text to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes a Test Purpose template to be used in TS-0018 – Test Suite Structure and Test Purposes.

Proposal

================ Start of  1st  Part: Test Purposes ==================

## 7.2	Test Purposes for oneM2M

Editor Note: The following TPs contain some test variables (using upper-case and italic) which will be instantiated during test execution.

| TP Id | TP/oneM2M/CSE/REG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE registration (allowed App-ID, C-AE-ID-STEM not provided by AE) |
| Reference | TS-0001 10.1.1.2.2 - case C, 9.6.19 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a CSEBase resource containing a ServiceSubscribedProfile resource containing a ServiceSubscribedNode resource containing RuleLinks attribute pointing to a ServiceSubscribedAppRule resource containing applicableCredIDs attribute set to None and allowedApp-IDs attribute indicating APP-ID and allowedAEs attribute indicating C-AE-ID-STEM } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing Resource-Type set to 2 (AE) and From set to empty and Content <AE> containing App-ID attribute set to APP-ID } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

================ Start of  1st  Part: Test Purposes ==================