| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Add contentType option to notification Create |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr monteil@laas.fr drira@laas.fr |
| Date:* | 2015-07-21 |
| Abstract:* | The contribution adds contentType option to notification Create for CoAP binding to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution adds contentType option to notification Create for CoAP binding to be added to TS-0013. The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

======Start of  1st Part: Proposed Test Descriptions ===========

### Notifcation Management

#### Notification Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_39 |
| Objective: | AE receives a notification request from the HOST CSE |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.12 [2] 7.4.1 |
| Pre-test conditions: | AE1 has created an application resource <AE> on registrar CSE AE1 has created a container resource <container> on registrar CSE AE1 has created a <subscription> as a child resource of a <container> AE2 has created an application resource <AE> on registrar CSE AE2 has permisions to CREATE a Content Instance in the container created by AE1 |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE2 is requested to send a Create request to create <contentInstance> in the <container> created by AE1. This triggers or causes the HOST CSE to send a notification to AE1. |
| 2 | Check Mca | PRO Check Primitive | op = 5 (Notify) to = notificationURI of subscription resource from = Registrar CSE-ID rqi = (token-string) pc = Serialized representation of Notification data object |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Request-Target: notificationURI of subscription resource Host: IP address or FQDN of notificationURI X-M2M-RI: (token-string) X-M2M-Origin: {CSEBaseName} Content-Type: application/vnd.onem2m-ntfy+xml; or application/vnd.onem2m-ntfy+json; Message-body: Serialized Representation of Notification data object |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: notificationURI host Uri-Port: notificationURI port Uri-Path: AE1 AE-ID oneM2M-FR: Registrar CSE-ID oneM2M-RQI: (token-string) Content-Type: application/vnd.onem2m-ntfy+xml; or application/vnd.onem2m-ntfy+json; Payload: Serialized Representation of Notification data object |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/<Registrar CSE-ID>/<AE-ID>” Payload: op = 5 (Notify) to = notificationURI of subscription resource fr = Registrar CSE-ID rqi = (token-string) pc = empty |
| 4 |  | IOP Check | Check if the notification representation |
| 7 | Check Mca | PRO Check Primitive | Sent response contains rsc = 2000 (OK) rqi = (token-string) same as received in request message |
|  |  | PRO Check HTTP | Sent response contains: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message |
|  |  | PRO Check CoAP | Sent response contains: Response Code = 2.01 oneM2M-RSC: 2000(OK) oneM2M-RQI: (token-string) same as received in request message |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/<Registrar CSE-ID>/<AE-ID>” Payload: to = Registrar CSE-ID fr = AE1 AE-ID rsc = 2000(OK) rqi = (token-string) same as received in request message |
| 8 |  | IOP Check | AE1 indicates notification received |
| IOP Verdict |  |
| PRO Verdict |  |

=========End of  1st Part: Proposed Test Descriptions ==================