| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Test retargeting with all resources |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr monteil@laas.fr drira@laas.fr |
| Date:* | 2015-08-31 |
| Abstract:* | Test retargeting with all resources |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution adds missing resource to retargeting test cases to be added to TS-0013. The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

=========Start of  1st Part: Proposed Test Descriptions ==================

## Single hop configuration testing

### Retargeting

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | AE creates a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Create Request to create <container> on the Hosting CSE. |
| 2 | Mca | PRO Check Primitive | op = 1 (Create) to = {CSEBaseName} fr = AE-ID rqi = (token-string) ty = 3 (Container) pc = Serialized representation of <container> resource |
| 3 |  | IOP Check | Check if possible that the request is forwarded by the registrar CSE of the AE to the Hosting CSE. |
| 4 | Mcc | PRO Check Primitive | op = 1 (Create) to = {CSEBaseName} fr = AE-ID rqi = (token-string) ty = 3 (Container) pc = Serialized representation of <container> resource |
| 5 |  | IOP Check | Check if possible that the <container> resource is created by the Hosting CSE. |
| 6 | Mcc | PRO Check Primitive | rsc = 2001 (CREATED) rqi = (token-string) same as received in request message pc = Serialized representation of <container> resource |
| 7 |  | IOP Check | Check if possible that the response is forwarded by the registrar CSE of the AE to the AE. |
| 8 | Mca | PRO Check Primitive | rsc = 2001 (CREATED) rqi = (token-string) same as received in request message pc = Serialized representation of <container> resource |
| 9 |  | IOP Check | AE indicates successful operation |
| 10 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 11 |  | IOP Check | Check the created resource is removed after the expiry of its lifetime |
| 12 |  | IOP Check | Repeat step 1-9 to create a RemoteCSE resource |
| 13 |  | IOP Check | Repeat step 1-9 to create an AE resource |
| 14 |  | IOP Check | Repeat step 1-9 to create a ContentInstance resource |
| 15 |  | IOP Check | Repeat step 1-9 to create a Group resource |
| 16 |  | IOP Check | Repeat step 1-9 to create a Subscription resource |
| 17 |  | IOP Check | Repeat step 1-9 to create an ACP resource |
| 18 |  | IOP Check | Repeat step 1-9 to create a PollingChannel resource |
| 19 |  | IOP Check | Repeat step 1-9 to create a Notification resource |
| 20 |  | IOP Check | Repeat step 1-9 to create a FanOut resource |
| 21 |  | IOP Check | Repeat step 1-9 to create a Node resource |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_02 |
| Objective: | AE retrieves a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | Resource <AE> has been created in Registrar CSE Resource <container> has been created in < AE> in Hosting CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Retrieve Request to retrieve <container> on the Hosting CSE. |
| 2 | Mca | PRO Check Primitive | op = 2 (Retrieve) to = {CSEBaseName}/{container} fr = AE-ID rqi = (token-string) |
| 3 |  | IOP Check | Check if possible that the request is forwarded by the registrar CSE of the AE to the Hosting CSE. |
| 4 | Mcc | PRO Check Primitive | op = 2 (Retrieve) to = {CSEBaseName}/{container} fr = AE-ID rqi = (token-string) |
| 5 |  | IOP Check |  |
| 6 | Mcc | PRO Check Primitive | rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of <container> resource |
| 7 |  | IOP Check | Check if possible that the response is forwarded by the registrar CSE of the AE to the AE. |
| 8 | Mca | PRO Check Primitive | rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of <container> resource |
| 9 |  | IOP Check | AE indicates successful operation |
| 10 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 11 |  | IOP Check | Check the created resource is removed after the expiry of its lifetime |
| 12 |  | IOP Check | Repeat step 1-9 to retrieve a CSEBase resource |
| 13 |  | IOP Check | Repeat step 1-9 to retrieve a RemoteCSE resource |
| 14 |  | IOP Check | Repeat step 1-9 to retrieve an AE resource |
| 15 |  | IOP Check | Repeat step 1-9 to retrieve a ContentInstance resource |
| 16 |  | IOP Check | Repeat step 1-9 to retrieve a Group resource |
| 17 |  | IOP Check | Repeat step 1-9 to retrieve a Subscription resource |
| 18 |  | IOP Check | Repeat step 1-9 to retrieve an ACP resource |
| 19 |  | IOP Check | Repeat step 1-9 to retrieve a PollingChannel resource |
| 20 |  | IOP Check | Repeat step 1-9 to retrieve a FanOut resource |
| 21 |  | IOP Check | Repeat step 1-9 to retrieve a Node resource |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_03 |
| Objective: | AE updates a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in < AE> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Create Request to create <container> on the Hosting CSE. |
| 2 | Mca | PRO Check Primitive | op = 3 (Update) to = {CSEBaseName}/{container} fr = AE-ID rqi = (token-string) pc = Serialized representation of <container> resource |
| 3 |  | IOP Check | Check if possible that the request is forwarded by the registrar CSE of the AE to the Hosting CSE. |
| 4 | Mcc | PRO Check Primitive | op = 3 (Update) to = {CSEBaseName}/{container} fr = AE-ID rqi = (token-string) pc = Serialized representation of <container> resource |
| 5 |  | IOP Check | Check if possible that the <container> resource is updated by the Hosting CSE. |
| 6 | Mcc | PRO Check Primitive | rsc = 2004 (CHANGED) rqi = (token-string) same as received in request message pc = Serialized representation of <container> resource |
| 7 |  | IOP Check | Check if possible that the response is forwarded by the registrar CSE of the AE to the AE. |
| 8 | Mca | PRO Check Primitive | rsc = 2004 (CHANGED) rqi = (token-string) same as received in request message pc = Serialized representation of <container> resource |
| 9 |  | IOP Check | AE indicates successful operation |
| 10 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 11 |  | IOP Check | Check the created resource is removed after the expiry of its lifetime |
| 12 |  | IOP Check | Repeat step 1-9 to update a RemoteCSE resource |
| 13 |  | IOP Check | Repeat step 1-9 to update an AE resource |
| 14 |  | IOP Check | Repeat step 1-9 to update a ContentInstance resource |
| 15 |  | IOP Check | Repeat step 1-9 to update a Group resource |
| 16 |  | IOP Check | Repeat step 1-9 to update a Subscription resource |
| 17 |  | IOP Check | Repeat step 1-9 to update an ACP resource |
| 18 |  | IOP Check | Repeat step 1-9 to update a PollingChannel resource |
| 19 |  | IOP Check | Repeat step 1-9 to update a FanOut resource |
| 20 |  | IOP Check | Repeat step 1-9 to update a Node resource |
| IOP Verdict |  |
| PRO Verdict |  |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_04 |
| Objective: | AE delete a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | Resource <AE> has been created in Registrar CSE Resource <container> has been created in Hosting CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Retrieve Request to retrieve <container> on the Hosting CSE. |
| 2 | Mca | PRO Check Primitive | op = 4 (Delete) to = {CSEBaseName}/{container} fr = AE-ID rqi = (token-string) |
| 3 |  | IOP Check | Check if possible that the request is forwarded by the registrar CSE of the AE to the Hosting CSE. |
| 4 | Mcc | PRO Check Primitive | op = 4 (Delete) to = {CSEBaseName}/{container} fr = AE-ID rqi = (token-string) |
| 5 |  | IOP Check | Check if possible that the <container> resource is deleted by the Hosting CSE. |
| 6 | Mcc | PRO Check Primitive | rsc = 2002 (DELETED) rqi = (token-string) same as received in request message |
| 7 |  | IOP Check | Check if possible that the response is forwarded by the registrar CSE of the AE to the AE. |
| 8 | Mca | PRO Check Primitive | rsc = 2002 (DELETED) rqi = (token-string) same as received in request message |
| 9 |  | IOP Check | AE indicates successful operation |
| 10 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 11 |  | IOP Check | Check the created resource is removed after the expiry of its lifetime |
| 12 |  | IOP Check | Repeat step 1-9 to delete a RemoteCSE resource |
| 13 |  | IOP Check | Repeat step 1-9 to delete an AE resource |
| 14 |  | IOP Check | Repeat step 1-9 to delete a ContentInstance resource |
| 15 |  | IOP Check | Repeat step 1-9 to delete a Group resource |
| 16 |  | IOP Check | Repeat step 1-9 to delete a Subscription resource |
| 17 |  | IOP Check | Repeat step 1-9 to delete an ACP resource |
| 18 |  | IOP Check | Repeat step 1-9 to delete a PollingChannel resource |
| 19 |  | IOP Check | Repeat step 1-9 to delete a FanOut resource |
| 20 |  | IOP Check | Repeat step 1-9 to delete a Node resource |
| IOP Verdict |  |
| PRO Verdict |  |

=========End of  1st Part: Proposed Test Descriptions ==================