| Input Contribution |
| --- |
| Meeting ID* | TST19 |
| Title:* | TS-0018-TP Definition conventions contribution |
| Source:* | Keebum Kim, TTA, keebum.kim@tta.or.kr Sookhyun Jeon, TTA, shjeon@tta.or.kr Kanghae Lee, TTA, kanghae@tta.or.kr |
| Uploaded Date:* | 2015-08-26 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | This contribution is to propose the TP Definition conventions to be added to TS-0018 (test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes TP Definition conventions to be used in TS-0018 – Test Suite Structure and Test Purposes.

================ Start of  1st  Part: TP definition conventions ==================

### 7.1.1	TP definition conventions

The Test Purposes are defined according to the following rules:

- TP Id: It is a unique identifier(TP/<IUT>/<GR>/<SGR>/<XX> - <NNN>).

It is specified according to the naming convention defined below:

- Each Test Purpose Identifier is introduced by the prefix “TP”.

- <IUT>: It is the entity type of IUT(Implementation Under Test).

- AE: Application Entity.

- CSE: Common Services Entity.

- <GR>: It identifies the entity role group of test cases.

- <SGR>: It identifies the resource management and common services functions subgroup of test cases.

- <XX>: It identifies the type of testing.

- BV: Valid Behavior Test.

- BI: Invalid Behavior Test.

- <NNN>: It is a sequential number that identifies test purpose.

- Test Objective: It is a description about the requirements to be tested.

- Reference: It contains the specification reference and clause to be checked by the TP.

- Config Id: It indicates the test configuration that shows the related Reference Point(Mca, Mcc).

- Applicability: It contains the PICS items that define if the Test Case is applicable or not for a specific device.

- Initial conditions: It indicates the state to which the IUT needs to be moved at the beginning of TC execution.

- Expected procedural behaviour: It describes the step to be followed in order to execute the test case.

================ End of  1st  Part: TP definition conventions ==================