| Input Contribution |
| --- |
| Meeting ID* | TST20 |
| Title:* | TS-0018-GMG_Test_Purposes_contribution |
| Source:* | Keebum Kim, TTA, keebum.kim@tta.or.kr Sookhyun Jeon, TTA, shjeon@tta.or.kr Kanghae Lee, TTA, kanghae@tta.or.kr |
| Uploaded Date:* | 2015-10-30 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes new Group Management(GMG) Test Purposes for the TS-0018 – Test Suite Structure and Test Purposes.

Proposal

================ Start of  1st  Part: Test Purposes ==================

## 7.2	Test Purposes for oneM2M

## 7.2.2	Group CSE

## 7.2.2.4		Group Management (GMG)

| TP Id | TP/oneM2M/CSE/GMG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of the <group> resource when member ID exceed max number of members. |
| Reference | TS-0001 10.2.7.2 & TS-0004 7.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to RESOURCE_TYPE and From set to AE-ID and Content <group> resource containing currentNrOfMembers set to larger number than maxNrOfMembers } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 6010 (MAX_NUMBER_OF_MEMBER_EXCEEDED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/002 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of the <group> resource when the memberType cannot be retrieved due to lack of privilege. |
| Reference | TS-0001 10.2.7.2 & TS-0004 7.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation the sub-group members being in the “inital state” and the sub-group members having RESOURCE_TYPE containing accessControlPolicyIDs attribute pointing to accessControlPolicy resource containing Privileges attribute containing accessControlRule containing accessControlOriginators not indicating AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to RESOURCE_TYPE and From set to AE-ID and Content <group> resource } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 5105 (NO_PRIVILEGE) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/003 |
| --- | --- |
| Test objective | Check that the IUT rejects the update of the <group> resource when the memberType cannot be retrieved due to lack of privilege. |
| Reference | TS-0001 10.2.7.4 & TS-0004 7.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform UPDATE operation the sub-group members being in the “inital state” and the sub-group members having RESOURCE_TYPE containing accessControlPolicyIDs attribute pointing to accessControlPolicy resource containing Privileges attribute containing accessControlRule containing accessControlOriginators not indicating AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to RESOURCE_TYPE and From set to AE-ID and Content <group> resource } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 5105 (NO_PRIVILEGE) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/004 |
| --- | --- |
| Test objective | Check that the IUT rejects the update of the <group> resource when member ID exceed max number of members. |
| Reference | TS-0001 10.2.7.4 & TS-0004 7.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to RESOURCE_TYPE and From set to AE-ID and Content <group> resource containing currentNrOfMembers set to larger number than maxNrOfMembers } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/005 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of the RESOURCE_TYPE resource by using <fanOutPoint> in <group> resource. |
| Reference | TS-0001 10.2.7.7 & TS-0004 7.3.14 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a <group> resource containing the memberIDs set to List of member resource IDs and the IUT having a <group> resource allowing the AE to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to FANOUTPOINT_ADDRESS and Resource Type set to RESOURCE_TYPE and From set to AE-ID and Content RESOURCE_TYPE } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) and Content attribute containing aggregatedResponse representation } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/006 |
| --- | --- |
| Test objective | Check that the IUT returns successfully the resource of the group members by using <fanOutPoint> in <group> resource. |
| Reference | TS-0001 10.2.7.8 & TS-0004 7.3.14 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a <group> resource containing the memberIDs set to List of member resource IDs and the IUT having a <group> resource allowing the AE to perform RETRIEVE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to FANOUTPOINT_ADDRESS and From set to AE-ID } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing aggregatedResponse representation } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/007 |
| --- | --- |
| Test objective | Check that the IUT accepts the update of the RESOURCE_TYPE resource by using <fanOutPoint> in <group> resource. |
| Reference | TS-0001 10.2.7.9 & TS-0004 7.3.14 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a <group> resource containing the memberIDs set to List of member resource IDs and the IUT having a <group> resource allowing the AE to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to FANOUTPOINT_ADDRESS and Resource Type set to RESOURCE_TYPE and From set to AE-ID and Content RESOURCE_TYPE } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (CHANGED) and Content attribute containing aggregatedResponse representation } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/008 |
| --- | --- |
| Test objective | Check that the IUT could delete the RESOURCE_TYPE resource by using <fanOutPoint> in <group> resource. |
| Reference | TS-0001 10.2.7.10 & TS-0004 7.3.14 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a <group> resource containing the memberIDs set to List of member resource IDs and the IUT having a <group> resource allowing the AE to perform DELETE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE request from AE containing To set to FANOUTPOINT_ADDRESS and From set to AE-ID } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2002 (DELETED) and Content attribute containing aggregatedResponse representation } | IUT ( AE |

================ End of  1st  Part: Test Purposes ==================