| Input Contribution |
| --- |
| Meeting ID* | TST #20 |
| Title:* | TS-0018-DIS_LOC_Test_Purpose_Contributions |
| Source:* | Keebum Kim, TTA, keebum.kim@tta.or.kr Sookhyun Jeon, TTA, shjeon@tta.or.kr Kanghae Lee, TTA, kanghae@tta.or.kr |
| Uploaded Date:* | 2015-11-03 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes DIS and LOC test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes new Discovery(DIS) and LOC(Location) Test Purposes for the TS-0018 – Test Suite Structure and Test Purposes.

Proposal

================ Start of  1st  Part: Test Purposes ==================

## 7.2	Test Purposes for oneM2M

## 7.2.2	Group CSE

## 7.2.2.5	Discovery (DIS)

| TP Id | TP/oneM2M/CSE/DIS/RET/BV/001 |
| --- | --- |
| Test objective | Check that the IUT returns successfully a list all discovered resource addresses |
| Reference | TS-0001 10.2.6 & TS-0004 7.2.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS allowing the AE to perform RETRIEVE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and FilterUsage set to 1 (Discovery Criteria) and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing URIList representation } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DIS/RET/BV/002 |
| --- | --- |
| Test objective | Check that the IUT returns successfully appropriate list of discovered resource when the filter criteria is provided in the request |
| Reference | TS-0001 8.1.3 & 10.2.6 & TS-0004 7.2.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS allowing the AE to perform RETRIEVE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request with specific filter criteria from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and FilterUsage set to 1 (Discovery Criteria) and FilterCriteria set to FILTER_CRITERIA_CONDITIONS and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing URIList representation } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DIS/RET/BV/003 |
| --- | --- |
| Test objective | Check that the IUT returns the empty address list when no result matching with filter criteria is discovered |
| Reference | TS-0001 8.1.3 & 10.2.6 & TS-0004 7.2.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS allowing the AE to perform RETRIEVE operation and FILTER_CRITERIA_CONDITIONS not being applicable to the IUT } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request with specific filter criteria from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and FilterUsage set to 1 (Discovery Criteria) and FilterCriteria set to FILTER_CRITERIA_CONDITIONSand no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and no Content attribute } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DIS/RET/BV/004 |
| --- | --- |
| Test objective | Check that the IUT returns successfully a list of discovered resource addresses with Non-hierarchical addressing form when the Discovery Result Type is provided in the request |
| Reference | TS-0001 8.1.3 & 10.2.6 & TS-0004 7.2.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS allowing the AE to perform RETRIEVE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request with specific filter criteria from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and FilterUsage set to 1 (Discovery Criteria) and DiscoveryResultType set to 2 (unstructured) and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing URIList representation containing unstructured addresses of discovered resources } | IUT ( AE |

## 7.2.2.6 Location (LOC)

| TP Id | TP/oneM2M/CSE/LOC/CRE/BV/001 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of the <locationPolicy> resource when locationSource attribute is set by Network Based and Location Server is not reachable. |
| Reference | TS-0001 8.5. & 10.2.10 & TS-0004 7.3.10 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having no connection to Location Server and the IUT having a CSEBase resource allowing the AE to perform CREATE operation and } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to CSEBase resource and From set to AE-ID and Content <locationPolicy> resource } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

Editor Note: To be updated

================ end of  2nd   Part: Test Purposes ==================

# Header

Text here.