| Input Contribution |
| --- |
| Meeting ID* | TST 20 |
| Title:* | TS-0018 SUB Test Purposes |
| Source:* | Sungchan Choi, KETI, csc@keti.re.kr Ting Martin Miao, KETI, novamartin@keti.re.kr Minu Ryu, KETI, minu@keti.re.kr Jaeho Kim, KETI, jhkim@keti.re.kr |
| Uploaded Date:* | 2015-11-02 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes Subscription and Notification (SUB) Test Purposes for the TS-0018 – Test Suite Structure and Test Purposes.

# 7	Test Purposes (TP)

## 7.2	Test Purposes for oneM2M

## 7.2.2	Group CSE

## 7.2.2.4		Subscription and Notification (SUB)

| TP Id | TP/oneM2M/CSE/SUB/CRE/BV/001 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of the <subscription> resource when the target subscribed-to resource is not subscribable. |
| Reference | TS-0001 10.2.11.2 & TS-0004 7.3.8.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation and the IUT having a resource PARENT_RESOURCE_ADDRESS not being subscribable resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource-Type set to <subscription> and From set to AE-ID and Content <subscription> resource } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 5203 (TARGET_NOT_SUBSCRIBABLE) and no Content attribute } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/SUB/CRE/BV/002 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of the <subscription> resource when the originator doesn’t have privileges for retrieving the subscribed-to resource. |
| Reference | TS-0001 10.2.11.2 & TS-0004 7.3.8.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a resource PARENT_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute pointing to accessControlPolicy resource containing Privileges attribute containing accessControlRule containing accessControlOriginators indicating AE-ID and accessControlOperations not indicating RETRIEVE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource-Type set to <subscription> and From set to AE-ID and Content <subscription> resource } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 5105 (NO_PRIVILEGE) and no Content attribute } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/SUB/CRE/BV/003 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of the <subscription> resource when the notificationURI is not the originator and the IUT cannot send the Notify request to the notificationURI with verificationRequest parameter set as TRUE |
| Reference | TS-0001 10.2.11.2 & TS-0004 7.3.8.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource-Type set to <subscription> and From set to AE-ID and Content <subscription> resource containing NotificationURI attribute set to NOTI_URI_ADDRESS(not the originator) and the IUTcannot send the Notify request to the NOTI_URI_ADDRESS in notificationURI attribute with verificationRequest parameter set to TRUE } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 5204 (SUBSCRIPTION_VERIFICATION_INITIATION_FAILED) and no Content attribute } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/SUB/CRE/BV/004 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of the <subscription> resource when the notificationURI is not the originator and the IUT send the Notify request to the notificationURI with verificationRequest parameter set as TRUE |
| Reference | TS-0001 10.2.11.2 & TS-0004 7.3.8.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource-Type set to <subscription> and From set to AE-ID and Content <subscription> resource containing NotificationURI attribute set to NOTI_URI_ADDRESS(not the originator) and the IUTsent the Notify request to the NOTI_URI_ADDRESS in notificationURI attribute with verificationRequest parameter set to TRUE and the IUT received the Notify response containing Response Status Code set to 4101 (SUBSCRIPTION_CREATOR_HAS_NO_PRIVILEGE) } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4101 (SUBSCRIPTION_CREATOR_HAS_NO_PRIVILEGE) and no Content attribute } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/SUB/BV/005 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of the <subscription> resource when the notificationURI is not the originator and the IUT send the Notify request to the notificationURI with verificationRequest parameter set as TRUE |
| Reference | TS-0001 10.2.11.2 & TS-0004 7.3.8.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource-Type set to <subscription> and From set to AE-ID and Content <subscription> resource containing NotificationURI attribute set to NOTI_URI_ADDRESS(not the originator) and the IUTsent the Notify request to the NOTI_URI_ADDRESS in NotificationURI attribute with verificationRequest parameter set to TRUE and the IUT received the Notify response containing Response Status Code set to 5205 (SUBSCRIPTION_HOST_HAS_NO_PRIVILEGE) } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 5205 (SUBSCRIPTION_HOST_HAS_NO_PRIVILEGE) and no Content attribute } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/SUB/BV/006 |
| --- | --- |
| Test objective | Check that the IUT sends Notification request for modification of the subscribed-to resource |
| Reference | TS-0001 10.2.11.2 & TS-0004 7.3.8.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having created a <subscription> resource containing NotificationURI attribute set to NOTI_URI_ADDRESS (AE address) and NotificationContentType attribute set to 1 (All Attributes) and eventType parameter in EventNotificationCriteria attribute set to 1 (Update of Resource) } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT having updated a subscribed-to resource and the IUT sends NOTIFY request message containing To set to NOTI_URI_ADDRESS in notificationURI and From set to CSE-ID and Content the subscribed-to resource } | IUT ( AE |
|  | then { the IUT receives a Response message containing Response Status Code set to 2000 (OK) and no Content attribute } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/SUB/BV/007 |
| --- | --- |
| Test objective | Check that the IUT sends Notification request for creation of a direct child of the subscribed-to resource |
| Reference | TS-0001 10.2.11.2 & TS-0004 7.3.8.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having created a <subscription> resource containing NotificationURI attribute set to NOTI_URI_ADDRESS (AE address) and eventType parameter in EventNotificationCriteria attribute set to 3 (Create of Direct Child Resource) } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT having created a direct child of the subscribed-to resource and the IUT sends NOTIFY request message containing To set to NOTI_URI_ADDRESS in notificationURI and Resource-Type set to RESOURCE_TYPE and From set to CSE-ID and Content a direct child resource of the subscribed-to resource } | IUT ( AE |
|  | then { the IUT receives a Response message containing Response Status Code set to 2000 (OK) and no Content attribute } | IUT ( AE |