| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Missing Single hop ACP verification test |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr khalil.drira@laas.fr thierry.monteil@laas.fr |
| Date:* | 2015-11-07 |
| Abstract:* | The contribution proposes Interoperability test descriptions for missing single hop ACP verification to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes Interoperability test descriptions for missing ACP verification to be added into the TS-0013.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

=================== Start of  1st Part: Proposed Test Descriptions ================

#### Unauthorized operation (Insufficient Access Rights)

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_10 |
| Objective: | AE delete request is rejected after access rights verification using retargeting. |
| Configuration: | M2M_CFG_03 |
| References: | [2] 7.3.1.2 |
| Pre-test conditions: | An <accessControlPolicy> resource with name {ACPName} has been created in remote hosting CSE, not allowing delete operation. AE has created an <AE> resource on registrar CSE with name {AEName} AE has created a <container> sub-resource in the <AE> resource with name {containerName} and having as accessControlPolicy-ID the ID of the remote <accessControlPolicy> . |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Request to delete the <container> resource from the registrar CSE. |
| 2 | Mca | PRO Check Primitive | op = 4 (Delete) to = URI of addressed resource fr = AE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = DELETE Request-Target: URI of addressed resource Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.04 (DELETE) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: URI of addressed resource oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/<AE-ID>/<Registrar CSE-ID>” Payload: op = 4 (Delete) to = URI of addressed resource fr = AE-ID rqi = (token-string) pc = empty |
| 3 |  | IOP Check | Check if possible that a request is sent by the registrar CSE to the Hosting CSE to retrive the corresponding remote <accessControlPolicy> resource. |
| 4 | Mcc | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = URI of addressed resource fr = Registrar CSE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: URI of addressed resource Host: IP address or the FQDN of Hosting CSE X-M2M-RI: (token-string) X-M2M-Origin: Registrar CSE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Hosting CSE Uri-Path: URI of addressed resource oneM2M-FR: Registrar CSE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/<Registrar CSE-ID>/<Hosting CSE-ID>” Payload: op = 2 (Retrieve) to = URI of addressed resource fr = Registrar CSE-ID rqi = (token-string) pc = empty |
| 5 |  | IOP Check | Check if possible that the response is sent by the hosting CSE to the registrar CSE. |
| 6 | Mcc | PRO Check Primitive | Hosting CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of <accessControlPolicy> resource |
|  |  | PRO Check HTTP | Hosting CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <accessControlPolicy> resource |
|  |  | PRO Check CoAP | Hosting CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of <accessControlPolicy> resource |
|  |  | MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/<Registrar CSE-ID>/<Hosting CSE-ID>” Payload: to = Registrar CSE-ID fr = Hosting CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of <accessControlPolicy> resource |
| 7 |  | IOP Check | Check if possible that an access denied error response is sent by registrar CSE to AE |
| 6 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 4103 (ACCESS_DENIED) rqi = (token-string) same as received in request message pc = empty |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 403 (Forbidden) X-M2M-RSC: 4103 X-M2M-RI: (token-string) same as received in request message Message-body: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 4.03 (Forbidden) oneM2M-RSC: 4103 oneM2M-RQI: (token-string) same as received in request message Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>” Payload: to = AE-ID fr = Registrar CSE-ID rsc = <Response Status Code(4103, ACCESS_DENIED> rqi = (token-string) same as received in request message pc = empty |
|  |  | IOP Check | Check if possible that the <container> resource has not been deleted. |
| 7 |  | IOP Check | AE indicates unsuccessful operation (Delete error – no privilege) |

#### ================= End of  1st Part: Proposed Test Descriptions ===============