| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Missing single hop Notify test |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr khalil.drira@laas.fr thierry.monteil@laas.fr |
| Date:* | 2015-11-07 |
| Abstract:* | The contribution proposes Interoperability test descriptions for missing single hop Notify to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes Interoperability test descriptions for missing Notify to be added into the TS-0013.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

=================== Start of  1st Part: Proposed Test Descriptions ================

#### Notification

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_10 |
| Objective: | AE receives a notification request from the remote hosting CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.12 [2] 7.4.1 |
| Pre-test conditions: | A <container> resource has been created on hosting CSE AE has created an <AE> resource on registrar CSE AE has created a <subscription> resource for the <container> resource on the remote hosting CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | A <contentInstance> sub-resource is created on the the <container> resource. This triggers or causes the hostting CSE to send a notification to AE. |
| 2 | Mca | PRO Check Primitive | op = 5 (Notify) to = URI of AE resource from = Hosting CSE-ID rqi = (token-string) pc = Serialized representation of Notification data object |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Request-Target: URI of AE resource Host: IP address or FQDN registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: Hosting CSE-ID Content-Type: application/vnd.onem2m-ntfy+xml; or application/vnd.onem2m-ntfy+json; Message-body: Serialized Representation of Notification data object |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: IP address or FQDN of registrar CSE Uri-Path: URI of AE resource oneM2M-FR: Hosting CSE-ID oneM2M-RQI: (token-string) Content-Format: application/vnd.onem2m-ntfy+xml; or application/vnd.onem2m-ntfy+json; Payload: Serialized Representation of Notification data object |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/<Hosting CSE-ID>/<Registrar-ID>” Payload: op = 5 (Notify) to = URI of AE resource fr = Hosting CSE-ID rqi = (token-string) pc = empty |
| 3 |  | IOP Check | Check if possible that the Notify request is forwarded by the registrar CSE to the AE-ID. |
| 4 | Mcc | PRO Check Primitive | op = 5 (Notify) to = AE from = Hosting CSE-ID rqi = (token-string) pc = Serialized representation of Notification data object |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Request-Target: AE Host: IP address or FQDN registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: Hosting CSE-ID Content-Type: application/vnd.onem2m-ntfy+xml; or application/vnd.onem2m-ntfy+json; Message-body: Serialized Representation of Notification data object |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: IP address or FQDN of registrar CSE Uri-Path: AE oneM2M-FR: Hosting CSE-ID oneM2M-RQI: (token-string) Content-Format: application/vnd.onem2m-ntfy+xml; or application/vnd.onem2m-ntfy+json; Payload: Serialized Representation of Notification data object |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/req/<Registrar CSE-ID>/<AE-ID>” Payload: op = 5 (Notify) to = AE fr = Hosting CSE-ID rqi = (token-string) pc = empty |
| 5 |  | IOP Check | Check if possible that the response is sent by the AE to the registrar CSE. |
| 6 | Mcc | PRO Check Primitive | AE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = empty |
|  |  | PRO Check HTTP | AE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Message-body: empty |
|  |  | PRO Check CoAP | AE sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Payload: empty |
|  |  | MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/<RegistrarCSE-ID>/<AE-ID>” Payload: to = Registrar CSE-ID fr = Hosting CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = empty |
| 7 |  | IOP Check | Check if possible that the response is forwarded by registrar CSE to Hosting CSE |
| 6 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = empty |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Message-body: empty |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: “/oneM2M/resp/<Hosting CSE-ID>/<Registrar CSE-ID>” Payload: to = Registrar CSE-ID fr = Hosting CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = empty |
|  |  | IOP Check | Check if possible that the <container> resource has not been deleted. |
| 7 |  | IOP Check | AE indicates unsuccessful operation (Delete error – no privilege) |

#### ================= End of  1st Part: Proposed Test Descriptions ===============