| Input Contribution |
| --- |
| Meeting ID* | TP-20 |
| Title:* | TS-0018 DMR Test Purposes with Result Content param |
| Source:* | Mahdi Ben Alaya, LAAS-CNRS, ben.alaya@laas.fr Thierry Monteil, LAAS-CNRS, monteil@laas.fr Khalil Drira, drira@laas.fr |
| Uploaded Date:* | 2015-11-08 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | This contribution proposes addional DMG DMR (Data Management and Repository) Test Purposes with Result Content parameter for TS-0018 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes addional DMR (Data Management and Repository) Test Purposes with Result Content parameter for TS-0018

Proposal

================ Start of  1st  Part: Test Purposes ==================

## 7.2	Test Purposes for oneM2M

## 7.2.2	Group DMR

## 7.2.2.1		Data Management and Repository (DMR)

| TP Id | TP/oneM2M/CSE/DMG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT returns successfully an empty content of TARGET_RESOURCE_ADDRESS resource according to Result Content parameter |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 0 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and no Content attribute } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMG/BV/002 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only attributes of TARGET_RESOURCE_ADDRESS resource according to Result Content parameter |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 1 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributes and no hierarchichal address and no child resources and no child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMG/BV/003 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only hierarchichal address of TARGET_RESOURCE_ADDRESS resource according to Result Content parameter |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 2 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing no attributes and hierarchichal address and no child resources and no child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMG/BV/004 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only attributes and hierarchichal address of TARGET_RESOURCE_ADDRESS resource according to Result Content parameter |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 3 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributes and hierarchichal address and no child resources and no child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMG/BV/005 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only attributes and child resources of TARGET_RESOURCE_ADDRESS resource according to Result Content parameter |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 4 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributes and no hierarchichal address and child resources and no child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMG/BV/006 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only attributes and child resource references of TARGET_RESOURCE_ADDRESS resource according to Result Content parameter |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 5 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributes and no hierarchichal address and no child resources and child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMG/BV/007 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only child resource references of TARGET_RESOURCE_ADDRESS resource according to Result Content parameter |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 6 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing no attributes and no hierarchichal address and no child resources and child resource references } | IUT  AE |

================ End of  1st  Part: Test Purposes ==================