| Input Contribution |
| --- |
| Meeting ID* | TST21.2 |
| Title:* | TS-0018-Test Purposes contribution |
| Source:* | Bob Flynn, InterDigital, Bob.Flynn@interdigital.com |
| Uploaded Date:* | 2016-02-22 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution addresses the Create <group> operation.

However, in the requirements annotations, the granularity of the test requirements need to be reduced to capture the conditions and scenarios captured in TS-0001.  Since we have already numbered many test requirement IDs, it is not adviseable to change the numbers.  I propose a solution to address this problem.

Also there are some overlapping concepts with regard to functionality defined for the DMR functionality.  I propose a solution to this ambiguity as well.

To address the first problem, where the granularity needs to be made smaller, in the general case where a new requirement is identified (could be due to additions or changes in the specification) we will need to provide a way to represent this to the rappoteur of the annotation document.

I propose that we use the preceeding requirement Id as the base and simply append a suffix “_n”, when n is a counter of the new requirements inserted, as shown below.

Additionally, if as in this case, the OLD requirement ID should be removed, then we indicate this with a suffix “_obsolete”, as shown below. This would remain in the document so that it is clear the the number was not missed or in some other location.

For the second issue, regarding overlapping functionality, the Group functionality highlighted below and repeated here for clarity overlaps with DMR functionality.

The request shall address <CSEBase>, <remoteCSE> or <AE> resource of a Hosting CSE.

I propose that we include a comment capturing the overlapping functionality, and also list the requirements that the particular caption overlaps with, as shown below.

FROM TS-0001  (our ANNOTATED VERSION)

#### 10.2.7.2	Create <group>

This procedure shall be used for creating a <group> resource.

Table 10.2.7.2-1: <group> CREATE

| <group> CREATE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <CSEBase>, <AE>, or <remoteCSE> where the <group> resource is intended to be Created Content: The representation of the <group> resource for which the attributes are described in clause 9.6.13 |
| Processing at Originator before sending Request | The Originator shall request to Create a <group> resource by using the CREATE operation. The request shall address <CSEBase>, <remoteCSE> or <AE> resource of a Hosting CSE. The Request shall also provide memberIDs and may provide expirationTime attributes. The Originator may be an AE or a CSE |
| Processing at Receiver | For the CREATE procedure, the Receiver shall: Check if the Originator has CREATE permissions on the <CSEBase> resource Check the validity of the provided attributes Validate that there are no duplicate members present in the memberIDs attribute Validate that the resource type of every member on each member Hosting CSE conforms to the memberType attribute in the request, if the memberType attribute of the <group> resource is not 'mixed'. Set the memberTypeValidated attribute to TRUE upon successful validation. Upon successful validation of the provided attributes, create a new group resource including the <fanOutPoint> child-resource in the Hosting CSE Conditionally, in the case that the group resource contains temporarily. unreachable Hosting CSE of sub-group resources as member resource, set the memberTypeValidated attribute of the <group> resource to FALSE Respond to the Originator with the appropriate generic Response with the representation of the <group> resource if the memberTypeValidated attribute is FALSE, and the address of the created <group> resource if the CREATE was successful As soon as any Hosting CSE that hosts the unreachable resource becomes reachable, the memberType validation procedure shall be performed. If the memberType validation fails, the Hosting CSE shall deal with the <group> resource according to the policy defined by the consistencyStrategy attribute of the <group> resource provided in the request. or by default if the attribute is not provided |
| Information in Response message | The representation of the <group> resource if the memberTypeValidated attribute is FALSE |
| Processing at Originator after receiving Response | None |
| Exceptions | No change from the basic procedure in clause 10.1.1 |

##### Create

Primitive specific operation after Recv-C-6.4 "Check validity of resource representation for the given resource type" and before Recv-C-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed ". See clause 7.2.2.2.

- Primitive specific operation: Validate the provided attributes. It shall also check whether the number of URIs present in the memberIDs attribute of the group resource representation does not exceed the maximum as specified by the attribute maxNrOfMembers. If the maximum is exceeded, the request shall be rejected with a Response Status Code indicating "MAX_NUMBER_OF_MEMBER_EXCEEDED" error.
If the memberType attribute of the <group> resource is not "MIXED", the hosting CSE shall also verify that all the member URIs including sub-groups in the attribute memberIDs of the <group> resource representation provided in the request shall conform to the memberType of the group resource.

In the case that the <group> resource contains sub-group member resources, the receiver shall retrieve the memberType of the sub-group member resources to validate the memberType. If the memberType cannot be retrieved due to lack of privilege, the request shall be rejected with a Response Status Code indicating "NO_PRIVILEGE" error. If the sub-group member resources are temporarily unreachable, the receiver shall set the memberTypeValidated attribute of the <group> resource to FALSE and return the result to the originator in the response of the request. As soon as any unreachable sub-group resource becomes reachable, the receiver shall perform the memberType validation procedure. The originator may get to know the validation result by subscribe to the created resource if the memberTypeValidated attribute is FALSE. Upon unsuccessful validation, the receiver shall delete the <group> resource if the consistencyStrategy of the <group> resource is ABANDON_GROUP, or remove the inconsistent members from the <group> resource if the consistencyStrategy attribute is ABANDON_MEMBER, or set the memberType attribute of the <group> resource to "MIXED" if the consistencyStrategy attribute is SET_MIXED.
The memberTypeValidated attribute shall be set to TRUE if all the members have been validated successfully.

Proposal

================ Start of  1st  Part: Test Purposes ==================

## 7.2.2.4		Group Management (GMG)

| TP Id | TP/oneM2M/CSE/GMG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of the <group> resource when duplicate member IDs are present in the memberIDs attribute. |
| Reference | REQ-0001-10030_1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS allowing a child resource type <group> and the AE having privileges to perform CREATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an invalid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to <group> and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS, MEMBER_RESOURCE_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2001 (CREATED) Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS } | IUT ( AE |

TARGET_RESOURCE_ADDRESS : resource type can be <CSEBase>, <AE>, <remoteCSE>

MEMBER_RESOURCE_ADDRESS: Any resource type

| TP Id | TP/oneM2M/CSE/GMG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT validates the resource type during the creation of the <group> resource when memberType attribute is not ‘mixed’. |
| Reference | REQ-0001-10030_2, REQ-0004-07123_4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS allowing a child resource type <group> and the AE having privileges to perform CREATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS having resourceType attribute RESOURCE_TYPE_1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to <group> and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS memberType attribute set to RESOURCE_TYPE_1 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2001 (CREATED) Content set to <group> resource containing memberTypeValidated attribute set to TRUE } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT handles unsuccessful validation of the resource type during the creation of the <group> resource when memberType attribute is not ‘mixed’ and the consistencyStrategy attribute is SET_MIXED. |
| Reference | REQ-0001-10030_2, REQ-0004-07123_3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS allowing a child resource type <group> and the AE having privileges to perform CREATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS having resourceType attribute RESOURCE_TYPE_1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to <group> and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS memberType attribute set to RESOURCE_TYPE_2 consistencyStrategy attribute set to SET_MIXED } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2001 (CREATED) Content set to <group> resource containing memberTypeValidated attribute set to FALSE memberType attribute set to MIXED } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT handles unsuccessful validation of the resource type during the creation of the <group> resource when memberType attribute is not ‘mixed’ and the consistencyStrategy attribute is ABANDON_MEMBER,. |
| Reference | REQ-0001-10030_2, REQ-0004-07123_2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS allowing a child resource type <group> and the AE having privileges to perform CREATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to <group> and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2 memberType attribute set to RESOURCE_TYPE_1 consistencyStrategy attribute set to ABANDON_MEMBER } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2001 (CREATED) Content set to <group> resource containing memberTypeValidated attribute set to TRUE memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1 } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT handles unsuccessful validation of the resource type during the creation of the <group> resource when memberType attribute is not ‘mixed’ and the consistencyStrategy attribute is ABANDON_GROUP. |
| Reference | REQ-0001-10030_2, REQ-0004-07123_1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS allowing a child resource type <group> and the AE having privileges to perform CREATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to <group> and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2 memberType attribute set to RESOURCE_TYPE_1 consistencyStrategy attribute set to ABANDON_GROUP } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2001 (CREATED) } | IUT ( AE |

================ End of  1st  Part: Test Purposes ==================

# Comments

REQ-0001-10030_obsolete

Should we test this as GMG function or DMR function (valid child resource)?

I propose DMR function. BUT the specific test should be run with these for certification perposes.  How do we capture this?

This is tested in DMR, req_ids: x,y,z

REQ-0001-10030_1

REQ-0001-10030_2

REQ-0001-10030_3

REQ-0001-10030_4

REQ-0001-10030_5

REQ-0001-10030_6

REQ-0001-10030_7

REQ-0004-07123

REQ-0004-07123_1

REQ-0004-07123_2

REQ-0004-07123_3

REQ-0004-07123_4

NOTE: TS-0001/0004 do not describe what should happen in this case.

SPEC CR REQUIRED -  IDCC

Resource respresentation of group with duplicate memberIDs removed.

SPEC CR REQUIRED  -  IDCC

NO RESPONSE CODE SPECIFIED.

SPEC CR NEEDED  -  IDCC