| Input Contribution |
| --- |
| Meeting ID* | TST22 |
| Title:* | ICS_AnnounceResources |
| Source:* | Bob Flynn, InterDigital, Bob.Flynn@interdigital.com |
| Uploaded Date:* | 2016-03-04 |
| Document(s) Impacted* | TS-0017 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some additional test cases for single hop configurations |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution introduces resource announcement functionality to TS-0017.

Change 1: Address the Capability Statement

Change 2: Addition to the Resource Type Statement

================ Start of  1st  Change ==================

A.5.2 Capability Statement

A list of capabilities defined in the oneM2M TS [1] are presented in Table A.5.2.1. The capability list can be used to check whether the IUT supports part or whole of the capabilities listed as below.

Table A.5.2. 1 Capabilities for oneM2M Conformance Testing

| Item | Capability | Mnemonic | Reference | Condition | Support |
| --- | --- | --- | --- | --- | --- |
| 1 | Registration |  | [1] 10.2.1 | C.1 | O Yes O No |
| 2 | Data Management |  | [1] 10.2.4, [1] 10.2.19 | C.1 | O Yes O No |
| 3 | Subscription and Notification |  | [1] 10.2.11 | C.2 | O Yes O No |
| 4 | Group Management |  | [1] 10.2.7 | C.2 | O Yes O No |
| 5 | Discovery |  | [1] 10.2.6 | C.2 | O Yes O No |
| 6 | Location Management |  | [1] 10.2.10 | C.2 | O Yes O No |
| 7 | Device Management |  | [1] 10.2.8 | C.2 | O Yes O No |
| 8 | Communication Management and Delivery Handling |  | [1] 10.2.5, [1] 10.2.20 | C.2 | O Yes O No |
| 9 | Resource Announcement |  | [1] 10.2.18 | C.2 | O Yes O No |

C.1: Mandatory IF the IUT is declaimed to be developed conforming to oneM2M TS[1], [2].

C.2: Optional IF the IUT is declaimed to be developed conforming to oneM2M TS[1], [2].

※ Editor’s Note: More capabilities will be added in this section later.

================ End of  1st  Change ==================

================ Start of  2nd  Change ==================

A.5.5 Resource Type Statement

This section presents a list of resource types specified in oneM2M standard. Table A.5.5.1 shown as below can be used to check whether the IUT supports the listed oneM2M resource type(s).

Table A.5.5. 1 oneM2M Resouce Type*

| Item | Resource Type | Reference | Condition | Support |
| --- | --- | --- | --- | --- |
| 1 | accessControlPolicy | [1] 9.6.2 | C.1 | O Yes O No |
| 2 | CSEBase | [1] 9.6.3 | C.1 | O Yes O No |
| 3 | remoteCSE | [1] 9.6.4 | C.1 | O Yes O No |
| 4 | AE | [1] 9.6.5 | C.1 | O Yes O No |
| 5 | container | [1] 9.6.6 | C.1 | O Yes O No |
| 6 | contentInstance | [1] 9.6.7 | C.1 | O Yes O No |
| 7 | subscription | [1] 9.6.8 | C.1 | O Yes O No |
| 8 | schedule | [1] 9.6.9 | C.1 | O Yes O No |
| 9 | locationPolicy | [1] 9.6.10 | C.1 | O Yes O No |
| 10 | delivery | [1] 9.6.11 | C.1 | O Yes O No |
| 11 | request | [1] 9.6.12 | C.1 | O Yes O No |
| 12 | group | [1] 9.6.13 | C.1 | O Yes O No |
| 13 | fanOutPoint | [1] 9.6.14 | C.1 | O Yes O No |
| 14 | mgmtObj | [1] 9.6.15 | C.1 | O Yes O No |
| 15 | mgmtCmd | [1] 9.6.16 | C.1 | O Yes O No |
| 16 | execInstance | [1] 9.6.17 | C.1 | O Yes O No |
| 17 | node | [1] 9.6.18 | C.1 | O Yes O No |
| 18 | m2mServiceSubscriptionProfile | [1] 9.6.19 | C.1 | O Yes O No |
| 19 | serviceSubscribedNode | [1] 9.6.20 | C.1 | O Yes O No |
| 20 | serviceSubscribedAppRule | [1] 9.6.29 | C.1 | O Yes O No |
| 21 | pollingChnnel | [1] 9.6.21 | C.1 | O Yes O No |
| 22 | pollingChannelURI | [1] 9.6.22 | C.1 | O Yes O No |
| 23 | statsConfig | [1] 9.6.23 | C.1 | O Yes O No |
| 24 | eventConfig | [1] 9.6.24 | C.1 | O Yes O No |
| 25 | statsCollect | [1] 9.6.25 | C.1 | O Yes O No |
| 26 | accessControlPolicyAnnc | [1] 9.6.26 | C.1 | O Yes O No |
| 27 | AEAnnc | [1] 9.6.26 | C.1 | O Yes O No |
| 28 | containerAnnc | [1] 9.6.26 | C.1 | O Yes O No |
| 29 | contentInstanceAnnc | [1] 9.6.26 | C.1 | O Yes O No |
| 30 | groupAnnc | [1] 9.6.26 | C.1 | O Yes O No |
| 31 | locationPolicyAnnc | [1] 9.6.26 | C.1 | O Yes O No |
| 32 | mgmtObjAnnc | [1] 9.6.26 | C.1 | O Yes O No |
| 33 | nodeAnnc | [1] 9.6.26 | C.1 | O Yes O No |
| 34 | remoteCSEAnnc | [1] 9.6.26 | C.1 | O Yes O No |
| 35 | scheduleAnnc | [1] 9.6.26 | C.1 | O Yes O No |

C.1: The IUT shall be explicitly declared to one or more than one of the above listed resource types per testing session.

※ Editor’s Note: More resource types will be added in this section later.

### ================ End of  2nd  Change ==================