| Input Contribution |
| --- |
| Meeting ID* | TST22 |
| Title:* | TS-0018-Test Purposes contribution |
| Source:* | Miguel A. Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org Laurent Velez, ETSI, Laurent.Velez@etsi.org |
| Uploaded Date:* | 2016-03-08 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes some changes in the existing TPs and adds permutation tables which complete the generic TPs. It covers group DMR/UPD of the TS-0018 – Test Suite Structure and Test Purposes.

Proposal

================ Start of  1st  Part: Test Purposes ==================

## 7.2	Test Purposes for oneM2M

## 7.2.2	Group CSE

## 7.2.2.1		Data Management and Repository (DMR)

Editor Note: The following TPs contain some test variables (using upper-case and italic) which will be instantiated during test execution and some constants (upper-case).

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/001 |
| --- | --- |
| Test objective | Check that the IUT updates successfully the value of the attribute ATTRIBUTE_NAME of the TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a RW attribute ATTRIBUTE_NAME set to VALUE_1 and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (UPDATED) and (optional) Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_2 } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 | VALUE_2 |
| --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BV/001_01 | TS-0001 10.2.4.3 | 3 (container) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/001_02 | TS-0001 10.2.7.4 | 9 (group) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/001_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/001_04 |  | 18 (schedule) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/001_05 | TS-0001 10.2.13.4 | 15 (pollingChallenge) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/001_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |  |  |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/002 |
| --- | --- |
| Test objective | Check that the IUT adds successfully the attribute ATTRIBUTE_NAME to the TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing no optional RW attribute ATTRIBUTE_NAME and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_1 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (UPDATED) and (optional) Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_1 } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BV/002_01 | TS-0001 10.2.4.3 | 3 (container) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BV/002_02 | TS-0001 10.2.7.4 | 9 (group) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BV/002_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BV/002_04 |  | 18 (schedule) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BV/002_05 | TS-0001 10.2.13.4 | 15 (pollingChallenge) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BV/002_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |  |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/003 |
| --- | --- |
| Test objective | Check that the IUT deletes successfully the attribute ATTRIBUTE_NAME from the TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing an optional RW attribute ATTRIBUTE_NAME and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to NULL } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (UPDATED) and (optional) Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BV/003_01 | TS-0001 10.2.4.3 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_02 | TS-0001 10.2.7.4 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_04 |  | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_05 | TS-0001 10.2.13.4 | 15 (pollingChallenge) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/004 |
| --- | --- |
| Test objective | Check that the IUT updates the value of the attribute ATTRIBUTE_NAME_1, and creates the ATTRIBUTE_NAME_2 and deletes the ATTRIBUTE_NAME_3 of the TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a RW attribute ATTRIBUTE_NAME_1 set to VALUE_1 and no optional RW attribute ATTRIBUTE_NAME_2 and an optional RW attribute ATTRIBUTE_NAME_3 and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME_1 set to VALUE_2 and ATTRIBUTE_NAME_2 set to VALUE_3 and ATTRIBUTE_NAME_3 set to NULL } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (UPDATED) and (optional) Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME_1 set to VALUE_2 and ATTRIBUTE_NAME_2 set to VALUE_3 and ATTRIBUTE_NAME_3 } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME_1 | ATTRIBUTE_NAME_2 | ATTRIBUTE_NAME_3 | VALUE_1 | VALUE_2 | VALUE_3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BV/004_01 | TS-0001 10.2.4.3 | 3 (container) | labels |  |  |  |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/004_02 | TS-0001 10.2.7.4 | 9 (group) | labels |  |  |  |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/004_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |  |  |  |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/004_04 |  | 18 (schedule) | labels |  |  |  |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/004_05 | TS-0001 10.2.13.4 | 15 (pollingChallenge) | labels |  |  |  |  |  |
| TP/oneM2M/CSE/DMR/UPD/BV/004_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |  |  |  |  |  |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BO/005 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to update an attribute of a TARGET_RESOURCE_ADDRESS resource which does not exist |
| Reference | TS-0001 10.1.3 – item 15) |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT not having created a resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_1 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BO/005_01 | TS-0001 10.2.4.3 | 3 (container) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/005_02 | TS-0001 10.2.7.4 | 9 (group) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/005_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/005_04 |  | 18 (schedule) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/005_05 | TS-0001 10.2.13.4 | 15 (pollingChallenge) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/005_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |  |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BO/006 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to update the attribute ATTRIBUTE_NAME of a TARGET_RESOURCE_ADDRESS resource without having privileges for the UPDATE operation |
| Reference | TS-0001 10.1.3 – 16) |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a RW attribute ATTRIBUTE_NAME set to VALUE_1 and the AE not having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_1 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4103 (ACCESS_DENIED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BO/006_01 | TS-0001 10.2.4.3 | 3 (container) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/006_02 | TS-0001 10.2.7.4 | 9 (group) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/006_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/006_04 |  | 18 (schedule) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/006_05 | TS-0001 10.2.13.4 | 15 (pollingChallenge) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/006_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |  |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BO/007 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to update a non-RW attribute ATTRIBUTE_NAME of a TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a non-RW attribute ATTRIBUTE_NAME set to VALUE_1 and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 | VALUE_2 |
| --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BO/007_01 | TS-0001 10.2.4.3 | 3 (container) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BO/007_02 | TS-0001 10.2.7.4 | 9 (group) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BO/007_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BO/007_04 |  | 18 (schedule) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BO/007_05 | TS-0001 10.2.13.4 | 15 (pollingChallenge) | labels |  |  |
| TP/oneM2M/CSE/DMR/UPD/BO/007_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |  |  |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BO/008 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to delete a mandatory RW attribute ATTRIBUTE_NAME of a TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a mandatory RW attribute ATTRIBUTE_NAME set to VALUE_1 and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to NULL } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BO/008_01 | TS-0001 10.2.4.3 | 3 (container) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/008_02 | TS-0001 10.2.7.4 | 9 (group) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/008_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/008_04 |  | 18 (schedule) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/008_05 | TS-0001 10.2.13.4 | 15 (pollingChallenge) | labels |  |
| TP/oneM2M/CSE/DMR/UPD/BO/008_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |  |

| TP Id | TP/oneM2M/CSE/RET/BO/009 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to update a RW attribute ATTRIBUTE_NAME of the TARGET_RESOURCE_ADDRESS resource with an UNACCEPTABLE_VALUE |
| Reference | TS-0001 10.1.3 – item 17) |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a RW attribute ATTRIBUTE_NAME set to VALUE_1 and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to UNACCEPTABLE_VALUE } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4102 (CONTENTS_UNACCEPTABLE) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BO/009_01 | TS-0001 10.2.4.3 | 3 (container) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_02 | TS-0001 10.2.7.4 | 9 (group) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_04 |  | 18 (schedule) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_05 | TS-0001 10.2.13.4 | 15 (pollingChallenge) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |  |

================ End of  1st  Part: Test Purposes ==================