| Input Contribution |
| --- |
| Meeting ID* | TST 22 |
| Title:* | TS-0018 Test Purposes for LOC |
| Source:* | Ting Miao, KETI, novamartin@keti.re.kr Sungchan Choi, KETI, csc@keti.re.kr Minu Ryu, KETI, minu@keti.re.kr Jaeho Kim, KETI, jhkim@keti.re.kr |
| Uploaded Date:* | 2016-03-11 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1. Introduction

This contribution introduces a conformance test purposes for Location CSF. We analyzed the requirements releated to <locationPolicy> resource and relevant resource management procedures stated in TS-0001 and TS-0004, and then annoted each requirement with an identifier so that the annotated requirement identifier can be used as a test purpose reference. Regarding the test purpose, we contributed valid behavioural, inopportune behavioural and invalid behavioural test cases to test the annotated conformance requirements.

============ Start of 1ST Part: Test Purpose Section 7.2==========================

# 7	Test Purposes (TP)

### 7.2	Test Purposes for oneM2M

#### 7.2.2         Group CSE

##### 7.2.2.6        Location (LOC)

Editor Note: all  the uppercased strings using underscore to connect string, e.g. NON_ZERO_VALUE, TARGET_RESOURCE_ADDRESS denote the user-input value.

###### 7.2.2.6.1 Valid Behavioural Test Cases

| TP Id | TP/oneM2M/CSE/LOC/BV/002 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of locationPolicy resource with locationSource attribute and locationUpdatePeriod attribute provided. |
| Reference | TS-0001 10.2.10.1, TS-0004 7.4.11.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource-Type set to <locationPolicy> and From set to AE_ID and Content attribute containing LocationSource set to 1 (Network_based) and LocationUpdatePeriod set to NON_ZERO_VALUE and LocationTargetID set to LOCATION_TARGET_ID and LocationServer set to LOCATION_SERVER_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

###### 7.2.2.6.2 Inopportune Behavioural Test Cases

| TP Id | TP/oneM2M/CSE/LOC/BO/001 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of <locationPolicy> resource when AE has no privilege to perform the creation request for the <locationPolicy> resource |
| Reference | TS-0001 10.2.10.1, TS-0004 7.4.11.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the originator AE and the AE not having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource-Type set to <locationPolicy> and From set to AE_ID and Content attribute containing LocationSource set to 1 (Network_based) and LocationUpdatePeriod set to NON_ZERO_VALUE and LocationTargetID set to LOCATION_TARGET_ID and LocationServer set to LOCATION_SERVER_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4103 (ACCESS_DENIED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/LOC/BO/002 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when receiving a creation request of <locationPolicy> resource target to the TARGET_RESOURCE_ADDRESS which does not exist in the Hosting CSE |
| Reference | TS-0001 10.2.10.1, TS-0004 7.4.11.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the originator AE and the IUT not having created a resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource-Type set to <locationPolicy> and From set to AE_ID and Content attribute containing LocationSource set to 1 (Network_based) and LocationUpdatePeriod set to NON_ZERO_VALUE and LocationTargetID set to LOCATION_TARGET_ID and LocationServer set to LOCATION_SERVER_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

###### 7.2.2.6.3 Invalid Behavioural Test Case

| TP Id | TP/oneM2M/CSE/LOC/BI/001 |
| --- | --- |
| Test objective | Check that the IUT rejects AE to update the <locationPolicy> resource identified with LOCATION_ID when receiving an update request containing an invalid attribute |
| Reference | TS-0001 10.2.10.1.3, TS-0004 7.3.3.4 & 7.4.11.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing an optional RW attribute ATTRIBUTE_NAME and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a UPDATE request with from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Contents attribute containing LocationUpdatePeriod set to INVALID_LOCATION_UPDATE_PERIOD } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

============ End of 1ST Part: Test Purpose Section 7.2==========================