| Input Contribution |
| --- |
| Meeting ID* | TST22.2 |
| Title:* | TS-0018-Test Purposes contribution |
| Source:* | Bob Flynn, Convida Wireless, Flynn.Bob@convidawireless.com |
| Uploaded Date:* | 2016-05-17 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution addresses the Create <group> operation.

FROM TS-0001  V1_13_2

#### 10.2.7.4	Update <group>

This procedure shall be used for updating an existing <group> resource.

Table 10.2.7.4-1: <group> UPDATE

| <group> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <group> resource |
| Processing at Originator before sending Request | The Originator shall request to update attributes of an existing <group> resource by using an UPDATE operation. The Request shall address the specific <group> resource of a CSE. The Originator may be an AE or a CSE |
| Processing at Receiver | The UPDATE procedure shall be: Check if the Originator has UPDATE permissions on the <group> resource. Check the validity of provided attributes Validate that there are no duplicated members present in the memberIDs attribute Validate that the resource type of every member on each member Hosting CSE conforms to the memberType attribute in the request, if the memberType attribute of the <group> resource is not 'mixed'. Set the memberTypeValidated attribute to TRUE upon successful validation Upon successful validation of the provided attributes, update the <group> resource in the Hosting CSE Conditionally, in the case that the <group> resource contains temporarily unreachable Hosting CSE of sub-group resources as members resource set the memberTypeValidated attribute of the <group> resource to FALSE Respond to the Originator with the appropriate generic response with the representation of the <group> resource if the memberTypeValidated attribute is FALSE, and the address of the created <group> resource if the UPDATE is successful As soon as any Hosting CSE that hosts unreachable resource becomes reachable, the memberType validation procedure shall be performed. If the memberType validation fails, the Hosting CSE shall deal with the <group> resource according to the policy defined by the consistencyStrategy attribute of the <group> resource provided in the request, or by default if the attribute is not provided |
| Information in Response message | The representation of the <group> resource if the memberTypeValidated attribute is FALSE |
| Processing at Originator after receiving Response | None |
| Exceptions | No change from the basic procedure in clause 10.1.3 |

FROM TS-0004  V_1_7

##### Update

- Primitive specific operation after Recv-6.4 "Check validity of resource representation for the given resource type" and before Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed ". See clause 7.2.2.2.Primitive specific operation: If the memberType attribute of the <group> resource is not "MIXED", the hosting CSE shall verify that all the member URIs including sub-groups in the attribute memberIDs of the <group> resource representation provided in the request shall conform to the memberType of the <group> resource.

In the case that the <group> resource contains sub-group member resources, the receiver shall retrieve the memberType of the sub-group member resource to validate the memberType. If the memberType cannot be retrieved due to lack of privilege, the request shall be rejected with a Response Status Code indicating "NO_PRIVILEGE" error. If the sub-group member resources are temporarily unreachable, the receiver shall set the memberTypeValidated attribute of the <group> resource to FALSE and return the result to the originator in the response of the request. As soon as any unreachable sub-group resource becomes reachable, the receiver shall perform the memberType validation procedure. The originator may get to know the validation result by subscribe to the created resource if the memberTypeValidated attribute is FALSE. Upon unsuccessful validation, the receiver shall delete the <group> resource if the consistencyStrategy of the <group> resource is ABANDON_GROUP, or remove the inconsistent members from the <group> resource if the consistencyStrategy attribute is ABANDON_MEMBER, or set the memberType attribute of the <group> resource to "MIXED" if the consistencyStrategy attribute is SET_MIXED.
The memberTypeValidated attribute shall be set to TRUE if all the members have been validated successfully.

Primitive specific operation: The hosting CSE shall check whether the number of provided memberIDs in the attribute members exceeds the limitation of maxNrOfMembers. The hosting CSE shall also check whether the value provided in maxNrOfMmembers is lesser than the currentNrOfMembers attribute value. If it exceeds, the hosting CSE shall reject the request with Response Status Code indicating "NOT_ALLOWED". error

REQ-0001-10032_1   TP/oneM2M/CSE/GMG/BV/011

REQ-0001-10032_2  TP/oneM2M/CSE/GMG/BV/012, 013,

REQ-0001-10032_7 TP/oneM2M/CSE/GMG/BV/013

REQ-0004-07xxx_6  TP/oneM2M/CSE/GMG/BV/013,015

REQ-0004-07xxx_7  TP/oneM2M/CSE/GMG/BV/013, 014

REQ-0004-07xxx_8  TP/oneM2M/CSE/GMG/BV/013

REQ-0004-07xxx_9  TP/oneM2M/CSE/GMG/BV/012

REQ-0004-07xxx_10  TP/oneM2M/CSE/GMG/BV/016

REQ-0004-07xxx_11  TP/oneM2M/CSE/GMG/BV/017

================ Start of  1st  Part: Test Purposes ==================

## 7.2.2.4		Group Management (GMG)

| TP Id | TP/oneM2M/CSE/GMG/BV/011 |
| --- | --- |
| Test objective | Check that the IUT detects the presence of duplicate member IDs during an update of the <group> resource and removes the duplicate member IDs prior to updating the <group> resource. |
| Reference | TS-0001 10.2.7.4, TS-0004 7.4.14.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS of type <group> containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1 and the AE having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_2, MEMBER_RESOURCE_ADDRESS_2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2004 (UPDATED) Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_2 } | IUT ( AE |

TARGET_RESOURCE_ADDRESS : resource type can be <CSEBase>, <AE>, <remoteCSE>

MEMBER_RESOURCE_ADDRESS: Any resource type

| TP Id | TP/oneM2M/CSE/GMG/BV/012 |
| --- | --- |
| Test objective | Check that the IUT validates the resource type during an UPDATE of the <group> resource when memberType attribute is not ‘mixed’. |
| Reference | TS-0001 10.2.7.4, TS-0004 7.4.14.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS of type <group> containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1 memberType attribute set to RESOURCE_TYPE_1 and the AE having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2004 (UPDATED) Content set to <group> resource containing memberTypeValidated attribute set to TRUE } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/013 |
| --- | --- |
| Test objective | Check that the IUT handles unsuccessful validation of the resource type during an UPDATE of the <group> resource when memberType attribute is not ‘mixed’ and the consistencyStrategy attribute is SET_MIXED. |
| Reference | TS-0001 10.2.7.4, TS-0004 7.4.14.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS of type <group> containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1 memberType attribute set to RESOURCE_TYPE_1 memberTypeValidated attribute set to TRUE consistencyStrategy attribute set to SET_MIXED and the AE having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2004 (UPDATED) Content set to <group> resource containing memberTypeValidated attribute set to FALSE memberType attribute set to MIXED } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/014 |
| --- | --- |
| Test objective | Check that the IUT handles unsuccessful validation of the resource type during an UPDATE of the <group> resource when memberType attribute is not ‘mixed’ and the consistencyStrategy attribute is ABANDON_MEMBER. |
| Reference | TS-0001 10.2.7.4, TS-0004 7.4.14.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS of type <group> containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1 memberType attribute set to RESOURCE_TYPE_1 memberTypeValidated attribute set to TRUE consistencyStrategy attribute set to ABANDON_MEMBER and the AE having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2 } | IUT ( AE |
|  | then { the IUT sends a valid Response message containing Response Status Code set 2004 (UPDATED) Content set to <group> resource containing memberTypeValidated attribute set to TRUE memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1 } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/015 |
| --- | --- |
| Test objective | Check that the IUT handles unsuccessful validation of the resource type during the creation of the <group> resource when memberType attribute is not ‘mixed’ and the consistencyStrategy attribute is ABANDON_GROUP. |
| Reference | TS-0001 10.2.7.4, TS-0004 7.4.14.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS of type <group> containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1 memberType attribute set to RESOURCE_TYPE_1 memberTypeValidated attribute set to TRUE consistencyStrategy attribute set to # (ABANDON_GROUP) and the AE having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2002 (DELETED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/016 |
| --- | --- |
| Test objective | Check that the IUT detects when the number of memberIDs exceeds the limitation of maxNrOfMembers. |
| Reference | TS-0001 10.2.7.4, TS-0004 7.4.14.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS of type <group> containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2 maxNrOfMembers attribute set to 2 and the AE having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_3 having resourceType attribute RESOURCE_TYPE_1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2, MEMBER_RESOURCE_ADDRESS_3 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/GMG/BV/017 |
| --- | --- |
| Test objective | Check that the IUT detects when the value provided for maxNrOfMembers attribute is less than the value of the currentNrOfMembers attribute. |
| Reference | TS-0001 10.2.7.4, TS-0004 7.4.14.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS of type <group> containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2, MEMBER_RESOURCE_ADDRESS_3 maxNrOfMembers attribute set to 3 and the AE having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_3 having resourceType attribute RESOURCE_TYPE_1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content set to <group> resource containing maxNrOfMembers attribute set to 2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

================ End of  1st  Part: Test Purposes ==================

# Comments

REQ-0001-10032

REQ-0001-10032_1

REQ-0001-10032_2

Should this validation happen on any update, or just memberIDs?

REQ-0001-10032_3

Updated?

REQ-0001-10032_4

REQ-0001-10032_5

REQ-0001-10032_6

REQ-0001-10032_7

REQ-0004-07xxx_1

REQ-0004007xxx_2

REQ-0004007xxx_3

REQ-0004007xxx_4

REQ-0004007xxx_5

REQ-0004007xxx_6

REQ-0004007xxx_7

REQ-0004007xxx_8

REQ-0004007xxx_9

REQ-0004007xxx_10

REQ-0004007xxx_11

REQ-0001-10032_1

REQ-0001-10032_1

REQ-0001-10032_2, REQ-0001-10032_7,  REQ-0004007xxx_8

REQ-0001-10032_2, REQ-0001-10032_7,  REQ-0004007xxx_8

REQ-0001-10032_2, REQ-0001-10032_7,  REQ-0004007xxx_8

REQ-0001-10032_2, REQ-0001-10032_7,  REQ-0004007xxx_8

REQ-0001-10032_1

REQ-0004007xxx_10

REQ-0004007xxx_11

REQ-0001-10032_1

REQ-0001-10032_2, REQ-0004007xxx_9

REQ-0001-10032_2, REQ-0001-10032_7,  REQ-0004007xxx_8

REQ-0004007xxx_7

REQ-0004007xxx_6

REQ-0004007xxx_10

REQ-0004007xxx_11