| Input Contribution |
| --- |
| Meeting ID* | TST23.2 |
| Title:* | TS-0018-Test Purposes contribution |
| Source:* | Miguel A. Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org Laurent Velez, ETSI, Laurent.Velez@etsi.org |
| Uploaded Date:* | 2016-05-03 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes some changes in the existing TPs for the groups DMR/CRE, DMR/RET and DMR/UPD of the TS-0018 – Test Suite Structure and Test Purposes.

Proposal

================ Start of  1st  Part: Test Purposes ==================

## 7.2.2	Group CSE

## 7.2.2.2		Data Management and Repository (DMR)

| TP Id | TP/oneM2M/CSE/DMR/BV/001 |
| --- | --- |
| Test objective | Check that the IUT returns successfully an empty content of TARGET_RESOURCE_ADDRESS resource when the ResultContent set to 0 (Nothing). |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and ResultContent set to 0 (Nothing) } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and no Content attribute } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMR/BV/002 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only attributes of TARGET_RESOURCE_ADDRESS resource when the Result Content ist set to 1 (attributes) |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 1 (attributes) } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing RESOURCE_TYPE resource containing attributes and no hierarchichal address and no child resources and no child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMR/BV/003 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only hierarchichal address of TARGET_RESOURCE_ADDRESS resource when the Result Content is set to 2 (hierarchical address and attributes) |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 2 (hierarchical address and attributes) } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing RESOURCE_TYPE resource containing no attributes and hierarchichal address and no child resources and no child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMR/BV/004 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only attributes and hierarchichal address of TARGET_RESOURCE_ADDRESS resource when Result Content is set 3 (attributes and hierarchichal address) |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 3 (attributes and hierarchichal address) } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing RESOURCE_TYPE resource containing attributes and hierarchichal address and no child resources and no child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMR/BV/005 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only attributes and child resources of TARGET_RESOURCE_ADDRESS resource when the Result Content is set to 4 (attributes and child resources) |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 4 (attributes and child resources) } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing RESOURCE_TYPE resource containing attributes and no hierarchichal address and child resources and no child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMR/BV/006 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only attributes and child resource references of TARGET_RESOURCE_ADDRESS resource when the Result Content is set to 5 (attributes and child resource references) |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 5 (attributes and child resource references) } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing RESOURCE_TYPE resource containing attributes and no hierarchichal address and no child resources and child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMR/BV/007 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only child resource references of TARGET_RESOURCE_ADDRESS resource when Result Content is set to 6 (child resource references) |
| Reference | TS-0001 10.1.3 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 6 (child resource references) } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing RESOURCE_TYPE resource containing no attributes and no hierarchichal address and no child resources and child resource references } | IUT  AE |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/001 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a RESOURCE_TYPE resource with resource name not provided by AE |
| Reference | TS-0001 10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to AE_RESOURCE_ADDRESS and Resource-Type set to RESOURCE_TYPE and From set to AE-ID and Content containing RESOURCE_TYPE resource containing no ResourceName attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) and Content containing RESOURCE_TYPE resource containing ResourceName attribute } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/001_01 | TS-0001 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_02 | TS-0001 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_03 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_05 | TS-0001 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_06 | TS-0001 10.2.11.2 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/002 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a RESOURCE_TYPE resource with a non-existing resource name provided by AE |
| Reference | TS-0001 10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS and the AE containing no child resource containing name attribute set to NAME } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to AE_RESOURCE_ADDRESS and Resource-Type set to RESOURCE_TYPE and From set to AE-ID and Content containing RESOURCE_TYPE resource containing ResourceName attribute set to NAME } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/002_01 | TS-0001 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/002_02 | TS-0001 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/BV/002_03 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/BV/002_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/BV/002_05 | TS-0001 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/BV/002_06 | TS-0001 10.2.11.2 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/003 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of a RESOURCE_TYPE resource with an existing resource name provided by AE |
| Reference | TS-0001 10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS and the AE containing a child resource containing ResourceName attribute set to NAME } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to AE_RESOURCE_ADDRESS and Resource-Type set to RESOURCE_TYPE and From set to AE-ID and Content containing RESOURCE_TYPE resource containing ResourceName attribute set to NAME } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 5106 (ALREADY_EXISTS) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/003_01 | TS-0001 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_02 | TS-0001 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_03 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_05 | TS-0001 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_06 | TS-0001 10.2.11.2 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/004 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of a RESOURCE_TYPE resource when AE has no privileges |
| Reference | TS-0001 10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE not having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to AE_RESOURCE_ADDRESS and Resource-Type set to RESOURCE_TYPE and From set to AE-ID and Content containing RESOURCE_TYPE resource } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4103 (ACCESS_DENIED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/004_01 | TS-0001 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/004_02 | TS-0001 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/BV/004_03 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/BV/004_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/BV/004_05 | TS-0001 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/BV/004_06 | TS-0001 10.2.11.2 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/001 |
| --- | --- |
| Test objective | Check that the IUT returns successfully the TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing the resource TARGET_RESOURCE_ADDRESS } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BV/001_01 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BV/001_02 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BV/001_03 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/001_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BV/001_05 | TS-0001 10.2.13.3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/BV/001_06 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BO/002 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to retrieve the resource TARGET_RESOURCE_ADDRESS which does not exist |
| Reference | TS-0001 10.1.2 - item 13) |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT not having created a resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/RET/BO/003 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to retrieve the resource TARGET_RESOURCE_ADDRESS without having privileges for the RETRIEVE operation |
| Reference | TS-0001 10.1.2 - item 14 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE not having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4103 (ACCESS_DENIED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BO/003_01 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BO/003_02 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BO/003_03 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BO/003_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BO/003_05 | TS-0001 10.2.13.3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/BO/003_06 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/004 |
| --- | --- |
| Test objective | Check that the IUT returns successfully the ATTRIBUTE of TARGET_RESOURCE_ADDRESS resource (“To” option) |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_ATTRIBUTE_ADDRESS and From set to AE_ID and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributeList containing ATTRIBUTE attribute } | IUT ( AE |
| Notes: TARGET_ATTRIBUTE_ADDRESS = TARGET_RESOURCE_ADDRESS # ATTRIBUTE ATTRIBUTE = Common attribute for all RESOURCE_TYPE resources listed in the table below |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BV/004_01 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BV/004_02 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BV/004_03 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/004_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BV/004_05 | TS-0001 10.2.13.3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/BV/004_06 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/005 |
| --- | --- |
| Test objective | Check that the IUT returns successfully the ATTRIBUTE of TARGET_RESOURCE_ADDRESS resource (“Content” option) |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing attributeList containing ATTRIBUTE name } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributeList containing ATTRIBUTE attribute } | IUT ( AE |
| Notes: ATTRIBUTE = Common attribute for all RESOURCE_TYPE resources listed in the table below |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BV/005_01 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BV/005_02 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BV/005_03 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/005_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BV/005_05 | TS-0001 10.2.13.3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/BV/005_06 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/006 |
| --- | --- |
| Test objective | Check that the IUT returns successfully multiple attributes of TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing attributeList containing ATTRIBUTE_1 name and ATTRIBUTE_2 name } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributeList containing ATTRIBUTE_1 attribute and ATTRIBUTE_2 attribute } | IUT ( AE |
| Notes: ATTRIBUTE_1 = Common attribute for all RESOURCE_TYPE resources listed in the table below ATTRIBUTE_2 = Common attribute for all RESOURCE_TYPE resources listed in the table below |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BV/006_01 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BV/006_02 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BV/006_03 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/006_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BV/006_05 | TS-0001 10.2.13.3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/BV/006_06 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BO/007 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to retrieve a non-existing attribute of the TARGET_RESOURCE_ADDRESS resource (“single” attribute case) |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing no attribute ATTRIBUTE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing attributeList containing ATTRIBUTE name } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BO/007_01 | TS-0001 10.2.4.2 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/007_02 | TS-0001 10.2.7.3 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/007_03 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/007_04 |  | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/007_05 | TS-0001 10.2.13.3 | 15 (pollingChallenge) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/007_06 | TS-0001 10.2.11.3 | 23 (subscription) | labels |

Editor Note: A common ATTRIBUTE has been chosen for all types of resource. A note could replace ATTRIBUTE column.

| TP Id | TP/oneM2M/CSE/DMR/RET/BO/008 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to retrieve a non-existing attribute of the TARGET_RESOURCE_ADDRESS resource (“multiple” attributes case) |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing no attribute ATTRIBUTE_1 and no attribute ATTRIBUTE_2 and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing attributeList containing ATTRIBUTE_1 name and ATTRIBUTE_2 name } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_1 | ATTRIBUTE_2 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BO/008_01 | TS-0001 10.2.4.2 | 3 (container) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/008_02 | TS-0001 10.2.7.3 | 9 (group) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/008_03 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/008_04 |  | 18 (schedule) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/008_05 | TS-0001 10.2.13.3 | 15 (pollingChallenge) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/008_06 | TS-0001 10.2.11.3 | 23 (subscription) | labels | announceTo |

Editor Note: The references to the TS-0001 for the operations (CREATE, RETRIEVE) procedures of the resource type <schedule> have not been found. To check whether these procedures are missing or they have been added in newer versions (TS-0001 v1.12.0 as basis)

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/001 |
| --- | --- |
| Test objective | Check that the IUT updates successfully the value of the attribute ATTRIBUTE_NAME of the TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a RW attribute ATTRIBUTE_NAME set to VALUE_1 and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (UPDATED) and (optional) Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_2 } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 | VALUE_2 |
| --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BV/001_01 | TS-0001 10.2.4.3 | 3 (container) | labels | “VALUE_1” | “VALUE_2” |
| TP/oneM2M/CSE/DMR/UPD/BV/001_02 | TS-0001 10.2.7.4 | 9 (group) | labels | “VALUE_1” | “VALUE_2” |
| TP/oneM2M/CSE/DMR/UPD/BV/001_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels | “VALUE_1” | “VALUE_2” |
| TP/oneM2M/CSE/DMR/UPD/BV/001_04 |  | 18 (schedule) | labels | “VALUE_1” | “VALUE_2” |
| TP/oneM2M/CSE/DMR/UPD/BV/001_05 | TS-0001 10.2.13.4 | 15 (pollingChannel) | labels | “VALUE_1” | “VALUE_2” |
| TP/oneM2M/CSE/DMR/UPD/BV/001_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels | “VALUE_1” | “VALUE_2” |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/002 |
| --- | --- |
| Test objective | Check that the IUT adds successfully the attribute ATTRIBUTE_NAME to the TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing no optional RW attribute ATTRIBUTE_NAME and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_1 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (UPDATED) and (optional) Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_1 } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BV/002_01 | TS-0001 10.2.4.3 | 3 (container) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BV/002_02 | TS-0001 10.2.7.4 | 9 (group) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BV/002_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BV/002_04 |  | 18 (schedule) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BV/002_05 | TS-0001 10.2.13.4 | 15 (pollingChannel) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BV/002_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels | “VALUE_1” |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/003 |
| --- | --- |
| Test objective | Check that the IUT deletes successfully the attribute ATTRIBUTE_NAME from the TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing an optional RW attribute ATTRIBUTE_NAME and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to NULL } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (UPDATED) and (optional) Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BV/003_01 | TS-0001 10.2.4.3 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_02 | TS-0001 10.2.7.4 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_04 |  | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_05 | TS-0001 10.2.13.4 | 15 (pollingChannel) | labels |
| TP/oneM2M/CSE/DMR/UPD/BV/003_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/004 |
| --- | --- |
| Test objective | Check that the IUT updates the value of the attribute ATTRIBUTE_NAME_1, and creates the ATTRIBUTE_NAME_2 and deletes the ATTRIBUTE_NAME_3 of the TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a RW attribute ATTRIBUTE_NAME_1 set to VALUE_1 and no optional RW attribute ATTRIBUTE_NAME_2 and an optional RW attribute ATTRIBUTE_NAME_3 and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME_1 set to VALUE_2 and ATTRIBUTE_NAME_2 set to VALUE_3 and ATTRIBUTE_NAME_3 set to NULL } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (UPDATED) and (optional) Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME_1 set to VALUE_2 and ATTRIBUTE_NAME_2 set to VALUE_3 and ATTRIBUTE_NAME_3 } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME_1 | ATTRIBUTE_NAME_2 | ATTRIBUTE_NAME_3 | VALUE_1 | VALUE_2 | VALUE_3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BV/004_01 | TS-0001 10.2.4.3 | 3 (container) | expirationTime | maxNrOfInstances | labels | - | "20001231T012345" | 5 |
| TP/oneM2M/CSE/DMR/UPD/BV/004_02 | TS-0001 10.2.7.4 | 9 (group) | groupName | accessControlPolicyIDs | labels | "VALUE_1" | "VALUE_2" |  |
| TP/oneM2M/CSE/DMR/UPD/BV/004_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | privileges | announceTo | labels | acos: 63 | acos: 61 | PX_URI_CSE |
| TP/oneM2M/CSE/DMR/UPD/BV/004_04 |  | 18 (schedule) | scheduleElement | announceTo | labels | "0,0,0 1 2,1,1,*" | "1,1,1 1 2,1,1,*" | PX_URI_CSE |
| TP/oneM2M/CSE/DMR/UPD/BV/004_05 | TS-0001 10.2.13.4 | 15 (pollingChannel) | - | accessControlPolicyIDs | labels | - | - |  |
| TP/oneM2M/CSE/DMR/UPD/BV/004_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels | accessControlPolicyIDs | expirationCounter | "VALUE_1" | "VALUE_2" |  |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BO/005 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to update an attribute of a TARGET_RESOURCE_ADDRESS resource which does not exist |
| Reference | TS-0001 10.1.3 – item 15) |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT not having created a resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_1 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BO/005_01 | TS-0001 10.2.4.3 | 3 (container) | expirationCounter | 1 |
| TP/oneM2M/CSE/DMR/UPD/BO/005_02 | TS-0001 10.2.7.4 | 9 (group) | expirationCounter | 1 |
| TP/oneM2M/CSE/DMR/UPD/BO/005_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | expirationCounter | 1 |
| TP/oneM2M/CSE/DMR/UPD/BO/005_04 |  | 18 (schedule) | expirationCounter | 1 |
| TP/oneM2M/CSE/DMR/UPD/BO/005_05 | TS-0001 10.2.13.4 | 15 (pollingChannel) | expirationCounter | 1 |
| TP/oneM2M/CSE/DMR/UPD/BO/005_06 | TS-0001 10.2.11.4 | 23 (subscription) | maxNrOfInstances | 5 |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BO/006 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to update the attribute ATTRIBUTE_NAME of a TARGET_RESOURCE_ADDRESS resource without having privileges for the UPDATE operation |
| Reference | TS-0001 10.1.3 – 16) |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a RW attribute ATTRIBUTE_NAME set to VALUE_1 and the AE not having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_1 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4103 (ACCESS_DENIED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BO/006_01 | TS-0001 10.2.4.3 | 3 (container) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BO/006_02 | TS-0001 10.2.7.4 | 9 (group) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BO/006_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BO/006_04 |  | 18 (schedule) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BO/006_05 | TS-0001 10.2.13.4 | 15 (pollingChannel) | labels | “VALUE_1” |
| TP/oneM2M/CSE/DMR/UPD/BO/006_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels | “VALUE_1” |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BO/007 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to update a non-RW attribute ATTRIBUTE_NAME of a TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a non-RW attribute ATTRIBUTE_NAME and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to VALUE_1 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BO/007_01 | TS-0001 10.2.4.3 | 3 (container) | creationTime | "20001231T012345" |
| TP/oneM2M/CSE/DMR/UPD/BO/007_02 | TS-0001 10.2.7.4 | 9 (group) | creationTime | "20001231T012345" |
| TP/oneM2M/CSE/DMR/UPD/BO/007_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | creationTime | "20001231T012345" |
| TP/oneM2M/CSE/DMR/UPD/BO/007_04 |  | 18 (schedule) | creationTime | "20001231T012345" |
| TP/oneM2M/CSE/DMR/UPD/BO/007_05 | TS-0001 10.2.13.4 | 15 (pollingChannel) | creationTime | "20001231T012345" |
| TP/oneM2M/CSE/DMR/UPD/BO/007_06 | TS-0001 10.2.11.4 | 23 (subscription) | creationTime | "20001231T012345" |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BO/008 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to delete a mandatory RW attribute ATTRIBUTE_NAME of a TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a mandatory RW attribute ATTRIBUTE_NAME and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to NULL } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BO/008_01 | TS-0001 10.2.4.3 | 3 (container) | expirationTime |
| TP/oneM2M/CSE/DMR/UPD/BO/008_02 | TS-0001 10.2.7.4 | 9 (group) | expirationTime |
| TP/oneM2M/CSE/DMR/UPD/BO/008_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | expirationTime |
| TP/oneM2M/CSE/DMR/UPD/BO/008_04 |  | 18 (schedule) | expirationTime |
| TP/oneM2M/CSE/DMR/UPD/BO/008_05 | TS-0001 10.2.13.4 | 15 (pollingChannel) | expirationTime |
| TP/oneM2M/CSE/DMR/UPD/BO/008_06 | TS-0001 10.2.11.4 | 23 (subscription) | expirationTime |

| TP Id | TP/oneM2M/CSE/RET/BO/009 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to update a RW attribute ATTRIBUTE_NAME of the TARGET_RESOURCE_ADDRESS resource with an UNACCEPTABLE_VALUE |
| Reference | TS-0001 10.1.3 – item 17) |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a RW attribute ATTRIBUTE_NAME set to VALUE_1 and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing RESOURCE_TYPE resource containing ATTRIBUTE_NAME set to UNACCEPTABLE_VALUE } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4102 (CONTENTS_UNACCEPTABLE) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME | VALUE_1 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BO/009_01 | TS-0001 10.2.4.3 | 3 (container) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_02 | TS-0001 10.2.7.4 | 9 (group) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_03 | TS-0001 10.2.21.3 | 1 (accessControlPolicy) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_04 |  | 18 (schedule) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_05 | TS-0001 10.2.13.4 | 15 (pollingChannel) | labels |  |
| TP/oneM2M/CSE/DMR/RET/BO/009_06 | TS-0001 10.2.11.4 | 23 (subscription) | labels |  |

================ End of  1st  Part: Test Purposes ==================