| CHANGE REQUEST |
| --- |
| Meeting:* | TST 24 |
| Source:* | KETI |
| Date:* | 2016-07-21 |
| Contact:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.kr SeungMyeong Jeong, KETI, sm.jeong@keti.re.kr Sungchan Choi, KETI, csc@keti.re.kr Jaeho Kim, KETI, jhkim@keti.re.kr |
| Reason for Change/s:* | Adding JSON serialization into TR-0025 |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0025 v1.0.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

We propose to add JSON serialization support into TR-0025.

## -----------------------Start of change 1--------------------------------------------

# 8	Implementation

## 8.1 	Introduction

Clasue 8 presents necessary procedures required for the implementation of the remote lights control use case, including assumption conditions met for the correct implementation of the current use case, and resource tree etc.

## 8.2 	Assumptions

Assumptions are presented as below in order to ensure the remote lights control use case could be correctly implemented.

- All the applications are server capable;

- Devices and application entites are independently addressable with host names resolved by DNS network services;

- Host port number 8080 is reserved for oneM2M services;

- Security is not considered in the current use case;

- HTTP binding of oneM2M primitives is used in the current use case;

- Both XML and JSON serialization of oneM2M primitives are used in the current use case;

- All mandatory HTTP headers are presented in the HTTP requests while optional headers are selectively used in the current use case;

- All mandatory resource attributes for resources presented in the current use case are presented in the HTTP requests while optional resource attributes are selectively used in the current use case;

- The IN-CSE and MN-CSE participated in the current use case are deployed within the same oneM2M Service Provider domain;

- All AEs participated in the current use case are initially registered with CSEs and the identifier of the AEs are assigned by the Registrar CSE of the AE accordinlgy, starting with a character of ‘C’;

- All resources created in the current use case could be addressable with the oneM2M Resource Identifier form of Hierarchical address;

- Short names for the representation of the resources and attributes are used in the current use case;

- Default access control policy has already created under IN-CSE and it is used for MN-CSE registration with IN-CSE;

- All request originators send Blocking Requests for accessing resources located in CSEs.

## -----------------------End of change 1---------------------------------------------

## -----------------------Start of change 2--------------------------------------------

## 8.4 	Modelling for Light State Data

The light state ON or OFF stored as the content of content instance resource is modelled as string in XML representation and  can be represented as <con>ON</con> or <con>OFF</con>, while represented as { … “con”:”ON” …} or {… “con”:“OFF” …}, respectively.

## -----------------------End of change 2---------------------------------------------

## -----------------------Start of change 3--------------------------------------------

## 8.7	Implementation Procedures

### 8.7.1 	Introduction

The implementation procedures in the current use case are mapped into HTTP binding and both XML and JSON serialization of oneM2M primitives, respectively, according to the standard APIs describing the references points mca and mcc, as defined in oneM2M TS-0001 [i.2], oneM2M TS-0004 [i.3], the HTTP binding TS-0009 [i.4].

In addition, short name for the representation of the resources and attributes are used in the implementation procedures.

### 8.7.2 	MN-CSE registration

The implementation procedure starts with the registration of MN-CSE with IN-CSE following procedure as below.

If the MN-CSE registration request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/in-cse/server?rcn=0 HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /mn-cse
Content-Type: application/vnd.onem2m-res+xml;ty=16

X-M2M-RI: incse/88643

<?xml version="1.0" encoding="UTF-8"?>

<m2m:csr xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”home_gateway”>

<csi>mn-cse</csi>

<cb>mn.provider.com/mn-cse</cb>

<rr>TRUE</rr>

<poa>http://mn.provider.com:8080</poa>

<cst>2</cst>

<acpi>/in-cse/acp-666957710</acpi>

</m2m:csr>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: incse/88643

Content-Location: /in-cse/csr-299409504

If the MN-CSE registration request body is represented in JSON, the request message looks as following example:

HTTP Request:

POST /~/in-cse/server?rcn=0 HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /mn-cse
Content-Type: application/vnd.onem2m-res+json;ty=16

X-M2M-RI: incse/88643

{

"m2m:csr":

{

“rn”: “home_gateway”,

“csi”: “mn-cse”,

“cb”: “mn.provider.com/mn-cse”,

“rr”: TRUE,

“poa”: [“http://mn.provider.com:8080”],

“cst”: 2,

“acpi”: “/in-cse/acp-666957710”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: incse/88643

Content-Location: /in-cse/csr-299409504

### 8.7.3 	Access control policy creation

When user creates the access control policy resource, user has to clearly specify the name of accessControlOriginator in acor field and the granted operations for the access control originator in the acop field.

The value of acop is set to 63 which indicates that the specified originator is granted to conduct CREATE, RETRIEVE, UPDATE, DELETE, DISCOVERY,and NOTIFY operations.

The creation of access control policy resource acp1 in MN-CSE could be implemented following procedure as below.

If the access control policy create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae
Content-Type: application/vnd.onem2m-res+xml;ty=1

X-M2M-RI: mncse/62948

<m2m:acp xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”gateway_acp”>

<pv>

<acr>

<acor>/in-cse/home_gateway /mn-cse/Cgateway_ae /mn-cse/Clight_ae1 /mn-cse/Clight_ae2 /in-cse/Csmartphone_ae</acor>

<acop>63</acop>

</acr>

</pv>

<pvs>

<acr>

<acor>/in-cse/home_gateway /mn-cse/Cgateway_ae /mn-cse/Clight_ae1 /mn-cse/Clight_ae2 /in-cse/Csmartphone_ae</acor>

<acop>51</acop>

</acr>

</pvs>

</m2m:acp>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/62948

Content-Location: /mn-cse/acp-805496226

If the access control policy create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae
Content-Type: application/vnd.onem2m-res+json;ty=1

X-M2M-RI: mncse/62948

{

"m2m:acp":

{

“rn”: “gateway_acp”,

“pv”:

{

“acr”:[{

“acor”:

[

“/in-cse/home_gateway”,

“/mn-cse/Cgateway_ae”,

“/mn-cse/Clight_ae1”,

“/mn-cse/Clight_ae2”,

“/in-cse/Csmartphone_ae”

],

“acop”:63

}]

},

“pvs”:

{

“acr”:[{

“acor”:

[

“/in-cse/home_gateway”,

“/mn-cse/Cgateway_ae”,

“/mn-cse/Clight_ae1”,

“/mn-cse/Clight_ae2”,

“/in-cse/Csmartphone_ae”

],

“acop”:51

}]

}

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/62948

Content-Location: /mn-cse/acp-805496226

The access control policy resource can be used to grant those applications that are registered with MN-CSE the access rights to conduct specific operations and access to specific resources. The list of applications could be obtained with a discovery procedure using filter criteria conditions. For more details about the discovery procedure, please go to clause  8.7.9. Here it is required that the list of applications registered with MN-CSE before creating the access control policy resource has already been discovered.

### 8.7.4 	Application entities registration

#### 8.7.4.1	Light application ADN-AE1

The registration of ADN-AE1 with MN-CSE could be implemented following procedure as below. Note that the access control policy Identifier (unstructured CSE-relative resourceID) which is assigned to ADN-AE1 is /mn-cse/acp-805496226.

If the ADN-AE registration request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /C
Content-Type: application/vnd.onem2m-res+xml;ty=2

X-M2M-RI: mncse/92345

<?xml version="1.0" encoding="UTF-8"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”light_ae1”>

<api>A01.com.company.lightApp1</api>

<rr>TRUE</rr>

<poa>http://192.168.0.10:9090</poa>

<acpi>/mn-cse/acp-805496226</acpi>

</m2m:ae>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/92345

Content-Location: /mn-cse/ae-CAE340304071

If the ADN-AE registration request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /C
Content-Type: application/vnd.onem2m-res+json;ty=2

X-M2M-RI: mncse/92345

{

"m2m:ae":

{

“rn”: “light_ae1”,

“api”: “A01.com.company.lightApp1”,

“rr”: TRUE,

“poa”: [“http://192.168.0.10:9090”],

“acpi”: “/mn-cse/acp-805496226”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/92345

Content-Location: /mn-cse/ae-CAE340304071

#### 8.7.4.2	Light application ADN-AE2

The registration of ADN-AE2 with MN-CSE could be implemented following procedure as below. Note that the access control policy Identifier (unstructured CSE-relative resourceID) which is assigned to ADN-AE2 is /mn-cse/acp-805496226.

If the ADN-AE registration request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /C
Content-Type: application/vnd.onem2m-res+xml;ty=2

X-M2M-RI: mncse/18346

<?xml version="1.0" encoding="UTF-8"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”light_ae2”>

<api>A01.com.company.lightApp2</api>

<rr>TRUE</rr>

<poa>http://192.168.0.20:9090</poa>

<acpi>/mn-cse/acp-805496226</acpi>

</m2m:ae>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/18346

Content-Location: /mn-cse/ae-CAE340304042

If the ADN-AE registration request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /C
Content-Type: application/vnd.onem2m-res+json;ty=2

X-M2M-RI: mncse/18346

{

"m2m:ae":

{

“rn”: “light_ae2”,

“api”: “A01.com.company.lightApp2”,

“rr”: TRUE,

“poa”: [“http://192.168.0.20:9090”],

“acpi”: “/mn-cse/acp-805496226”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/18346

Content-Location: /mn-cse/ae-CAE340304042

#### 8.7.4.3	Home gateway application MN-AE

The registration of MN-AE with MN-CSE could be implemented following procedure as below. Note that the access control policy Identifier (unstructured CSE-relative resourceID) which is assigned to MN-AE is /mn-cse/acp-805496226.

If the MN-AE registration request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /C
Content-Type: application/vnd.onem2m-res+xml;ty=2

X-M2M-RI: mncse/19347

<?xml version="1.0" encoding="UTF-8"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”gateway_ae”>

<api>A01.com.company.gatewayApp</api>

<rr>FALSE</rr>

<acpi>/mn-cse/acp-805496226</acpi>

</m2m:ae>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/19347

Content-Location: /mn-cse/ae-CAE340303271

If the MN-AE registration request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /C
Content-Type: application/vnd.onem2m-res+json;ty=2

X-M2M-RI: mncse/19347

{

"m2m:ae":

{

“rn”: “gateway_ae”,

“api”: “A01.com.company.gatewayApp”,

“rr”: FALSE,

“acpi”: “/mn-cse/acp-805496226”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/19347

Content-Location: /mn-cse/ae-CAE340303271

#### 8.7.4.4	Smartphone application IN-AE

The registration of IN-AE with IN-CSE could be implemented following procedure as below. Note that the access control policy Identifier (unstructured CSE-relative resourceID) which is assigned to IN-AE is /in-cse/acp-666957710.

If the IN-AE registration request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/in-cse/server?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /C
Content-Type: application/vnd.onem2m-res+xml;ty=2

X-M2M-RI: incse/16346

<?xml version="1.0" encoding="UTF-8"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”smartphone_ae”>

<api>A01.com.company.lightControlApp</api>

<rr>FALSE</rr>

<acpi>/in-cse/acp-666957710</acpi>

</m2m:ae>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: incse/16346

Content-Location: /in-cse/ae-CAE340304178

If the IN-AE registration request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/in-cse/server?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /C
Content-Type: application/vnd.onem2m-res+json;ty=2

X-M2M-RI: incse/16346

{

"m2m:ae":

{

“rn”: “smartphone_ae”,

“api”: “A01.com.company.lightControlApp”,

“rr”: FALSE,

“acpi”: “/mn-cse/acp-666957710”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: incse/16346

Content-Location: /in-cse/ae-CAE340304178

### 8.7.5 	Containers creation

#### 8.7.5.1	Create a container of ADN-AE1

The creation of container resource for ADN-AE1 could be implemented following procedure as below.

If the container create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae1
Content-Type: application/vnd.onem2m-res+xml;ty=3

X-M2M-RI: mncse/13345

<m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”light”>

</m2m:cnt>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/13345

Content-Location: /mn-cse/cnt-582759912

If the container create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae1
Content-Type: application/vnd.onem2m-res+json;ty=3

X-M2M-RI: mncse/13345

{

"m2m:cnt":

{

“rn”: “light”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/13345

Content-Location: /mn-cse/cnt-582759912

#### 8.7.5.2 	Create a container of ADN-AE2

The creation of container resource for ADN-AE2 could be implemented following procedure as below.

If the container create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae2
Content-Type: application/vnd.onem2m-res+xml;ty=3

X-M2M-RI: mncse/62345

<m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”light”>

</m2m:cnt>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/62345

Content-Location: /mn-cse/cnt-582769893

If the container create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae2
Content-Type: application/vnd.onem2m-res+json;ty=3

X-M2M-RI: mncse/62345

{

"m2m:cnt":

{

“rn”: “light”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/62345

Content-Location: /mn-cse/cnt-582769893

### 8.7.6 	ContentInstances creation

#### 8.7.6.1	Create a content instance of ADN-AE1

The creation of content instance resource under container of ADN-AE1 with initial content OFF could be implemented following procedure as below.

If the contentInstance create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae1
Content-Type: application/vnd.onem2m-res+xml;ty=4

X-M2M-RI: mncse/24345

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<con>OFF</con>

<cnf>text/plain:0</cnf>

</m2m:cin>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/24345

Content-Location: /mn-cse/cin-394798749

Content-Type: application/vnd.onem2m-res+xml

If the contentInstance create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae1
Content-Type: application/vnd.onem2m-res+json;ty=4

X-M2M-RI: mncse/24345

{

"m2m:cin":

{

“con”: “OFF”,

“cnf”: “text/plains:0”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/24345

Content-Location: /mn-cse/cin-394798749

Content-Type: application/vnd.onem2m-res+json

#### 8.7.6.2	Create a content instance of ADN-AE2

The creation of content instance resource under container of ADN-AE2 with initial content OFF could be implemented following procedure as below.

If the contentInstance create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae1
Content-Type: application/vnd.onem2m-res+xml;ty=4

X-M2M-RI: mncse/22345

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<con>OFF</con>

<cnf>text/plain:0</cnf>

</m2m:cin>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/22345

Content-Location: /mn-cse/cin-256599578

If the contentInstance create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae1
Content-Type: application/vnd.onem2m-res+json;ty=4

X-M2M-RI: mncse/22345

{

"m2m:cin":

{

“con”: “OFF”,

“cnf”: “text/plains:0”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/22345

Content-Location: /mn-cse/cin-256599578

### 8.7.7 	Groups creation

#### 8.7.7.1	Create a group for updating all light states

The creation of group resource group1 in MN-AE could be implemented following procedure as below. The group resource is created with two initial member id 0 and 1.

If the group create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/gateway_ae?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae
Content-Type: application/vnd.onem2m-res+xml;ty=9

X-M2M-RI: mncse/76905

<?xml version="1.0" encoding="UTF-8"?>

<m2m:grp xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”containers_grp”>

<mt>3</mt>

<mid>/mn-cse/cnt-582759912 /mn-cse/cnt-582769893</mid>

<mnm>10</mnm>

</m2m:grp>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/76905

Content-Location: /mn-cse/grp-977978327

If the group create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/gateway_ae?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae
Content-Type: application/vnd.onem2m-res+json;ty=9

X-M2M-RI: mncse/76905

{

“m2m:grp”:

{

“rn”:”containers_grp”,

“mt”: 3,

“mid”:[“/mn-cse/cnt-582759912”, “/mn-cse/cnt-582769893”],

“mnm”: 10

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/76905

Content-Location: /mn-cse/grp-977978327

#### 8.7.7.2	Create a group for retrieval of all latest light states

The creation of group resource group2 in MN-AE could be implemented following procedure as below. The group resource is created with two initial member id 0 and 1.

If the group create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/gateway_ae?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae
Content-Type: application/vnd.onem2m-res+xml;ty=9

X-M2M-RI: mncse/12980

<?xml version="1.0" encoding="UTF-8"?>

<m2m:grp xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”lightstates_grp”>

<mt>4</mt>

<mid>/mn-cse/cnt-582759912/la /mn-cse/cnt-582769893/la</mid>

<mnm>10</mnm>

</m2m:grp>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/12980

Content-Location: /mn-cse/grp-677974227

If the group create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/gateway_ae?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae
Content-Type: application/vnd.onem2m-res+json;ty=9

X-M2M-RI: mncse/12980

{

“m2m:grp”:

{

“rn”:”lightstates_grp”,

“mt”: 4,

“mid”:[“/mn-cse/cnt-582759912/latest”, “/mn-cse/cnt-582769893/latest”],

“mnm”:10

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/12980

Content-Location: /mn-cse/grp-677974227

### 8.7.8 	Subscriptions creation

#### 8.7.8.1	Subscription to the content instance of ADN-AE1

When user creates a subscription resource, parameter notification content type (short for nct) is set to value 1 to indicate that all attributes of the subscribed resource will be notified to the subscriber.

ADN-AE1 creates a subscription resource including the notification URI set to the resource identifier of ADN-AE1 so that the ADN-AE1 could get notified whenever there are changes to the content instance of container in ADN-AE1 following procedures as below.

If the subscription create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae1
Content-Type: application/vnd.onem2m-res+xml;ty=23

X-M2M-RI: mncse/67891

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sub xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”lightstate_sub1”>

<enc>

<net>3</net>

</enc>

<nu>/mn-cse/ae-CAE340304071</nu>

<nct>1</nct>

</m2m:sub>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/67891

Content-Location: /mn-cse/sub-856593979

If the subscription create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae1
Content-Type: application/vnd.onem2m-res+json;ty=23

X-M2M-RI: mncse/67891

{

“m2m:sub”:

{

“rn”:”lightstate_sub1”,

“enc”:

{

“net”:[3]

},

“nu”:[“/mn-cse/ae-CAE340304071”],

“nct”:1

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/67891

Content-Location: /mn-cse/sub-856593979

#### 8.7.8.2	Subscription to the content instance of ADN-AE2

When user creates a subscription resource, parameter notification content type (short for nct) is set to value 1 to indicate that all attributes of the subscribed resource will be notified to the subscriber.

ADN-AE2 creates a subscription resource including the notification URI set to the resource identifier of ADN-AE2 so that the ADN-AE2 could get notified whenever there are changes to the content instance of container in ADN-AE2 following procedures as below.

If the subscription create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae2
Content-Type: application/vnd.onem2m-res+xml;ty=23

X-M2M-RI: mncse/29387

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sub xmlns:m2m="http://www.onem2m.org/xml/protocols" rn=”lightstate_sub2”>

<enc>

<net>3</net>

</enc>

<nu>/mn-cse/ae-CAE340304042</nu>

<nct>1</nct>

</m2m:sub>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/29387

Content-Location: /mn-cse/sub-856463728

If the subscription create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /mn-cse/Clight_ae2
Content-Type: application/vnd.onem2m-res+json;ty=23

X-M2M-RI: mncse/29387

{

“m2m:sub”:

{

“rn”:”lightstate_sub2”,

“enc”:

{

“net”:[3]

},

“nu”:[“/mn-cse/ae-CAE340304042”],

“nct”:1

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/29387

Content-Location: /mn-cse/sub-856463728

### 8.7.9 	Discovery

#### 8.7.9.1	Introduction

The discovery functionality in oneM2M service platform could be implemented using RETRIEVE operation along with one or multiple filter criteria parameters.

In order to enable the retrieve operation for resource discovery, parameter filterUsage (short for fu)  has to be presented in the RETRIEVE request as a query string.

In addition, parameter resource type (short for rty) could be used as filterCriteria condition for the discovery of single light and group light members. The parameter discovery result type (short for drt) is set to 2 to indicate that the format of elements of URIList is unstructured. The detailed discovery procedures are presented in clauses 8.7.9.2 and 8.7.9.3.

#### 8.7.9.2	Discovery of single light registered with MN-CSE

The discovery of single light registered with MN-CSE could be implemented by in-ae following procedures as below.

If the discovery response is preferred to be returned in representation of JSON, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway?fu=1&rty=3&drt=2 HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/99882
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/99882

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:uril xmlns:m2m="http://www.onem2m.org/xml/protocols">

/cnt-582759912

/cnt-582769893

</m2m:uril>

If the discovery response is preferred to be returned in representation of JSON, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway?fu=1&rty=3&drt=2 HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/99882
Accept: application/json

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/99882

Content-Type: application/json

{

"m2m:uril":

[

"/cnt-582759912",

"/cnt-582769893"

]

}

User using smartphone application can retrieve a list of URIs representing containers registered with MN-CSE from the response message, e.g. /cnt-582759912 which is the URI of container created in ADN-AE1. The retrieved URIs of the discovered containers could be used for the group member update operations.

#### 8.7.9.3	Discovery of groups located in MN-CSE

The discovery of groups located in MN-CSE could be implemented by in-ae following procedures as below.

If the discovery response is preferred to be returned in representation of XML, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway?fu=1&rty=9&drt=2 HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/15001
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/15001

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:uril xmlns:m2m="http://www.onem2m.org/xml/protocols">

/mn-cse/grp-977978327

/mn-cse/grp-677974227

</m2m:uril>

If the discovery response is preferred to be returned in representation of JSON, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway?fu=1&rty=9&drt=2 HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/15001
Accept: application/json

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/15001

Content-Type: application/json

{

"m2m:uril":

[

"/grp-977978327",

"/grp-677974227"

]

}

User using smartphone application can retrieve a list of URIs representing group resources located in MN-CSE from the response message, e.g. /mn-cse/grp-977978327 which is the URI of group group1. The retrieved URIs of the discovered group resource could also be used for the group member update operations.

### 8.7.10 	Latest content instances retrieval

#### 8.7.10.1	Introduction

User could retrieve the latest light states via sending a latest content instance RETRIEVE request attached with a virtual resource latest (short for la).

User could also retrieve a group of latest light states via sending a group RETRIEVE request attached with a virtual resource fanOutPoint (short for fopt).

#### 8.7.10.2	Retrieve the latest content instance of ADN-AE1

The latest content instance of container light in ADN-AE1 could be retrieved following procedures as below.

If the response is preferred to be returned in representation of XML, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae1/light/la HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/11223
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/11223

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cin

xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="cin-394798749">

<ty>4</ty>

<ri>cin-394798749</ri>

<pi>cnt-181049109</pi>

<ct>20150925T045938</ct>

<lt>20150925T045938</lt>

<et>20151107T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>3</cs>

<con>OFF</con>

</m2m:cin>

If the response is preferred to be returned in representation of JSON, the HTTP request message is sent as following example:

GET /~/mn-cse/home_gateway/light_ae1/light/latest HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/11223
Accept: application/json

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/11223

Content-Type: application/json

{

“m2m:cin”:

{

“ty”:4,

“ri”:”cin-394798749”,

”pi”:”cnt-181049109”,

“rn”:”cin-394798749”,

”ct”:”20150925T045938”,

”lt”:”20150925T045938”,

”et”:”20151107T154802”,

”st”:0,

”cnf”:”text/plain:0”,

”cs”:3,

“con”:”OFF”

}

}

#### 8.7.10.3	Retrieve the latest content instance of ADN-AE2

The latest content instance of container light in ADN-AE2 could be retrieved following procedures as below.

If the response is preferred to be represented in XML, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae2/light/la HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/22336
Accept: application/xml

HTTP Response:

200 OK
X-M2M-RSC: 2000

X-M2M-RI: mncse/22336

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cin

xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="cin-256599578">

<ty>4</ty>

<ri>cin-256599578</ri>

<pi>cnt-790965889</pi>

<ct>20150925T050515</ct>

<lt>20150925T050515</lt>

<et>20151107T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>3</cs>

<con>OFF</con>

</m2m:cin>

If the response is preferred be returned in representation of JSON, the HTTP request message is sent as following example:

GET /~/mn-HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/22336
Accept: application/json

HTTP Response:

200 OK
X-M2M-RSC: 2000

X-M2M-RI: mncse/22336

Content-Type: application/json

{

“m2m:cin”:

{

“ty”:4,

“ri”:”cin-256599578”,

“pi”:”cnt-790965889”,

“rn”:”cin-256599578”,

“ct”:”20150925T050515”,

“lt”:”20150925T050515”,

“et”:”20151107T154802”,

“st”:0,

“cnf”:”text/plain:0”,

“cs”:3,

“con”:”OFF”

}

}

#### 8.7.10.4	Retrieve a group of latest content instances for all light states

A group of latest content instances could be achieved via sending a group RETRIEVE request following procedures as below.

If the response is preferred to be returned in representation of XML, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway/gateway_ae/lightstates_grp/fopt HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/55667
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/55667

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:agr

xmlns:m2m="http://www.onem2m.org/xml/protocols">

<m2m:rsp>

<rsc>2000</rsc>

<rqi>ae/55667</rqi>

<pc>

<m2m:cin rn="cin-394798749">

<ty>4</ty>

<ri>cin-394798749</ri>

<pi>cnt-181049109</pi>

<ct>20150925T045938</ct>

<lt>20150925T045938</lt>

<et>20151107T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>3</cs>

<con>OFF</con>

</m2m:cin>

</pc>

<to>/in-cse/ae-CAE340304178</to>

<fr>/mn-cse/cnt-582759912/la</fr>

</m2m:rsp>

<m2m:rsp>

<rsc>2000</rsc>

<rqi>ae/55667</rqi>

<pc>

<m2m:cin rn="cin-256599578">

<ty>4</ty>

<ri>cin-256599578</ri>

<pi>cnt-790965889</pi>

<ct>20150925T050515</ct>

<lt>20150925T050515</lt>

<et>20151107T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>3</cs>

<con>OFF</con>

</m2m:cin>

</pc>

<to>/in-cse/ae-CAE340304178</to>

<fr>/mn-cse/cnt-582769893/la</fr>

</m2m:rsp>

</m2m:agr>

If the response is preferred to be returned in representation of JSON, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway/HTTP/1.1
Host: http://in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse/55667
Accept: application/json

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/55667

Content-Type: application/json

{

“m2m:agr”:

{[

“m2m:rsp”:

{

“rsc”:”2000”,

“rqi”:”ae/55667”,

“pc”:

{

“m2m:cin”:

{

“ty”:4,

“ri”:”cin-394798749”,

“pi”:”cnt-181049109”,

“rn”:”cin-394798749”,

“ct”:”20150925T045938”,

“lt”:”20150925T045938”,

“et”:”20151107T154802”,

“st”:0,

“cnf”:”text/plain:0”,

“cs”:3,

“con”:”OFF”

}

},

“to”:”/in-cse/ae-CAE340304178”,

“from”:”/mn-cse/cnt-582759912/latest”

},

“m2m:rsp”:

{

“rsc”:”2000”,

“rqi”:”ae/55667”,

“pc”:

{

“m2m:cin”:

{

“ty”:4,

“ri”:”cin-256599578”,

“pi”:”cnt-790965889”,

“rn”:”cin-256599578”,

“ct”:”20150925T050515”,

“lt”:”20150925T050515”,

“et”:”20151107T154802”,

“st”:0,

“cnf”:”text/plain:0”,

“cs”:3,

“con”:”OFF”

}

},

“to”:”/in-cse/ae-CAE340304178”,

“from”:”/mn-cse/cnt-582769893/latest”

}

]}

}

### 8.7.11 	Light state modification

#### 8.7.11.1	Introduction

Once the smartphone application in-ae is registered with IN-CSE, the in-ae could be granted for accessing resources including containers located in IN-CSE so that smartphone application users could send light control commands for modifying the light states.

When smartphone application user makes a change on the light state via the smartphone user interface, the in-ae performs a new content instance creation procedure carrying the new state.

The modification of single light state could be implemented by creating a new content instance resource for the specific container with access control policy acp1 (gateway_acp) while the modification of all light states could be implemented by creating a new content instance resource for each member of group (lightstates_grp) with access control policy acp1 (gateway_acp). The implementation of the latter case is to create a <fanOutPoint> resource with the content of new content instance resource for the group1 lightstates_grp so that the content of all members of the group1 could be updated together.

#### 8.7.11.2	Create a content instance under container of ADN-AE1

If the contentInstance create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/vnd.onem2m-res+xml;ty=4

X-M2M-RI: mncse/11123

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<con>ON</con>

<cnf>text/plain:0</cnf>

</m2m:cin>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/11123

Content-Location: /mn-cse/cin-789356234

If the contentInstance create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/vnd.onem2m-res+json;ty=4

X-M2M-RI: mncse/11123

{

"m2m:cin":

{

“con”: “ON”,

“cnf”: “text/plains:0”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/11123

Content-Location: /mn-cse/cin-789356234

#### 8.7.11.3	Create a content instance under container of ADN-AE2

If the contentInstance create request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/vnd.onem2m-res+xml;ty=4

X-M2M-RI: mncse/12222

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<con>ON</con>

<cnf>text/plain:0</cnf>

</m2m:cin>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/12222

Content-Location: /mn-cse/cin-237896783

If the contentInstance create request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/vnd.onem2m-res+json;ty=4

X-M2M-RI: mncse/12222

{

"m2m:cin":

{

“con”: “ON”,

“cnf”: “text/plains:0”

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/12222

Content-Location: /mn-cse/cin-237896783

#### 8.7.11.4	Update  the state of all lights using group fanout

If the fanOutPoint request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_gateway/gateway_ae/lightstates_grp/fopt HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/vnd.onem2m-res+xml

X-M2M-RI: mncse/33344

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<con>ON</con>

<cnf>text/plain:0</cnf>

</m2m:cin>

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/33344

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:agr

xmlns:m2m="http://www.onem2m.org/xml/protocols">

<m2m:rsp>

<rsc>2001</rsc>

<rqi>ae/33344</rqi>

<pc>

<m2m:cin rn="cin-479874939">

<ty>4</ty>

<ri>cin-479874939</ri>

<pi>cnt-181049109</pi>

<ct>20151025T045938</ct>

<lt>20151025T045938</lt>

<et>20151207T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>2</cs>

<con>ON</con>

</m2m:cin>

</pc>

<to>/in-cse/ae-CAE340304178</to>

<fr>/mn-cse/cnt-582759912</fr>

</m2m:rsp>

<m2m:rsp>

<rsc>2001</rsc>

<rqi>ae/33344</rqi>

<pc>

<m2m:cin rn="cin-659957825">

<ty>4</ty>

<ri>cin-659957825</ri>

<pi>cnt-790965889</pi>

<ct>20151025T045938</ct>

<lt>20151025T045938</lt>

<et>20151207T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>2</cs>

<con>ON</con>

</m2m:cin>

</pc>

<to>/in-cse/ae-CAE340304178</to>

<fr>/mn-cse/cnt-582769893</fr>

</m2m:rsp>

</m2m:agr>

If the fanOutPoint request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /~/mn-cse/home_HTTP/1.1
Host: http://mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/vnd.onem2m-res+json

X-M2M-RI: mncse/33344

{

"m2m:cin":

{

“con”: “ON”,

“cnf”: “text/plains:0”

}

}

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse/33344

Content-Type: application/json

{

“m2m:agr”:

{[

“m2m:rsp”:

{

“rsc”: “2001”,

“rqi”:“ae/33344”,

“pc”:

{

“m2m:cin”:

{

“ty”: 4,

“ri”: “cin-479874939”,

“pi”: “cnt-181049109”,

“rn”: “cin-479874939”,

“ct”: “20151025T045938”,

“lt”: “20151025T045938”,

“et”: “20151207T154802”,

“st”: 0,

“cnf”: “text/plain:0”,

“cs”: 2,

“con”: “ON”

}

},

“to”: “/in-cse/ae-CAE340304178”,

“from”: “/mn-cse/cnt-582759912”

},

“m2m:rsp”:

{

“rsc”: 2001,

“rqi”: “ae/33344”,

“pc”:

{

“m2m:cin”:

{

“ty”: 4,

“ri”: “cin-659957825”,

“pi”: “cnt-790965889”,

“rn”: “cin-659957825”,

“ct”: “20151025T050515”,

“lt”: “20151025T050515”,

“et”: “20151207T154802”,

“st”: 0,

“cnf”: “text/plain:0”,

“cs”: 2,

“con”: “ON”

}

},

“to”: “/in-cse/ae-CAE340304178”,

“from”: “/mn-cse/cnt-582769893”

}

]}

}

### 8.7.12 	Notifications

#### 8.7.12.1	Introduction

Each time a content instance is created under container of ADN-AE, then a latest notification containing the whole created content instance is posted to the targeted subscriber i.e. AE application adn-ae1 or adn-ae2, that can actuate into the light the new state received as notification, respectively.

#### 8.7.12.2	Post a notification to ADN-AE1

#### If the notification request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST / HTTP/1.1

Host: http://192.168.0.10:9090

X-M2M-Origin: /mn-cse

X-M2M-RI: notif/12345

Content-Type: application/vnd.onem2m-ntfy+xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sgn

xmlns:m2m="http://www.onem2m.org/xml/protocols">

<nev>

<rep>

<cin>

<con>ON</con>

<cnf>text/plain:0</cnf>

</cin>

<rss>201</rss>

</rep>

</nev>

<sur>

/mn-cse/sub-856593979

</sur>

</m2m:sgn>

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: notif/12345

If the notification request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST / HTTP/1.1

Host: http://192.168.0.10:9090

X-M2M-Origin: /mn-cse

X-M2M-RI: notif/12345

Content-Type: application/vnd.onem2m-ntfy+json

{

“m2m:sgn”:

{

“nev”:{

“rep”:

{

“cin”:

{

“con”: “ON”,

“cnf”: ”text/plain:0”

},

“rss”:201

}

},

“sur”:”/mn-cse/sub-856593979”

}

}

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: notif/12345

#### 8.7.12.3	Post a notification to ADN-AE2

If the notification request body is represented in XML, the HTTP request message looks as following example:

HTTP Request:

POST /  HTTP/1.1

Host: http://192.168.0.20:9090

X-M2M-Origin: /mn-cse

X-M2M-RI: notif/12346

Content-Type: application/vnd.onem2m-ntfy+xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sgn

xmlns:m2m="http://www.onem2m.org/xml/protocols">

<nev>

<rep>

<cin>

<con>ON</con>

<cnf>text/plain:0</cnf>

</cin>

<rss>201</rss>

</rep>

</nev>

<sur>

/mn-cse/sub-856463728

</sur>

</m2m:sgn>

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI:  notif/12346

If the notification request body is represented in JSON, the HTTP request message looks as following example:

HTTP Request:

POST /  HTTP/1.1

Host: http://192.168.0.20:9090

X-M2M-Origin: /mn-cse

X-M2M-RI: notif/12346

Content-Type: application/vnd.onem2m-ntfy+json

{

“m2m:sgn”:

{

“nev”:{

“rep”:

{

“cin”:

{

“con”: “ON”,

“cnf”: ”text/plain:0”

},

“rss”:201

}

},

“sur”:”/mn-cse/sub-856463728”

}

}

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI:  notif/12346

## -----------------------End of change 3---------------------------------------------

# Comments

{

"m2m:csr":

{

"ty": 16,

"pi": "/in-cse",

"ri": "/in-cse/csr-299409504",

"rn": "home_gateway",

"ct": "20150617T072709",

"lt": "20150617T072709",

"cst": 2,

"poa": [“http://mn.provider.com:8080”],

"cb": "mn.provider.com/mn-cse",

"csi": "mn-cse",

"rr": TRUE

}

}

PRO-2016-0312 AGREED