| CHANGE REQUEST |
| --- |
| Meeting:* | TST #24.1 |
| Source:* | InterDigital |
| Date:* | 2016-08-22 |
| Contact:* | Bob Flynn (bob.flynn@InterDigital.com) Kushal Shah (KushalkumarNareshkumar.Shah@InterDigital.com) |
| Reason for Change/s:* | Addition of discovery test scenarios with level and offset filter criteria confitions |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0013-Interoperability_Testing-V1_1_1 |
| Clauses/Sub Clauses* | 8.1.6.5, 8.1.6.6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This STE CR proposes addition of Discovery test cases with discovery filter criteria level and offset conditions.

These test cases check interoperability of Release 2 functionality.

## ----------------------- Start of change 1 -----------------------

# References

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: "Functional Architecture" V2.9.1.

[2]	oneM2M TS-0004: "Service Layer Core protocol Specification" V2.7.0.

[3]	oneM2M TS-0008: "CoAP Protocol Binding" V1.3.2.

[4]	oneM2M TS-0009: "HTTP Protocol Binding" V1.5.1.

[5]	oneM2M TS-0010: "MQTT Protocol Binding" V1.5.1.

[6]	oneM2M TS-0015: "Testing Framework".

[7]	oneM2M TS-0011: "Common Terminology".

[8]	IETF RFC 3986: "Uniform Resource Identifier (URI): Generic Syntax".

[9]	IETF RFC 7230: "Hypertext Transfer Protocol (HTTP/1.1): Message Syntax and Routing".

[10]	oneM2M TS-0005: "Management Enablement (OMA)".

[11]	oneM2M TS-0006: "Management Enablement (BBF)".

[12]	                 oneM2M TS-0003: “Security Solutions” V1.4.2.

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

#### 8.1.6.5	Discovery with level filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_22 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using the level filter criteria value set to 1 |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.6 TS-0004 [2], clause 7.3.3.14 |
| Pre-test conditions: | <AE1> and <AE2> resources are created in Registrar CSE. A <Container> resource is created under both <AE> resources in Registrar CSE. A <ContentInstance> resource is created under both <Container> resources in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE1 is requested to send a Discovery request in order to discover specific resources located in Registrar CSE using level filter criteria value set to 1 |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 lev=1 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&lev=1 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE1-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE1-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: lev=1 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE1-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu = 1 lev=1 pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the address of both <AE> resources |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of both <AE> resources |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of both <AE> resources |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE1-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the address of both <AE> resources |
| 4 |  | IOP Check | AE1 indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_23 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using the level filter criteria value set to 2 |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.6 TS-0004 [2], clause 7.3.3.14 |
| Pre-test conditions: | <AE1> and <AE2> resources are created in Registrar CSE. A <Container> resource is created under both <AE> resources in Registrar CSE. A <ContentInstance> resource is created under both <Container> resources in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE1 is requested to send a Discovery request in order to discover specific resources located in Registrar CSE using level filter criteria value set to 2 |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 lev=2 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&lev=2 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE1-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE1-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: lev=2 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE1-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu = 1 lev=2 pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the address of all <AE> and <Container> resources |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of all <AE> and <Container> resources |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of all <AE> and <Container> resources |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE1-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the address of all <AE> and <Container> resources |
| 4 |  | IOP Check | AE1 indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_24 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using the level filter criteria value set to 3 |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.6 TS-0004 [2], clause 7.3.3.14 |
| Pre-test conditions: | <AE1> and <AE2> resources are created in Registrar CSE. A <Container> resource is created under both <AE> resources in Registrar CSE. A <ContentInstance> resource is created under both <Container> resources in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE1 is requested to send a Discovery request in order to discover specific resources located in Registrar CSE using level filter criteria value set to 3 |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 lev=3 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&lev=3 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE1-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE1-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: lev=3 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE1-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu = 1 lev=3 pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the address of all <AE>, <Container> and <ContentInstance>resources |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of all <AE>, <Container> and <ContentInstance>resources |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of all <AE>, <Container> and <ContentInstance>resources |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE1-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the address of all <AE>, <Container> and <ContentInstance>resources |
| 4 |  | IOP Check | AE1 indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.6.6	Discovery with offset filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_25 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using the offset filter criteria value set to 3 |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.6 TS-0004 [2], clause 7.3.3.14 |
| Pre-test conditions: | <AE1> and <AE2> resources are created in Registrar CSE. A <Container> resource is created under both <AE> resources in Registrar CSE. A <ContentInstance> resource is created under both <Container> resources in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE1 is requested to send a Discovery request in order to discover specific resources located in Registrar CSE using offset filter criteria value set to 3 |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 ofs=3 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&ofs=3 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE1-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE1-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: ofs=3 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE1-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu = 1 ofs=3 pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message cnst = 1 cnot = 5 pc = Serialized representation of data object containing the address of any 3 resources based on the response received from data base |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message X-M2M-CNST:1 X-M2M-CNOT:5 Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of any 3 resources based on the response received from data base |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message X-M2M-CNST:1 X-M2M-CNOT:5 Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of any 3 resources based on the response received from data base |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE1-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message X-M2M-CNST:1 X-M2M-CNOT:5 pc = Serialized representation of data object containing the address of any 3 resources based on the response received from data base |
| 4 |  | IOP Check | AE1 indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_26 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using the offset filter criteria value set to 5 |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.6 TS-0004 [2], clause 7.3.3.14 |
| Pre-test conditions: | <AE1> and <AE2> resources are created in Registrar CSE. A <Container> resource is created under both <AE> resources in Registrar CSE. A <ContentInstance> resource is created under both <Container> resources in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE1 is requested to send a Discovery request in order to discover specific resources located in Registrar CSE using offset filter criteria value set to 5 |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 ofs=5 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&ofs=5 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE1-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE1-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: ofs=5 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE1-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu = 1 ofs=5 pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message cnst = 2 pc = Serialized representation of data object containing the address of any 1 resource based on the response received from data base |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message X-M2M-CNST: 2 Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of any 1 resource based on the response received from data base |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message X-M2M-CNST: 2 Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of any 1 resource based on the response received from data base |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE1-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message X-M2M-CNST: 2 pc = Serialized representation of data object containing the address of any 1 resource based on the response received from data base |
| 4 |  | IOP Check | AE1 indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_27 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using the offset filter criteria value set to 0 |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.6 TS-0004 [2], clause 7.3.3.14 |
| Pre-test conditions: | <AE1> and <AE2> resources are created in Registrar CSE. A <Container> resource is created under both <AE> resources in Registrar CSE. A <ContentInstance> resource is created under both <Container> resources in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE1 is requested to send a Discovery request in order to discover specific resources located in Registrar CSE using offset filter criteria value set to 0 |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 ofs=0 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&ofs=0 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE1-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE1-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: ofs=0 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE1-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu = 1 ofs=0 pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message cnst = 2 pc = Serialized representation of data object containing the address of all 6 resources |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message X-M2M-CNST: 2 Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of all 6 resources |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message X-M2M-CNST: 2 Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of all 6 resources |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE1-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message X-M2M-CNST: 2 pc = Serialized representation of data object containing the address of all 6 resources |
| 4 |  | IOP Check | AE1 indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_28 |
| Objective: | AE discovers all the accessible resources residing in Registrar CSE using the offset filter criteria value set to 0 and limit filter criteria value set to 2 |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.6 TS-0004 [2], clause 7.3.3.14 |
| Pre-test conditions: | <AE1> and <AE2> resources are created in Registrar CSE. A <Container> resource is created under both <AE> resources in Registrar CSE. A <ContentInstance> resource is created under both <Container> resources in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE1 is requested to send a Discovery request in order to discover specific resources located in Registrar CSE using offset filter criteria value set to 0 and discovered uri list limit is set to 2 in Registrar CSE policy |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 ofs=0 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&ofs=0 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE1-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE1-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: ofs=0 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE1-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu = 1 ofs=0 pc = empty |
| 3 |  | IOP Check | Registrar CSE sends success response to AE1 |
| 4 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message cnst=1 cnot=2 pc = Serialized representation of data object containing the address of any 2 resources based on the response received from data base |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message X-M2M-CNST:1 X-M2M-CNOT:2 Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of any 2 resources based on the response received from data base |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message X-M2M-CNST:1 X-M2M-CNOT:2 Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of any 2 resources based on the response received from data base |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE1-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message X-M2M-CNST:1 X-M2M-CNOT:2 pc = Serialized representation of data object containing the address of any 2 resources based on the response received from data base |
| 5 |  | IOP Check | AE1 sends discovery request to Registrar CSE with offset filtercriteria value set to 2 |
| 6 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 ofs=2 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&ofs=2 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE1-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE1-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: ofs=2 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE1-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu = 1 ofs=2 pc = empty |
| 7 |  | IOP Check | Registrar CSE sends success response to AE1 |
| 8 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message cnst=1 cnot=4 pc = Serialized representation of data object containing the address of any 2 resources based on the response received from data base |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message X-M2M-CNST:1 X-M2M-CNOT:4 Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of any 2 resources based on the response received from data base |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message X-M2M-CNST:1 X-M2M-CNOT:4 Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of any 2 resources based on the response received from data base |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE1-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message X-M2M-CNST:1 X-M2M-CNOT:4 pc = Serialized representation of data object containing the address of any 2 resources based on the response received from data base |
| 9 |  | IOP Check | AE1 sends discovery request to Registrar CSE with offset filtercriteria value set to 4 |
| 10 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 ofs=4 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&ofs=4 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE1-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE1-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: ofs=4 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE1-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu = 1 ofs=4 pc = empty |
| 11 |  | IOP Check | Registrar CSE sends success response to AE1 |
| 12 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message cnst=2 pc = Serialized representation of data object containing the address of remanining 2 resources based on the response received from data base |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message X-M2M-CNST:2 Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of remanining 2 resources based on the response received from data base |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message X-M2M-CNST:2 Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of remanining 2 resources based on the response received from data base |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE1-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message X-M2M-CNST:2 pc = Serialized representation of data object containing the address of remanining 2 resources based on the response received from data base |
| 13 |  | IOP Check | AE1 indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

## ----------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?