| Input Contribution |
| --- |
| Meeting ID* | TST 25 |
| Title:* | Device Profile for Actuating Services |
| Source:* | Ting Martin MIAO, KETI, novamartin@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.kr SeungMyeong Jeong, KETI, sm.jeong@keti.re.kr Sungchan Choi, KETI, csc@keti.re.kr Jaeho Kim, KETI, jhkim@keti.re.kr |
| Uploaded Date:* | 2016-10-21 |
| Document(s) Impacted* | TS-0025 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

We propose a definition for actuating service profiles containing fundamental and extandable features required for devices to implement oneM2M actuating service.

---------------------Start of Change 1-----------------------

# 7 	Product Profiles

## 7.5	Actuating Service Profile

### 7.5.1	Profile description

Devices implementing actuating services is characterized with converting a controller command signal into a change in a physical parameter and changing one type of physical quantity into another alternative form.

In a smart home scenario, smart sockets which are designed to manage and control the energy consumption of home devices, are usually plugged into temperature sensors, for instance, to trigger airconditioner or heater when the temperature is higher or lower than the configured temperature setting.

The controller command signal for triggering airconditioner or heater is generated by a handler that handles the comparison operations between the sensed temperature value and the programmed threshold and then sent to the triggered devices. In oneM2M architecture, the transmission of controller command signal can be achieved by deploying notification mechanism. To this end, the airconditioner or heater has to subscribe to the temperature sensor in advance.

### 7.5.2	Profile usage example

This profile applies to oneM2M devices that desire to implement actuating services. The actuating service profile assists device manufacturers to easily and clearly choose fundamental and extendable features for their oneM2M compliant devices to implement oneM2M actuating services.

Taking smart socket as an example, when a manufacturer-A decides to design a smart socket with oneM2M actuating service, he can refer to the Actuating Service Profile to check the minimum features that are required to implement. The features for Actuating Service Profile are defined in Section 7.3.3 Feature Set. When another manufacturer-B also designs a smart socket complying with the Actuating Service Profile, these two smart sockets produced from two different manufacturers are interoperable potentially to work together to implement complex tasks.

### 7.5.3	Fundamental feature set

The feature set shown in Table 7.3.3.1 consist of a group of features that all oneM2M compliant devices have to implement in order to implement actuating services.

Based on the nature of actuator that generates and transmits control command signal to trigger a target device, oneM2M compliant actuating devices have to be able to subscribe to sensing devices so that whenever the sensing device uploads sensing measurement, the actuating device can be notified with the new measurement. Similarly, actuating devices have to be able to send notifications including control commands to physical devices designated to be triggered.

In summary, oneM2M actuating service profile consists of fundamental features to implement actuating services as following:

- Subscription creation: creates a <subscription> resource as a child resource of sensing devices (AE)’s <container> resource to enable the actuating devices subscribe to sensing devices.

- Notification management: sends a single/aggregated notification to the target devices by including <contentInstance> resource(s) including control commands.

<The clause will just include the mandatory features and the optional feature that are essential for the profile. All features in this clause shall be implemented to be certifed>

Table 7.5.3.1 Fundamental feature set for actuating service profile

| No. | CSF | Sub-function | Feature |
| --- | --- | --- | --- |
| 1 | Subscription Management | Subscription | Creation of <subscription> resource with mandatory attributes |
|  |  |  | Creation of <subscription> resource with full attributes |
|  |  |  | ….. |
| 2 | Notification Management | Notification | Post of <notification> resource with mandatory attributes |
|  |  | Aggregate notification | Post of <aggregatedNotification> resource with mandatory attributes |

Editor’s Node: The table is suggest to the feature catalogue. Will need to be updated with the feature IDs once the feature definition is done.

### 7.5.4	Extendable feature set

<The clause will include the optional features. The features in this clause is recommended and suggested by the profile, the implementer may choose to implement or not. The feature is not essential for certification of the profile.>

Editor’s Node: The table is suggest to the feature catalogue. Will need to be updated with the feature IDs once the feature definition is done.

Table 7.5.4.1 Extendable feature set for actuating service profile

| No. | CSF | Sub-function | Feature |
| --- | --- | --- | --- |
| 1 | Registration | AE Registration | Creation of <AE> resource with mandatory attributes |
| 2 | DMR | Data Management of Container | Creation of <container> resource with mandatory attributes |
|  |  |  | Creation of <container> resource with full attributes |
|  |  |  | ….. |
|  |  | Data Management of ContentInstance | Creation of <contentInstance> resource with mandatory attributes |
|  |  |  | Creation of <contentInstance> resource with full attributes |

--------------------End of Change 1-----------------

# Comments

(1) Remove this part to generic device profile

(1) Remove this part to generic device profile