| Input Contribution |
| --- |
| Meeting ID* | TST#25 |
| Title:* | TS-0015-Conformance Test Configuration for AE |
| Source:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Abdullah Aziz, KETI, G2016FFM082@sju.ac.kr |
| Uploaded Date:* | 2016-10-06 |
| Document(s) Impacted* | TS-0015 V2.0.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes some text for the clause 6.3.3.3 (Test Configurations) of conformance testing section of the TS-0015 Testing framework. Current examples of Test Configurations for IUT and Test System do not simulate the testing of AE under the presence of TE (Trigger Entity)  in test system which notifies AE, So that this contribution provides another example of test configuration which simulate an AE and TE (Trigger Entity) in a CF03.

In this example scenario AE in IUT will be in listening state and when TE sends an event to AE to perform specific task then AE will perform that specific task. For example, when TE notify an AE to register itself in CSE then AE will send registration request to CSE.

## -----------------------Start of change 1--------------------------------------------

#### 6.3.3.3	Test configurations

The test suite uses test configurations in order to cover the different test scenarios.

In following 3 examples, the IUT is tested by the test system simulating an AE in CF01 (no hop configuration) or an AE and a CSE in a CF02 (single hop configuration) or a CSE and Triggering Entity(TE) in a CF03(single hop configuration).

Note: Test configuration 3 (CF03) is designed for testing AE case.

EXAMPLE 1:	Test configuration 1 (CF01):

EXAMPLE 2:	Test configuration 2 (CF02):

EXAMPLE 3:	Test configuration 3 (CF03):

Note: Triggering Entity (TE) is a logical function module in Test Tystem which triggers IUT (AE) to perform specific tasks.

Note: Tca is a reference point for communication flows between Triggering Entity in Test System and an Application Entity (AE) for the purpose of AE testing. These flows enable the TE to send a triggering command to a target AE.

## -----------------------End of change 1--------------------------------------------

# Text boxes

IUT

TEST SYSTEM

AE

CSE

Mca

Mcc

IUT

TEST SYSTEM

AE

CSE

Mca

CSE

Mca

IUT

TEST SYSTEM

TE

AE

CSE

Tca