| Input Contribution |
| --- |
| Meeting ID* | TST#25 |
| Title:* | TS-0015-Conformance Test Configuration for AE |
| Source:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Abdullah Aziz, KETI, G2016FFM082@sju.ac.kr |
| Uploaded Date:* | 2016-10-06 |
| Document(s) Impacted* | TS-0015 V2.0.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes some text for the clause 6.3.3.3 (Test Configurations) of conformance testing section of the TS-0015 Testing framework. There is no test configurations for Test System to simulate CSE to test IUT acting as AE. In this contribution, we propose to add another example of test configuration to test IUT acting as AE.

## -----------------------Start of change 1--------------------------------------------

#### 6.3.3.3	Test configurations

The test suite uses test configurations in order to cover the different test scenarios.

In following 3 examples, the IUT is tested by the test system simulating an AE in CF01 (no hop configuration) or an AE and a CSE in a CF02 (single hop configuration) or a CSE in a CF03(single hop configuration).

EXAMPLE 1:	Test configuration 1 (CF01):

EXAMPLE 2:	Test configuration 2 (CF02):

EXAMPLE 3:	Test configuration 3 (CF03):

Note: Test configuration 3 (CF03) is designed for testing AE.

## -----------------------End of change 1--------------------------------------------

# Text boxes

IUT

TEST SYSTEM

AE

CSE

Mca

Mcc

IUT

TEST SYSTEM

AE

CSE

Mca

CSE

Mca

IUT

TEST SYSTEM

AE

CSE