| Input Contribution |
| --- |
| Meeting ID* | TST#25 |
| Title:* | TS-0018 Test Purposes for Group AE |
| Source:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Abdullah Aziz, KETI, G2016FFM082@sju.ac.kr |
| Uploaded Date:* | 2016-10-05 |
| Document(s) Impacted* | TS-0018 V0.1.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes two test purposes for AE REG group to address AE registration and AE re-registration case. Currently clasue 7.2.1 of Section 7.2 is empty and is not describing any test purpose for Group AE. This contribution will add Registration test purpose (7.2.1.1) with two cases, one for registration and second for re-registration.

## -----------------------Start of change 1--------------------------------------------

### 7.2.1	Group AE

## 7.2.1.1		Registration (REG)

Editor’s Note: Short name “TS” denotes “Test System” in Section 7.2.1.

| TP Id | TP/oneM2M/AE/REG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT sends an AE registration request including attribute allowedApp-IDs set to APP-ID but no AE-ID-STEM provided when receiving a triggering command from Testing System. |
| Reference | TS-0001 10.1.1.2.2 - case C, 9.6.19 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being in the "initial state" and the Test System (TS) triggering IUT to send REG request and the TS having a CSEBase resource containing a ServiceSubscribedProfile resource containing a ServiceSubscribedNode resource containing RuleLinks attribute pointing to a ServiceSubscribedAppRule resource containing applicableCredIDs attribute set to None and allowedApp-IDs attribute indicating APP-ID and allowedAEs attribute indicating C-AE-ID-STEM } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid CREATE request to CSE containing Resource-Type set to 2 (AE) and From set to empty and Content <AE> containing App-ID attribute set to APP-ID and requestReachability set to REQUEST_REACHABILITY } | CSE ( IUT |
|  | then { the IUT receives a Response message containing Response Status Code set to 2001 (CREATED) } | CSE ( IUT |

| TP Id | TP/oneM2M/AE/REG/BV/002 |
| --- | --- |
| Test objective | Check that the IUT sends an AE re-registration request including both attribute allowedApp-IDs set to APP-ID and AE-ID-STEM when receiving a triggering command from Testing System. |
| Reference | TS-0001 10.1.1.2.2 - case d, 9.6.19 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being in the "initial state" and the Test System (TS) triggering IUT to send REG request and the TS having a CSEBase resource containing a ServiceSubscribedProfile resource containing a ServiceSubscribedNode resource containing RuleLinks attribute pointing to a ServiceSubscribedAppRule resource containing applicableCredIDs attribute set to None and allowedApp-IDs attribute indicating APP-ID and allowedAEs attribute indicating C-AE-ID-STEM } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid CREATE request to CSE containing Resource-Type set to 2 (AE) and From set to C-AE-ID-STEM and Content <AE> containing App-ID attribute set to APP-ID and requestReachability set to REQUEST_REACHABILITY } | CSE ( IUT |
|  | then { the IUT receives a Response message containing Response Status Code set to 2001 (CREATED) } | CSE ( IUT |

Editor’s Note: More test purposes for AE group will be added here.

## -----------------------End of change 1--------------------------------------------