| CHANGE REQUEST |
| --- |
| Meeting:* | TST#25 |
| Source:* | Huawei Technologies Co., Ltd. |
| Date:* | 2016-10-08 |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* |  |
| CR against: Release* | Three |
| CR against: WI* | Active WI-0055 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0025 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contribution proposes a new product profile for constraint sensor.

### -----------------------Start of change 1-------------------------------------------

## 7.2	Constraint sensor

### 7.2.1	Profile description

The profile defines constraint sensor that is powered by battery and intended to be used for years after deployment without any human interference for maintenance. Therefore, the function of  constraint sensor need to be very limited.

A sensor is intended to be reporting sensed data to the CSE periodically or according to some other period. Everytime the sensor reports data, it sends one message to the CSE. In order to save battery, the sensor can be sleeping before and after the reporting of sensed data.

For the successful report of data, there is needed some context resource architecture like the AE resource, the container resource etc. The resource architecture can be pre-configured in order to minimize the complexity of the constraint sensor.

### 7.2.2	Profile usage examples

The profile applies to constraint sensors that report periodically sensed data. Some example of this kind of product include:

Electricity, water, gas meters that report consumed amount of electricity, water or gas to the CSE. The meters are deployed inside houses and are powered by battery.

Temperature, humidity sensors that are deployed in the open air for environment monitoring. The sensors can be deployed in places that are hardly reachable for people that the sensor’s need to be working without human inference for years powered with battery.

### 7.2.3	Fundamental feature sets

The Creation of <contentInstance> resource.

Editor’s note: to be indexed to feature catalogue.

### 7.2.4	Extendable feature sets

The Creation of <AE> resource.

Editor’s note: to be indexed to feature catalogue.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

Does this CR contain changes related to only one particular issue/problem?

Have any mirror crs been posted?

Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

Does this change request follow the drafting rules?

Are all pictures editable?

Have you checked the spelling and grammar?

Have you used change bars for all modifications?

Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?