| Input Contribution |
| --- |
| Meeting ID* | TST 25 |
| Title:* | DMR Container and Latest ContentInstance Test Purposes |
| Source:* | Ting Martin MIAO, KETI, novamartin@keti.re.kr SeungMyeong Jeong, KETI, sm.jeong@keti.re.kr |
| Uploaded Date:* | 2016-10-15 |
| Document(s) Impacted* | TS-0018 V0.1.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

We propose to add new test purposes to address DMR functionality for container and contentInstance especially for latest contentInstance.

# -------------Reference from TS-0001-------------------

### 9.6.1.3.2  Common attributes

The following attributes are commonly used in multiple, but not all, resource types which are normal, not virtual or announced. Common attributes for announced resource types are independently defined in clause 9.6.26.3.

NOTE:	The list of attributes in table 9.6.1.3.2-1 is not exhaustive.

Table 9.6.1.3.2-1: Common Attributes

| Attribute Name | Description |
| --- | --- |
| accessControlPolicyIDs | The attribute contains a list of identifiers of an <accessControlPolicy> resource. The privileges defined in the <accessControlPolicy> resource that are referenced determine who is allowed to access the resource containing this attribute for a specific purpose (e.g. Retrieve, Update, Delete, etc.). If a resource type does not have an accessControlPolicyIDs attribute definition, then the accessControlPolicyIDs for that resource is governed in a different way, for example, the accessControlPolicy associated with the parent may apply to a child resource that does not have an accessControlPolicyIDs attribute definition, or the privileges for access are fixed by the system. Refer to the corresponding resource type definitions and procedures to see how access control is handled in such cases. If a resource type does have an accessControlPolicyIDs attribute definition, but the (optional) accessControlPolicyIDs attribute is not set, or it is set to a value that does not correspond to valid<accessControlPolicy> resource(s), or it refers to an <accessControlPolicy> resource(s) that is not reachable (e.g. because it is located on a remote CSE that is offline or not reachable), then the system default access privileges shall apply. All resources are accessible if and only if the privileges(i.e. stored as privileges or selfPrivileges attribute of <accessControlPolicy> resource) allow it, therefore all resources shall have an associated AccessControlPolicyIDs attribute, either explicitly (setting the attribute in the resource itself) or implicitly (either by using the parent privileges or the system default policies). Which means that the system shall provide a default access privileges in case that the Originator does not provide a specific accessControlPolicyIDs during the creation of the resource. To update this attribute, a Hosting CSE shall check whether an Originator has Update permission in any selfPrivileges of the <accessControlPolicy> resources which this attribute originally indicates. |
| stateTag | An incremental counter of modification on the resource. When a resource is created, this counter is set to 0, and it will be incremented on every modification of the resource (see notes 1 and 2). The modification also includes direct child resource creation and deletion. |
| announceTo | This attribute may be included in a CREATE or UPDATE Request in which case it contains a list of addresses/CSE-IDs where the resource is to be announced. For the case that CSE-IDs are provided, the announced-to CSE shall decide the location of the announced resources based on the rules described in clause 9.6.26. For the original resource, this attribute shall only be present if it has been successfully announced to other CSEs. This attribute maintains the list of the resource addresses to the successfully announced resources. Updates on this attribute will trigger new resource announcement or de-announcement. If announceTo attribute includes resource address(s), the present document does not provide any means for validating these address(s) for announcement purposes. It is the responsibility of the Hosting-CSE referenced by the resource address(s) to validate the access privileges of the originator of the Request that triggers the announcement. |
| announcedAttribute | This attributes shall only be present at the original resource if some Optional Announced (OA) type attributes have been announced to other CSEs. This attribute maintains the list of the announced Optional Attributes (OA type attributes) in the original resource. Updates to this attribute will trigger new attribute announcement if a new attribute is added or de-announcement if the existing attribute is removed. |
| labels | Tokens used as keys for discovering resources. This attribute is optional and if not present it means that the resource cannot be found by means of discovery procedure which uses labels as key parameter of the discovery. |
| NOTE 1: In order to enable detection of overflow, the counter needs to be capable of expressing sufficiently long numbers. NOTE 2: This attribute has the scope to allow identifying changes in resources within a time interval that is lower than the one supported by the attribute lastModifiedTime (e.g. less than a second or millisecond). This attribute can also be used to avoid race conditions in case of competing modifications. |

### 9.6.27	Resource Type latest

The <latest> resource is a virtual resource because it does not have a representation. It is the child resource of a <container> resource. When a request addresses the <latest> resource, the Hosting CSE shall apply the request to the latest <contentInstance> resource among all existing <contentInstance> resources of the <container> resource.

The <latest> resource inherits access control policies that apply to the parent <container> resource.

### 9.6.28	Resource Type oldest

The <oldest> resource is a virtual resource because it does not have a representation. It is the child resource of a <container> resource. When a request addresses the <oldest> resource, the Hosting CSE shall apply the request to the oldest <contentInstance> resource among all existing <contentInstance> resources of the <container> resource.

The <oldest> resource inherits access control policies that apply to the parent <container> resource.

### 10.2.19	<contentInstance> Resource Procedures

#### 10.2.19.1	Introduction

This clause describes the management procedures for the <contentInstance> resource. Since <contentInstance> resource is immutable once created, there is no procedure for updating it.

#### 10.2.19.2	<contentInstance> CREATE

This procedures shall be used for creating a <contentInstance> resource.

Table 10.2.19.2-1: <contentInstance> CREATE

| <contentInstance> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.7. |
| Processing at Originator before sending Request | According to clause 10.1.1.1. |
| Processing at Receiver | According to clause 10.1.1.1. If the newly created <contentInstance> resource violates any of the policies defined in the parent <container> resource (e.g. maxNrOfInstances or maxByteSize), then the oldest <contentInstance> resources shall be removed from the <container> to enable the creation of the new <contentInstance> resource. |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <contentInstance> resource, according to clause 10.1.1.1. |
| Processing at Originator after receiving Response | According to clause 10.1.1.1. |
| Exceptions | According to clause 10.1.1.1. |

#### 10.2.19.3	<contentInstance> RETRIEVE

This procedure shall be used for retrieving the attributes of a <contentInstance> resource.

Table 10.2.19.3-1: <contentInstance> RETRIEVE

| <contentInstance> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | According to clause 10.1.2. |
| Processing at Originator before sending Request | According to clause 10.1.2. |
| Processing at Receiver | According to clause 10.1.2. |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with specific details for: Content: Attributes of the <contentInstance> resources as defined in clause 9.6.7. |
| Processing at Originator after receiving Response | According to clause 10.1.2. |
| Exceptions | According to clause 10.1.2. |

#### 10.2.19.4	<contentInstance> UPDATE

The Update operation shall not apply to <contentInstance> resource.

#### 10.2.19.5	<contentInstance> DELETE

This procedure shall be used for deleting a <contentInstance> resource residing under a <container> resource.

Table 10.2.19.5-1: <contentInstance> DELETE

| <contentInstance> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply. |
| Processing at Originator before sending Request | According to clause 10.1.4. |
| Processing at Receiver | According to clause 10.1.4. The Receiver shall delete the <contentInstance> resource. |
| Information in Response message | According to clause 10.1.4. |
| Processing at Originator after receiving Response | According to clause 10.1.4. |
| Exceptions | According to clause 10.1.4. |

### 10.2.22	<latest> Resource Procedures

#### 10.2.22.0	Introduction

Only Retrieve and Delete operations shall be allowed for the <latest> resource.

#### 10.2.22.1	Retrieve <latest>

This procedure shall apply to the latest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If there is no <contentInstance> resource in the parent, then the Receiver shall respond with an error.

This procedure is the same as the procedures in clause 10.2.19.3 <contentInstance> RETRIEVE.

#### 10.2.22.2	Delete <latest>

This procedure shall apply to the latest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If there is no <contentInstance> resource in the parent, then the Receiver shall responsed with an error.

After deletion, the <latest> contentInstance will point to the latest <contentlnstance> among all remaining <contentInstance> resources in the parent <container> resource. This procedure is the same as the procedures in clause 10.2.19.4 <contentInstance> DELETE.

### 10.2.23	<oldest> Resource Procedure

#### 10.2.23.0	Introduction

Only Retrieve and Delete operations shall be allowed for the <oldest> resource.

#### 10.2.23.1	Retrieve <oldest>

This procedure shall apply to the oldest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If there is no <contentInstance> resource in the parent, then the Receiver shall responsed with an error.

This procedure is the same as the procedures in clause 10.2.19.3 <contentInstance> RETRIEVE

#### 10.2.23.2	Delete <oldest>

This procedure shall apply to the oldest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If there is no <contentInstance> resource in the parent, then the Receiver shall responsed with an error.

After deletion, the <oldest> contentInstance will point to the oldest <contentlnstance> among all remaining <contentInstance> resources in the parent <container> resource.

This procedure is the same as the procedure in as clause 10.2.19.4 <contentInstance> DELETE.

------------Reference from TS-0001-----------------------END---------------

# ---------------Reference from TS-0004-----------------------

### Resource Type <container>

#### Introduction

This resource represents a container for data instances. It is used to share information among other entities and potentially to track the data. A <container> resource has no associated content, only attributes and child resources.

The detailed description can be found in clause 9.6.6 in TS-0001 [오류! 참조 원본을 찾을 수 없습니다.].

Table 7.4.7.1-1: Data type definition of <container> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Container | CDT-container-v1_10_0오류! 참조 원본을 찾을 수 없습니다..xsd |  |

Table 7.4.7.1-2: Universal/Common Attributes of <container> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| stateTag | NP | NP |
| labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |

Table 7.4.7.1-3: Resource Specific Attributes of <contianer> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| creator | O | NP | m2m:ID | No default |
| maxNrOfInstances | O | O | xs:nonNegativeInteger | No default |
| maxByteSize | O | O | xs:nonNegativeInteger | No default |
| maxInstanceAge | O | O | xs:nonNegativeInteger | No default |
| currentNrOfInstances | NP | NP | xs:nonNegativeInteger | No default (This is generated by the Hosting CSE and limited by the maxNrOfInstances) |
| currentByteSize | NP | NP | xs:nonNegativeInteger | No default (This is generated by the Hosting CSE and limited by the maxByteSize) |
| locationID | O | O | xs:anyURI | No default |
| ontologyRef | O | O | xs:anyURI | No default |

Table 7.4.7.1-4: Child resources of <container> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <contentInstance> | [variable] | 0..n | Clause 7.4.8 |
| <subscription> | [variable] | 0..n | Clause 오류! 참조 원본을 찾을 수 없습니다. |
| <container> | [variable] | 0..n | Clause 7.4.7 |
| <latest> | latest | 1 | Clause 7.4.28 |
| <oldest> | oldest | 1 | Clause 7.4.29 |

#### <container> resource specific procedure on CRUD operations

This clause describes container resource specific behaviour for CRUD operations.

##### Create

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

Primitive specific operation on Recv-6.4 is performed with following exceptions for optional attributes while executing clause 오류! 참조 원본을 찾을 수 없습니다. procedures.

The Hosting CSE may assign default values based on local policy for optional attributes maxNrOfInstances, maxByteSize and maxInstanceAge.

If the maxNrOfInstances, maxByteSize or maxInstanceAge attributes are present in the resource representation, but their value indicates an invalid value, then the request shall be rejected with a Response Status Code indicating "BAD_REQUEST" error.

There are two cases where the Hosting CSE shall configure or overrride an maxNrOfInstances , maxByteSize or maxInstanceAge value that differs from the value specified in the resource representation (if present).

- The Originator does not specify a value

The Hosting CSE determines the maxNrOfInstances , maxByteSize or maxInstanceAge requested by the Originator doesn’t meet its requirements (E.g. based on a local policy)

In each of these cases, the Hosting CSE shall configure a maxNrOfInstances , maxByteSize or maxInstanceAge into the resource according to local policy. In addition, the Hosting CSE shall communicate the modified value back to the originator in the response if the Result Content parameter permits this.

No other changes from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다.

##### Retrieve

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

##### Update

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

.

##### Delete

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

### Resource Type <contentInstance>

#### Introduction

The <contentInstance> resource represents a data instance in the container.

The detailed description can be found in clause 9.6.7 in TS-0001 [오류! 참조 원본을 찾을 수 없습니다.].

Table 7.4.8.1-1: Data type definition of <contentInstance> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| contentInstance | CDT-contentInstance-v1_10_0.xsd |  |

Table 7.4.8.1-2: Universal/Common Attributes of <contentInstance> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create |
| @resourceName | O |
| resourceType | NP |
| resourceID | NP |
| parentID | NP |
| expirationTime | O |
| creationTime | NP |
| lastModifiedTime | NP |
| stateTag | NP |
| labels | O |
| announceTo | O |
| announcedAttribute | O |

Table 7.4.8.1-3: Resource Specific Attributes of <contentInstance> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create |  |  |
| creator | O | m2m:ID |  |
| contentInfo | O | m2m:contentInfo | No default. |
| contentSize | NP | xs:nonNegativeInteger | No default. |
| ontologyRef | O | xs:anyURI | No default. |
| content | M | xs:anySimpleType | No default (Transfer encoding may be applied, and indicated applied encoding as part of the contentInfo attribute). |

The contentInfo attribute shall provide meta information about the stored data in content. m2m:encodingType (0:plain, 1:base64 encoded string, 2:base64 encoded binary), and is optional.

#### <contentInstance> resource specific procedure on CRUD operations

##### Create

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

Primitive specific operation on Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed":

- The Hosting CSE shall set the contentSize to the size in bytes of the content attribute.

- currentNrOfInstances and currentByteSize of direct parent <container> resorce shall be updated. If currentNrOfInstances and/or currentByteSize exceeds maxNrOfInstances and/or maxByteSize of direct parent <container> resource respectively, the Hosting CSE shall return the response primitive with a Response Status Code indicating " NOT_ACCEPTABLE" error.

- stateTag attribute of direct parent <container> resource shall be incremented and copied into the stateTag of this <contentInstance> resource.

No other changes from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다.. The Originator may omit the name of the <contentInstance> resource unless the Originator need to refer specific content later.

##### Retrieve

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다.. The Originator may omit the name of the targeted <contentInstance> resource when the latest version of stored content is requested.

##### Update

Originator:

The <contentInstance> resource shall not be Updated via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

##### Delete

Originator:

Primitive specific operation on Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed":

- currentNrOfInstances and currentByteSize of direct parent <container> resorce shall be updated.

Receiver:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

### Resource Type latest

#### Introduction

The <latest> resource is a virtual resource because it does not have a representation. It is a child resource of the <container> resource. Whenever a request addresses the <latest> resource, the Hosting CSE shall apply the request to the latest <contentInstance> resource among all existing <contentInstance> resources of the <container> resource.

#### <latest> Resource Specific Procedure on CRUD Operations

##### Introduction

This sub-clause describes <latest> resource specific behaviour for operations. Among operations, only Retrieve and Delete operations shall be allowed for the <latest> resource.

##### Create

Originator:

The <latest> resource shall not be created via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received, the Receiver CSE shall execute the following steps in order.

  - "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

  - "Send the Response primitive".

##### Retrieve

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다. except the following modification:

Recv-6.2	Check the existence of the latest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If the resource exists, the subsequent procedures of the Receiver (i.e., after Recv-6.2) shall be performed for the resource. If the resource does not exist, the Hosting CSE shall reject the request with a Response Status Code indicating "NOT_FOUND" error.

##### Update

Originator:

The <latest> resource shall not be updated via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received, the Receiver CSE shall execute the following steps in order.

  - "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

  - "Send the Response primitive".

##### Delete

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다. except the following modification:

Recv-6.2	Check the existence of the latest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If the resource exists, the subsequent procedures of the Receiver (i.e., after Recv-6.2) shall be performed for the resource. If the resource does not exist, the Hosting CSE shall reject the request with a Response Status Code indicating "NOT_FOUND" error.

### Resource Type oldest

#### Introduction

The <oldest> resource is a virtual resource because it does not have a representation. It is a child resource of the <container> resource. Whenever a request addresses the <oldest> resource, the Hosting CSE shall apply the request to the oldest <contentInstance> resource among all existing <contentInstance> resources of the <container> resource.

#### <oldest> Resource Specific Procedure on CRUD Operations

##### Introduction

Among operations, only Retrieve and Delete operations shall be allowed for the <oldest> resource.

##### Create

Originator:

The <oldest> resource shall not be created via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received, the Receiver CSE shall execute the following steps in order.

  - "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

  - "Send the Response primitive".

##### Retrieve

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다. except the following modification:

Recv-6.2	Check the existence of the oldest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If the resource exists, the subsequent procedures of the Receiver (i.e., after Recv-6.2) shall be performed for the resource.  If the resource does not exist, the Hosting CSE shall reject the request with a Response Status Code indicating "NOT_FOUND" error.

##### Update

Originator:

The <oldest> resource shall not be updated via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received, the Receiver CSE shall execute the following steps in order.

  - "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

  - "Send the Response primitive".

##### Delete

Originator:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다..

Receiver:

No change from the generic procedures in clause 오류! 참조 원본을 찾을 수 없습니다. except the following modification:

Recv-6.2	Check the existence of the oldest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If the resource exists, the subsequent procedures of the Receiver (i.e., after Recv-6.2) shall be performed for the resource. If the resource does not exist, the Hosting CSE shall reject the request with a Response Status Code indicating "NOT_FOUND" error.

------------Reference from TS-0004-----------------------END---------------

## -----------------------Start of change 1--------------------------------------------

# 7	Test Purposes (TP)

## 7.2	Test Purposes for oneM2M

## 7.2.2.2		Data Management and Repository (DMR)

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/005 |
| --- | --- |
| Test objective | Check that the IUT rejects the CREATE request of <container> resource when the RW ATTRIBUTE is provided with an invalid value |
| Reference | TS-0001 10.2.4.1, TS-0004 7.4.7.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource-Type set to <container> type and no name attribute and Content attribute containing a RW ATTRIBUTE } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

| TP ID | Reference | ATTRIBUTE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/005_01 | TS-0001 9.6.6, TS-0004 7.4.7.1 | MaxNrOfInstances |
| TP/oneM2M/CSE/DMR/CRE/BV/005_02 | TS-0001 9.6.6, TS-0004 7.4.7.1 | MaxByteSize |
| TP/oneM2M/CSE/DMR/CRE/BV/005_03 | TS-0001 9.6.6, TS-0004 7.4.7.1 | maxInstanceAge |

Editor’s note: When one or more than one of the ATTRIBUTE list as above is/are included in the <contianer> CREATE request, the IUT will respond with BAD_REQUEST error.

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/006 |
| --- | --- |
| Test objective | Check that the IUT returns a default value to RW ATTRIBUTE in the response of a <container> CREATE request where no a RW ATTRIBUTE is provided by AE |
| Reference | TS-0001 10.2.4.1, TS-0004 7.4.7.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource-Type set to <container> type and no name attribute and no Content attributes representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) and Content attribute containing ATTRIBUTE with assigned field value by the IUT } | IUT ( AE |

| TP ID | Reference | ATTRIBUTE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/006_01 | TS-0001 9.6.6, TS-0004 7.4.7.1 | MaxNrOfInstances |
| TP/oneM2M/CSE/DMR/CRE/BV/006_02 | TS-0001 9.6.6, TS-0004 7.4.7.1 | MaxByteSize |
| TP/oneM2M/CSE/DMR/CRE/BV/006_03 | TS-0001 9.6.6, TS-0004 7.4.7.1 | maxInstanceAge |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/007 |
| --- | --- |
| Test objective | Check that the IUT responds with error when the newly created <contentInstance> results in that the field value of attribute currentNrOfInstances exceeds the field value of maxNrOfInstances in the parent <container> resource. |
| Reference | TS-0001 10.2.19.2, TS-0004 7.4.8.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a container resource TARGET_RESOURCE_ADDRESS containing attribute currentNrOfInstances set to value MAX_NUMBER_OF_INSTANCES and attribute maxNrOfInstances set to value MAX_NUMBER_OF_INSTANCES and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource-Type set to <contentInstance> type and no name attribute and no Content attributes representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 5207 (NOT_ACCEPTABLE) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/008 |
| --- | --- |
| Test objective | Check that the IUT responds with error when the newly created <contentInstance> results in the field value set in attribute currentByteSize exceeds the field value set in maxByteSize in the parent <container> resource. |
| Reference | TS-0001 10.2.19.2, TS-0004 7.4.8.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE a container resource TARGET_RESOURCE_ADDRESS containing attribute maxByteSize set to value MAX_BYTE_SIZE_OF_DATA and attribute currentByteSize set to value MAX_BYTE_SIZE_OF_DATA and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource-Type set to <contentInstance> type and no name attribute and no Content attributes representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 5207 (NOT_ACCEPTABLE) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/009 |
| --- | --- |
| Test objective | Check that the IUT increaments and then copies the field value of attribute stateTag in parent <container> resource when <contentInstance> resource is created as the direct child of the parent <container> |
| Reference | TS-0001 9.6.1.3.2, TS-0004 7.4.7.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE a container resource TARGET_RESOURCE_ADDRESS containing attribute stateTag set to COUNT_NUMBER and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource-Type set to <contentInstance> type and no name attribute and no Content attributes representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) and Content attribute containing stateTag set to value (COUNT_NUMBER + 1) } | IUT ( AE |

Editor’s Note: The stateTag gets increased whenever there are child resources created, updated or deleted.

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/010 |
| --- | --- |
| Test objective | Check that the IUT rejects the UPDATE request of an existing <contentInstance> resource with error “OPERATION_NOT_ALLOWED” |
| Reference | TS-0001 10.2.19.4, TS-0004 7.3.2.1 & 7.4.8.2.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing a <contentInstance> resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/DEL/BV/001 |
| --- | --- |
| Test objective | Check that the IUT decreases the field value of attribute currentNrOfInstances and currentByteSize of direct parent <container> respectively when a latest <contentInstance> resource is deleted successfully |
| Reference | TS-0001 10.2.19.5, TS-0004 7.4.8.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing a latest <contentInstance> resource TARGET_RESOURCE_ADDRESS containing currentNrOfInstances set to NUMBER_OF_INSTANCES and currentByteSize set to BYTE_SIZE_OF_DATA } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a DELETE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attributes representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (DELETED) and Content attribute containing currentNrOfInstances set to value (NUMBER_OF_INSTANCES – 1) and currentByteSize set to value (BYTE_SIZE_OF_DATA minus DELETED_DATA_BYTE_SIZE) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BI/010 |
| --- | --- |
| Test objective | Check that the IUT rejects the CREATE request of a <latest> resource as a direct child of a <container> resource with error “OPERATION_NOT_ALLOWED” |
| Reference | TS-0001 10.2.22, TS-0004 7.4.28.2.2 & 7.3.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> TARGET_RESOURCE_ADDRESS resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no name attribute and Content attributes representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/009 |
| --- | --- |
| Test objective | Check that the IUT accepts the RETRIEVE request of the latest <contentInstance> target to a <container> resource |
| Reference | TS-0001 10.2.22.1, TS-0004 7.4.28.2.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing a <contentInstance> resource containing attribute creationTime having the most rencent resource creation time } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing Representation of <contentInstance> } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/RET/BO/010 |
| --- | --- |
| Test objective | Check that the IUT rejects the RETRIEVE request of a <latest> resource target to a <container> resource that has no direct child <contentInstance> resources. |
| Reference | TS-0001 10.2.22.1, TS-0004 7.4.28.2.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing no direct child <contentInstance> resources } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BI/011 |
| --- | --- |
| Test objective | Check that the IUT rejects the UPDATE request of a <latest> resource as a direct child of a <container> resource with error “OPERATION_NOT_ALLOWED” |
| Reference | TS-0001 10.2.22, TS-0004 7.4.28.2.4 & 7.3.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing a <contentInstance> resource containing attribute creationTime set to the latest time } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no name attribute and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/DEL/BV/002 |
| --- | --- |
| Test objective | Check that the IUT accepts the DELETE request of the latest <contentInstance> resource target to a <container> resource |
| Reference | TS-0001 10.2.22.2, TS-0004 7.4.28.2.5 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing a latest <contentInstance> resource TARGET_RESOURCE_ADDRESS containing currentNrOfInstances set to NUMBER_OF_INSTANCES and currentByteSize set to BYTE_SIZE_OF_DATA } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (DELETED) and Contribute attribute containing currentNrOfInstances set to value (NUMBER_OF_INSTANCES – 1) and currentByteSize set to value (BYTE_SIZE_OF_DATA minus DELETED_DATA_BYTE_SIZE) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/DEL/BO/003 |
| --- | --- |
| Test objective | Check that the IUT rejects the DELETE request of a <latest> resource in a <container> resource that has no direct child <contentInstance> resources. |
| Reference | TS-0001 10.2.22.2, TS-0004 7.4.28.2.5 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing no <contentInstance> resources } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a DELETE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BI/011 |
| --- | --- |
| Test objective | Check that the IUT rejects the CREATE request of a <oldest> resource as a direct child of a <container> resource with error “OPERATION_NOT_ALLOWED” |
| Reference | TS-0001 10.2.23, TS-0004 7.4.29.2.2 & 7.3.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> TARGET_RESOURCE_ADDRESS resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource-Type set to A_RESOURCE_TYPE_VALUE and no name attribute and Content attributes representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/011 |
| --- | --- |
| Test objective | Check that the IUT accepts the RETRIEVE request of the oldest <contentInstance> target to a <container> resource |
| Reference | TS-0001 10.2.23.1, TS-0004 7.4.29.2.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing <contentInstance> resource(s) } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing Representation of <contentInstance> } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/RET/BO/012 |
| --- | --- |
| Test objective | Check that the IUT rejects the RETRIEVE request of a <oldest> resource target to a <container> resource that has no direct child <contentInstance> resources. |
| Reference | TS-0001 10.2.23.1, TS-0004 7.4.29.2.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing no direct child <contentInstance> resources } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/UPD/BI/012 |
| --- | --- |
| Test objective | Check that the IUT rejects the UPDATE request of a <oldest> resource as a direct child of a <container> resource with error “OPERATION_NOT_ALLOWED” |
| Reference | TS-0001 10.2.23, TS-0004 7.4.29.2.4 & 7.3.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing <contentInstance> resource(s) } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no name attribute and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/DEL/BV/004 |
| --- | --- |
| Test objective | Check that the IUT accepts the DELETE request of the oldest <contentInstance> resource target to a <container> resource |
| Reference | TS-0001 10.2.23.2, TS-0004 7.4.29.2.5 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing a latest <contentInstance> resource TARGET_RESOURCE_ADDRESS containing currentNrOfInstances set to NUMBER_OF_INSTANCES and currentByteSize set to BYTE_SIZE_OF_DATA } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a DELETE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2004 (DELETED) and Contribute attribute containing currentNrOfInstances set to value (NUMBER_OF_INSTANCES – 1) and currentByteSize set to value (BYTE_SIZE_OF_DATA minus DELETED_DATA_BYTE_SIZE) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/DMR/DEL/BO/005 |
| --- | --- |
| Test objective | Check that the IUT rejects the DELETE request of a <oldest> resource in a <container> resource that has no direct child <contentInstance> resources. |
| Reference | TS-0001 10.2.23.2, TS-0004 7.4.29.2.5 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a <container> resource containing no <contentInstance> resources } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

## -----------------------End of change 1--------------------------------------------

# Comments

REQ-0001-09017

REQ-0001-09348

REQ-0001-09349

REQ-0001-10115

To check that the IUT deletes the oldest <contentInstance> resource when the newly created <contentInstance> under the targeted container results in the number of <contentInstance> resources exceeds the field value set in attribute maxNrOfInstances in parent <container> resource.

TP/oneM2M/CSE/DMR/CRE/BV/005

REQ-0001-10117

To check that the  IUT rejects the UPDATE request to an existing <contentInstance>

MAPPING TO REQ-0004-07096

REQ-0001-10118

REQ-0001-10127

To check that the IUT responds with error when receiving  a <latest>  RETRIEVE request to a <container> resource that has no direct <contentInstance> resources created.

REQ-0001-10128

To check that the IUT responds with error when receiving  a <latest>  DELETE request to a <container> resource that has no direct <contentInstance> resources created.

REQ-0001-10128

To check that the IUT points the <latest> resource to the latest direct child <contentInstance> resource in a <container> resource after a <latest> resource in that <container> is deleted successfully.

REQ-0001-10129

To check that the IUT responds with error when receiving  a <oldest>  RETRIEVE request to a <container> resource that has no direct <contentInstance> resources created.

REQ-0001-10130

To check that the IUT responds with error when receiving  a <oldest>  DELETE request to a <container> resource that has no direct <contentInstance> resources created.

REQ-0001-10130

To check that the IUT points the <oldest> resource to the oldest direct child <contentInstance> resource in a <container> resource after a <oldest> resource in that <container> is deleted successfully.

REQ-0004-07085

To check that the IUT rejects the CREATE request of <container> resource when the RW ATTRIBUTE is provided with an invalid value

RW ATTRIBUTE:

- MaxNrOfInstances REF: 7.4.7.1

- MaxByteSize

- maxInstanceAge

REQ-0004-07085

To check that the IUT assigns a default value to RW ATTRIBUTE that is contained in the response of a <container> CREATE request where no RW ATTRIBUTE is provided. (the response contains the assigned attribute value)

RW ATTRIBUTE:

- MaxNrOfInstances REF: 7.4.7.1

- MaxByteSize

- maxInstanceAge

the local policy???

REQ-0004-07085

Map to that the  IUT responds with the assigned value of ATTRIBUTE  to the originator

REQ-0004-07094

REQ-0004-07094

To check that the IUT responds with error when the newly created <contentInstance> results in the field value set in RW ATTRIBUTE (currentNrOfInstances and/or attribute currentByteSize) exceeds the field value set in maxNrOfInstances in the parent <container> resource.

(Three cases)

- CurrentNrOfInstances

- currentByteSize

- CurrentNrOfInstances  and currentByteSize

REQ-0004-07094

To check that the IUT increaments the field value set in attribute stateTag of  a <container> resorce when <contentInstance> resource is created as the direct child of the parent <container>.

REFERENCE: 9.6.1.3.2-1

Direct Child resource creation and delete

REQ-0004-07096

To check that the IUT rejects the UPDATE request to an existing <contentInstance> resource with error “OPERATION_NOT_ALLOWED”

REFERENCE: TS-0004 7.3.2.1 (check the validity of the received request primitive)

REQ-0004-07097

To check that the IUT decreases the field value set in attribute currentNrOfInstances and currentByteSize of direct parent <container> respectively when a <contentInstance> resource is deleted successfully.

MAPPING TO REQ-0001-10118

REQ-0004-07184

To check that the IUT rejects the CREATE request of a <latest> resource as a direct child of a <container> resource with error “OPERATION_NOT_ALLOWED”

REFERENCE: TS-0004 7.3.2.1 (check the validity of the received request primitive)

REQ-0004-07185

To check the IUT accepts the latest <contentInstance> resource RETRIEVE request from a <container> resource.

REQ-0004-07185

To check that the IUT rejects the RETRIEVE request of a <latest> resource in a <container> resource that has no direct child <contentInstance> resources.

REQ-0004-07186

To check that the IUT rejects the UPDATE request of a <latest> resource as a direct child of a <container> resource with error “OPERATION_NOT_ALLOWED”

REQ-0004-07187

To check the IUT accepts the latest <contentInstance> resource DELETE request from a <container> resource.

REQ-0004-07187

To check that the IUT rejects the DELETE  request of a <latest> resource in a <container> resource that has no direct child <contentInstance> resources.

REQ-0004-07188

To check that the IUT rejects the CREATE  request of a <oldest> resource as a direct child of a <container> resource with error “OPERATION_NOT_ALLOWED”

REQ-0004-07189

To check the IUT accepts the oldest <contentInstance> resource RETRIEVE request from a <container> resource.

REQ-0004-07189

To check that the IUT rejects the RETRIEVE  request of a <oldest> resource in a <container> resource that has no direct child <contentInstance> resources.

REQ-0004-07190

To check that the IUT rejects the UPDATE  request of a <oldest> resource as a direct child of a <container> resource with error “OPERATION_NOT_ALLOWED”

REQ-0004-07191

To check the IUT accepts the oldest <contentInstance> resource DELETE request from a <container> resource.

REQ-0004-07191

To check that the IUT rejects the DELETE  request of a <oldest> resource in a <container> resource that has no direct child <contentInstance> resources.

The resource type value might be an any resource type value. No resource type value is defined for virtual resources

The resource type value might be an any resource type value. No resource type value is defined for virtual resources