| oneM2M Technical Specification |
| --- |
| Document Number | TS-0028-v0.0.1 |
| Document Name: | Security Test Suite Structure and Test Purposes |
| Date: | 2016-October-5 |
| Abstract: | The Security Test Suite Structure and Test Purposes document for conformance testing consists of: - Defining the test suite structure by grouping the test purposes according to different criteria; - Specifing test purposes for security conformance test. A test purpose is an informal description of the expected test behaviour. |
| Template Version:23 February 2015 (Dot not modify) |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC).

All rights reserved.

The copyright extends to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	4

2	References	4

2.1	Normative references	4

2.2	Informative references	4

3	Definitions, symbols and abbreviations	4

3.1	Definitions	4

3.2	Symbols	5

3.3	Abbreviations	5

3.4	Acronyms	5

4	Conventions	6

5	Prerequisites and Test Configurations	6

5.1	Test Configurations	6

6	Test Suite Structure (TSS)	6

6.1	Structure for oneM2M tests	6

6.2	Test groups	6

6.2.1 Functional Entity Groups	7

6.2.2 Common Services Functions Subgroups	7

6.3	Test Suite Structure (TSS) for oneM2M	7

7	Test Purposes (TP)	8

7.1	Introduction	8

7.1.1	TP definition conventions	8

7.1.2	TP Identifier naming conventions	8

7.1.3	Rules for the behaviour description	8

7.1.4	Source of TP definitions	8

7.1.5	ICS reference	8

7.2	Test Purposes for oneM2M	9

7.2.1	Group AE	9

7.2.2	Group CSE	9

7.2.2.1	Registration (REG)	9

7.2.2.2	Data Management and Repository (DMR)	13

7.2.2.3	Subscription and Notification (SUB)	36

7.2.2.4	Group Management (GMG)	39

7.2.2.5	Discovery (DIS)	47

7.2.2.5.1 Valid Behavioral Test Case	47

7.2.2.5.2 Inopportune Behavioral Test Cases	50

7.2.2.5.3 Invalid Behavioral Test Case	51

7.2.2.6 	Location (LOC)	52

7.2.2.6.1 Valid Behavioural Test Cases	52

7.2.2.6.2 Inopportune Behavioural Test Cases	53

7.2.2.6.3 Invalid Behavioural Test Case	54

Proforma copyright release text block	55

Annexes	55

Annex <A> Conformance Test Requirement	55

Annex <B>(Informative): TP template	57

Annex <y>: Bibliography	57

History	57

# 1	Scope

The present document …

EXAMPLE:	The present document provides the necessary adaptions to the endorsed document.

The Scope shall not contain requirements.

# 2	References

The following text block applies.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

Clause 2.1 only shall contain normative (essential) references which are cited in the document itself. These references have to be publicly available and in English.

The following referenced documents are necessary for the application of the present document.

Use the EX style, enclose the number in square brackets and separate it from the title with a tab (you may use sequence fields for automatically numbering references, see clause A.4: "Sequence numbering") (see example).

EXAMPLE:

[1]	 ETSI TR 102 473: "<Title>".

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

Use the EX style, add the letter "i" (for informative) before the number (which shall be in square brackets) and separate this from the title with a tab (you may use sequence fields for automatically numbering references).

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

# 3	Definitions, symbols and abbreviations

Delete from the above heading the word(s) which is/are not applicable.

## 3.1	Definitions

Clause numbering depends on applicability.

A definition shall not take the form of, or contain, a requirement.

The form of a definition shall be such that it can replace the term in context. Additional information shall be given only in the form of examples or notes (see below).

The terms and definitions shall be presented in alphabetical order.

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply:

Definition format

<defined term>: <definition>

If a definition is taken from an external source, use the format below where [N] identifies the external document which must be listed in Section 2 References.

<defined term>[N]: <definition>

example 1: text used to clarify abstract rules by applying them literally

NOTE:	This may contain additional information.

## 3.2	Symbols

Clause numbering depends on applicability.

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

Abbreviations should be ordered alphabetically.

Clause numbering depends on applicability.

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

Abbreviation format

<ABREVIATION1>	<Explanation>

<ABREVIATION2>	<Explanation>

<ABREVIATION3>	<Explanation>

## 3.4	Acronyms

Acronyms should be ordered alphabetically.

Clause numbering depends on applicability.

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

Acronym format

<ACRONYM1>	<Explanation>

<ACRONYM2>	<Explanation>

<ACRONYM3>	<Explanation>

# 4	Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	Prerequisites and Test Configurations

## 5.1	Test Configurations

# 6	Test Suite Structure (TSS)

## 6.1	Structure for oneM2M tests

## 6.2	Test groups

The test groups are organized in 2 levels. The first level defines the functional entity of oneM2M. The second level defines the common services functions which are represented in oneM2M security architecture.

### 6.2.1 Functional Entity Groups

The functional entity groups identify the types of entity which are specified in oneM2M functional architecture(TS-0001).

- AE

- CSE

### 6.2.2 Common Services Functions Subgroups

The common services functions subgroups identify the general procedures in each common services functions specified in oneM2M security architecture(TS-0003).

## 6.3	Test Suite Structure (TSS) for oneM2M

The Test Suite Structure (TSS) for oneM2M will be present as bellow:

- Group 1: AE(AE)

- Group 2: CSE(CSE)

# 7	Test Purposes (TP)

## 7.1	Introduction

### 7.1.1	TP definition conventions

The TP definition is constructed according to Test Suite Structure & Test Purposes(TSS&TP) in Testing Framework(TS-0015).

### 7.1.2	TP Identifier naming conventions

The identifier of the TP is constructed according to table 7.1.2.-1.

Table 7.1.2.-1: TP naming convention for oneM2M

| TP/<root>/<gr>/<sgr>/<xx>/<nnn> |
| --- |
| <root> = root | oneM2M | oneM2M |
| <gr> = group | AE | Application Entity |
|  | CSE | Common Services Entity |
| <sgr> = sub- group |  |  |
| <xx> = type of testing | BV | Valid Behaviour tests |
|  | BI | Invalid Behaviour tests |
| <nnn> = sequential number |  | 001 to 999 |

### 7.1.3	Rules for the behaviour description

### 7.1.4	Source of TP definitions

### 7.1.5	ICS reference

Editor note: the table 7.1.5.-1 and 7.1.5.-2 are for examples and are here for being referenced in the Table 7.1.5.-3: mnemonics for PICS reference. Table 7.1.5.-1 and 7.1.5.-2 should be included in the ICS TS-0017.

Table 7.1.5.-1: Node

| Item | Name of field | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | ASN (Application Service Node) | 6.1 | o.1 |  |
| 2 | ADN (Application Dedicated Node) | 6.1 | o.1 |  |
| 3 | IN (Infrastructure Node) | 6.1 | o.1 |  |
| 4 | MN (Middle Node) | 6.1 | o.1 |  |
| o.1: Exactly one item shall be supported |

Table 7.1.5.-2: Functional entity type

| Prerequisite: A.1 |
| --- |
| Item | Name of field | Reference | Status | Support |
| 1 | AE | 5.2.1 | c.1 |  |
| 2 | CSE | 5.2.1 | c.2 |  |
| c.1: If A.1-1 or A.1-2 then m else o c.2: If A.1-2 x else m |

Table 7.1.5.-3: Mnemonics for PICS reference

| Mnemonic | PICS item |
| --- | --- |
| PICS_AE | A.2/1 [PICS document] |
| PICS_CSE | A.2/2 [PICS document] |
| PICS_ASN | A.1/1 [PICS document] |
| PICS_ADN | A.1/2 [PICS document] |
| PICS_IN | A.1/3 [PICS document] |
| PICS_MN | A.1/4 [PICS document] |

## 7.2	Test Purposes for oneM2M

Editor Note: The following TPs contain some test variables (using upper-case and italic) which will be instantiated during test execution.

## 7.2.1	Group AE

## 7.2.2	Group CSE

| TP Id | TP/oneM2M/CSE/SEC/BI/007_03 |
| --- | --- |
| Test objective | Check that the IUT refuses any service related procedure before Security Association Establishment procedure (SAEP) between CSE and IN-CSE |
| Reference | TS-0003, 6.1.2.2.1 par. 2, 3 |
| Config Id | CF03 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { The IUT being in the "initial state" and the IUT having registered the CSE with CSE_ID set to CSE2 and Security Association Establishment procedure set to None } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION request from CSE containing From set to CSE2 } | IUT  CSE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  CSE |

| TP Id | Reference | OPERATION |
| --- | --- | --- |
| TP/oneM2M/CSE/SEC/BI/007_03_01 | TS-0001 10.1.1 | CREATE |
| TP/oneM2M/CSE/SEC/BI/007_03_02 | TS-0001 10.1.2 | RETRIEVE |
| TP/oneM2M/CSE/SEC/BI/007_03_03 | TS-0001 10.1.3 | UPDATE |
| TP/oneM2M/CSE/SEC/BI/007_03_04 | TS-0001 10.1.4 | DELETE |
| TP/oneM2M/CSE/SEC/BI/007_03_05 | TS-0001 10.1.5 | NOTIFY |

| TP Id | TP/oneM2M/CSE/SEC/BI/007_04 |
| --- | --- |
| Test objective | Check that the IUT refuses any service related procedure before Security Association Establishment procedure (SAEP) between AE and IN-CSE |
| Reference | TS-0003, 6.1.2.2.1 par. 2, 3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { The IUT being in the "initial state" and the IUT having registered the AE with AE_ID set to AE1 and Security Association Establishment procedure set to None } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION request from AE containing From set to AE1 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

| TP Id | Reference | OPERATION |
| --- | --- | --- |
| TP/oneM2M/CSE/SEC/BI/007_04_01 | TS-0001 10.1.1 | CREATE |
| TP/oneM2M/CSE/SEC/BI/007_04_02 | TS-0001 10.1.2 | RETRIEVE |
| TP/oneM2M/CSE/SEC/BI/007_04_03 | TS-0001 10.1.3 | UPDATE |
| TP/oneM2M/CSE/SEC/BI/007_04_04 | TS-0001 10.1.4 | DELETE |
| TP/oneM2M/CSE/SEC/BI/007_04_05 | TS-0001 10.1.5 | NOTIFY |

| TP Id | TP/oneM2M/CSE/SEC/BI/008_02 |
| --- | --- |
| Test objective | Check that the IUT refuses any service related procedure before Security Association Establishment procedure (SAEP) between IN-CSE and IN-CSE |
| Reference | TS-0003, 6.1.2.2.1 par. 2, 4 |
| Config Id | CF03 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { The IUT being in the "initial state" and the IUT having registered the CSE with CSE_ID set to IN_CSE3 and Security Association Establishment procedure set to None } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION request from CSE containing From set to IN_CSE3 } | IUT  IN-CSE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  IN-CSE |

| TP Id | Reference | OPERATION |
| --- | --- | --- |
| TP/oneM2M/CSE/SEC/BI/008_02_01 | TS-0001 10.1.1 | CREATE |
| TP/oneM2M/CSE/SEC/BI/008_02_02 | TS-0001 10.1.2 | RETRIEVE |
| TP/oneM2M/CSE/SEC/BI/008_02_03 | TS-0001 10.1.3 | UPDATE |
| TP/oneM2M/CSE/SEC/BI/008_02_04 | TS-0001 10.1.4 | DELETE |
| TP/oneM2M/CSE/SEC/BI/008_02_05 | TS-0001 10.1.5 | NOTIFY |

| TP Id | TP/oneM2M/CSE/SEC/BI/007_01 |
| --- | --- |
| Test objective | Check that the IUT trusts a raw public key certificate with a public key identifier for the public key in the certificate and accepts service related procedures only if the SAEP (Certificate based) is established between AE and IN-CSE |
| Reference | TS-0003, 6.1.2.2.1 par. 2, 3 ; 8.1.2.4 - entity B, case "raw public key" |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { The IUT being in the "initial state" and the IUT having registered the AE with AE_ID set to AE1 and Security Association Establishment procedure set to Certificate } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION request from AE containing From set to AE1 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) } | IUT  AE |

| TP Id | Reference | OPERATION |
| --- | --- | --- |
| TP/oneM2M/CSE/SEC/BI/007_01_01 | TS-0001 10.1.1 | CREATE |
| TP/oneM2M/CSE/SEC/BI/007_01_02 | TS-0001 10.1.2 | RETRIEVE |
| TP/oneM2M/CSE/SEC/BI/007_01_03 | TS-0001 10.1.3 | UPDATE |
| TP/oneM2M/CSE/SEC/BI/007_01_04 | TS-0001 10.1.4 | DELETE |
| TP/oneM2M/CSE/SEC/BI/007_01_05 | TS-0001 10.1.5 | NOTIFY |

| TP Id | TP/oneM2M/CSE/SEC/BI/007_02 |
| --- | --- |
| Test objective | Check that the IUT accepts service related procedures only if the SAEP is established between CSE and IN-CSE |
| Reference | TS-0003, 6.1.2.2.1 par. 2, 3 |
| Config Id | CF03 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { The IUT being in the "initial state" and the IUT having registered the CSE with CSE_ID set to CSE2 and Security Association Establishment procedure set to Certificate } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION request from CSE containing From set to CSE2 } | IUT  CSE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) } | IUT  CSE |

| TP Id | Reference | OPERATION |
| --- | --- | --- |
| TP/oneM2M/CSE/SEC/BI/007_02_01 | TS-0001 10.1.1 | CREATE |
| TP/oneM2M/CSE/SEC/BI/007_02_02 | TS-0001 10.1.2 | RETRIEVE |
| TP/oneM2M/CSE/SEC/BI/007_02_03 | TS-0001 10.1.3 | UPDATE |
| TP/oneM2M/CSE/SEC/BI/007_02_04 | TS-0001 10.1.4 | DELETE |
| TP/oneM2M/CSE/SEC/BI/007_02_05 | TS-0001 10.1.5 | NOTIFY |

| TP Id | TP/oneM2M/CSE/SEC/BI/008_01 |
| --- | --- |
| Test objective | Check that the IUT accepts service related procedures only if the SAEP is established between IN-CSE and IN-CSE |
| Reference | TS-0003, 6.1.2.2.1 par. 2, 4 |
| Config Id | CF03 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { The IUT being in the "initial state" and the IUT having registered the CSE with CSE_ID set to IN_CSE3 and Security Association Establishment procedure set to Certificate } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION request from CSE containing From set to IN_CSE3 } | IUT  IN-CSE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) } | IUT  IN-CSE |

| TP Id | Reference | OPERATION |
| --- | --- | --- |
| TP/oneM2M/CSE/SEC/BI/008_02_01 | TS-0001 10.1.1 | CREATE |
| TP/oneM2M/CSE/SEC/BI/008_02_02 | TS-0001 10.1.2 | RETRIEVE |
| TP/oneM2M/CSE/SEC/BI/008_02_03 | TS-0001 10.1.3 | UPDATE |
| TP/oneM2M/CSE/SEC/BI/008_02_04 | TS-0001 10.1.4 | DELETE |
| TP/oneM2M/CSE/SEC/BI/008_02_05 | TS-0001 10.1.5 | NOTIFY |

| TP Id | TP/oneM2M/CSE/SEC/BI/022_02 |
| --- | --- |
| Test objective | Check that the IUT responds the originator with an error when the originator sends a request including a different AE identifier |
| Reference | TS-0003, 7.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { The IUT being in the "initial state" and the IUT having registered the AE with AE_ID set to AE1 and Security Association Establishment procedure set to None } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION request from AE containing From set to AE3 } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

| TP Id | Reference | OPERATION |
| --- | --- | --- |
| TP/oneM2M/CSE/SEC/BI/022_02_01 | TS-0001 10.1.1 | CREATE |
| TP/oneM2M/CSE/SEC/BI/022_02_02 | TS-0001 10.1.2 | RETRIEVE |
| TP/oneM2M/CSE/SEC/BI/022_02_03 | TS-0001 10.1.3 | UPDATE |
| TP/oneM2M/CSE/SEC/BI/022_02_04 | TS-0001 10.1.4 | DELETE |
| TP/oneM2M/CSE/SEC/BI/022_02_05 | TS-0001 10.1.5 | NOTIFY |

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A> Conformance Test Requirement

A.1	MQTT Protocol Conformance Test Requirement

| Test Items | TS Chapter | Obligation | Condition for Optional Item | Checking point | Fail condition |
| --- | --- | --- | --- | --- | --- |
| Commonly Repeated Items | TS-0010, Sec5.1 | Mandatory |  | "QoS=1" | Fail when QoS is other than “1” |
|  | TS-0010, Sec5.1 | Mandatory |  | "Retain" flag set as "0" | Fail if DUT sends with “Retain” flag=1 |
| Connection Items | Connect | TS-0010, Sec6.3 | Mandatory |  | Prefix A:: or C:: is added to the ID | Fail if Prefix A:: or C:: are not added to the ID |
|  |  | TS-0010, Sec6.3 | Mandatory |  | if Clean session (ex: Retain) flag is set to “False” in CONNECT | Fail when clean session is “True” when DUT want to be connected |
|  |  | TS-0010, Sec6.3 | Mandatory |  | if “Will Flag” is not set in CONNECT | Fail when will flag is enabled |
|  | Disconnect | TS-0010, Sec6.3 | Mandatory |  | if Clean session (ex: Retain) flag is set to “True” in CONNECT | Fail when clean session is “False” when DUT want to be disconnected |
| Subscription Items | TS-0010, Sec5.1 | Mandatory |  | if the message is set to Durable | Fail is the message is not Durable |
|  | TS-0010, Sec6.4.4 | Conditional | (for Initial Registration) when Originator doesn’t knows it’s ID | if DUT’s Initial ID assigning /oneM2M/reg_req/<originator>/<receiver> oneM2M/reg_resp/<originator>/<receiver> | Fail if DUT's ID assigning is other than this |
| Publish Item | TS-0010, Figure 6.4.5-2 | Conditional | when Originator knows it’s ID | if DUT’s Initial ID assigning oneM2M/req/<Originator>/<Receiver> | Fail if DUT's ID assigning is other than this |
|  | TS-0010, Figure 6.4.5-2 | Conditional | When Originator uses wild card | if DUT’s Initial ID assigning oneM2M/req/+/<Receiver> | Fail if DUT's ID assigning is other than this |
|  | MQTT v3.1.1 | Conditional |  | if the has proper Primitive contents (“op”, “fr”, “to”, “ri”, “pc”, “ty”) | Fail if any of primitive contents feature wrong |
| Reception Item | TS-0010, Figure 6.4.5-2 | Conditional | when Originator knows it’s ID | if DUT’s Initial ID assigning oneM2M/resp/<Originator>/<Receiver> | Fail if DUT's ID assigning is other than this |
|  | TS-0010, Figure 6.4.5-2 | Conditional | When Originator uses wild card | if DUT’s Initial ID assigning oneM2M/resp/<Originator>/+ | Fail if DUT's ID assigning is other than this |
|  | TS-0010, Figure 6.4.5-2 | Conditional |  | server Delete received contents properly not storing data | Fail if Receiver stores message |
|  | TS-0010, Figure 6.4.5-2 | Conditional |  | If the receiver sends PubACK when receives messages | Fail if the receiver doesn’t send PubACK |
|  | MQTT v3.1.1 | Mandatory |  | if the has proper Primitive contents (“op”, “fr”, “to”, “ri”, “pc”, “ty”) | Fail if any of primitive contents feature wrong |

<PAGE BREAK>

Annex <B>(Informative): TP template

| TP Id |  |
| --- | --- |
| Test objective |  |
| Reference |  |
| Config Id |  |
| PICS Selection |  |
| Initial conditions |  |
| Expected behaviour | Test events | Direction |
|  | when { } | IUT ( AE |
|  | then { } | IUT ( AE |

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

Publication history

| Draft history (to be removed on publication) |
| --- |
| V.0.0.1 | 21 September 2016 | Initial Draft Version (based on TS0018) |

# Text boxes

Figure 1. Test configuration 1 (CF01)

IUT

TEST SYSTEM

AE

CSE

Mca

Mcc

IUT

TEST SYSTEM

AE

CSE

Mca

CSE

Figure 2. Test configuration 2 (CF02)

Figure 3. Test configuration 3 (CF03)

IUT

TEST SYSTEM

CSE

CSE

Mcc