| CHANGE REQUEST |
| --- |
| Meeting:* | TST 25.1 |
| Source:* | Convida |
| Date:* | 2016-11-07 |
| Contact:* | Bob Flynn (Bob.Flynn@interdigital.com) Shruti Asmita (Shruti.Asmita@radisys.com) |
| Reason for Change/s:* | Add the specification of the flexContainer to the test cases |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0013-Interoperability_Testing-V2_0_0 |
| Clauses/Sub Clauses* | 8.1.14 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution aims at adding flexContainer validation scenarios which include create, retrieve, update, delete, subscription-notification and discovery call flows against a custom XSD already known to application which it sends to CSE at the time of flexContainer create in containerDefinition attribute.

## ----------------------- Start of change 1 -----------------------

### 8.1.14	FlexContainer Management

#### 8.1.14.1	FlexContainer Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_49 |
| Objective: | AE creates a flexcontainer resource in Registrar CSE via a flexcontainer Create Request |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.29.1 TS-0004 [2], clause 7.4.37.2.1 |
| Pre-test conditions: | AE has created an application resource <AE> on Registrar CSE |
| Prerequsites: | Custom XSD CDT-allJoynProperty-v2_7_0 contains information about all custom attributes and is known to AE. AE sends the details of custom XSD in containerDefinition attribute with flexContainer create request. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE sends a request to create a <flexContainer> |
| 2 | Mca | PRO Check Primitive | op = 1 (Create) to = {CSEBaseName} fr = AE-ID rqi = (token-string) ty = 28 (flexContainer) pc = Serialized representation of <flexContainer> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Request-Target:{CSEBaseName} Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; ty=28 or application/vnd.onem2m-res+json; ty=28 Message-body: Serialized representation of <flexContainer> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/URI of <AE> resource Content-type: application/vnd.onem2m-res+xml or application/vnd.onem2m res+json oneM2M-TY: 28 oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: Serialized representation of <flexContainer> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/< AE-ID>/<Registrar CSE-ID>" Payload: op = 1 (Create) to = {CSEBaseName}/URI of <AE> resource fr = AE-ID rqi = (token-string) ty = 28 (flexContainer) pc = Serialized representation of <flexContainer> resource |
| 3 |  | IOP Check | Check if possible that the <flexContainer> resource is created in Registrar CSE. |
| 4 | Mca | PRO Check Primitive | rsc = 2001 (CREATED) rqi = (token-string) same as received in request message pc = Serialized representation of <flexContainer> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 201 (Created) X-M2M-RSC: 2001 X-M2M-RI: (token-string) same as received in request message Content-Location: URI of the created resource. Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <flexContainer> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.01 oneM2M-RSC: 2001 oneM2M-RQI: (token-string) same as received in request message Location-Path: URI of the created resource Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of <flexContainer> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rsc = 2001 (CREATED) rqi = (token-string) same as received in request message pc = Serialized representation of <flexContainer> resource |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.14.2	FlexContainer Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_50 |
| Objective: | AE retrieves information of a flexContainer resource via a flexContainer Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.29.2 TS-0004 [2], clause 7.4.37.2.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a flexContainer resource <flexContainer> on Registrar CSE |
| Prerequsites: | Custom XSD CDT-allJoynProperty-v2_7_0 contains information about all custom attributes and is known to AE. AE has already sent the details of custom XSD in containerDefinition attribute with flexContainer create request. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Retrieve Request for a <flexContainer> |
| 2 | Mca | PRO Check Primitive | op = 2 (Retrieve) to = {CSEBaseName}/URI of <flexContainer> resource fr = AE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}/URI of <flexContainer> resource Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/URI of <flexContainer> resource oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/< AE-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName}/URI of <flexContainer> resource fr = AE-ID rqi = (token-string) pc = empty |
| 3 | Mca | PRO Check Primitive | rsc =2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of <flexContainer> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <flexContainer> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 (OK) oneM2M-RSC: 2000(OK) oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of <flexContainer> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rsc 2000(OK) rqi = (token-string) same as received in request message pc = Serialized representation of <flexContainer> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.14.3	FlexContainer Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_51 |
| Objective: | AE updates attribute in application resource via a flexContainer Update Request |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.29.3 TS-0004 [2], clause 7.4.37.2.3 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a flexContainer resource <flexContainer> on Registrar CSE |
| Prerequsites: | Custom XSD CDT-allJoynProperty-v2_7_0 contains information about all custom attributes and is known to AE. AE has already sent the details of custom XSD in containerDefinition attribute with flexContainer create request. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a flexContainer Update Request to update the any customAttribute of the resource. |
| 2 | Mca | PRO Check Primitive | op = 3 (Update) to = {CSEBaseName}/URI of <flexContainer> resource fr = AE-ID rqi = (token-string) pc = Serialized representation of updated <flexContainer> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = PUT Request-Target:{CSEBaseName}/URI of <flexContainer> resource Host : IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of updated <flexContainer> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.03 (PUT) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/URI of <container> resource oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of updated <flexContainer> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/ req /< AE-ID>/<Registrar CSE-ID>" Payload: op = 3 (Update) to = {CSEBaseName}/URI of <flexContainer> resource fr = AE-ID rqi = (token-string) pc = Serialized representation of updated <flexContainer> resource |
| 3 |  | IOP Check | Check if possible that the < flexContainer > resource is updated in Registrar CSE. |
| 4 | Mca | PRO Check Primitive | rsc = 2004 (Updated) rqi = (token-string) same as received in request message pc = Serialized representation of <flexContainer> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 (Ok) X-M2M-RSC: 2004 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <flexContainer> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.04 oneM2M-RSC: 2004 oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload : Serialized representation of <flexContainer> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rsc = 2004 (Updated) rqi = (token-string) same as received in request message pc = Serialized representation of modified <flexContainer> resource |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.14.4	FlexContainer Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_52 |
| Objective: | AE deletes a specific container resource via a container Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.29.4 TS-0004 [2], clause 7.4.37.2.4 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a flexContainer resource <flexContainer> on Registrar CSE |
| Prerequsites: | Custom XSD CDT-allJoynProperty-v2_7_0 contains information about all custom attributes and is known to AE. AE has already sent the details of custom XSD in containerDefinition attribute with flexContainer create request. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a flexContainer Delete Request |
| 2 | Mca | PRO Check Primitive | op = 4 (Delete) to = {CSEBaseName}/URI of <flexContainer> resource fr = AE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = DELETE Request-Target: {CSEBaseName}/URI of <flexContainer> resource Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-body: Empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.04 (DELETE) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/URI of <flexContainer> resource oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/< AE-ID>/<Registrar CSE-ID>" Payload: op = 4 (Delete) to = {CSEBaseName}/URI of <flexContainer> resource fr = AE-ID rqi = (token-string) pc = empty |
| 3 |  | IOP Check | Check if possible that the <flexContainer> resource is deleted in Registrar CSE. |
| 4 | Mca | PRO Check Primitive | rsc = 2002 (DELETED) rqi = (token-string) same as received in request message pc = empty |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2002 X-M2M-RI: (token-string) same as received in request message Message-body: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.02 oneM2M-RSC: 2002(DELETED) oneM2M-RQI: (token-string) same as received in request message Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rsc = 2002(DELETED) rqi = (token-string) same as received in request message |
| 5 |  | IOP Check | Check if possible that the <flexContainer> resource has been removed in Registrar CSE. |
| 6 |  | IOP Check | AE indicates successful operation. |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.14.5	Notification Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_53 |
| Objective: | AE receives a notification request on flexContainer update from the HOST CSE |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.1.5 TS-0004 [2], clause 7.4.1 |
| Pre-test conditions: | AE1 has created an application resource <AE> on Registrar CSE AE1 has created a flexContainer resource <flexContainer> on Registrar CSE AE1 has created a <subscription> as a child resource of a <flexContainer> AE2 has created an application resource <AE> on Registrar CSE AE2 has permisions to UPDATE customAttributes of flexContainer. |
| Prerequsites: | Custom XSD CDT-allJoynProperty-v2_7_0 contains information about all custom attributes and is known to AE1. AE1 has already sent the details of custom XSD in containerDefinition attribute with flexContainer create request. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE2 is requested to send a update request to <flexContainer> for updating customAttribute. This triggers or causes the HOST CSE to send a notification to AE1. |
| 2 | Check Mca | PRO Check Primitive | op = 5 (Notify) to = notificationURI of subscription resource from = Registrar CSE-ID rqi = (token-string) pc = Serialized representation of Notification data object |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Request-Target: notificationURI of subscription resource Host: IP address or FQDN of notificationURI X-M2M-RI: (token-string) X-M2M-Origin: {CSEBaseName} Content-Type: application/vnd.onem2m-ntfy+xml; or application/vnd.onem2m-ntfy+json; Message-body: Serialized Representation of Notification data object |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: notificationURI host Uri-Port: notificationURI port Uri-Path: AE1 AE-ID oneM2M-FR: Registrar CSE-ID oneM2M-RQI: (token-string) Content-Format: application/vnd.onem2m-ntfy+xml; or application/vnd.onem2m-ntfy+json; Payload: Serialized Representation of Notification data object |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<Registrar CSE-ID>/<AE-ID>" Payload: op = 5 (Notify) to = notificationURI of subscription resource fr = Registrar CSE-ID rqi = (token-string) pc = empty |
| 3 |  | IOP Check | Check if the notification representation |
| 4 | Check Mca | PRO Check Primitive | Sent response contains rsc = 2000 (OK) rqi = (token-string) same as received in request message |
|  |  | PRO Check HTTP | Sent response contains: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message |
|  |  | PRO Check CoAP | Sent response contains: Response Code = 2.01 oneM2M-RSC: 2000(OK) oneM2M-RQI: (token-string) same as received in request message |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<Registrar CSE-ID>/<AE-ID>" Payload: to = Registrar CSE-ID fr = AE1 AE-ID rsc = 2000(OK) rqi = (token-string) same as received in request message |
| 5 |  | IOP Check | AE1 indicates notification received |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.14.6	Discovery with attribute filter criteria over customAttributes

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_54 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using attribute filter criteria which has a customAttribute name and value assigned to it. |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.6 TS-0004 [2], clause 7.3.3.14 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a flexContainer resource <flexContainer> on Registrar CSE with customAttribute set to a specific value “x”, created on Registrar CSE. |
| Prerequsites: | Custom XSD CDT-allJoynProperty-v2_7_0 contains information about all custom attributes and is known to AE. AE has already sent the details of custom XSD in containerDefinition attribute with flexContainer create request. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request in order to discover the <Container> resource using attribute filter criteria |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE-ID rqi = (token-string) fu=1 atr=<nm>,<val> pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&<nm>=<val> Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: atr=<nm>,<val> Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = Registree CSE-ID rqi = (token-string) fu = 1 atr=<nm>,<val> pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the addresse of the <flexContainer> address |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of the <flexContainer> address |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of the <flexContainer> address |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the address of the <flexContainer> address |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?