| CHANGE REQUEST |
| --- |
| Meeting:* | TST #25.1 |
| Source:* | InterDigital |
| Date:* | 2016-11-07 |
| Contact:* | Bob Flynn (flynn.bob@convidawireless.com) |
| Reason for Change/s:* | bug fixes |
| CR against: Release* | Rel-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0013-Interoperability_Testing-V1_2_0 |
| Clauses/Sub Clauses* | 8.1.6.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

## From TS-0009 v1_7_0

#### 6.2.2.2 Query component

The query component (e.g. query-string) may include  the optional primitive parameters listed in Table 6.2.2-1 compliant with RFC 7230 [1]. Each applicable request primitive parameters and elements of Filter Criteria parameter shown in Table 6.2.2-1 shall be represented as pair of field-name and value in query-string. Multiple such pairs shall be concatenated with an ampersand ‘&’ character used as separator between two pairs.

Table 6.2.2-1 also shows the permitted multiplicity of occurrence of field names in the query-string. Multiplicity ‘0..1’ means that a  parameter  is optional and can occur at most once. Parameters with multiplicity ‘0..n’, may occur multiple times in the query-string in the form of  <query field name> = value.  For example, if the resourceType element of the Filter Criteria parameter is represented by a list of 3 values ‘2 3 4’ (see clause 6.3.4.7 in TS-0004 [3]), it would be mapped to ty=2+3+4 in the query-string. At the receiver side, this query string can be reverted back into the list type of representation. The same representation shall be applied for multiple occurrences of contentType and labels elements.

#### m2m:filterCriteria

Used indirectly in the <request> resource and for the  Filter Criteria parameter in a request.

Table 6.3.5.8-1: Type Definition of m2m:filterCriteria

| Element Path | Element Data Type | Mutiplicity | Note |
| --- | --- | --- | --- |
| createdBefore | m2m:timestamp | 0..1 |  |
| createdAfter | m2m:timestamp | 0..1 |  |
| modifiedSince | m2m:timestamp | 0..1 |  |
| unmodifiedSince | m2m:timestamp | 0..1 |  |
| stateTagSmaller | xs:positiveInteger | 0..1 |  |
| stateTagBigger | xs:nonNegativeInteger | 0..1 |  |
| expireBefore | m2m:timestamp | 0..1 |  |
| expireAfter | m2m:timestamp | 0..1 |  |
| labels | m2m:labels | 0..1 |  |
| resourceType | list of m2m:resourceType | 0..1 |  |
| sizeAbove | xs:nonNegativeInteger | 0..1 |  |
| sizeBelow | xs:positiveInteger | 0..1 |  |
| contentType | m2m:typeOfContent | 0..n |  |
| attribute | m2m:attribute | 0..n |  |
| filterUsage | m2m:filterUsage | 0..1 |  |
| limit | xs:nonNegativeInteger | 0..1 |  |

From Table 6.3.3-1: oneM2M Simple Data Types

| m2m:labels | list of xs:token | printers networkwifi1 home_energy | A list of tokens used as keys for discovering resources (searching wifi connected printer from vendor 1) |
| --- | --- | --- | --- |

## ----------------------- Start of change 1 -----------------------

#### 8.1.6.4	Discovery with multiple filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_21 |
| Objective: | AE discovers accessible resources residing in Registrar CSE using multiple Filter Criteria |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.6 TS-0004 [2], clause 7.2.3.13 |
| Pre-test conditions: | Two <Container> resources with labels "key1" and "key2" are created in Registrar CSE. A <Group> resources with labels "key1" and "key2" is created in Registrar CSE. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Discovery request in order to discover specific resources located in Registrar CSE using multiple filter criteria (label, resource type and limit) |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE-ID rqi = (token-string) fu=1 lbl=key1 lbl=key2 ty=3 lim=1 pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}?fu=1&lbl=key1+key2&ty=3&lim=1 Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Uri-Query: fu=1 Uri-Query: lbl=key1 Uri-Query: lbl=key2 Uri-Query: ty=3 Uri-Query: lim=1 Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName} fr = AE-ID rqi = (token-string) fu = 1 lbl=key1 key2 ty=3 lim=1 pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the address of one of the <Container> resources |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of data object containing the address of one of the <Container> resources |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of data object containing the address of one of the <Container> resources |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = Registree CSE-ID fr = Registrar CSE-ID rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing the address of one of the <Container> resources |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?