| CHANGE REQUEST |
| --- |
| Meeting:* | TST 26 |
| Source:* | Ting Martin MIAO, KETI, novamartin@keti.re.kr |
| Date:* | 2016-12-03 |
| Contact:* | Ting Martin MIAO, KETI, novamartin@keti.re.kr |
| Reason for Change/s:* | Reflect update found during IoP3 |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 ver 0.1.4 |
| Clauses/Sub Clauses* | 7.2.2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Several test purposes in Section 7.2.2.2 of TS-0018 v1.4 are designed to test RETRIEVE operation with parameter Result Content as following:

TP/oneM2M/CSE/DMR/BV/001: ResultContent = 0 (Nothing)

TP/oneM2M/CSE/DMR/BV/003: ResultContent = 2 (hierarchical address)

TP/oneM2M/CSE/DMR/BV/004: ResultContent = 3 (attributes and hierarchichal address)

However, TS-0001 defines parameter ResultContent is not valid for RETRIEVE operation when ResultContent is set to either 0, 2 or 3.

We propose to remove those three test purposes and add three more test purposes to DMR CREATE subgroup.

### -----------------------Start of change 1-------------------------------------------

## Data Management and Repository (DMR)

Update test purpose TP/oneM2M/CSE/DMR/BV/001 and delete test purpose TP/oneM2M/CSE/DMR/BV/003 and TP/oneM2M/CSE/DMR/BV/004: ResultContent = 3 (attributes and hierarchichal address) from Section 7.2.2.2.

### Valid Behavior Test of Result Content for RETRIEVE operation

### Update TP/oneM2M/CSE/DMR/BV/001:

| TP Id | TP/oneM2M/CSE/DMR/BV/001 |
| --- | --- |
| Test objective | Check that the IUT rejects a RETRIEVE request target to TARGET_RESOURCE_ADDRESS resource when the ResultContent set to RESULT_CONTENT |
| Reference | TS-0001 8.1.2, TS-0004 7.3.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to A_RESULT_CONTENT_VALUE } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4000 (BAD_REQUEST) and no Content attribute } | IUT  AE |

| TP ID | Reference | RESULT CONTENT |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/BV/001_01 | TS-0004 6.3.4.2.7 | 0 (Nothing) |
| TP/oneM2M/CSE/DMR/BV/001_02 |  | 2 (hierarchical address) |
| TP/oneM2M/CSE/DMR/BV/001_03 |  | 3 (attributes and hierarchichal address) |

Remove TP/oneM2M/CSE/DMR/BV/003 and TP/oneM2M/CSE/DMR/BV/004:

EDITOR’S NOTE: Test cases in TS-0019 that are mapped with those three test purposes (TP/oneM2M/CSE/DMR/BV/001, TP/oneM2M/CSE/DMR/BV/003, and TP/oneM2M/CSE/DMR/BV/004) have to be removed.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## Data Management and Repository (DMR)

Add three new test purposes designed to test parameter ResultContent value 0, 2, and 3 for CREATE operation, respectively.

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/012 |
| --- | --- |
| Test objective | Check that the IUT returns successfully an empty content of TARGET_RESOURCE_ADDRESS resource when the ResultContent set to 0 (Nothing) |
| Reference | TS-0001 8.1.2, 8.1.3 &10.1.1.1, TS-0004 6.3.4.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource-Type set to A_RESOURCE_TYPE_VALUE and Result Content set to 0 (nothing) and Content attributes representation } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/012_01 | TS-0001 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/012_02 | TS-0001 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/BV/012_03 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/BV/012_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/BV/012_05 | TS-0001 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/BV/012_06 | TS-0001 10.2.11.2 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/013 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only hierarchichal address of TARGET_RESOURCE_ADDRESS resource when the Result Content is set to 2 (hierarchical address) |
| Reference | TS-0001 8.1.2, 8.1.3 &10.1.1.1, TS-0004 6.3.4.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource-Type set to A_RESOURCE_TYPE_VALUE and Result Content set to 2 (hierarchical address and attributes) } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) and Content attribute containing Hierarchical address representation of the created resource } | IUT  AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/013_01 | TS-0001 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/013_02 | TS-0001 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/BV/013_03 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/BV/013_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/BV/013_05 | TS-0001 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/BV/013_06 | TS-0001 10.2.11.2 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/014 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only attributes and hierarchichal address of TARGET_RESOURCE_ADDRESS resource when Result Content is set 3 (attributes and hierarchichal address) |
| Reference | TS-0001 8.1.2, 8.1.3 &10.1.1.1, TS-0004 6.3.4.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource-Type set to A_RESOURCE_TYPE_VALUE and Result Content set to 3 (attributes and hierarchichal address) } | IUT  AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2001 (CREATED) and Content attribute containing Both hierarchical address representation of the created resource and attributes representation } | IUT  AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/014_01 | TS-0001 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/014_02 | TS-0001 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/BV/014_03 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/BV/014_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/BV/014_05 | TS-0001 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/BV/014_06 | TS-0001 10.2.11.2 | 23 (subscription) |

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

“If the Result Content is invalid for a given operation (Refer TS-0001 Table 8.1.2-1: Summary of Result Content Values) then the Hosting CSE shall reject the request with a Response Status Code indicating "BAD_REQUEST" error.

”