| Input Contribution |
| --- |
| Meeting ID* | TST 26 |
| Title:* | TS-0028-Security Test Purposes contribution (Rel2) |
| Source:* | Easy Global Market |
| Uploaded Date:* | 2016-12-03 |
| Document(s) Impacted* | TS-0028 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes some additional TPs for the TS-0028 – Security Test Suite Structure and Test Purposes, Release 2.

Proposal

================ Start of  1st  Part: Test Purposes ==================

| TP Id | TP/oneM2M/CSE/SEC/BV/001 |
| --- | --- |
| Test objective | Check that the IUT sends a new ESPrimRandObject when the old one is expired |
| Reference | TS-0003 8.4.2 – step B.2C.2, TS-0004 7.5.1.2.11 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with AE and the AE obtained e2eSecInfo resource from IUT with a Suid set to {13,23,33,43} and sharedReceivedESPrimRandObject with esprimRandExpiry expired } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY request from AE containing To set to CSE-ID and From set to AE-ID and Content containing securityInfo containing securityInfoType set to 3 } | IUT ( AE |
|  | then { the IUT sends a notification Response/Request message containing Content containing securityInfo containing securityInfoType set to 4 and esprimRandObject set to a generated ESPrim Object } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/SEC/BV/002 |
| --- | --- |
| Test objective | Check that the IUT can retrieve the list of security features available on the CSE |
| Reference | TS-0003 8.4.2 – step B.2B |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with AE and the IUT having created a resource e2eSecInfo and the AE having privileges to perform RETRIEVE operation on the resource e2eSecInfo } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to CSE-ID/e2eSecInfo and From set to AE-ID and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributeList containing e2eSecInfo } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/SEC/BV/003 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when there is no e2eSecInfo attribute |
| Reference | TS-0003 8.4.2 – step B.2B |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to CSE-ID/e2eSecInfo and From set to AE-ID and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

================ End of  1st  Part: Test Purposes ==================

# Comments

This structure doesn’t exist in the XSD, but it is mentioned multiple times in TS-0003 and TS-0004.

Here should be at least one of those 4, depending on what the IUT is supporting.

This is not clear in TS-0004, once it is stated “… the Receiver sends a notification response…”, then it states “… in the Notify request primitive”

As before, it doesn’t exist in XSD

Is it necessary to check if the ACP will allow this or should be RETRIEVE-able by default?

As before, it doesn’t exist in XSD